USERS displays a short list of who's logged into the system, or
another VAX/VMS system reachable by DECnet-VAX.  It is written in
in MACRO-32 for use on a VAX/VMS V3.x system.  No optional
software products are required for compilation; a DECnet license
is needed for multi-node operation.  WORLD privilege is required
to obtain information via the $GETJPI system service; NETMBX is
required to establish a DECnet connection.  The image is normally
INSTALLed with WORLD privilege (this can be cured, see below).

This directory contains the following files:

	USERS.DOC	This
	USERS.HLP	HELP text
	USERS.MAR	Source code
	USERS.OPT	LINK options

Compilation/Installation:

(do this once)
	$ MACRO USERS
	$ LINK/NOTRACE/EXE=SYS$SYSTEM: USERS,USERS/OPT
	$ SET PROT=(S:RWED,O:RWED,G:RWED,W:RE) -
	  SYS$SYSTEM:USERS.EXE
	$ DELETE USERS.OBJ;
(do this once and add to your site-specific startup procedure)
	$ MCR INSTALL
	USERS/PRIV=WORLD
	^Z

It is suggested that you define USERS as a foreign command via
SYS$SYLOGIN:

	$ U*SERS:==$USERS

Note: It is not necessary for USERS.EXE to reside in SYS$SYSTEM.
Should you decide to place USERS.EXE somewhere else these
procedures should be modified accordingly.  You may also need to
raise the SYSGEN parameter KFILSTCNT to accomodate an additional
known file listhead.

Installing the help file:

We do not recommend altering SYS$HELP:HELPLIB.HLB.  In a V3.1 or
later system
(do this once)
	$ LIBRARY/HELP/CREATE SYS$HELP:LOCAL USERS
(do this once and add to your site-specific startup procedure)
	$ ASSIGN/SYSTEM LOCAL HLP$LIBRARY
will create a secondary help library that will not conflict with
DIGITAL's.


Highly optional stuff to do:

It is possible to make USERS a "true" command (as opposed to a
"foreign" command).

(do this once)
	$ CREATE USERS.CLD
	DEFINE VERB USERS
		IMAGE USERS
		PARAMETER P1,VALUE(TYPE=$INFILE)
	^Z
	$ SET COMMAND/TABLES=SYS$SHARE:DCLTABLES-
	  /OUTPUT=SYS$SHARE:DCLTABLES USERS

It is also possible to eliminate the need to INSTALL USERS (and
similar programs) by fixing what is widely regarded as a VMS
stupidity, namely the privilege restrictions on $GETJPI.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
* THE FOLLOWING IS OFFERED FOR INFORMATIONAL PURPOSES ONLY.  IT *
* IS NOT REQUIRED FOR SUCCESSFUL USE OF THIS SOFTWARE.  AS WITH *
* ANY CUSTOMER PATCH TO DIGITAL-SUPPLIED SOFTWARE, INSTALLATION *
* MAY VOID YOUR SOFTWARE WARRANTY.  USE AT YOUR OWN RISK!!!	*
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

All process control services share a common routine (EXE$NAMPID)
to map process id/process name into PCB address.  Thus the purely
informational $GETJPI service is subject to the same privilege/
association restrictions as the potentially dangerous ones.
This modification eliminates the need to install images with
elevated privileges resulting in a savings of system resources
as well as reducing the likelyhood of a malicious user illicitly
obtaining privileges sufficient to interfere with system operation.
Some programs that previously had to be implemented as privileged
images can now be coded as DCL command files using the F$GETJPI and
F$PID lexical functions.

The DEC-distributed system image must be preserved in order to
apply upgrades.  Minor releases "contain patches to the system
image rather than a reassembled and relinked executive" hence
this procedure should not require modification until the next
major release of VAX/VMS.  Upgrades should be performed on an
unmodified system and this patch reapplied.  V3.x only!!!

	[ Log in as SYSTEM ]
	$ SET DEFAULT SYS$SYSTEM
	$ PATCH SYS
	SET ECO 97
	SET PATCH_AREA 8000C452
	REPLACE/I 8000A124
	'CMPW W^8A(R2),W^8A(R4)'
	EXIT
	'CMPL (SP),#80009FEC'
	'BEQL 8000A132'
	'CMPW W^8A(R2),W^8A(R4)'
	EXIT
	UPDATE
	EXIT
	$ RENAME SYS.EXE.-1 *.DEC.*  ! Or don't PURGE!

*** WARNING ***  Do NOT delete SYS$SYSTEM:SYS.DEC.  If DEC
distributes patches to the system image in the future you will
need to delete the new SYS.EXE and RENAME SYS.DEC back to
SYS.EXE before applying the upgrade.

Type @SYS$SYSTEM:SHUTDOWN to shut down the system.  The new
SYS.EXE will be used after you reboot.

				Eric P. Scott
				Mail Stop 171-235
				Jet Propulsion Laboratory
				4800 Oak Grove Drive
				Pasadena, CA  91109
				(818) 354-6518 (FTS) 792-6518
				<EPS@JPL-VLSI.ARPA>