USING FPAINT SCREENS: AN EXAMPLE APPLICATION

                                                                     Page 1


     Using FPaint Screens - general considerations


          FPaint builds a  package  of  FORTRAN  subroutines  that  may  be
     considered  the  abstraction  of a data entry screen.  Each screen has
     the following characteristics:

          - A five character name ( referred to below as <NAME> )

          - A specific height (in rows) and width (in columns)

          - A number of fixed text fields

          - A number of data fields of varying characteristics

          - A screen help line



     In addition, the following operations may be performed on a screen:

          - Clear        - clear the area occupied by the screen

          - Display Text - display screen text

          - Display Data - display screen data field contents

          - Edit         - begin edit of screen data fields

          - Validate     - validate all screen data fields


          Using an FPaint screen successfully therefore depends on invoking
     the  above routines properly and in the correct order.  The first task
     is thus to examine each routine in detail.


     FPaint Screen Operations - A Detailed Description


     Clear

     The Clear operation is invoked as

     call <NAME>Clear( Row, Col )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner.

     Clear causes the rectangular area of the CRT occupied by the screen to
     be erased.  The given area extends from rows "Row" to "Row"+Height and
     from columns "Col" to "Col"+Width.

                                                                     Page 2


     Text Display

     The Text Display operation is invoked as

     call <NAME>TextDsp( Row, Col )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner.

     Text Display causes all screen text fields to be displayed on the  CRT
     relative the the screen origin.


     Data Display

     The Data Display operation is invoked as

     call <NAME>DataDsp( Row, Col, {Data} )

          where Row and Col give the origin of the upper left of the screen
          in rows and cloumns on the CRT relative to the upper left corner,
          and {Data} is the list of variables that correspond to the FPaint
          data fields.

     Data Display causes the current values of all screen data fields to be
     displayed  on  the  CRT relative the the screen origin.  Note that all
     data should be initialized prior to invoking this routine.


     Edit

     The Edit operation is invoked as

     call <NAME>Edit( Row, Col, CurrentField, TermKeys, {Data},
                      Next, Previous, Refresh, Exit, LastKey )

          where,

          Row and Col give the origin of the upper left of  the  screen  in
          rows and cloumns on the CRT relative to the upper left corner;

          CurrentField is, on input, the field at which editing is to begin
          and, on output, the last field edited;

          TermKeys is a 30 element integer*2 array to be discussed later;

          {Data} is the list of variables that  correspond  to  the  FPaint
          data fields;

          Next is a termination flag that indicates a  carraige  return  or
          down arrow was pressed during edit of the last field;

          Previous is a termination flag that indicates  an  up  arrow  was
          pressed during edit of the first field;

                                                                     Page 3


          Refresh       is a termination flag  that  indicates  the  screen
          image should be refreshed;

          Exit is a termination flag that indicates the edit is complete;

          LastKey is the last key typed by the operator.

     The Edit operation initiates data entry or edit of the  entire  screen
     beginning  with  the  current  field.   This operation continues until
     terminated by the operator.

     Edit is terminated by any one of the following events:

        - The operator presses a carriage return  or  a  down  arrow  while
          editing the last field of the screen.  In this case, Next is set,
          which, for multi screen  applications,  means  "go  to  the  next
          screen".

        - The operator presses an up arrow while editing the first field of
          the  screen.   In  this  case,  Previous is set, which, for multi
          screen applications, means "go to the previous screen".

        - The operator presses control R.  In this case,  Refresh  is  set,
          which  means  "refresh  the  entire  screen  image".  This may be
          necessary if, during data entry, a system message  covers  up  an
          area of the screen.

        - The operator presses control Z.  In this case, Exit is set, which
          means "data entry/edit is complete".

        - The operator presses a programmer defined termination key ( named
          TermKeys  in  the  Edit  parameter  list ).  No flags are set but
          LastKey holds the ASCII value of the pressed key.


     Programmer Defined Termination Keys


          As mentioned above, a special set  of  keys,  called  termination
     keys,  may  be  defined  by the programmer.  During an edit operation,
     pressing one of these keys causes the edit  to  terminate.   A  thirty
     element integer array contains the termination key information.

          As if to complicate things, two types  of  termination  keys  may
     reside in the array simultaneously as separate lists.  These two types
     will be refered to as edit termination keys and immediate  termination
     keys.

          When an edit  termination  key  is  pressed,  FPaint  checks  the
     validity  of  the  current  field  being  edited.   If valid, the edit
     terminates, otherwise an error message is issued and edit continues.

          An immediate termination key, as  its  name  implies,  causes  an
     immediate  and  unconditional termination of the edit.  A possible use
     for such a device might be that of popping up a help screen to give an

                                                                     Page 4


     operator  additional  assistance  upon  demand.   Another  obvious use
     includes the aborting of an operation.

          The  result  of  immediate  termination  is  slightly   different
     depending  on whether or not the current field is numeric.  If, during
     the edit of a numeric data field,  an  immediate  termination  key  is
     pressed,  the  edit  is,  in  effect, aborted and the partially edited
     value lost.  A non-numeric data field  retains  the  partially  edited
     value.

     Important:  It is the programmers responsibility to reenter  the  edit
     routine after processing an immediate termination key without changing
     the edit state.

          The structure of the termination key array is best  described  by
     example.   Figure  1 shows the logical contents of the termination key
     array.  In addition, an example is given below.


     Example 1  A possible array of termination keys

     TermKeys(1) = 4           { 4 edit termination keys }
     TermKeys(2) = 1           { ^A }
     TermKeys(3) = 141         { PF1 }
     TermKeys(4) = ichar('?')  { ? }
     TermKeys(5) = 4           { ^D }

     TermKeys(6) = 2           { 2 immediate termination keys }
     TermKeys(7) = 142         { PF2 }
     TermKeys(8) = 143         { PF3 }

     Appendix III contains the numeric values of function and keypad keys.


     Integrating the Operations


          Having fully described each screen operation, the next  objective
     is  the  synthesis  of  a  working  FPaint  screen.   In  general, the
     following logic is employed:

          - Choose an appropriate origin for the screen.

          - Define all termination keys.

          - Initialize all screen data fields.

          - Clear the screen.

          - Display the screen text.

          - Display the screen data.

          - Perform the edit operation starting with a given field number.
            On return from the edit, process the termination flags and




	   Array Element	Contents
	   -------------	--------

	        1               Number of Edit Termination Keys, NE
		2		Edit Termination Key 1
		3		Edit Termination Key 2
		.			.
		.			.
		.			.
	       1+NE		Edit Termination Key NE

	      (NE+2)		Number of Immediate Termination Keys, NI
	      (NE+2)+1		Immediate Termination Key 1
	      (NE+2)+2		Immediate Termination Key 2
		.
		.
		.
	      (NE+2)+NI		Immediate Termination Key NI


                       Figure 1. Termination Key Array.





	   Program Profilometer

	   Initialize Terminal Routines

	   Display Specimen Group Information

	   Repeat

	     Get Specimen Group Information

	     Repeat

	       Display and Get Specimen Information

	       Collect and Plot Test Data

	       More Specimens?
	         if Yes then Display Specimen Group Information

	     Until No More Specimens

	     Another Specimen Group?

	   Until No More Specimen Groups

	   Program End


                       Figure 2. Main program pseudo code.

                                                                     Page 5


            keys.

          - Insure that all data is valid ( If not, repeat the edit
            operation starting with the invalid field ).

     Rather than elaborating on the above, a specific example will be
     considered in detail.


     Example Program Description


          Appendix I contains the listing of a  program  that  incorporates
     two FPaint screens to perform operator input.  It is based on a system
     that is used to acquire data from a device capable  of  measuring  the
     surface  roughness  of  a  steel specimen.  The example presented here
     serves  merely  to  illustrate  the  use  of  FPaint  screens  in   an
     application;   the  routine  that would perform any useful work is, of
     course, a stub.

          Presumably, an operator runs the program to measure the roughness
     of  a group of replicate specimens.  Data entry is made at two levels.
     First, information common to all  specimens  is  entered  through  the
     FPaint  screen  named Group.  Then, before each specimen is processed,
     the specimen ID and orientation is entered through the  FPaint  screen
     named Spec.

          The operator may enter individual specimen information repeatedly
     until all replicates of a given group have been processed.  The choice
     is then made either to exit the program or  repeat  the  process  with
     another group of specimens.

          Figure 2 outlines the program logic and processes.



     The FPaint Screens


          Before considering the details of the  FPaint  interface,  it  is
     worthwhile to examine the screens individually.

          Group is the specimen group screen and  Spec  is  the  individual
     specimen screen.

          The final composite screen (from the operator's  point  of  view)
     includes  Group  with  the  upper left corner origin at (1,1) and Spec
     with origin at (11,39).


     A Detailed Examination of the Example


          As mentioned previously, Appendix I contains the  listing  of  an
     example program, Profil.For.  The following is detailed examination of

                                                                     Page 6


     the FORTRAN source code.

     Lines 10-180 contain declarations  for  the  Group  screen  variables.
     Notice the similarity to the declarations given in the Group auxillary
     file listed in Appendix II.

     Lines 210-290 contain declarations  for  the  Spec  screen  variables.
     Notice  the  similarity to the declarations given in the Spec auxilary
     file listed in Appendix II.

     Lines 320-350 contain declarations for local variables.

     Lines 620-930 serve to initialize  constants  and  variables.   Notice
     that screen variables must be initialized in the application.

     Lines 1220-1250 deserve special attention.

          TTYinit must be called before any FPaint  operation  is  invoked.
     This  is especially true for a VAX hosted system.  TTYinit initializes
     both the display and a package of display routines.  It  may  also  be
     called during program exit to clean up the display state.

          EchoOff  should  be  called  in  DEC-10  environments.   It  will
     eliminate any problems associated with echoed type ahead.

          KpdOn may be called to place the terminal in  keypad  application
     mode.  Note that it is not necessary in this application.

     Line 1300:  First field to edit for Group screen is 3.

     Line 1320:  Clear the Group screen.

     Line 1340:  Display the Group screen text.

     Lines 1360-1390:  Display the Group screen data.

     Line 1430:  Start of loop "repeat until no more specimen groups".

     Lines 1470-1690:  Edit the Group screen  starting  with  field  three.
     Process the termination state as follows:

          [1520] if the operator pressed PF1 ( abort ) then  turn  off  the
          key pad, clear the screen, and stop program;

          [1570] if "go to next screen" ( i.e.  Next is set )  then  simply
          wrap to field number three of the same screen;

          [1600] if "go to previous screen" ( i.e.  Previous is set )  then
          simply wrap to the last field;

          [1630] if "screen needs to  be  refreshed"  goto  100  to  clear,
          redisplay, and continue the edit of Group.

          [1690] if "data entry/edit is not complete" goto 300 to  continue
          the edit.

                                                                     Page 7


     Line 1830:  First field to edit for Spec screen is 1.

     Line 1860:  Start of loop "repeat until no more specimens".

     Line 1900:  Clear the Spec screen.

     Line 1920:  Display the Spec screen text.

     Lines 1940-1960:  Display the Spec screen data.

     Lines 1980-2000:  Edit  the  Spec  screen  starting  with  field  one.
     Process the termination state as follows:

          [2020] if "go to next screen" ( i.e.  Next is set )  then  simply
          wrap to field number one of the same screen;

          [2050] if "go to previous screen" ( i.e.  Previous is set )  then
          simply wrap to the last field;

          [2080] if "screen needs to be refreshed" then clear and redisplay
          the  Group  screen  and  then  goto  400 to clear, redisplay, and
          continue the edit of Spec.

          [2200] if "data entry/edit is not complete" goto 500 to  continue
          the edit.

     Line 2230:  This is the call to some routine that  would  utilize  the
     FPaint  input  and perform some useful work.  The routine is a stub in
     this example ( see the listing of Subs.For in Appendix I ).

     Line 2260:  Ask operator if more specimens are to be tested  for  this
     group ( see the listing of Subs.For in Appendix I ).

     Lines 2280-2360:  If more specimens for  this  group  then  clear  and
     redisplay  the  group  screen ( just for looks ).  As the loop repeats
     the specimen screen will again be overlayed on the group screen.

     Line 2440:  End of loop "repeat until no more specimens".

     Line 2470:  Ask operator if more groups of specimens are to be  tested
     ( see the listing of Subs.For in Appendix I ).

     Line 2500:  End of loop "repeat until no more specimen groups".

     Lines 2530-2550:  Key pad off, clear screen, and terminate program.


     Custom Validation of FPaint Data Fields


          Appendix I contains a listing of the file Subs.For, a  collection
     of  subroutines  called  by  the example program.  Of interest to this
     discussion is the routine ValScr.

          Whenever the edit of an FPaint data field is  completed  ( either

                                                                     Page 8


     as  a  result  of  moving  to another field or terminating the edit ),
     validation is performed as prescribed when the field was created.   In
     addition,  if  the  data  field  passes  the  FPaint  validation,  the
     subroutine ValScr is called in order that  custom  validation  may  be
     performed by the application.

          ValScr is present in the standard FPaint library as a  stub  that
     sets  the  Valid  flag  true,  thus  imposing no additional validation
     constraints on the data.

          If a subroutine named ValScr is included in the  application,  it
     will  supersede  the  library  stub,  enabling custom validation to be
     performed.  See the example in  Subs.For  for  a  description  of  the
     parameters.   The  logic  of  any such custom routine should always be
     similar to the pseudocode given below:

       if Name is equal to the screen to be validated then

          if Field is equal to the field to be validated then

             check the value of Intg, Rl, or Str  depending  on  the  field
             type ( which is known a priori )

             if the value is OK then
               Valid = .true.
             else
               Valid = .false.
               display some appropriate error message via
               the routine ErrMsg
             end if

          end if

       end if


     FPaint From the User's Viewpoint


          Up to this point, the description of FPaint has  been  programmer
     oriented.   The application user, of course, is interested in the ease
     with which data may be entered and edited.

          Editing is performed at  two  levels.   Screen  editing  involves
     moving  from one field to another.  This is accomplished with the keys
     described below.

          Up arrow        - Move to the previous data field.
          Down arrow      - Move to the next data field.
          Carriage Return - Move to the next data field.

          Editing may also occur at the individual field level.   The  keys
     listed below perform field edit functions.

          Control B       - Move to beginning of field

                                                                     Page 9


          Control E       - Move to end of field
          Tab             - Move to next word
          Control X       - Move to previous word
          Control W       - Toggle insert/overwrite
          Control U       - Abort edit ( restore original value )
          Control J       - Delete to end of line
          Control K       - Delete word

          [Dec-10 or IBM PC]
          Backspace       - delete one character backward
          Del             - delete character at cursor

          [Vax]
          Del             - delete one character backward
          Key pad ,       - delete character at cursor
                            ( if the key pad is on )


          In addition to the editing keys, the function of  Control  R  and
     Control  Z  are worth repeating at this point.  They have the meanings
     given below.

          Control R       - Refresh screen image
          Control Z       - Data entry/edit is complete







		                  APPENDIX I


                           EXAMPLE PROGRAM LISTINGS







		See the files Profil.for and Subs.for







		                 APPENDIX II


                        FPAINT AUXILIARY FILE LISTINGS






		See the files Group.aux and Spec.aux







		                  APPENDIX III


                  NUMERIC CODES FOR FUNCTION AND KEY PAD KEYS







       KEY              NUMERIC CODE

       Up Arrow            128
       Down Arrow          129
       Left Arrow          130
       Right Arrow         131

       PF1                 141
       PF2                 142
       PF3                 143
       PF4                 144

       Key Pad 0           157
       Key Pad 1           158
       Key Pad 2           159
       Key Pad 3           160
       Key Pad 4           161
       Key Pad 5           162
       Key Pad 6           163
       Key Pad 7           164
       Key Pad 8           165
       Key Pad 9           166
       Key Pad -           167
       Key Pad ,           168       	( 8 for VAX version )
       Key Pad .           169
       Key Pad Enter       170

       Back Tab            132          ( generated by ^X )
       Del Char at Cursor  127		( generated by Del or Backspace )
       Del Char Backward     8		( generated by Backspace or key pad , )


	For IBM PC

	Keypad Keys

	Insert		    23	(^W)
	Delete		   127	(Del)
	Home		     2	(^B)
	End		     5	(^E)
	PgUp		   133
	PgDn		   134

	Function Keys	Un-Shifted	Shifted

	F1		   141	   	  151
	F2		   142	   	  152
	F3		   143       	  153
	F4		   144       	  154
	F5		   145       	  155
	F6		   146       	  156
	F7		   147       	  157
	F8		   148       	  158
	F9		   149       	  159
	F10		   150		  160