Name:	
	RMS_PARSE

Modifications:
	30-SEP-1987	Joe Bryan
	Creation.

Abstract:
	Provides a simple interface to the RMS $PARSE service.

Call format:
	RMS_PARSE	fil-spc ,fil-nam ,[def-nam] ,[field] ,[type]

Action:
	The RMS $PARSE service is called with the file-name and default-name
	fields as specified.  The field argument is used to specify which 
	components of the parsed file specification are to be returned in the 
	file-spec argument.  The type argument is used to set the NAM$B_NOP 
	field in the NAM block.

Return:
	RMS $PARSE service completion status.  If RMS$_ESS is returned, the 
	fil-spc output string was truncated.

Arguments:
	While all five arguments must be supplied, arguments 3, 4 and 5 may 
	be zero or blank.


	fil-spc

	VMS usage:	VMS file specification
	useage:		fixed length character string
	type:		write only
	mechanism:	by descriptor

	String that will receive the segment(s) of the parsed file specification
	requested by the field argument.  This argument must be specified.


	fil-nam

	VMS usage:	VMS file specification
	useage:		fixed length character string
	type:		read only
	mechanism:	by descriptor

	Primary components of file specification.  Any components not specified 
	will be filed in buy the def-nam string and process environment default.
	This argument must be specified.


	def-nam

	VMS usage:	VMS file specification
	useage:		fixed length character string
	type:		read only
	mechanism:	by descriptor

	Default components of file specification.  Any components not specified
	by either the fil-nam or def-nam strings will be filled in by the 
	default file specification defined for the user's process (using the 
	DCL command SET DEFAULT <file-spec>).  If the def-nam string is blank 
	or this argument is zero, only the process default will be used.


	field

	VMS usage:	unsigned_byte 
	useage:		byte (unsigned)
	type:		read only
	mechanism:	by reference

	Bit mask that specifies the components of the parsed file specification
	that are to be returned in the fil-spc string.  These codes may be 
	or'ed together to return more than one component of the specification.
	If no bits are set or this argument is zero, the complete file 
	specification will be returned.

	The field codes are identical to the FSCN$M_<field> codes defined in 
	the $FSCNDEF modules.  The numeric values are listed below:

	File spec	Bit field	Decimal		Symbolic
	Field:		Offset		Value		Mask name
	-------------------------------------------------------------
	Node		0		1		FSCN$M_NODE
	Device		1		2		FSCN$M_DEVICE
	Root		2		4		FSCN$M_ROOT
	Directory	3		8		FSCN$M_DIRECTORY
	Name		4		16		FSCN$M_NAME
	Type		5		32		FSCN$M_TYPE
	Version		6		64		FSCN$M_VERSION


	type

	VMS usage:	unsigned_byte 
	useage:		byte (unsigned)
	type:		read only
	mechanism:	by reference

	Bit mask that specifies the type of parse to perform.  This argument is 
	used to set the NAM$B_NOP field in the NAM block.  If this argument is 
	zero, or no bits are set, the standard defaults will be used.

	These bit masks are defined in the $NAMDEF modules.  The numeric values 
	are listed below:

	Parse			Bit field	Decimal		Symbolic
	Type:			Offset		Value		Mask name
	-----------------------------------------------------------------------
	Perform syntax
	check only		3		8		NAM$M_SYNCHK

	Don't conceal
	device, directory
	logical			4		16		NAM$M_NOCONCEAL


Implicit arguments:
	None.

Side effects:
	None.

Function characteristics:
	AST re-entrant, shareable.