VMS Virtual Disk

Have you ever wanted to break up those 3 GB single volume disks?
Ever wanted to be able to put a few tens of thousands of blocks
into a temporary ODS1 structure? Wanted lots of volume ACLs but not
had volumes to use?
  This is the answer. VD: for VMS!
  VD: (vddriver) allows you to take a contiguous file on any VMS
volume and treat it as a complete disk volume of its own. You assign
a file to a VD: unit or deassign it using a privileged image, and
the driver will make the file look like a volume. Any normal VMS
commands will act as though VD: were just another attached disk
on your system.
  An earlier driver I did had serious design problems with multiblock
QIOs which this one fixes (sheepish grin) and this driver has been
tried on VMS V4.7 with no problems whatever. VMS V5 code exists and
is conditionalized by the VMS$V5 symbol. It has not yet been tested.
  This driver uses the same mechanism for controlling its host driver
that the MSCP server does, and should be able to work on any VMS
device, bar none, though I have not tried it with the MSCP server; some
"device ID" strings may not be quite right as I have them. They
represent my best guess as to a servable disk however.
  I have executed images from VD:, written to it, read from it, and
compared files on the host disk with virgin copies to make sure nothing
was corrupted. All works as it should. Tests were done on a VAX11/750
running VMS 4.7. Tests were also done on a uVax 2000 running VMS 4.6 with
4 MB memory. Note that analyze/disk reports spurious errors, but the
disk appears intact for all that. I suspect that it looks at the
device type (rp06) and assumes real rp06 geometry, which VD: definitely
lacks. VD: has more sectors/track than DEC disks and this could also be
confusing analyze/disk. Nothing else seems to have trpuble.

	Generation:

	Use the command file VDMAKE.COM to assemble and build the
VD: driver. Comments therein describe how to use SYSGEN to actually
load the driver. I assume you can copy VDDRIVER.EXE into sys$system.
	You must set command asnvd.cld before using ASNVD.EXE, and
you MUSH have the CMKRNL privilege to use it, or install ASNVD
with that privilege. This is needed to access the host and the VD:
UCBs. You need to be able to read file attributes of the container
file also.
	ADVD/ASSIGN VDn: device:[directory]file.type
		assigns the file to device VDn:
	ADVD/DEASSIGN VDn:
		deassigns the file from device VDn:

Note that the file is NOT locked. Nor does ADVD know how to create
the file. Another limitation of the system as presented here is that
ASNVD has a hardwired physical disk structure of 64 sectors/track,
1 track/cylinder, and as many cylinders as needed to cover the file.
This means that the container file will be used only out to the
last integral multiple of 64 blocks. Another structure can be generated,
as VDDRIVER does not care, but the ASNVD image lacks such niceties. To
produce images of physical disks, you may want to make modified versions
of ASNVD to reflect their physical structure. The structure chosen was
designed to allow fairly large virtual disks with only one filestructure.
	You need to edit VDDRIVERV3.MAR if you want to increase the
number of units beyond the default maximum of 8. The program works by
using a hook in VMS I/O postprocessing that calls code in VDDRIVER
when doing postprocessing. The hook is that if IRP$L_PID in an IRP
is negative, the iopost interrupt does a JSB to that address rather
than any postprocessing. VDDRIVER saves the original IRP$L_PID,
stuffs its own postprocessor address there (one address per unit, hence
a table of entries), and queues the packet to the host. On host I/O
completion, the packet comes back to VD: which restores IRP$L_PID
and performs normal I/O completion in the context of the VD: driver.
This means that all completion processing, including multipart virtual
I/O and page/swap I/O is done correctly regardless of how many
parts are needed. Since the MSCP server uses this hook also, it is
likely to remain in VMS indefinitely. It offers interesting possibilities
for building VD: versions that do shadowing or encryption, since
control is returned after the I/O also. The method is clean and has
no problems operating. Since the I/O packet is operated on directly,
it does NOT impose QIO overhead twice, and is fairly efficient.

	I would like to ask anyone willing to test VD: in VMS V5.x
systems to please try it out and let me know what if anything is
needed. I have done my best to insert VMS V5.x code here, but
have not the facilities for a complete test locally.
	Thank you
Glenn Everhart
Everhart%Arisia.decnet@crd.ge.com	Arpanet
Everhart@Arisia.ge.com			uucp
voice: 215 354 7610 office    215 358 3866 home




Performance:

VD: is very fast...fast enough to be used in production environments in a
routine way. It adds a few instructions to each QIO$ but needs no extra
context switches. In effect it calls the real driver as a subroutine (though
this isn't exactly the detail...look at the source!) and avoids any operations
that will give delays. There is a fair amount of "defensive code" added to 
make sure it can't mess anything up either. This has made it fairly easy
to get working under VMS 5.x at other sites.
  VD: could be modified easily to do writes to a pair of containers (and
perhaps alternate between containers on read). There's no logic here for
a catch-up mode, though, so containers MUST start out alike. A catchup mode
would need to ensure that the driver did a read/write from one disk to
the other as a single operation. This could perhaps be added as a special
operation, keeping the VD: unit busy until both operations were done. Such
is needed to fully implement shadowing in software. (Non-atomic read/writes
could encounter standard database update problems of noninterlocked writes.)
  Sometime I may do this, or may advise others in doing so.
  You the reader are invited to beat me to it.