VAX/VMS Implementation

   When implementing a blackboard system, several key ideas must be kept in
mind:

   The blackboard data structure must permit efficient read/write access
      to a multitude of knowledge source programs written in different
      languages and possibly running in parallel.
   The agenda data structure will receive response frames from knowledge
      sources possibly running in parallel.  The response frames must be
      available to the scheduler.


   The monitor program must be able to invoke knowledge source programs
      possibly in parallel.

Onto this list one should add the following:

   To make the implementation easier, VMS services should be used whenever
      possible.

Note in the following sections, FORTRAN code will be listed to assist in
describing the implementation.  For a complete listing of the system, refer
to [KMSKIT.BLACKBOARD] in the DECUS 1990 Spring Symposia Tape.  For further
elaboration on methods, mechanisms and VMS system services, see [9, 10, 11].


Implementing the Blackboard

   The blackboard is a global database which permits process to process
communication.  It will be created when the blackboard system starts up, will
stay in existence during the blackboard application and disappear when the
blackboard application terminates.

   VMS supports two mechanisms for sharing memory resident data among
processes:

   1. Global sections
   2. Logical names


Global Sections

   A global section is a set of continuous pages in memory which can be
shared among processes.  In its simplest form the global section is nothing
more than an installed COMMON block which is referenced by two or more
programs.

   For the blackboard application, global sections have two disadvantages:

   1. Data sharing among knowledge sources written in different languages
        may be difficult.
   2. Global sections are fixed in size.

   One of the advantages of a blackboard system is that the knowledge
sources can be written in the language which best supports them.  However, a
global section that contains dynamic data structures consisting of variant
records written by a knowledge source coded in PASCAL, may be next to
impossible to manipulate by a knowledge source written in LISP.

   Once the global section is created and mapped, its size cannot change.
This requires you to know beforehand the maximum amount of memory the
blackboard application will require.  Due to the nature of knowledge source
interaction, you may not be able to calculate the worst case amount.  If you
request more than what is needed, you have wasted space.  If you don't create
enough space, the system will halt.


Logical Names

   A logical name is a user specified character string that is equivalenced
to another character string.  Logical names and their equivalenced names have
a maximum length of 255 characters.  Logical names are contained in logical
name tables.  Logical names can be shared among processes by placing them in
a shared logical name table.

   For the blackboard system, logical names offer a number of advantages:

   1. They can be read and written by system service routines and therefore
        are accessible to any VAX language.
   2. Access time is very short.
   3. From our point of view, logical name tables are dynamic in size.

   The biggest disadvantage to logical names is that they can only be
equivalenced to character strings that are no more than 255 characters long.
This means that numeric values must be encoded to, and decoded from ASCII.
Values longer than 255 characters must either be split up into multiple
logical names or reside in a disk file whose name resides in a logical name.
Even with these disadvantages, the benefits of using logical names for the
blackboard outweigh both their disadvantages and the advantages of global
sections and hence are used in this implementation.  Note - if the knowledge
sources can be restricted to a single language, global sections may be a
better choice.

   To create the logical name table called 'BLACKBOARD' in the system
directory table (which makes it shareable among processes), the instruction:
<bb=1><font=9><ps=10>

   return_status = SYS$CRELNT ( LNM$M_CREATE_IF, , , , 0, 'blackboard',
   
'LNM$SYSTEM_DIRECTORY' )

is executed when the blackboard system starts up.   The attribute
LNM$M_CREATE_IF prevents creation if the logical name table already exists.
Since the blackboard resides in the system directory, the creating process
needs the SYSPRIV privilege or write access to the system directory to
guarantee creation.

   When the blackboard system terminates,  the instruction:
<bb=1><font=9><ps=10>

   return_status = SYS$DELLNM ( 'LNM$SYSTEM_DIRECTORY', 'blackboard',
                                                       %REF ( PSL$C_SUPER )
)

will delete the logical name table.  It is executed when the blackboard
system terminates.  Including the access mode PSL$C_SUPER insures the table
is deleted when the instruction executes.  As with table creation, the
deleting process must have the SYSPRIV privilege.

   We now require routines to read/write data from/to the blackboard.  The
following subroutine will set the IDENTIFIER to the VALUE in the blackboard:

   SUBROUTINE put_blackboard_data ( identifier, value )

   INTEGER*4 return_status
   CHARACTER*(*) identifier, value

   return_status = LIB$SET_LOGICAL ( identifier, value, 'blackboard', , )
   RETURN
   END

   Likewise, the following routine will return the VALUE of the IDENTIFIER
stored in the blackboard:


   SUBROUTINE get_blackboard_data ( identifier, value, value_length )

   INCLUDE '( $LNMDEF )'/NOLIST

   INTEGER*2 value_length
   INTEGER*4 return_status
   CHARACTER*(*) identifier, value

   STRUCTURE / item_list_record /
         INTEGER*2 buffer_length
         INTEGER*2 item_code
         INTEGER*4 buffer_address
         INTEGER*4 return_length_address
         INTEGER*4 terminator
   END STRUCTURE

   RECORD / item_list_record / item_list

   item_list.buffer_length = 255
   item_list.item_code = LNM$_STRING
   item_list.buffer_addr = %LOC ( value )
   item_list.return_length_addr = %LOC ( value_length )
   return_status = SYS$TRNLNM ( LNM$M_CASE_BIND, 'blackboard', identifier,
                                ,item_list )
   RETURN
   END

The $TRNLNM instruction can return different attributes of logical names
(e.g. length, index level, table name, equivalenced name, etc).  The
ITEM_LIST record describes the information that SYS$TRNLNM is to return, in
this instance the equivalence name.  The attribute LNM$M_CASE_BIND signals to
the translate to ignore character case in the identifier name (e.g. CaPiTaLs
= cApItAlS).


Implementing the Agenda

   The agenda is a list of knowledge source right-hand sides that can be run
at any given point in time.  They are ordered such that the highest rated
right-hand side will contribute the most to solving the particular problem.
As outlined in section 4.0, a number of quantitative values can be
incorporated into the rating.  In this implementation, the values the
knowledge source left-hand sides need to transfer to the agenda include:

   The number of left-hand side conditions satisfied
   Then name of the right-hand side program
   A qualitative value indicating how important the right-hand results are
      to furthering the problem solving (certainty) on a scale of 0 to 100.
   The approximate running time in seconds of the right-hand side.

Once these items have been  transferred from the knowledge sources to the
agenda, the scheduler can compute the rating and order them.

   As with the blackboard, the agenda is created when the blackboard system
starts up, stays in existence during the blackboard application and
disappears when the blackboard application terminates.  The difference from
the blackboard database is that the agenda is cleared after the scheduler has
invoked the highest ranked right-hand side program.  As an additional
constraint, the agenda must be able to handle any number of left-hand side
programs writing to it at the same time.  

   VMS supports two mechanisms for exchanging messages among processes:

   Mailboxes
   DECnet-VAX network links

In this implementation, knowledge sources will only run on one processor.
Therefore, using DECnet-VAX network links to exchange data need not be
considered.

   Mailboxes are a record-orientated pseudo I/O device that can hold
messages written by one or more processes for reading by one or more
processes.  Mailboxes can operate on one of two modes: synchronous or
asynchronous.  In synchronous mode, once a message is sent to the mailbox,
that message must be read from the mailbox before the next message can be
sent.  In asynchronous mode, any number of messages can be sent to the
mailbox before they need to be read.  It is the asynchronous mode that will
allow the mailbox to accept response frames from knowledge sources running in
parallel.

   The left-hand side programs will write their response frames to a single
mailbox called AGENDA_MAILBOX.  We will let VMS take care of serializing
parallel writes.  After the last left-hand side program has completed, the
scheduler will read all the response frames from the mailbox.

   The instruction necessary to create the mailbox AGENDA_MAILBOX is as
follows:

   return_status = SYS$CREMBX ( , mailbox_channel, , , , , 'agenda_mailbox'
                              )

The channel assigned to the mailbox is returned in MAILBOX_CHANNEL.  This
instruction is executed when the system starts up.

   The mailbox is deleted when the system terminates.  To accomplish this,
the instruction:

   return_status = SYS$DELMBX ( %VAL ( mailbox_channel ) )

is executed.

   To write a response frame contained in the string variable
RESPONSE_FRAME, to the mailbox, each knowledge source left-hand side must
execute the following code:

   write_code = IO$_WRITEVBLK .OR. IO$M_NOW
   return_status = SYS$ASSIGN ( 'agenda_mailbox', mailbox_channel )
   return_status = SYS$QIOW ( , %VAL ( mailbox_channel ), %VAL (
                              write_code ), , , ,
                              %REF ( response_frame ),
                              %VAL ( LEN ( response_frame ) ), , , , )
   return_status = SYS$DELMBX ( %VAL ( mailbox_channel ) )

Note that the $DELMBX executed by the left-hand side does not delete the
mailbox from the application, but only removes access to it from the left-
hand side program.  The function code IO$M_NOW indicates we are writing and
reading mailbox messages asynchronously.

   Once the last left-hand side program has completed, response frames can
be read from the mailbox and inserted into the agenda.  The following code
segment will read a message from the mailbox attached to MAILBOX_CHANNEL and
put the message in the string RESPONSE_FRAME:

   STRUCTURE / io_status_block_record /
         INTEGER*2 status
         INTEGER*2 byte_count
         INTEGER*4 general_longword
   END STRUCTURE

   RECORD / io_status_block_record / io_status_block

   read_code = IO$_READVBLK .OR. IO$M_NOW
   DO WHILE ( io_status_block.status .NE. SS$ENDOFFILE )
         return_status = SYS$QIOW ( , %VAL ( mailbox_channel ), %VAL (
                                    read_code ), io_status_block, , ,
                                    %REF ( response_frame ),
                                    %VAL ( LEN ( response_frame ) ), , , , )
      :
      :
   END DO

Although a QIO instruction can be issued which will return the number of
messages in the mailbox, for simplicity the code simply reads the mailbox in
a loop and exits when the error SS$_ENDOFFILE is returned.


Implementing the Monitor

   The monitor performs initialization, termination and orchestrates the
knowledge sources and the scheduler to from a functioning system.  The
algorithm outlined in section 4.0 is coded as follows:

   PROGRAM blackboard

   INTEGER*2 chosen_ks
   LOGICAL*1 done

   CALL initialize_blackboard_system
   CALL read_ks_description_file
   DO WHILE ( .NOT. done )
         CALL execute_all_left_hand_sides
         CALL wait_for_lhs_completion
         CALL insert_responses_into_agenda ( done )
         IF ( .NOT. done )
            CALL resolve_agendas ( chosen_ks )
            CALL execute_chosen_ks ( chosen_ks )
         END IF
   END DO
   CALL exit_blackboard_system
   END

The routines are described in the following sections


initialize_blackboard_system

   Creates the blackboard logical name table and the agenda mailbox as
described in section 5.1.2 and 5.2.


read_ks_description_file

   This routine prompts the user to enter the name of a file which contains
a list of all knowledge source left-hand side program names.  The names are
checked for validity (e.g. a-z, A-Z, 0-9, $, _ ) and the .EXE files are
checked for existence.  If the knowledge source name passes all the tests, it
is entered into the knowledge source description table.  The format of the
table is as follows: 

   INTEGER*2 max_number_of_ks_names
   PARAMETER ( max_number_of_ks_names = 512 )

   STRUCTURE / ks_description_record /
         CHARACTER*31 ks_lhs_name
         INTEGER*4 ks_process_id
   END STRUCTURE

   RECORD / ks_description_record /
               ks_description_table( max_number_of_ks_names )


execute_all_left_hand_sides

   For each knowledge source in the knowledge source table, the following
spawn command is executed:  

   PARAMETER ( no_wait = 1 )

   return_status = LIB$SPAWN ( 'RUN ' //
                                ks_description_table( index ).ks_lhs_name
                                , , , no_wait, ,
                                ks_description_table( index ).ks_process_id )

The NO_WAIT parameter indicates that we do not want to wait for the
subprocess to complete.  Also note that the identifier of the process is
returned and saved in the knowledge source description table.


wait_for_lhs_completion

   Once all the left-hand side programs have been spawned, the system must
wait for all to complete.  To do this we simply loop through the list of
returned process identifiers (from above) and call the $GETJPIW
service.  If the status of the process is non-existent (SS$_NONEXPTR), we
know the process completed.  Mark it by replacing the process identifier with
a -1.  When all process identifiers are equal to -1, all left-hand side
programs have completed.  This is coded as follows:

   item_list.buffer_+length = 4
   item_list.item_code = JPI$_STATE
   item_list.buffer_address = %LOC ( subprocess_state )
   item_list.return_length_address = %LOC ( return_length )
   item_list.terminator = 0
   IF ( ks_description_table( index ).ks_process_id .NE. -1 ) THEN
         return_status = SYS$GETJPIW ( ,
                                   ks_description_table( index ).ks_process_id,
                                   , item_list, io_status_block, , )
         IF ( io_status_block.status .EQ. SS$_NONEXPTR ) THEN
               ks_description_table( index ).ks_process_id = -1
         END IF
   END IF

The ITEM_LIST record is the same as was used in GET_BLACKBOARD_DATA (section
5.1).


insert_responses_into_agenda

   This routine executes the code segment shown in section 5.2 to read the
response frames from the mailbox into the agenda.  The agenda data structure
is as follows:

   INTEGER*2 max_number_of_ks_names
   PARAMETER ( max_number_of_ks_names = 512 )

   STRUCTURE / ks_agenda_record /
         CHARACTER*31 ks_rhs_name
         INTEGER*2 number_conditions_matched
         REAL*4 cpu_time_sec, certainty_of_result
   END STRUCTURE

   RECORD / ks_agenda_record / ks_agenda( max_number_of_ks_names )


resolve_agendas

   Given an agenda filled with the names of knowledge source right-hand
sides, and for each, the parameters listed in section 5.2, this routine
applies the following formula:

   ranking = number_of_conditions_satisfied * 100 + certainty_of_result -
cpu_time_seconds

Once done, the routine goes through the list and returns the index of the
highest rated right-hand-side.


execute_chosen_ks

   Given a pointer to the highest rated knowledge source right-hand side,
this routine will invoke it using the code:
<bb=1><font=9><ps=10>

   return_status = LIB$SPAWN ( 'RUN ' //
                                ks_agenda( chosen_ks_index ).ks_rhs_name, , , )


exit_blackboard_system

   This routine deletes the agenda mailbox and the blackboard logical name
table using the code in section 5.1.2.


Building the blackboard

   The blackboard is constructed by running BUILD_BLACKBOARD.COM.  Since
routines refer to the include files as BLACKBOARD$DIR:..., this logical name
must be defined BEFORE the command file is run.


Blackboard logical names

   The file SETUP_BLACKBOARD_LOGICALS_SYMBOLS defines three logical names and
one symbol:

   DEFINE blackboard$dir kms$isgusr2:[schebor.submission.blackboard]
   DEFINE share_blackboard_utilities -
          kms$isgusr2:[schebor.submission.blackboard.lisp_support_routines]
   DEFINE ops5_support_dir -
          kms$isgusr2:[schebor.submission.blackboard.ops5_support_routines]
   blackboard :== RUN blackboard$dir:blackboard

These must be defined BEFORE anything (compiling,linking,running) can be done.
If few people will be using the system, place this code in their LOGIN.COM.
To enable the blackboard across the system, add the /SYSTEM parameter to the
DEFINE commands and execute them in SYSTARTUP_V5.COM.  The blackboard symbol
can be placed in SYSLOGIN.COM.

Notes on running the blackboard

   Since the blackboard logical name table resides in the system directory
(LNM$SYSTEM_DIRECTORY) it must be created by a process which has SYSPRV
i.e. either the user has SYSPRV or the user runs a priviliged command file.
Since the blackboard will spawn all the knowledge source left-hand-sides
in parallel, users must have appropriate values for MAXACCTJOBS, MAXDETACH
and MAXJOBS.  

Knowledge Source File Format

   When the blackboard starts up, the user is prompted to:

   Enter the knowledge source description filename:

   This file contains a list of all the knowledge source left-hand-sides
that are to be run.  The format is one knowledge source name per line.  For
example, the knowledge source file for the tic-tac-toe example is:

   display_board_lhs
   finish_tic_tac_toe_lhs
   get_computer_move_lhs
   get_human_move_lhs
   recognize_cat_win_lhs
   recognize_win_lhs
   start_tic_tac_toe_lhs

Any number of spaces may preceed the filename.  If no extension is given,
then .EXE is assumed.  The .EXE files should exist in the directory from 
which the blackboard system was started. The maximum number of characters
in a knowledge source name is a compile time constant defined in
BLACKBOARD_SYSTEM_PARAMETERS and is currently set to 31.  The maximum
number of knowledge sources is also a compile time constant in the above
mentioned file and is currently set to 64.