Alpha Miniloader Howto
  David A. Rusling, david.rusling@reo.mts.dec.com
  v0.3, 17th October 1995

  This document describes the Miniloader, a program for Alpha based sys-
  tems that can be used to initialize the machine and load Linux.  The
  Alpha Linux Miniloader (to give it it's full name) is also known as
  Milo.

  1.  What is Milo?

  On Intel based PC systems, the BIOS firmware sets up the system and
  then loads the image to be run from the boot block of a DOS file
  system.  This is more or less what Milo does on an Alpha based system,
  however there are several interesting differences between BIOS
  firmware and Milo, not least of which is that Milo includes and uses
  standard Linux device drivers unmodified.  Milo is firmware, unlike
  LILO, which relies on the BIOS firmware to get itself loaded.	 The
  main functional parts of Milo are:


  1. PALcode,

  2. Memory set up code (builds page tables and turns on virtual
     addressing),

  3. VGA initialisation code (simple ISA VGA or BIOS emulation code),

  4. Linux kernel code.	 This includes real Linux kernel code (for
     example, the interrupt handling) and ersatz or mock Linux kernel,

  5. Linux block device drivers (for example, the floppy driver),

  6. File system support (ext2),

  7. User inteface code (MILO),

  8. Kernel interface code (sets up the HWRPB and memory map for linux),

  9. Optional x86 emulator to initialize graphics cards.


  The following paragraphs describe these functional parts in more
  detail.


  PALcode can be thought of as a tiny software layer that tailors the
  chip to a particular operating system.  It runs in a special mode
  (PALmode) which has certain restrictions but it uses the standard
  Alpha instruction set with just five extra instructions.  In this way,
  the Alpha chip can run such diverse operating systems as Windows NT,
  OpenVMS, Digital Unix and, of course, Linux.	The PALcode that Milo
  uses (and therefore Linux itself) is, like the rest of Milo, freeware.
  It is derived from Digital's Evaluation Board software example Digital
  Unix PALcode..  The differences between the different PALcodes are
  because of differences in address mapping and interrupt handling that
  exist between the Alpha chips (21066 based systems have a different
  I/O map to 21064+2107x systems) and different Alpha based systems.


  For Milo to operate properly it needs to know what memory is
  available, where Linux will eventually be running from and it must be
  able to allocate temporary memory for the Linux device drivers.  The
  code maintains a memory map that has entries for permanent and
  temporary allocated pages.  It effectively discards itself as it
  passes control to Linux and tells Linux just what memory is available.
  This means that Milo is very frugal with memory and only reserves
  enough memory for the PALcode (8 pages) and the HWRPB and page tables
  (3 pages).  This leaves *most* of the memory in the system for Linux
  itself.


  The final act of the memory code is to set up and turn on virtual
  addressing so that the data structures that Linux expects to see are
  at the correct place in virtual memory.


  You have the choice of two forms of VGA initialisation.  There is
  standard, very simple ISA VGA initialisation code which is somewhat
  restrictive.	Milo also contains BIOS emulation code which allows it
  to run the on-board BIOS from video cards in order to properly
  initialise them.


  The x86 emulator that Milo uses to execute the BIOS initialization
  code found on graphics cards is basically an 8086 emulator with just
  enough 386 support to get some of the graphics cards initialized.


  Linux device drivers live within the kernel and expect certain
  services from the kernel.  Some of these services are provided
  directly by Linux kernel code, for example the interrupt handling and
  some is provided by kernel look-alike routines.


  Milo's most powerful feature is that you can embed unaltered Linux
  device drivers into it.  This gives it the potential to support every
  device that Linux does.  Milo includes all of the block devices that
  are configured into the Linux kernel that it is built against as well
  as a lot of the block device code (for example, ll_rw_blk()).


  The only supported file system at the moment is the EXT2 filesystem.
  This means that Milo can load Linux (or flash update utilities)
  directly off of real file systems rather than from boot blocks and
  other strange places.	 Gzip'd files are supported and these are
  recommended, particularly if you are loading from floppy which is a
  rather slow medium.


  Built into Milo is a simple keyboard driver which, together with an
  equally simple video driver allows it to have a simple user interface.
  That interface allows you to list file systems on configured devices,
  boot Linux or run flash update utilities and set environment variables
  that control the system's booting.  Like LILO, you can pass arguments
  to the Kernel.


  Milo must tell the Linux kernel what sort of system this is, how much
  memory there is and which of that memory is free.  It does this using
  the HWRPB (Hardware Restart Parameter Block) data structure and
  associated memory cluster descriptions.  These are placed at the
  appropriate place in virtual memory just before control is passed to
  the Linux kernel.


  2.  Pre-Built Standard Milo Images.

  If you are planning to run Linux on a standard Alpha based system,
  then there are pre-built "standard" Milo images that you might use.
  These (along with the sources and other interesting stuff) can be
  found on gatekeeper.dec.com in pub/Digital/Linux-Alpha/Miniloader.
  The images subdirectory contains a directory per standard system with
  Milo images starting with milo and having the following naming
  convention:


  1. bios - includes BIOS emulation code,

  2. floppy - contains only floppy drivers (explicitly *not* SCSI),

  3. arc - Windows NT ARC firmware loadable Milo image.


  The .floppy images are particularly useful when first powering up a
  non-standard system, for example to test a different SCSI driver.  You
  could use this Milo image to load Linux and see that the device
  drivers work correctly before embedding those drivers into Milo.


  Updateflash utilities are all called updateflash and use the same
  naming convention as Milo images.


  Files ending in .dd are full floppy disk images and should be written
  using rawrite.exe on DOS or dd on Linux.  Files ending in .gz are
  gzip'd to save space.


  3.  How To Build Milo.

  You build Milo seperately from the Kernel.  As Milo requires parts of
  the kernel to function (for example interrupt handling) you must first
  configure and build the kernel that matches with Milo that you want to
  build.  Mostly this means building the kernel with the same version
  number.  So, miniboot-1.3.31.tgz will build against
  linux-1.3.31.tar.gz.	Milo *may* build against a higher version of the
  kernel, but there again it may not.  In the remainder of this
  discussion, I assume that your kernel sources and object files are
  stored in the subtree at /usr/src/linux.


  Before you try to build Milo, you should note that you can build Milo
  in two basic ways, the first is with vmlinux embedded in it and the
  second is with Linux device drivers in it.  I suggest that you read
  the section on loading Milo before you answer this question, but
  embedding vmlinux into Milo makes the image too large for most
  flash/roms.


  To build Milo, change your working directory to the milo source
  directory and invoke make with:


	    make KSRC=/usr/src/linux config





  Just like the Linux kernel, you will be asked a series of questions



	    Make a WNT ARC loadable image (MINI_ARC) [n]



  Take the default and answer "n" as this option is not yet fully
  working and released (it will be).  The next question is:



	    Include BIOS emulation code (MINI_BIOSEMU) [y]





  You should answer yes if you have a video card that is of any type
  other than simple ISA VGA.  See the list at the end of this howto to
  see if your video card is known to be supported.  The next question
  asks you if you want to see Milo output (and input) echoed to the
  serial port of your system:



	    Echo output to the serial port' MINI_SERIAL_ECHO [y]





  It's a good idea to echo kernel printk to /dev/ttyS0 if you can.  If
  you can (and want to), then type "y", otherwise "n".


  You are now free to build Milo.  So go ahead and type:



	    make KSRC=/usr/src/linux.noname





  All being well, all of the images that this target requires will be
  built.  The following files are of interest:


     milo
	The main item on the menu.

     milo.rom
	A ROMable or FLASHable version of Milo.

     updateflash.gz
	This is a utility that can be loaded by Milo.  It can update the
	flash with a Milo image so that you don't have to boot from
	floppy or the network.	This contains a copy of Milo.

     mboot, bootm
	Used in building an SRM boot block floppy for systems that
	support them, such as Noname.


  4.  Supported Systems.

  Milo has been built and tested on the following systems (if you know
  of others than please do mail me):



  1. AXPpci33 (aka Noname)

  2. EB66+, 266Mhz 21066 based Alpha Evaluation Board,

  3. AlphaPC64 (aka Cabriolet), 275Mhz, APECS (2107x) based board and
     clones.


  The system configurations that I have access to (and therefore tested
  with) include the following devices (and if you know of more, please
  let me know):


  1. Number 9 GXE ISA Video cards and the Number 9 GXE PCI video cards,

  2. NCR 8100 SCSI,

  3. IDE disks,

  4. Standard 14" VGA monitors, Digital VRC16 Monitor,

  5. Digital LK450-AA keyboards


  The BIOS emulation code is known to work with the following cards:



       bus card type:		       chip:   BIOS version:		       Note:
       --- --------------------------- ------  ---------------------------     -----
       ISA #9 GXE Level 12	       S3 928  #9GXE BIOS Version 1.13.03S
       PCI #9 GXE 64 PCI	       S3 864  #9-864 BIOS Version 1.02.09u
       PCI Diamond Stealth 64 DRAM PCI S3 864  BIOS Version 1.14	       1
       PCI Diamond Video 64 DRAM PCI   S3 868  BIOS Version 1.02	       1

       Notes:
       ------
       #1:     Reported by pgwduane@mail.atnet.net.





  If you know of any other graphics cards that work, please report your
  result to davidm@azstarnet.com (mailto:davidm@azstarnet.com).	 If your
  card doesn't work, you may want to report this also but there no
  guarantee that the problem will be fixed quickly.


  I'm not saying that it will not work with other video cards, however
  it does contain basic VGA initialisation code that *should* work with
  most ISA cards.


  In general, you are advised to pick an S3 based video card as
  currently the only Alpha X display driver is for the S3 chipset
  (unless you want to run character cell only).


  5.  How To Load Milo.

  How you do this depends on what system you are trying to load.
  Generally, it is a two step process.	First load and test Milo, then
  program Milo into flash.  There are several ways of loading Milo, from
  a failsafe boot block floppy, from the Windows NT ARC firmware, from
  an Alpha Evaluation Board Debug Monitor and from flash or ROM.  Which
  of these methods is supported and just how you do it depends on what
  system you're running.


  5.1.	System Specific Information

  5.1.1.  AxpPCI33 (Noname)

  The Noname board can load from a failsafe boot block floppy and from
  the Windows NT ARC firmware.	A flash update utility, runnable from
  Milo is available so that once Milo is running, it can be blown into
  flash.  However, be warned that once you have done this you will lose
  the previous image held there as there is only room for one image.


  The way that Noname boots is controlled by a set of jumpers on the
  board, j29 and j28.  These look like:


			   4
	       J29     2 x x x 6
		       1 x x x 5

	       J28     2 x x x 6
		       1 x x x 5
			   3




  The two options that we're interested in are J28, pins 1-3 which boots
  the console/loader from flash and J29, pins 1-3 which boots the
  console/loader from a boot block floppy.  The second option is the one
  that you need to first boot Milo on the Noname board.


  Once you've selected the boot from floppy option via the jumpers, put
  the SRM boot block floppy containing Milo into the floppy and reboot.
  In a few seconds (after the floppy light goes out) you should see the
  screen blank to white and Milo telling you what's going on.


  If you are really interested in technical stuff, the Noname loads
  images off of the floppy into physical address 0x104000 and images
  from flash into 0x100000.  For this reason, Milo is built with it's
  PALcode starting at 0x200000.	 When it is first loaded, it moves
  itself to the correct location (see relocate.S).


  5.1.2.  EB66+

  The EB66+, like all of the Alpha Evaluation Boards built by Digital
  contain the Evaluation Board Debug Monitor and so this is available to
  load Milo.  Quite often (although not always) boards whose design is
  derived from these include the Debug Monitor also.  Usually, the
  boards include the Windows NT ARC firmware.


  These systems have two boot images in flash controlled by jumpers.  I
  usually wire the jumper to the turbo switch (who needs a turbo switch
  when you have an Alpha?).


  Blowing an image into flash is exactly the same proceedure as for the
  AlphaPC64.

  5.1.3.  AlphaPC64 (Cabriolet)

  The AlphaPC64, like the EB66+, includes two images in flash, the first
  is the Evaluation Board Debug Monitor and the second is the Windows NT
  ARC firmware.	 You select between these boot options (and Milo when
  it's been put into flash) using a combination of jumpers and a boot
  option which is saved in the NVRAM of the TOY clock.

  The jumper is J2, SP bits 6 and 7 have the following meanings:

  o  SP bit 6 should always be out.  If this jumper is set then the SROM
     mini-debugger gets booted,

  o  SP bit 7 in is boot image selected by the boot option byte in the
     TOY clock,

  o  SP bit 7 out is boot first image in flash.


  So, with bit 7 out, the Debug Monitor will be booted as it is *always*
  the first image in flash.  With bit 7 in, the image selected by the
  boot option in the TOY clock will be selected.  The Debug Monitor, the
  Windows NT ARC firmware and Milo all support setting this boot option
  byte but you must be very careful using it.  In particular, you cannot
  set the boot option so that next time the system boots Milo when you
  are running the Windows NT ARC firmware, it only allows you to set
  Debug Monitor or Windows NT ARC as boot options.


  To get Milo into flash, you'll need a flashable image.  The build
  proceedures make milo.rom by default for systems that support this,
  but you can make a rom image using the makerom tool in the Debug
  Monitor software that comes with the board:


      > makerom -v -i7 -l200000 Milo -o mini.flash




  (type makerom to find out what the arguments mean, but 7 is a flash
  image id used by the srom and -l200000 gives the load address for the
  image as 0x200000).


  Load that image into memory (via the Debug Monitor commands flload,
  netload, and so on) at 0x200000 and then blow the image into flash:



	    AlphaPC64> flash 200000 8





  (200000 is where the image to be blown is in memory and 8 is the
  segment number where you put the image.   There are 16 1024*64 byte
  segments in the flash and the Debug Monitor is at seg 0 and the
  Windows NT ARC firmware is at seg 4).


  Set up the image that the srom will boot by writing the number of the
  image into the TOY clock.


	    AlphaPC64> bootopt 131




  (131 means boot the 3rd image, 129 = 1st, 130 = 2nd and so on).


  Power off, put jumper 7 on and power on and you should see the Milo
  burst into life.  If you don't then take jumper 7 back off and reboot
  the Debug Monitor.


  5.2.	Loading Milo from the Evaluation Board Debug Monitor

  Before you consider this method, you should note that the current
  versions of the Evaluation Board Debug Monitor do not include video or
  keyboard drivers and so you must be prepared to connect another system
  via the serial port so that you can use the Debug Monitor.  It's
  interface is very simple and typing help shows a whole heap of
  commands.  The ones that are most interesting include the word boot or
  load in them.


  The Evaluation Board Debug Monitor can load an image either via the
  network (netboot) or via a floppy (flboot).  In either case, set the
  boot address to 0x200000 (> bootadr 200000) before booting the image.


  If the image is on floppy (and note that only DOS formatted floppies
  are supported), then you will need to type the following command:



	    AlphaPC64> flboot <Milo-image-name>





  5.3.	Loading Milo from a Failsafe Boot Block Floppy

  If you do not have a standard pre-built Milo .dd image, then you may
  need to build an SRM boot block floppy.  Once you have built Milo, you
  need to do the following on Digital Unix box:



	    fddisk -fmt /dev/rfd0a
	    cat mboot bootm > /dev/rfd0a
	    disklabel -rw rfd0a 'rx23' mboot bootm





  Or on a Linux box:



	    cat mboot bootm > /dev/fd0





  If you have a standard Milo image available (say milo.bios.dd) then
  you would build a boot block floppy using the following command:



	    dd if=mini.bios.dd of=/dev/fd0





  As well as the boot block floppy you will need the following:

  1. vmlinux on an EXT2 format floppy, SCSI or IDE disk (gzip'd is
     better),

  2. updatefloppy.gz on an EXT2 format floppy disk (if you want to write
     Milo into flash).


  5.4.	Loading Milo from Flash

  This is always system specific.


  5.5.	Loading Milo from the Windows NT ARC firmware

  The Windows NT ARC firmware is an environment in which programs can
  run and make callbacks into the firmware to achieve actions.	The
  Windows NT OSLoader is a program that does exactly this.   Linload.exe
  is a much simpler program which does just enough to load and execute
  the Alpha Linux Miniloader (MILO).  It loads the appropriate image
  file into memory at 0x00000000 and then makes a swap-PAL PALcall to
  it.  Milo relocates itself to 0x200000 and continues on through the
  PALcode reset entry point as before.


  By default (and design) the ARC loadable Milo built in the standard
  distribution tree contains no video or keyboard initialisation code.
  This is because this has already been carried out by the Windows NT
  ARC console and doesn't need doing yet again.


  Before you add a Linux boot option, you will need to copy linload.exe
  and the ARC loadable Milo that you wish to load to someplace that the
  Windows NT ARC firmware can read from.  In my example, I assume that
  you're booting from a DOS format floppy disk:


  1. At the boot menu, select "Supplementary menu..."

  2. At the "Supplementary menu", select "Set up the system..."

  3. At the "Setup menu", select "Manage boot selection menu..."

  4. In the "Boot selections menu", choose "Add a boot selection"

  5. Choose "Floppy Disk 0"

  6. Enter "linload.exe" as the osloader directory and name

  7. Say "yes" to the operating system being on the same partition as
     the osloader

  8. Enter "

  9. I usually enter "Linux" as the name for this boot selection

  10.
     Say "No" you do not want to initialise the debugger at boot time

  11.
     You should now be back in the "Boot selections menu", choose the
     "Change a boot selection option" and pick the selection you just
     created as the one to edit

  12.
     Use the down arrow to get "OSLOADFILENAME" up and then type in the
     name of the Milo ARC image that you wish to use, for example
     "noname.arc" followed by return.

  13.
     Press ESC to get back to the "Boot Selections menu"

  14.
     Choose "Setup Menu" (or hit ESC again) and choose "Supplementary
     menu, and save changes" option

  15.
     ESC will get you back to the "Boot menu" and you can attempt to
     boot Milo.	 If you do not want Linux as the first boot option, then
     you can alter the order of the boot options in the "Boot selections
     menu".


  At the end of all this, you should have a boot selection that looks
  something like:



       LOADIDENTIFIER=Linux
       SYSTEMPARTITION=multi(0)disk(0)fdisk(0)
       OSLOADER=multi(0)disk(0)fdisk(0)\linload.exe
       OSLOADPARTITION=multi(0)disk(0)fdisk(0)
       OSLOADFILENAME=\noname.arc
       OSLOADOPTIONS=





  You can now boot Milo (and then Linux).  No doubt you can do this from
  a file system that Windows NT understands such as NTFS or DOS on a
  hard disk, but I've not yet tried this.


  6.  Milo's User Interface.

  Once you have correctly installed/loaded/run Milo you will see the
  MILO (for MIniLOader) prompt displayed on your screen.  There is a
  very simple interface that you must use in order to boot a particular
  Linux kernel image.  Typing "help" is a good idea as it gives a useful
  summary of the commands:









    MILO command summary:

    ls [dev:[dir]]   - List files in the specified dir on the specified device
    boot [dev:file] [boot string]
		     - Boot Linux from the specified device and file
		     - and pass the boot string supplied
    run dev:file     - Run the standalone program in dev:file
    bootopt num	     - Select firmware type to use on next power up
    resetenv	     - Delete all environment variables
    setenv VAR VALUE - Set the variable VAR to the specified VALUE
    unsetenv VAR     - Delete the specified environment variable
    printenv	     - Display the current environment variable settings
    show	     - Display all known devices
    help	     - Print this text

  Devices are specified as: fd0, hda, sda...
  Environment variables that MILO cares about:
    MEMORY_SIZE	     - System memory size in megabytes
    AUTOBOOT	     - If set, MILO attempts to boot on powerup
		       and enters command loop only on failure
    AUTOBOOT_TIMEOUT - Seconds to wait before auto-booting on powerup
    BOOT_DEV	     - Specifies the default boot device
    BOOT_FILE	     - Specifies the default boot file
    BOOT_STRING	     - Specifies the boot string to pass to the kernel
    SCSIn_HOSTID     - Specifies the host id of the n-th SCSI controller.





  Note that the bootopt command only appears on AlphaPC64 (and similar)
  systems.  Refer to the board's dcoumentation to find out just what it
  means.


  6.1.	Booting Linux

  To boot a Linux kernel you will need to have an EXT2 formated disk
  (either SCSI or floppy) available to Milo.  You can gzip the image, in
  this case Milo will recognise that it is gzip'd by the .gz suffix.
  You should note that the version of Milo does not usually have to
  match the version of the Linux kernel that you are loading.  You can
  boot using the following commands:



	    MILO> boot fd0:vmlinux.gz
	    MILO> boot sdb2:vmlinux.gz





  If you're installing BLADE, then you'll need to specify a root device
  and so on.  So you'd use:



	    MILO> boot fd0:vmlinux.gz root=/dev/fd0 ramdisk=1440





  Milo will automatically contain the block devices that you configure
  into your vmlinux.  I've tested the floppy driver, the IDE driver and
  the NCR SCSI driver, these work fine.	 Others may or may not.	 One
  word of warning about the NCR SCSI driver.  I've found that so long as
  you build the driver with OPTION_IO_MAPPED defined, then all works
  well.	 Also, it is important to set the host id of the SCSI controller
  to a reasonable value.  By default, MILO will initialize it to the
  highest possible value (7) which should normally work just fine.
  However, if you wish, you can explicitly set the host id of the n-th
  SCSI controller in the system by setting environment variable
  SCSIn_HOSTID to the appropriate value.  For example, to set the hostid
  of the first SCSI controller to 7, you can issue the following command
  at the MILO prompt:



	    setenv SCSI0_HOSTID 7





  6.2.	Running the Flash Update Utility

  At the moment, the flash update utility is only available for the
  Noname board, but over time others will be supported.	 Before you
  start you'll need a device available to Milo that contains the
  updateflash program.	This (like vmlinux) can be gzip'd.  You need to
  run the update flash utility	program from the Milo using the (>run)
  command:



	    MILO> run fd0:updateflash.gz





  Wait until it has completed before powering off your system.


  7.  Some Restrictions.

  Unfortunately this is not a perfect world and there, as always, some
  restrictions that you should be aware of.


  Milo is not meant to load operating systems other than Linux, although
  it can load images linked to run at the same place in memory as Linux
  (which is 0xFFFFFC0000310000).  This is how the flash update utilities
  can be run.


  The PALcode sources included in miniboot/palcode/blah are correct,
  however there are problems when they are built using the latest gas.
  They do build if you use the ancient a.out gas that's supplied in the
  Alpha Evaluation Board toolset (and that's how they were built).  I'm
  trying to get someone to fix the new gas.  Meanwhile, as a workaround,
  I've provided pre-built PALcode for the supported boards and David
  Mosberger-Tang has a fixed gas on his ftp site.


  I've not yet written/tested the flash update stuff for the EB66+ and
  AlphaPC64, but I have given instructions on how to load the Milo into
  flash on those systems using the Alpha Evaluation Board Debug Monitor
  which ships with those systems.

  Several people reported having problems reading files from the floppy
  disk using the Evaluation Board Debug Monitor supplied with Digital
  Alpha Evaluation Boards such as the AlphaPC64.  Usually, the Debug
  Monitor can load the first few sectors all right, but then goes into
  an endless loop complaining about "bad sectors."  Apparently, there is
  an incompatibility between the DOS file system as expected by the
  Debug Monitor and the Linux implementation of DOSFS.	To make the long
  story short: if you run into this problem, try using DOS to write the
  floppy disk.	For example, if loading the file milo.cab doesn't work,
  use a DOS machine, insert the floppy and then do:



	    copy a:milo.cab c:
	    copy c:milo.cab a:
	    del c:milo.cab





  Then try booting from that floppy again.  This normally solves the
  problem.


  The x86 emulator that Milo uses to execute the BIOS initialization
  code found on graphics cards is basically an 8086 emulator with just
  enough 386 support to get some of the graphics cards initialized.  At
  present, are currently known not to work:



       bus card type:		       chip:   BIOS version:		       Note:
       --- --------------------------- ------  ---------------------------     -----
       PCI ATI Graphics Pro Turbo      ???     ???			       1

       Notes:
       ------
       #1:     Reported by cruff@niwot.scd.ucar.EDU.





  A word of warning: if you do try using MILO with the x86 emulator
  enabled and it doesn't work with the graphics card in your system, it
  may damage your monitor.  Thus, please be careful before doing this on
  a system with an untested graphics card.


  When loading Milo via the Windows NT ARC firmware, Windows NT seems to
  store time in a different format from Linux and so the Windows NT ARC
  firmware complains every time the system boots and the date is wrong
  on Linux every time it boots.	 I use date and clock to put this right
  by hand each time I boot.  This makes life hard if you want to co-
  exist with Windows NT, but if you're using Milo to blow another image
  into flash then there's no problem at all.


  8.  Acknowledgements.

  I would like to thank Eric Rasmussen and Eilleen Samberg, the original
  authors of the PALcode, Jim Paradis for the keyboard driver and the
  original MILO interface and David Mosberger-Tang for the BIOS
  emulation as well as his support and encouragement.

  There are a number of things that still need doing to Milo, amongst
  which are proper flash support for the AlphaPC64 and ISO9660 file
  system support.  If you want to add something yourself, then do let me
  know so that we do not duplicate our efforts.


  Finally, a big thank you to Digital for producing such a wonderful
  chip (and paying me to do this).