TECO MACRO CROSSREFERENCER




                             Michael J. Allen
                    Electronics Engineering Department
                       Lawrence Livermore Laboratory
                        Livermore, California 94550

                                 ABSTRACT

                         The TECO macro CREF.TEC gener-
                    ates  a  crossreference  listing of
                    TECO macros which can be printed on
                    a  line  printer debugged and docu-
                    mented by referring to  the  cross-
                    reference  listing.   CREF.TEC  was
                    developed using RT-11 TECO  version
                    29  but some care has been taken to
                    exclude TECO features  not  present
                    in other implementations.

                               RESTRICTIONS

          CREF.TEC will not do everything that  some  implementations  will
     permit but should prove useful under a variety of operating systems on
     various computers.  For maximum clarity of documentation the following
     rules  should be followed by TECO macro programmers:  1) Separate com-
     mands and tags by at least one space.  2) ASCII literals should be  in
     the  double  up-arrow form rather than their numerical equivalent when
     the ASCII code is thirty-three decimal or greater.

                            OPERATIONAL EXAMPLE

     To use CREF.TEC under RT-11 V3B,  type  EDIT/EXECUTE  CREF.TEC.   TECO
     will prompt for filespec of macro to be crossreferenced and generate a
     listing on the device on which the macro resides with a file extension
     of .LST.

                          Discussion of CREF.TEC

          Please refer to the Appendix regarding the discussion  that  fol-
     lows.  The Appendix contains a listing of CREF.TEC.

     LINES 1-2:  the text buffer is cleared and the typeout  flag  is  ini-
     tialized.   Operator  enters filename and extension of the macro to be
     crossreferenced.

     LINES 3-5:  A complete scan of the macro is done and  the  "invisible"
     control  characters  are  made visible by inserting a leading up-arrow
     character and adding 64 decimal to  the  character.   Note  expecially
     LINE 5, columns 28-49.



                                                                   Page   2



     LINES 6-7:  CREF.TEC assigns line numbers to each line and  inserts  a
     blank line between lines for clarity.

     LINES 8-9:  The macro is scanned again to find tag  definitions.   All
     tags  found  are pushed on to the Q-register push down list along with
     the associated line number via Q-register B.  Q-register C counts  the
     number of tags found.

     LINE 8 COLUMNS 12-14:  Preserves the end of the text buffer for bound-
     ed  local  searches later on.  For a tag to be recognized, the initial
     exclamation point must be preceeded by a space.

     LINES 10-13:  Adds the column headings at the end of the text buffer.

     LINE 14:  Pops each tag off the Q-register push  down  list  and  into
     Q-register  B.   From there the tag and its associated line number are
     appended to the text buffer.

     LINES 15-17:  Initiates a bounded local search of the text buffer  for
     references to the tags and lists all tag references by line number and
     column number.

     LINE 17 COLUMNS 41-48:  Computes the column number of the  last  char-
     acter of each tag reference and saves it in Q-register E.

     LINE 16 COLUMNS 13-23 and LINE 17 COLUMNS 5-15:  Specifies the criter-
     ia for identifying a tag reference command.  Other commands within the
     lines 14-20 perform the column formatting function seen in the  cross-
     reference table.

     LINES 21-23:  Adds the column heading at the  beginning  of  the  text
     buffer.

     LINES 24-25:  Creates the output listing file with a file extension of
     .LST and exits from TECO returning to the monitor operating system.

                           CROSSREFERENCE TABLE

          Three features are apparent in  the  crossreference  table.   The
     first is a listing of tags found.  Secondly the line number where that
     tag is defined.  Thirdly the coordinates where all references to  each
     tag may be found.  The format is "linenumber:columnumber".

                                  SUMMARY

          The TECO macro "CREF.TEC" provides a convenient way of clarifying
     and  documenting  TECO  macros as well as formatting them for hardcopy
     printing devices.


APPENDIX

CROSSREFERENCE LISTING OF CREF.TEC

         1         2         3         4         5         6         7
1234567890123456789012345678901234567890123456789012345678901234567890123456789

1   HK 2ET ^AEnter filespec: ^A < ^TI$ -1A-13"E -D 10^T 27I$

2   BJ IER$ HXA HK MA Y 0;' >

3   BJ < Z-."E 0;' 0AUZ 31-QZ"L ONXTCHR$' 8-QZ"L 14-QZ"G ONXTCHR$' ' D

4   QZ-27"E ^^$I$ ONXTCHR$' ^^^I$ 28-QZ"G (QZ+64)I$ ONXTCHR$'

5   QZ-29"G QZ-30"E ^^^I$ ONXTCHR$' ^^_I$' !NXTCHR! 1C>

6   ZJ -1A-10"N 13I$ 10I$' BJ 0UZ !NEXTLINE! .+3-Z"G OTAGS$' %Z .UB QZ\

7   4+QB-.<32I$> L 13I$ 10I$ ONEXTLINE$

8   !TAGS! ZUF ZJ 13I$ 10I$ BJ 0UC

9   <S!$; -2A-32"E. UA S!$ QA,.-1XB .UA 0L \UB %C [B QAJ' >

10  ZJ 1UZ 9< QZ\ %Z > 7< 0UZ 10< QZ\ %Z > >

11  13I$ 10I$ 1UZ 7< 9< 32I$ >QZ\ %Z> 3< 13I$ 10I$ >

12  ZJ 19<32I$> ICROSSREFERENCE TABLE$ 2<13I$ 10I$>

13  @I/TAGS    DEFN       REFERENCES    LINE#:COL#/ 2<13I$ 10I$>

14  QC< ]B GB -(0^Q)UE (10*(QE/10+1)-QE-1)<32I$> QB\

15  BJ !TAGSRCH! QF-.,1:S^EQB$"E ZJ 13I$ 10I$ ORPT$'

16  0A-^^$"E (^S-1)A-^^O"N OTAGSRCH$' OTGRF$' 0A-(^S-1A)"N OTAGSRCH$'

17  (^S-3)A-^^@"N OTAGSRCH$' !TGRF! .UA -(0^Q)UE [E 0L \UB

18  ZJ -(0^Q)UE

19  QE-60"G 13I$ 10I$ ZJ 10<32I$> 10UE' (10*(QE/10+1)-

20  QE-1)<32I$> ZJ ]E QB\ ^^:I$ QE\ QAJ OTAGSRCH$ !RPT! >

21  BJ ICROSSREFERENCE LISTING OF $ G* 2<13I$ 10I$>

22  1UZ 7< 9< 32I$ >QZ\ %Z> 13I$ 10I$

23  1UZ 9< QZ\ %Z > 7< 0UZ 10< QZ\ %Z > >

24  2<13I$ 10I$> BJ G* -3D @I/LST$/

25  .UA BJ IEW$ B,QA+2XA B,QA+2K MA EX$


1234567890123456789012345678901234567890123456789012345678901234567890123456789
         1         2         3         4         5         6         7




                   CROSSREFERENCE TABLE

TAGS    DEFN       REFERENCES    LINE#:COL#

RPT      20        15:50
TGRF     17        16:43
TAGSRCH  15        16:35     16:67     17:26     20:48
TAGS     8         6:58
NEXTLINE 6         7:38
NXTCHR   5         3:39      3:64      4:25      4:59      5:33