DRIVER FEATURES

o	Independent control of reader and punch (i.e., reader and
	punch can work at same time, can even be assigned to
	different users).

o	Punch generates header/trailer tape of null bytes (may be
	disabled if not desired, length of header/trailer can be
	set by user).  A control-Z character (decimal 26) is punched
	before the trailer null bytes to indicate end-of-file (control-Z
	byte punching may be suppressed by user).

o	Driver performs error logging; the following errors are 
	reported: reader/punch timeout, reader/punch hardware
	error.

o	Powerfail recovery during punching of user's first QIO
	request, or during punching of trailer tape; powerfailure
	at other times is unrecoverable (user told how many bytes
	read/punched before powerfailure occurred).

o	Reader off-line error message sent to console (every 30
	seconds) until reader turned on-line (if reader turned
	off-line before QIO request, or between QIO requests; if
	reader turned off while reading tape, condition inter-
	preted as end-of-file, and user told how many bytes read
	before end-of-file condition recognized). The tape must be in
	the reader before a read request is issued (regardless of
	whether the reader is on or off line).

o	If any error condition occurs, user informed in second word
	of IOSB how many bytes read/punched before error occurred.

o	Can use DCL COPY command to read/punch data/files.  When
	punching a file (i.e., $COPY file_name PC1:) no line separator
	information is sent (e.g., no CR, LF, or SOS line numbers).
	Therefore, if you ask for a file to be punched, and then read
	it back in, it will not look exactly the same.  You may need to
	write your own copy program that sends carriage returns, line
	feeds, and line numbers.  (Note that this problem is not caused
	by the driver, since it only reads/punches what/how much it is
	told; the system just isn't giving the driver the line separator
	information.)  You may even want to write byte counts preceding
	data that is punched, so that it can be easily restored (on a
	line by line basis).



	  	SUPPORTED FUNCTION CODES

IO$_READVBLK,IO$_READLBLK,IO$_READPBLK

Restrictions:

	Reader only.
	Tape must be in reader before read QIO is issued.
	Logical and physical codes require appropriate privilege.
	If the first non-zero length read QIO issued by the user is 
	   a virtual or logical read, characters
	   are read until the first non-null character is found (i.e.,
	   the header is skipped); a physical QIO returns header null
	   bytes as real data.  As soon as an EOF byte (decimal 26)
	   is encountered, an end-of-file condition is signalled
	   (unless user has disabled searching for an EOF byte).  If the
	   first non-zero length read QIO issued by the user was a
	   physical read, the default is not to look for an EOF byte.
	   Note that if you are not looking for an EOF byte, the reader
	   reads until the end-of-tape is encountered; if the tape end
	   is not torn evenly, you could read some garbage data at the
	   end of the file.  Also note that if you request a read after
	   receiving an end-of-file error message, you will receive
	   another end-of-file error message (with 0 bytes read); this
	   is done so the DCL $COPY command can work.  If you issue a
	   second read, then the tape will be read normally.

Parameters:

	P1 = address of buffer into which data is to be read
	P2 = number of bytes to read (<65536)

________________________________________________________________________

IO$_WRITEVBLK,IO$_WRITELBLK,IO$_WRITEPBLK,IO$_WRITEOF

Restrictions:

	Punch only.
	Logical and physical codes require appropriate privilege.
	If the first non-zero length write QIO issued by the
	   user is not a physical write, a header of null bytes
	   is punched (default is 50 null bytes; can be changed by
	   IO$_MODIFY QIO); no header is punched for physical code.
	   The default is for an EOF byte (control-Z) to be punched
	   preceding the trailer, if the first non-zero length write
	   QIO was not a write physical QIO.
	IO$_WRITEOF only applies if paper tape ACP (PCACP) is
	   running; ACP translates this function code into
	   IO$_WRITEVBLK code.  Not really useful, used to illustrate
	   how ACPs are written.  Requires logical I/O privilege.

Parameters:

	P1 = address of buffer containing data to be punched
	P2 = number of bytes to be punched (<65536)





IO$_MODIFY

Restrictions:

	Punch only.

Parameters:

	P2 = number of null bytes to be punched in header/trailer
	     (<65536).

________________________________________________________________________


IO$_DELETE

Restrictions:

	Punch only.

Parameters:

	None	Resets default (50) number of bytes to punch in header/
	        trailer.

________________________________________________________________________


IO$_DEACCESS

Restrictions:

	Punch only.

Parameters:

	IOSB should be specified.  Second longword of IOSB will contain
	number of null bytes to be punched in header/trailer.

________________________________________________________________________


IO$_MOUNT

Restrictions:

	Issued only by ACPMNT image to create paper tape ACP (PCACP).
	Requires MOUNT privilege.

Parameters:

	None	Note that the ACP (PCACP) is not required for the
		driver to work. In fact, the ACP will rarely be in
		the system, since its only value is as an instructional
		tool (used to show how ACPs are written).








IO$_ACPCONTROL

Restrictions:

	Issued only by PCDMT image to cause the ACP (PCACP) to be
	dismounted.

Parameters:

	None

________________________________________________________________________


IO$_CREATE

Restrictions:

	None

Parametere:

	None

		For reader, enables searching for end-of-file byte.
		Not needed if first read QIO was virtual/logical read.

		For punch, enables punching of end-of-file byte.  Not
		needed if first write QIO was write virtual/logical QIO.


________________________________________________________________________


IO$_READPROMPT


Restrictions:

	None

Parameters:

	None

		For reader, used to disable searching for end-of-file
		byte.  Not needed if first read QIO is physical read.

		For punch, used to disable punching of end-of-file byte.
		Not needed if first QIO is a write physical QIO.








		DRIVER-SPECIFIC ERROR CODES


	In addition to errors detected by the operating system, the
driver returns the following error codes:


SS$_CANCEL	User issued $CANCEL system service.

SS$_DEVNOTMOUNT	User issued MOUNT QIO from program other than ACPMNT,
		or user issued WRITEOF function code and PCACP is not
		running.

SS$_DRVERR	Device hardware error, no tape in punch, or no
		power to punch.

SS$_ENDOFFILE	User specified more bytes to be read than there were
		on the tape; could also be caused if reader turned
		off-line during the middle of a read request, or if
		there is no power supplied to the reader.  This error
		code used when an EOF byte is found (control-Z).  The
		first read following an EOF read also returns this
		error code, with 0 bytes read in the IOSB.

SS$_ILLIOFUNC	User tried to read from punch, write to reader, or
		issued an unsupported function code.

SS$_NOPRIV	User tried to mount PCACP without MOUNT privilege.

SS$_TAPEPOSLOST	Unrecoverable powerfail error.

SS$_TIMEOUT	Device timed out (probably a hardware error, or a very
		very very busy system).








		DRIVER INSTALLATION


	The following commands should be used to load the paper tape
reader/punch driver (PCDRIVER).  Note that the reader is ALWAYS PC0:,
and the punch is always PC1:.


$MCR SYSGEN
LOAD SYS$SYSTEM:PCDRIVER		! may have to change filespec
CONNECT PCA0/ADAPTER=3-			! depending on where you keep
/NUMVEC=2-				! file PCDRIVER.EXE
/VECTOR=%O70-
/CSR=%O777550-
/DRIVER=PCDRIVER
CONNECT PCA1/ADAPTER=3-
/NUMVEC=1-
/VECTOR=%O74-
/CSR=%O777554-
/DRIVER=PCDRIVER
EXIT


Notice that the paper tape reader punch ACP (PCACP) is not required
in order for the driver to work properly (in fact, PCACP is only used
as an illustration of how to write ACPs).  If you want the ACP in your
system, you may have to modify the filespecs in programs ACPMNT and
PCDMT to find file PCACP.EXE (the default is SYS$SYSTEM:).

To mount PCACP, type $MCR ACPMNT (you will need CMKRNL, MOUNT, and
DETACH privileges).  To dismount PCACP, type $MCR PCDMT (you will
need CMKRNL privilege).  (This assumes you have ACPMNT.EXE and
PCDMT.EXE in the SYS$SYSTEM: directory.)