TERMINAL EMULATION PROGRAM (TEMPRO)

                 Hugh L.  Scott
		 Division 2644
		 Sandia National Laboratories
		 Albuquerque, NM 87185
                 June 1,1981


    OPERATING SYSTEM:   RT-11 V03B
    SOURCE LANGUAGE:   MACRO
    MEMORY REQUIRED:  6K words
    SPECIAL HARDWARE REQUIRED:  DL-11 or DLV-11,Bell 103 or Vadic 3434


    ABSTRACT:   The terminal emulation program (TEMPRO) allows a PDP-11 to
    emulate  a  remote  terminal  for  a  time  sharing  computer.  It was
    initially created  to  operate  with  a  VAX  11/780  but  with  minor
    modifications  it  will  work  even with NOS.  The data link is over a
    telephone line using an asynchronous serial interface ,DL11 or  DLV11,
    and  a  BELL 103 or VADIC 3434 equivalent data set.  TEMPRO has a very
    large console printer ring buffer, 20000 characters, which allows  the
    users  with  300  baud  terminals  to  communicate at much higher data
    transmission rates with the host computer.  In normal mode the  PDP-11
    console  acts  as  a VAX remote terminal.  Certain control characters,
    however, allow the user to transfer ASCII files between the PDP-11 and
    the  VAX.   The  following  is  a description of these special control
    characters.


                 CONTROL CHARACTERS


    Control-C
                 Control-C operates normally, for the PDP-11 that is.   It
                 terminates  TEMPRO  and  returns to PDP-11 monitor level.
                 VAX never knows anything has happened and continues  what
                 ever  it  was  doing.   You  ask,  "How  do  I  then send
                 control-C to VAX "


    Control-A 
                 Control-A is intercepted by TEMPRO  and  a  control-C  is
                 sent to VAX.


    Control-X
                 Due to the way  that  TEMPRO  gets  characters  from  the
                 PDP-11  console keyboard, control-S and control-Q are not
                 recognized.  Therefore to say WHOA to VAX  you  must  use
                 control-X.


    Control-V
                 Send control-V in order for VAX to resume transmission of
                 data.

    Control-P
		Send control-P if you wish to transmit a BREAK.

                                                                  Page   2



    Control-R
                 When you want to send an ASCII file which has been stored
                 on  a PDP-11 mass storage device to VAX, use control-R (R
                 for READ).  TEMPRO now asks you for the filespec  of  the
                 file  and  prompts  you  with "*".  A typical filespec is
                 also given as an  example.   After  the  transmission  is
                 complete,  TEMPRO  closes  the  file  and  VAX returns to
                 monitor level with the "$" prompt.  You must  create  the
                 file at VAX  before  using control-R.  It seems that some 
		 characters at  the end of the file are  lost transmitting 
		 them to VAX.  Adding about three dummy lines to your file
		 will solve this problem.

                 
    Control-W
                 To store a VAX file on the PDP-11  mass  storage  device,
                 push  control-W  (W  for WRITE).  You are again asked for
                 the filespec for storage.  After your response,  you  are
                 now  talking  with  VAX.  Any key you push is now sent to
                 VAX, echoed back to your terminal and therefore goes into
                 your  file.   Therefore, you should tell VAX to type some
                 file stored at VAX.  For example, 

                         TYPE USER$DISK[HLSCOTT]LOGIN.COM 

                 Your terminal acts  normally  and  displays  all  of  the
                 characters  from  the file LOGIN.COM.  When finished, VAX
                 responds with the monitor level prompt "$".  Beware  that
                 your  file  is not closed on your mass storage device and
                 any subsquent characters sent to VAX are also going  into
                 your file.


    Control-T
                 When transmission of your file from VAX is complete, push
                 control-T to close it.

    Control-E    Since control-W is used to setup file transfer, control-E
                 may be issued to transmit a control-W to VAX.

    Control-N    Sending a control-N toggles the output to the aux. printer.

                 EDITING TEMPRO FOR YOUR PDP-11

         Three lines in the file TEMPRO.MAC must be edited for the code to
    run  on  your  particular PDP-11.  The receive control status register
    and vector must be changed to those corresponding to your serial  line
    interface.

    That is,   RCSR=176560   must be changed to
               RCSR=XXXXXX   (XXXXXX) is your address,
    and        VEC=160   should be replaced by
               VEC=XXX   (XXX) is your vector.  

    The aux. printer's transmit control status register must also be changed.
	       PCCSR=176504 must be changed to
	       PCCSR=XXXXXX  (XXXXXX) is your aux. printer address.