;+++
;
; FACILITY
;	OAK RIDGE NATIONAL LABORATORY
;	FUSION ENERGY DIVISION
;	TOKAMAK SECTION
;
; ABSTRACT
;
;	This library contains a collection of procedures
;	designed to provide status checking support for the
;	VAX CAMAC system developed for the ORNL Fusion Energy 
;	Division VAX-11/780 computer system(s). These procedures 
;	are designed to conform to VAX linkage conventions and 
;	as such should be callable from any VAX supported high-level 
;	language. Specifically, this library contains the following 
;	procedures:
;
;	CAM$ERROR
;	-Analyzes the I/O status block from a CAMAC request to determine
;	 if any errors occurred on the transaction,
;	CAM$X
;	-Analyzes the I/O status block from a CAMAC request to determine
;	 if the X response was generated,
;	CAM$Q
;	-Analyzes the I/O status block from a CAMAC request to determine
;	 if the Q response was generated,
;	CAM$XANDQ
;	-Performs the equivalent of (CAM$X .AND. CAM$Q),
;	CAM$GET_STAT
;	-Returns raw I/O status block from the CAMAC image block to the
;	 user.
;	CAM$SHOW_STAT
;	-Performs analysis and formatted display of CAMAC I/O status block.
;
;
;	A brief synopsis of each access procedure is included
;	in the preamble for that procedure.
;
; AUTHOR
;	E. T. Blair
;
; REVISION HISTORY
;	V01-001, E.T. Blair, 8-SEP-1982
;	Made changes necessary to support the parallel highway. These changes
;	are primarily assembly time checks made via the ASSUME macro to
;	verify consistency of parallel control register and error/status 
;	register fields in the IOSB with their counterparts in the serial
;	control register and error/status register.
;
;	V01-002, E.T. Blair, 9-SEP-1982
;	Added CAM$SHOW_STAT procedure to the CAMAC status library. This
;	procedure analyzes the CAMAC I/O status block and produces a
;	formatted display of it's contents. 
;
;---


;+++
;
;	Procedure:
;	CAM$ERROR(X,Q[,IOSB])
;
;	Description:
;	This procedure determines if a CAMAC transaction error
;	occurred and returns a logical value as the function output
;	(ERROR=.TRUE.; NOERROR=.FALSE.). Specifically, a .TRUE. return
;	value indicates one of the following conditions exists:
;		A system detected I/O error occurred(in which case
;			the first longword of the IOSB contains a
;			system status value),
;		A CAMAC transmission error occurred causing the CAMAC
;			transaction to terminate with 'ERROR' status,
;		The X/Q response from the CAMAC transaction is
;			inconsistent with the expected X/Q response.
;
;	If further clarification of the nature of the error is required
;	the CAM$X, CAM$Q, CAM$XANDQ or CAM$SHOW_STAT functions may be
;	used.
;
;	If no I/O status block is specified for the call, 
;	the procedure uses the I/O status block from the CAMAC 
;	image block. If the I/O status block is specified, it is 
;	assumed that valid CAMAC I/O status is contained in the 
;	block. This capability enables the CAM$ERROR function to 
;	be used to interrogate I/O status from proceed mode CAMAC requests.
;
;	Parameters:
;	X- address of a LOGICAL variable(any length) specifying
;		the expected state of the CAMAC X response(may be
;		specified as null for DON'T CARE),
;	Q- address of a LOGICAL variable(any length) specifying
;		the expected state of the CAMAC Q response(may be
;		specified as null for DON'T CARE),
;	IOSB- address of a quadword CAMAC I/O status block. If
;		not specified, the IOSB from the last CAMAC request
;		is utilized.
;
;	Return Status:
;	.TRUE. if a CAMAC transmission error occurred or if the
;	resultant X and Q states are inconsistent with the expected
;	values of those states, otherwise, the value .FALSE. is
;	returned. 
;
;---


;+++
;
;	Procedure:
;	CAM$X([IOSB])
;
;	Description:
;	This procedure determines the X response from a CAMAC I/O
;	and returns a logical value as the function output
;	(X=.TRUE.; NO X=.FALSE.). If no I/O status block
;	is specified for the call, the procedure uses the I/O
;	status block from the last CAMAC request. If the I/O
;	status block is specified, it is assumed that valid
;	CAMAC I/O status is contained in the block. This capability
;	enables the CAM$X function to be used to interrogate
;	I/O status from proceed mode CAMAC requests.
;
;	Parameters:
;	IOSB- address of a quadword CAMAC I/O status block. If
;		not specified, the IOSB from the last CAMAC request
;		is utilized.
;
;	Return Status:
;	.TRUE. if X=1 response received,
;		.FALSE. if X=0 response received.
;
;---


;+++
;
;	Procedure:
;	CAM$Q([IOSB])
;
;	Description:
;	This procedure determines the Q response from a CAMAC I/O
;	and returns a logical value as the function output
;	(Q=.TRUE.; NO Q=.FALSE.). If no I/O status block
;	is specified for the call, the procedure uses the I/O
;	status block from the last CAMAC request. If the I/O
;	status block is specified, it is assumed that valid
;	CAMAC I/O status is contained in the block. This capability
;	enables the CAM$Q function to be used to interrogate
;	I/O status from proceed mode CAMAC requests.
;
;	Parameters:
;	IOSB- address of a quadword CAMAC I/O status block. If
;		not specified, the IOSB from the last CAMAC request
;		is utilized.
;
;	Return Status:
;	.TRUE. if Q=1 response received,
;		.FALSE. if Q=0 response received.
;
;---


;+++
;
;	Procedure:
;	CAM$XANDQ([IOSB])
;
;	Description:
;	This procedure determines the logical AND of the X and Q
;	responses from a CAMAC I/O and returns a logical value
;	as the function output( X=1 .AND. Q=1 returns .TRUE.;
;	X=0 .OR. Q=0 returns .FALSE.). If no I/O status block
;	is specified for the call, the procedure uses the I/O
;	status block from the last CAMAC request. If the I/O
;	status block is specified, it is assumed that valid
;	CAMAC I/O status is contained in the block. This capability
;	enables the CAM$Q function to be used to interrogate
;	I/O status from proceed mode CAMAC requests.
;
;	Parameters:
;	IOSB- address of a quadword CAMAC I/O status block. If
;		not specified, the IOSB from the last CAMAC request
;		is utilized.
;
;	Return Status:
;	.TRUE. if (X=1 .AND. Q=1),
;		.FALSE. if (X=0 .OR. Q=0).
;
;---


;+++
;
;	Procedure:
;	CAM$GET_STAT(IOSB)
;
;	Description:
;	This procedure provides a means for a CAMAC user to sample the
;	CAMAC image block I/O status block(which is used as the default
;	IOSB for all CAMAC I/O requests). The contents of the 
;	CIB IOSB is returned in the quadword buffer specified by
;	the caller(IOSB). Function status is always returned as
;	SS$_NORMAL.
;
;	Parameters:
;	IOSB- address of a quadword buffer to receive the CAMAC image
;		block IOSB contents.
;
;---


;+++
;
;	Procedure:
;	CAM$SHOW_STAT([IOSB])
;
;	Description:
;	This procedure performs an analysis of the CAMAC I/O status
;	block resulting from a CAMAC I/O request. The quadword IOSB
;	is interpreted as follows:
;
;		If (.not.IOSB(1)) then
;			IOSB(1) contains a system status code(SS$_xx),
;			IOSB(2) contents are unpredictable.
;		Else
;			IOSB_W(1) contains final CTR state(SCT/PCT),
;			IOSB_W(2) contains net transfer count(bytes),
;			IOSB_W(3) contains final ESR state(SES/PES),
;			IOSB_W(4) contains net reply list count(bytes).
;		End If
;
;	The resulting display of the CAMAC IOSB consists of either an
;	appropriate system status message or a collection of CAMAC status
;	messages.
;
;	If the optional I/O status block parameter is specified, it is assumed
;	that it represents a valid CAMAC I/O status block. If not specified,
;	the call defaults to the I/O status block in the CAMAC image block.
;
;	Parameters:
;	IOSB- address of a quadword buffer containing valid CAMAC I/O status.
;		If not specified, defaults to CIB IOSB.
;
;---


;---