CHAPTER 2
 
                        USING A HOST-BASED PAD
 
 
 
2.1  INTRODUCTION
 
As mentioned in Chapter 1, X.29 terminals communicate with remote DTEs
through  a  PAD  using  the  X.3, X.28, and X.29 protocols.  The PPSNs
provide PADs which you can access over  leased  lines  or  by  dial-up
lines.  If your terminal is connected to a VAX/VMS system running PSI,
you can use the host-based PAD facility to connect your terminal to  a
remote  DTE  (converting the local terminal to an X.29 terminal for as
long as you are using the PAD program).
 
The host-based PAD has a number of advantages over  a  PPSN  PAD.   It
costs  less;   you  do  not have to pay for a dial-up call and can use
existing leased lines that are connected to the VAX.  It  is  quicker;
the  link between the host-based PAD and your terminal usually runs at
9600 baud, a dial-up line would run at 300 or 1200 baud.  It  is  more
reliable;   dial-up  lines  in  particular  are prone to errors due to
interference.
 
This chapter explains how to log on to and exit from a host-based PAD.
If  you  are  using a PPSN PAD, refer to the documentation supplied by
your PPSN for accessing their PADs.  The chapter  also  describes  the
command  signals  that  control  the  host-based  PAD  and the service
signals that the PAD returns to the X.29 terminal.  Refer to  Appendix
B for the CCITT command and service signals.
 
 
 
2.2  LOGGING ON TO A HOST-BASED PAD
 
To invoke the PAD program use the following command:
 
     $ RUN SYS$SYSTEM:PSIPAD
 
When the PAD program starts, it displays:
 
     PAD>
 
To make the PAD program easier to access,  define  a  symbol  in  your
LOGIN.COM file, as follows:
 
     PAD :=="$PSIPAD"
 
If you try to run the PAD program on a system which does not have  the
PSI software running, the PAD program displays:
 
     %PAD-E-PSINOTLD, PSI not loaded

USING A HOST-BASED PAD                                        Page 2-2
 
2.3  PAD COMMAND SIGNALS
 
The following sections describe the commands that control the PSI-PAD.
Using the PAD commands, you can:
 
      .  Establish a call to a remote DTE with the A command
 
      .  Display and set the PAD parameters using the  PAR?   and  SET
         commands
 
      .  Display the PAD status with the STAT command
 
      .  Send break, interrupt, and reset signals to  the  remote  DTE
         with the BREAK, INTERRUPT, and RESET commands.
 
      .  Include up to one line of data in  the  call  request  packet
         with the U command
 
The  commands  are  described  in  alphabetical  order.   Appendix   A
describes the PAD parameters.
 
If you enter an incorrect command, the PAD program displays:

 		     %PAD-E-ERR, ERR??, Error in command
and reprompts:
		     PAD>
 
Other PAD service signals are described in Section 2.4.
 
 
2.3.1  Call Request (A Dte-address)
 
Use the A command to connect your terminal with  a  remote  DTE.   The
format for the command is:
 
     PAD>A dte-address
 
where dte-address is  the  12-character  DTE  address  (including  the
4-digit DNIC) for the remote DTE.
 
You need not reenter the DTE address if:
 
     1.  You fail to establish the call at the first attempt.
 
     2.  The link with the DTE is broken, returning  you  to  the  PAD
         command mode.
 
When you enter A, the PAD tries to establish the call  using  the  DTE
address specified on the failed call.
 
When the circuit is established, the PAD program displays the  service
signal:
 	     %PAD-I-COM, COM, Call connected
 
The start of the login procedure for the remote DTE is also displayed.
The  PAD is now in data transfer mode.  Return to the PAD command mode
by typing <CTRL/P>.  You can then enter one PAD command,  after  which

USING A HOST-BASED PAD                                        Page 2-3
 
(unless  you  have cleared the call using CLR or EXIT) the PAD returns
you to the remote DTE.
 
If PAD parameter 1 is set  to  0,  the  PAD  does  not  recognize  any
character  as  an  escape  to  command  mode character (<CTRL/P>).  To
return to  the  PAD  command  mode,  type  nine  consecutive  <CTRL/Y>
characters.  If you enter a tenth <CTRL/Y>, the PAD program clears the
call and exits.
 
PSI sets a default value of 1 for parameter 1 on the host-based PAD.
 
You can DEFINE logical names for DTE addresses  and  use  the  logical
name  in  place of the full DTE address when trying to connect to that
DTE.
 
 
2.3.2  Break (BREAK)
 
Use the BREAK command to send a break signal to  the  host-based  PAD.
The format for the command is:
 
     PAD> BREAK
 
The following values  for  PAD  parameter  7  determine  how  the  PAD
responds when it receives the break signal:
 
     0   No action
 
     1   PAD sends an interrupt to the remote DTE
 
     2   PAD sends a reset to the remote DTE
 
     4   PAD sends an Indication Break PAD message to the remote DTE
 
     8   PAD leaves the Data Transfer state and enters the waiting for
         command state
 
    16   PAD discards output to the terminal by setting parameter 8 to
         1
 
    21   Combination of 1+4+16
 
PSI sets a default value of 0 for parameter 7 on the host-based PAD.
 
The BREAK command is needed because the PAD program ignores any  break
characters  typed  at  the  terminal  (because the VMS terminal driver
discards break characters).
 
 
2.3.3  Call Status Request (STAT)
 
Use the STAT command to find out if you have established a  call  from
the terminal that you are using.  The format for the command is:
 
     PAD> STAT
 
If there is a call in progress from that terminal, the PAD displays:
 
     %PAD-I-ENGAGED, PAD engaged

USING A HOST-BASED PAD                                        Page 2-4
 
If there is no call in progress, the PAD displays:
 
     %PAD-I-FREE, PAD free
 
 
2.3.4  Interrupt (INT)
 
Use the INT command to transmit an interrupt packet to the remote DTE.
The format for the command is:
 
     PAD> INT
 
When the host-based PAD sends the interrupt, you may lose any data  in
transfer between the host-based PAD and the remote DTE,
 
The effect of the interrupt on the remote DTE depends on how  the  DTE
is  set  up.  For example, if the DTE was running VAX-11 PSI, it would
ignore an interrupt.
 
If you try to send a second interrupt before the remote  DTE  and  the
PAD  have  completed  handling the previous interrupt, the PAD program
displays:
 
     %PAD-W-WARNINT, Previous interrupt incomplete
 
 
 
2.3.5  Read PAD Parameter Values (PAR?)
 
The PAR?  command lists the current values of all the PAD  parameters.
The format for the command is:
 
     PAD> PAR?
 
The PAD program displays:
 
PAR 1:1,2:1,3:126,4:10,5:1,6:1,7:0,8:0,9:0,10:80,11:14,12:1,13:0,14:0,15:1,16:12
7,17:24,18:18
 
The values for parameters 16, 17, and 18 are displayed  only
if you set the WRAPAROUND terminal SET-UP feature to on (1).
 
You can display the values  for  a  specific  parameter  (or
parameters).  For example, if you enter:
 
     PAR?  3,4,9
 
the  PAD  program  displays  the  current  values  for   PAD
parameters 3, 4, and 9:
 
     PAR 3:126,4:10,9:0
 
See Appendix A for a description of the PAD  parameters  and
values.

USING A HOST-BASED PAD                             Page 2-5
 
2.3.6  Reset the Circuit (RESET)
 
The RESET command transmits  a  RESET  to  the  remote  DTE,
resetting the virtual call.  The format for the command is:
 
     PAD> RESET
 
Use this command if, for example, the  line  is  slow.   Any
data  in  transfer between the remote DTE and the host-based
PAD may be lost.
 
If you try to send a second reset before the remote DTE  and
the  PAD have completed handling the previous reset, the PAD
displays:
 
     %PAD-W-WARNRES, Previous reset incomplete
 
 
2.3.7  Set Parameter Values (SET)
 
Use the SET command to set the values  for  PAD  parameters.
The format for the command is:
 
     PAD> SET i:x,j:y,k:z ...
 
The letters i, j,  and  k  represent  the  parameters  whose
values  you want to change to x, y, and z respectively.  For
example, to set the values of PAD parameters 3, 4, 5, and 10
to 48, 160, 0, and 132 respectively, enter:
 
     PAD> SET 3:48,4:160,5:0,10:132
 
If you do not specify any parameters, the PAD  program  sets
all  supported  parameters  to their initial values (section
2.5 lists the default values for the PAD  parameters).   See
Appendix  A  for  a  description  of  the PAD parameters and
values.
 
                            NOTE
 
               Use  the  SET  command  before
               establishing a call.  The X.29
               terminal   driver   will   not
               recognize     any     terminal
               characteristics changed  by  a
               SET  command  after a call has
               been established.   Therefore,
               you  have to use the PSISETPAD
               utility    to    change    PAD
               parameters   during   a  call.
               Section 3.3  explains  how  to
               use PSISETPAD.
 
 If you want to change parameter values and display  the  new
values, enter:
 
     PAD> SET?  i:x,j:y,k:z

USING A HOST-BASED PAD                   		Page 2-6
 
The SET?  command sets the specified  parameter  values  and
confirms  the  settings  by  displaying  the  new  parameter
values.  For example, if you enter:
 
     PAD> SET?  3:126,4:20
 
the PAD program displays:
 
     PAR 3:126,4:20
 
 
2.3.8  User Data - (U)
 
The U command lets you specify the contents of the user data
field  in  the  call  request  packet.   Therefore, use this
command before using the A command to establish the call.
 
Use this command in the following way:
 
     U ccccc
 
where ccccc is user data.   Enter  user  data  in  the  call
request packet only if the remote DTE subscribes to the Fast
Select facility provided by your PPSN.
 
Note that the data that you enter must contain only printing
characters  (the PAD discards non-printing characters).  The
PAD program converts all lowercase characters to uppercase.
 
 
2.3.9  Clear a Virtual Call (CLR)
 
The CLR command clears any  virtual  call  in  progress  and
returns you to the PAD program.
 

2.3.10  Exiting from the Host-Based PAD (EXIT)
 
The EXIT command clears any virtual  call  in  progress  and
exits the PAD program.
 
  
2.4  PAD SERVICE SIGNALS
 
The host-based PAD returns service signals  in  response  to
command  signals  or  data  from  the  X.29  terminal.  This
section describes the format of  the  PAD  service  signals,
lists  their  effects, and indicates when they are likely to
occur.  If they indicate an  error,  the  required  recovery
action is also described.
 
%PAD-W-CLR, Call cleared
 
     A remote DTE has received a CLR command signal from the
     host-based  PAD,  and is in the process of clearing the
     call.  The PAD program may also display:

USING A HOST-BASED PAD           			Page 2-7
 
     %PAD-I-msg, CLR msg, txt
     %PAD-I-CAUSEDIAG, Cause code xx, diagnostic code yy
 
     The first message  is  an  information  message,  which
     explains why the call has been cleared.  These messages
     are  listed  below,  with   the   appropriate   acronym
     replacing msg, and explanatory text replacing txt.  The
     second message gives the cause code and the  diagnostic
     code  (in  hexadecimal), here represented by xx and yy.
     Refer to your  PPSN's  technical  documentation  for  a
     description  of  the cause and diagnostic codes used on
     your network.
 
     The information messages are as follows:
 
     %PAD-I-DER, CLR DER, Remote DTE is out of order
 
         The remote DTE is not running.
 
     %PAD-I-DTE, CLR DTE, Remote DTE cleared the call
 
         The remote DTE cleared the call (cause code = 0).
 
     %PAD-I-ER, CLR ERR, Local procedure error
 
         The local machine detected a protocol error.   This
         may  indicate  that  the  local  machine is wrongly
         configured.
 
     %PAD-I-INV, CLR INV, Invalid facility request
 
         The network detected an error in the  call  request
         packet.   This  is usually because you specified an
         invalid DTE address.
 
     %PAD-I-NA, CLR NA, Access barred
 
         The remote DTE is in a closed user group  to  which
         you have no access.
 
     %PAD-I-NC, CLR NC, Network congestion
 
         The network cannot complete the call.
 
     %PAD-I-NP, CLR NP,Number for DTE is not obtainable
 
         You selected a non-existent remote DTE.
 
     %PAD-I-NRC, CLR NRC, No reverse charging
 
         You specified a reverse charge call, but the remote
         DTE does not accept reverse charging.
 
     %PAD-I-OCC, CLR OCC, Number busy
 
         The remote DTE cannot accept the call at this time.

USING A HOST-BASED PAD                         	Page 2-8
 
     %PAD-I-RPE,CLR RPE, Remote procedure error
 
         The remote DTE detected a protocol error.

     %PAD-I-LINDWN, Line down
 
         The connection between the local host and the  PPSN
         went down.  Any calls in progress have been lost.
 
     %PAD-I-LINREST, Line restart
 
         The connection between the local host and the  PPSN
         has  been  reestablished.   The  line  is  probably
         working again, but all calls in progress  when  the
         line failed have been lost.
 
     %PAD-I-NETPROT, Network protocol error
 
         The PSI  software  at  the  local  DTE  detected  a
         protocol error.
 
     %PAD-I-OPACT, Operator action
 
         Operator action has caused the call to be cleared.
 
     %PAD-I-TIMOUT, Timeout no response
 
         The timer operated by the PSI software at the local
         host  ran  out  before  the  remote DTE accepted or
         rejected the call.  Usually, the timer operated  by
         the network will run out first.
 
%PAD-I-CLRCONF, CLR CONF, Clear confirmation received
 
     The remote DTE has cleared the call as a result of  the
     CLR command signal it received from the host-based PAD.
 
%PAD-E-ERR, ERR ??, Error in command
 
     The PAD program  cannot  set  up  the  call.   The  PAD
     program may also display:
 
     %PAD-E-NOLINES, No lines available for call
     %PAD-I-IOSB, IOSB, iosb[0] xx, iosb[1] yy
 
     This indicates either that the lines are not working or
     that  they  already have the maximum number of circuits
     in use.
 
     iosb[0]xx, iosb[1]yy displays the contents of  the  I/O
     Status  Block, where xx is the first longword and yy is
     the second (in hexadecimal).  See the VAX-11  PSI  X.25
     Programmer's Guide for a full description of the status
     information held in the IOSB.
 

USING A HOST-BASED PAD                   		Page 2-9


%PAD-I-INTERRUPT, INTERRUPT received
 
     The remote DTE has sent an interrupt  and  the  PAD  is
     confirming receipt of the interrupt.
 
 
%PAD-I-RESET, RESET received
 
     The PAD program also displays:
 
     %PAD-I-CAUSEDIAG, Cause code OD, diagnostic code xx, yy
 
     The  letters  xx  represent  the  cause  code,  yy  the
     diagnostic  code  (in hexadecimal).  The remote DTE has
     sent a reset to the  host-based  PAD.   Refer  to  your
     PPSN's technical documentation for a description of the
     cause and diagnostic codes used on your network.
 
 
XXX
 
     Sent by the host-based PAD to  the  terminal  when  you
     delete  a  line from the PAD's editing buffer.  See PAD
     Parameters 15,16, 17, and 18 (1980 only) in Appendix  A
     for  details  of  editing  PAD command signals and user
     data held in the editing  buffer.   The  value  of  PAD
     parameter 17 determines the delete-line character.
 
 
 
2.5  PARAMETER VALUES FOR THE HOST-BASED PAD
 
The host-based PAD supports the 18 parameters as defined  by
the CCITT X.3 recommendation (1980).
 
Table 2-1 lists initial values of these parameters (the  PAD
profile) for the host-based PAD.  Some values are determined
by the terminal characteristics (see Chapter 3, Section  3.2
for details on setting terminal characteristics) and are not
set until after call set-up and you have logged  in  to  the
remote DTE.

USING A HOST-BASED PAD                      	Page 2-10
 
                                    Table 2-1
                              Host-Based PAD Profile
 
    Parameter                   Value
 
        1               1
 
        2               Set by ECHO characteristic
 
        3               126
 
        4               10
 
        5               Set by HOSTSYNC characteristic
 
        6               1
        
        7               0
 
        8               0
 
        9               Set by CRFILL characteristic
 
        10              Set by WRAP characteristic and terminal width
 
        11              Set by terminal speed
 
        12              Set by TTSYNC characteristic
 
        13              0
 
        14              Set by LFFILL characteristic
 
        15              1
 
        16              127 (Delete character)
 
        17              18 (control R)
 
        18              24 (control X)
 
     Read Chapter 3 and Appendix A before  changing  any  of
the above values.
 
NOTES
 
Parameter 1
 
     Values 2 to 31 allow escape to command  mode  with  the
     corresponding   control   character.   CCITT  does  not
     specify action on these values.
 
Parameter 3
 
     Setting parameter 3 to 128  sets  the  data  forwarding
     characters  to  all  control  characters not defined by
     CCITT values.  CCITT does not specifiy what these other
     characters are.

USING A HOST-BASED PAD                                                   Page 2-11
 
 
     This parameter is generally set by the remote DTE,  and
     you should not need to change the setting.
 
 
Restrictions
 
1.   The PAD program sets the terminal to  PASSALL  mode  so
     that the program receives all characters.  As a result,
     the  terminal  does  not  display  broadcast  messages.
     Chapter   3  describes  the  terminal  characteristics,
     including PASSALL.
 
     If you use the PAD program from another machine  (using
     SET  HOST) and the DECnet logical link goes down, or if
     the PAD program does not exit normally  for  any  other
     reason,  the terminal characteristics do not get reset.
     In particular  the  characteristics  are  left  set  to
     PASSALL and NOECHO.
 
2.   The PAD program will be slow if parameter 5 is set to 1
     and  you have SET HOST from another machine in order to
     use the program.
 
3.   The PAD program  echoes  input  of  characters  itself.
     This  may  cause  a  delay  in  echoing,  and  may also
     increase the CPU time that it uses.
 
4.   Do not enter CTRL/P from the  console  terminal  unless
     you  have  set  the  terminal to LOCAL DISABLE with the
     keyswitch.