PIP10

                             by

                      Paul Kinzelman
                      Digital Equipment Corp
                      ML1-3/E63
                      146 Main St.
                      Maynard, Ma. 01746

                      April 1, 1980




1.0  ABSTRACT


PIP10 allows a user to interchange  both  ASCII  and  PDP-11
binary format files via magtape between a TOPS-10 or TOPS-20
system running the standard PIP or COPY and an RT-11  system
running PIP10.




2.0  OPERATION (PDP-10 TO PDP-11)


Write a tape on the 10 system with COPY or PIP.   Leave  the
system  defaults  alone  for parity, format and record size,
and set the default density to the desired density.  Do  not
use  wild  card characters in the file specification because
there is no directory on the tape and you won't  know  which
file  is  which without looking at the file itself.  You may
write any number of files mixing ASCII and  binary  formats.
An example of TOPS-20 commands is:

        @COPY FILE1.EXT MTA0:
        @COPY FILE2.EXT MTA0:
        <etc.>

Take the tape to  the  RT-11  system  and  run  PIP10.   The
program will print the question:

        PIP10 V34, /H FOR HELP:

Type the  drive  you  are  using,  i.e.,  MS0:,  MT1:,  etc.
followed  by any switches (see later).  Then, for each file,
you are asked:

        TYPE FILE.EXT<CR> -

Type the file name of the file about to be read in  followed
by  any  switches.  When PIP10 has read all the files on the


                                                      Page 2


tape, the  tape  is  rewound  and  the  program  returns  to
monitor.

When you transfer a file in ASCII  mode,  line  numbers  are
automatically   deleted  (PDP-10  bit  35  is  on  for  line
numbers).

If the extension of the file name is .BIN or .OBJ, the  file
is  processed  in binary format.  Otherwise the format is in
ASCII.  You may override these defaults  by  typing  /A  for
ASCII or /B for binary after the file.  Note that the binary
format must be compressed (4  bytes  per  PDP-10  word)  not
image.

If the file name you type already exists, you will be warned
that  you  are  about to overwrite an existing file.  If you
don't want to be warned, type /N when you type  the  magtape
number to the first question.

If you have a lot of files to transfer, what I do is to make
an  indirect  file  to do the transfer on the 10.  The first
file I write on the tape is the indirect file so when I read
the  file  on  the  RT system, I have a list of files on the
tape after the indirect file.  For repeated  transfers,  you
could make up a batch control file on the RT-11 system.




3.0  OPERATION (PDP-11 TO PDP-10)


In response to the first question, type the  magtape  to  be
used  followed  by  the /W switch that signifies you want to
write the tape.  Then type the desired file(s) to  the  next
and following questions.  When you type the file name of the
last file, type /U and the tape will be  rewound  after  the
file is written.  You could also type ^C to the file request
question and the tape would still be terminated properly.

Take the tape to the 10 system and read  the  tape  file  by
file  with  PIP or the COPY command.  Again, do not use wild
cards as you can't be sure of the order of the transfer.  An
example of the COPY command is:

        @COPY MTA0: FILE1.EXT
        @COPY MTA0: FILE2.EXT
        <etc.>

Again, if the file extension is .BIN or .OBJ, the file  will
be  transfered  in  binary format.  Otherwise the default is
ASCII.  Typing /A or /B overrides the default  to  ASCII  or
binary respectively.