May 19, 1983

               The patches and programs in  this  submission  are  for
          running  the KMC-11 debugging tools designed for the PDP-11.
          By modifying compatibility mode programs to include resident
          common  program  sections  and installing global sections in
          the VAX/VMS system it is possible for these programs to  map
          to  the  I/O  pages (UNIBUS address space).  The two Digital
          Equipment Corporation proprietary programs KMCLDR and  KMCDA
          are patched to include these sections and address them as if
          they are the I/O pages.


          BUSCOM          ______

               BUSCOM is used to create or delete two permanent  group
          global sections in memory.  The two sections UBUS0 and UBUS1
          are located at the UNIBUS zero and UNIBUS one address  space
          on  an  11/780.   The  program  should be run before the KMC
          loader or debugger is run.  All members in  the  same  group
          can  then  run  the  loader  or debugger.  The sections that
          BUSCOM creates will stay resident until the system is booted
          or  until  the  sections  are  deleted.   Two privileges are
          required to run this program, map to specific physical pages
          (PFNMAP)  and  create  permanent  global  sections (PRMGBL).
          These will be enabled by the program for the duration of its
          execution.
               To verify that the global sections have  been  created,
          issue  the  command "MCR INSTALL /GLOBAL".  The two sections
          will appear as "UBUS0_001" and "UBUS1_001" under the listing
          of  "Group Global Sections" with the group number from which
          the program BUSCOM was run.  Change mode to kernal  (CMKRNL)
          privilege is required for this command.
               BUSCOM asks a single  question,  whether  you  wish  to
          create,  delete  or  exit.   Either  case  single  character
          answers will suffice and no acknowledgement is made  if  the
          operation  is  successful.  If an error occurs then a status
          message will be printed.


          UBUS0 and UBUS1          _____ ___ _____

               The  files  UBUS0.*  and  UBUS1.*  are  used  when  the
          compatibility mode loader and debugger are built so that the
          task builder (TKB) can use the symbol tables for  reference.
          Both  the  tasks  (UBUS0.TSK  and  UBUS1.TSK) and the symbol
          tables (UBUS0.STB and UBUS1.STB)  must  be  present  in  the
          directory when building the loader and debugger.  The symbol
          tables and  tasks  are  necessary  because  the  loader  and
          debugger  are built so that they reference a resident common
          data area.
               If it becomes necessary  to  rebuild  either  of  these
          tasks   command  files  UBUS0BLD.COM  and  UBUS1BLD.COM  are
          provided.

                                                                Page 2


          PROPRIETARY SOURCE          ___________ ______

               The loader and debugger  are  named  KMCLDR  and  KMCDA
          respectively.   The  two programs are proprietary to DEC and
          therefore they could not be  included  in  this  submission.
          The  patches  that  are  described  here were applied to the
          following distribution from DEC, an RK05 pack dated  5/30/78
          with the label:

                                   AN-C914A-SC
                                   KMC-11 TOOLS V1 RK05

               The loader has the  ".ident"  of  /X01/  and  the  last
          change  is  from "J OLAPURATH 8/25/76".  The debugger has an
          ".ident"   of   /V0001A/   and    last    modification    of
          23-SEPTEMBER-77  by DAVID J.  MITTON.  I believe the current
          product number is QJ633 "KMC11 TOOLS".
               Also included in this distribution  was  a  macro  file
          (KMCMAC.MAC)  which  defines  all the KMC-11 mnemonics and a
          file which is used to set up break points in the KMC-11 code
          (BRKPNT.MAC).


          APPLYING PATCHES          ________ _______

               The two source language patch files are KMCLDR.SLP  and
          KMCDA.SLP.   They  should  be  invoked  as DCL command files
          ("@KMCLDR.SLP" and "@KMCDA.SLP").  They  include  checksums,
          and expect the PDP-11 versions of the loader and debugger to
          be in  the  current  directory.   A  differences  comparison
          listing  was generated and these are in the files KMCLDR.DIF
          and KMCDA.DIF.
               Two files KMCLDRBLD.COM and KMCDABLD.COM  are  provided
          for assembling and linking the loader and debugger.


          RUNNING KMCLDR AND KMCDA          _______ ______ ___ _____

               The only additional input to the programs beyond asking
          for  the  CSR  of the KMC is that both will ask for a UNIBUS
          number.  This should be answered with either a "0" or a "1".
          The  CSR  question  should be answered as normally with a 16
          bit value.


          EXAMPLE PROGRAM          _______ _______

               The files DRECHO.* contain an  example  KMC-11  program
          that will take input from a DR-11K and echo it back out.  It
          will continue until an interrupt and then it will perform an
          internal loop.  It must be stopped manually.
               The program can be loaded using KMCLDR, and then  after
          invoking KMCDA, a "G"o command will start it.

                                                                Page 3


          ASSEMBLING AND LINKING          __________ ___ _______

               To assemble and link KMC-11 source files a command file
          is  provided  with  the  name  KMCBLD.COM.   It  expects the
          KMCMAC.MAC (supplied with the debugging tools) macros to  be
          in the current directory.


          CLN TECO MACRO          ___ ____ _____

               The CLN.TEC file is used to clean up  assembly  listing
          files.  The programs should be assembled with the KMCMAC.MAC
          file provided and with a ".LIST MEB" directive.   The  clean
          macro will remove all the expansions and leave the addresses
          and machine code.  This is extremely helpful for  debugging.
          To  invoke  the  TECO macro you must already be TECO'ing the
          listing file and invoke the command "EICLN$$".


          COMMENTS AND SUGGESTIONS          ________ ___ ___________

               I welcome any comments or suggestions:


                                   Thomas J. Linscomb
                                   Computation Center
                                   The University of Texas at Austin
                                   Austin, TX 78712

                                   PHONE:  (512) 471-3241