FILE TRANSFER PROGRAM

FTP is a menu driven utility for copying files using DECnet.  It was written
for use by our system programming staff to aid in the task of keeping all
the system files consistent between two VAX's connected by DECnet.  It
provides a quick way to ship files back and forth between nodes.  Defaults
eliminate much of the extra typing needed with COPY commands.  FTP also allows
specification of file ownership, which COPY does not support.  FTP also
correctly handles copying of indexed files in some situations where COPY
does not.  The philosophy in chosing the defaults was to make it as simple
as possible to "distribute" system programs and command procedures to
several nodes.

FTP is written in VAX MACRO.  A sample command procedure is included for
building the program (the directory names probably will need to be changed).
FTP uses the Runtime Library Screen handling package to display the menu.
The display is not very elegant (junk gets left around sometimes).

The menu is divided into two parts.  The first part prompts once for the
source and destination node names and remote access username.  The option
shown in brackets is the default.  Enter a carriage return to pick it.  The 
second part of the menu prompts for the information related to each file to be
transferred.  Wildcard input filespecs are allowed.  This part of the menu 
repeats.  Enter a control-Z at any point to terminate FTP.  At any prompt you 
can enter a "?" to get a short summary of the legal responses.

The prompts and an explanation of the legal responses is given below:

Enter Source Node [current node]

	Requests the nodename to be prefixed to the source filespecs.  Enter
	the nodename.  A carriage return defaults to no nodename (i.e. this
	node.)  Entering a "." also selects the current node.  Entering 
	"." followed by a string appends that string to the default node
	prefix.  For example entering ".A" will select (in the distributed
	version of FTP) the node BCLVXA.
	This prefix is (alas) hard-coded into FTP.  It can be
	changed by changing the string given at the label OUR_PREFIX.

Enter Destination Node [all known nodes]

	Requests the nodename to be prefixed to the output filespecs.  Enter
	the nodename or a list of node names separated by commas.  The default,
	selected by entering a carriage return, is to send a copy of the file
	to all known nodes, described by the logical name FTP_KNOWN_NODES.
	For example, defining the logical name with

	$DEFINE FTP_KNOWN_NODES "XXA,XXB,XXC"

	will cause FTP to (by default) route the file to the nodes XXA, XXB,
	and XXC.  Entering a "*" will also select all known nodes.
	Entering a "@" will select all known nodes, except the current node.
	The "." and ".string" notation described above can also be used here.
	

Enter Remote Access Username [current username]

	Requests the username to be used when accessing a file on a remote 
	system.  This name is used to build a DECnet access control string
	used for any file which does not reside on the local node.
	Enter the username to be used.  The default, selected by a carriage
	return is the username from which FTP is running.  Entering a "."
	also selects the current username.  Entering ".S" selects the
	username SYSTEM.

Enter Remote Access Password

	Requests the password to accompany the above username.  The password
	must be supplied and is not echoed.  There is no default for this 
	response.

Enter Source Filespec

	Requests the filespec of files to be transferred.  Wildcard filespecs
	are allowed.  There is no default for this response.

Enter Destination Filespec

	Requests the filespec to be used when creating the copy of the file.
	Enter the filespec.  If the filename or type information is omitted,
	it defaults from the source file.  If the device information is 
	omitted, it defaults to the default device for the Remote Access
	Username.  If the directory information is omitted, it defaults to
	the default directory for the Remote Access Username.  If an empty
	pair of brackets [] appear in the filespec, they are replaced by the
	current default directory spec of the user running FTP.  The default
	selected by a carriage return or a "*" character is to exactly 
	duplicate the source filespec.

Enter File Owner UIC [existing file owner]

	Requests the UIC under which to create the destination file.  
	The Remote Access Username must be suitable privileged to set the
	file ownership to a UIC different from that of the Remote Access 
	Username.  The UIC can be entered with or without brackets.
	If a carriage return is entered, an attempt to locate an existing
	version of the destination file. If the file exists, the new version
	is created with the same ownership. If the file does not exist,
	ownership defaults to the Remote Access Username.  Specifying
	".X" also selects eXisting file ownership. Enter ".S" to select the
	SYSTEM uic, [1,4].  Enter ".D" to make the file owned by the Remote
	Access Username.  Selecting ".I" duplicates the ownership of the
	input file.

Enter File Protection [existing file's prot:]

	Requests the protection to be set for the destination file.  Enter
	a standard VMS file protection string, with or without the parens.
	If a carriage return is entered, FTP attempts to locate an
	existing version of the destination file.  If the file exists, the
	new version is created with the same protection.  If the file does
	not exist, protection defaults to the default for the Remote
	Access Username.  Specifying the abbreviation ".X" also selects
	eXisting file protection.  Specifying ".I" duplicates the protection
	of the input file.  Specifying the abbreviation ".P" selects the
	protection string (S:RWE,G:RWE,O:RWE,W).  Entering the 
	abbreviation ".R" selects the same protections as ".P", with the
	addition of world Read access.  Entering ".E" adds World execute
	access to ".P".  Entering ".RE" adds World read and execute
	access.  Selecting ".N" specifies the protection
	(S:RWE,G:RWED,O:RWED,W).

Please refer any comments, questions, (and maybe even criticisms) to:

	Gary L. Grebus
	Battelle Columbus Laboratories
	505 King Avenue
	Columbus, OH  43201
	(614)424-7156