1.0  INTRODUCTION

     This document describes the arithmetic  expression  handling
     facility  of  the  CDF Data Manipulation program.  Section 2
     describes  the  data  flow  during  expression   processing,
     Section  3  describes  the  data  structures and values used
     within the facility, and  Section  4  provides  the  calling
     sequences  for each of the modules comprising the expression
     processing software.







                                                           Page 2


     2.0  DATA FLOW

     The data  flow  for  the  expression  handling  facility  is
     described  in  Figure  1.   The expression handling facility
     consists  of  two  parts,  an  expression  parser   and   an
     interpreter.  An expression, in the form of an ASCII string,
     is passed into the expression parser.  The parser scans  the
     expression  and  produces a program consisting of constants,
     operators, and references to symbol  table  entries.   These
     references  are  converted  from the ASCII name of an entity
     into a symbol table index by a user  supplied  symbol  table
     access   routine.   The  interpreter  executes  the  program
     produced by the parser.  It gets the value associated with a
     symbol  table  index by calling a user supplied symbol table
     load routine.





                      !-------------!
                      !             !       ------------------
       Arithmetic     !    Parse    !          "Program" in
       Expression --->! Expression  !----->   Reverse Polish
                      !             !            Notation
                      !-------------!       ------------------
                        !      ^                         !
                        !      !                         !
                        !      !                         !
                        !      !                         !
                Symbol Name   Symbol Table               !
                        !      !  Index                  !
                        !      !                         !
                        !      !                         !
                        v      !                         !
                   ------------------                    v
                                      Type, Value !---------------!
                      Symbol Table   ------------>!               !  Result,
                                     <------------!   Interpret   !   Type,
                   ------------------   Symbol    !    Program    !-------->
                                      Table Index !               !  Value 
                                                  !---------------!




          Figure 1.  Expression Handling Facility Data Flow






                                                           Page 3


     3.0  INTERNAL DATA STRUCTURES

     The expression parser communicates the specified  expression
     to  the  interpreter by way of a "program" in reverse Polish
     notation.  The format of this program is  described  in  the
     following  three  tables.   Table  1  describes the opcodes,
     their modifiers, and their operands.  Table 2 describes  the
     modifier  field  for  the  UNARY opcode.  It lists the unary
     (i.e., single operand) operators, their internal code value,
     and  their  representation  in the expression text.  Table 3
     describes the modifier field  for  the  BINARY  opcode.   It
     lists  the  binary  (i.e.,  two  operand)  operators,  their
     internal  code  value,  and  their  representation  in   the
     expression text.




               Table 1 -- Polish Notation String Format


     The polish notation string consists of a series of opcodes
     followed by modifiers followed by operands.  All opcodes are
     one byte long.  The set of opcodes is: 

     name    value           description
     ----    -----           -----------
     halt      0          End of string.
     var       1          Push a variable onto stack.  The opcode
                            is followed by an operand (longword) 
                            containing the index of the variable
                            in the symbol table.  It has the format 
                            of an index as returned by getrtn (Section 4.6).
     const     2          Push a constant onto stack.  The opcode is 
                            followed by a modifier (one byte) and an
                            operand (quadword).  The modifier specifies
                            the type of the operand.  The operand
                            specifies the value of the constant to be
                            pushed onto the stack.
     unary     3          Execute a unary operator.  The opcode is
                            followed by a modifier (one byte) specifying
                            the specific operation to be performed.
                            (See Table 2.)
     binary    4          Execute a binary operator.  The opcode is 
                            followed by a modifier (one byte) specifying
                            the specific operand to be performed.
                            (See Table 3.)
     assign    5          Execute the assignment operator.  The opcode is
                            followed by a zero byte.






                                                           Page 4


                     Table 2 -- Unary Operations


           operation                code      symbol       
           ---------                ----      ------       
           negation                   1       -            
           arccosine                  2       acos         
           arcsine                    3       asin         
           arctangent                 4       atan         
           cosine                     5       cos          
           sine                       6       sin          
           tangent                    7       tan          
           arccosine (degrees)        8       acosd        
           arcsine (degrees)          9       asind        
           arctangent (degrees)      10       atand        
           cosine (degrees)          11       cosd         
           sine (degrees)            12       sind         
           tangent (degrees)         13       tand         
           square root               14       sqrt         
           exponential               15       exp          
           natural logarithm         16       log          
           common logarithm          17       log10, alog10
           absolute value            18       abs          
           integer value             19       int          
           nearest integer value     20       nint         
           real*4 value              21       real, float  
           zero extend               22       zext         
           real*8 value              23       dble         






                     Table 3 -- Binary Operations


              operation                code      symbol
              ---------                ----      ------
              addition                  1        +     
              subtraction               2        -     
              exponentiation            3        **    
              multiplication            4        *     
              division                  5        /     








                                                           Page 5


     4.0  MODULE SPECIFICATIONS

     The following sections  describe  the  three  modules  which
     comprise  the  expression  handling  facility.   Section 4.1
     describes the expression parser  (EXP_PARSE).   Section  4.2
     describes  the expression interpreter (EXP_INTERP).  Section
     4.3 describes a module which identifies fatal and  non-fatal
     error  conditions  (EXP_FATAL).   Section  4.4 describes the
     calling sequence for the symbol table load routine (LOADRTN)
     which must be supplied to EXP_INTERP.  Section 4.5 describes
     the calling sequence for  the  symbol  table  store  routine
     (STORERTN)  which  must  be supplied to EXP_INTERP.  Section
     4.6 describes the calling  sequence  for  the  symbol  table
     lookup routine (GETRTN) which must be supplied to EXP_PARSE.






                                                           Page 6


     4.1  EXP_PARSE


     module:  exp_parse

     purpose:  parse an arithmetic expression

     calling sequence:

             istat = exp_parse(inline, getrtn, flags, p_list, p_len, errmsg)

     argument list:

         name      type   i/o   description
         ----      ----   ---   -----------
         istat      i4     o    status return 
                                  .true. (odd) if successful
                                  .false. (even) if not successful
         inline    c*(*)   i    string containing arithmetic
                                  expression (should be converted
                                  to upper case prior to call)
         getrtn     ep     i    symbol table access routine
                                  (see Section 4.6 for details)
         flags      l4     i    flags controlling parser
                                  bit 0 = 1 => "=" not allowed
         p_list    c*(*)   o    polish notation list 
         p_len      i4     o    length of "program" in p_list
         errmsg    c*(*)   o    error message text. 
                                  valid if istat is .false.

     specific error values:

         exp__syntaxerr      syntax error in input
         exp__namenotfnd     zero was returned from getrtn
         exp__noassign       assignment operator was included in 
                             inline, but bit 0 in flags was set
         exp__exptoolarge    the exponent on a floating point
                             constant was too large
         exp__overflow       the "program" defined by inline
                             cannot fit in p_list








                                                           Page 7


     4.2  EXP_INTERP


     module:  exp_interp
      
     purpose:  to interpret a polish notation string
      
     calling sequence:

             istat = exp_interp(p_list, loadrtn, storertn, type, value)
      
     argument list:

         name          type   i/o   description
         ----          ----   ---   -----------
         istat         i*4     o    status return.
                                      .true. (odd) if successful
                                      .false. (even) if not successful
         p_list        c*(*)   i    polish notation string
         loadrtn       ep      i    symbol table access routine
                                      (see Section 4.4 for details)
         storertn      ep      i    symbol table access routine
                                      (see Section 4.5 for details)
         type          byte    o    type of expression
                                         1 = byte
                                         2 = integer*2
                                         3 = integer*4
                                         4 = real*4
                                         5 = real*8
         value        i*4/r*8  o    value of expression.  
                                         i*4 if type = 1,2,3
                                         r*8 if type = 4,5

     specific error values:

         exp__nolist         p_list is empty
         exp__badtype        bad type value in p_list 
                             or from loadrtn
         exp__nohalt         no halt opcode in p_list
         exp__badindex       "var" opcode had bad index 
                             (returned by loadrtn, storertn)
         exp__novalue        (returned by loadrtn)
         exp__badopcode      invalid opcode in p_list
         various SS$xxx, MTH$xxx, LIB$xxx codes, generally 
                             indicating an arithmetic error
                             or invalid argument to an
                             intrinsic function








                                                           Page 8


     4.3  EXP_FATAL

       
     module:  exp_fatal
       
     purpose:  determine whether an error from exp_interp should be fatal
       
     calling sequence:

             logical exp_fatal
             flag = exp_fatal(istat)
       
     argument list:

         name          type   i/o   description
         ----          ----   ---   -----------
         istat           i     i    status code from exp_interp
       






                                                           Page 9


     4.4  LOADRTN

       

     module:  loadrtn
      
     purpose:  load values from symbol table
      
     calling sequence:

             istat = loadrtn(index, type, value)
      
     argument list:

         name          type   i/o   description
         ----          ----   ---   -----------
         istat          i*4    o    status return 
                                      .true. (odd) if successful
                                      .false. (even) if not successful
         index          i*4    i    index of entry to load value from
         type          byte    o    type of expression
                                       1 = byte
                                       2 = integer*2
                                       3 = integer*4
                                       4 = real*4
                                       5 = real*8
         value        i*4/r*8  o    value of expression.  
                                       i*4 if type = 1,2,3
                                       r*8 if type = 4,5

     specific error values:

         exp__novalue        fill or no value stored
         exp__badindex       index is invalid
         exp__badtype        type is invalid


       






                                                          Page 10


     4.5  STORERTN

       

     module:  storertn
      
     purpose:  store a value in the symbol table
      
     calling sequence:

             istat = storertn(index, type, value)
      
     argument list:

         name          type   i/o   description
         ----          ----   ---   -----------
         istat          i*4    o    status return 
                                       .true. (odd) if successful
                                       .false. (even) if not successful
         index          i*4    i    index of entry to store value into
         type          byte    i    type of expression
                                         1 = byte
                                         2 = integer*2
                                         3 = integer*4
                                         4 = real*4
                                         5 = real*8
         value      i*4/r*8    i    value of expression.  
                                         i*4 if type = 1,2,3
                                         r*8 if type = 4,5

     specific error values:

         exp__badindex       index is invalid
         exp__badtype        type is invalid







                                                          Page 11


     4.6  GETRTN


     module:  getrtn
      
     purpose:  to determine the symbol table index 
         corresponding to a symbol name
      
     calling sequence:

             index = getrtn(name)
      
     argument list:

         name          type   i/o   description
         ----          ----   ---   -----------
         index         i*4     o    symbol table index or
                                      0 if symbol not found
         name          c*(*)   i    symbol to lookup in table