BLDSHR COMMAND PROCEDURE
  
  				Author:	Stanley S. Leroy
  					Code Code 5707.11
  					Naval Research Laboratory
  					4555 Overlook Avenue
  					Washington D.C. 20375
  
  		This procedure enables one to create
  	a shareable image library from an existing object
  	module library.  This is accomplished by generating
  	the transfer vectors for all the entry points in the
  	library.  In addition, all PSECTS other than $TRANS 
  	are changed from GBL,SHR to LCL,NOSHR.
  
  		Before the BLDSHR procedure is utilized, one line of
  	the DCL code must be tailored to be site specific. The logical
  	name for HDRMAR must be defined so as to properly point to the
  	resident directory where all the BLDSHR components are located.
  	In the command file this line is located at the beginning as
  	follows :
  	
    Define the directory for the resident BLDSHR components
  	This next line is site-specific :
  
   ***************************************************************
$	DEFINE HDRMAR DRA0:[STAN77]SHRHDR.MAR
   ***************************************************************
  	
  	Modify the device and directory name as required.
  
  		To begin with, the procedure requests the user 
  	to enter the filenames of 3 files. These are :
  
  	1 - THE FILENAME OF THE SOURCE OBJECT MODULE LIBRARY FILE
  	2 - THE FILENAME OF THE TRANSFER VECTOR MACRO FILE TO BE CREATED
  	3 - THE FILENAME OF THE LINK COMMAND FILE TO B CREATED
  
  	Only the FILENAME portion of the filespecifier should
  	be entered for these.
  
  		The last input requested is for the minor-id for
  	the GSMATCH options parameter. Generally, the default may
  	be taken. The user is referred to the VAX/VMS LINKER
  	REFERENCE MANUAL for complete details on this option.
  
  		The procedure executes two LINK operations of
  	the MACRO object.  The first generates the required LINK
  	MAP from which all required PSECTS are extracted and the
  	second to attempt to generate the final .EXE file for the
  	shareable image. If no PSECTS exist, then only one LINK
  	operation is required.
  
  		If, after these LINK operations, there are any
  	undefined symbols remaining, the required objects must
  	then be placed into the newly created LINK command file
  	and then re-linked during PHASE 3 of the procedure.
  	These symbols may be resolved in any of the usual ways,
  	that is, via object modules, object libraries, or even
  	other shareable image libraries.
  	
  		Once the .EXE file has been built, the system
  	manager creates a logical name in the SYSTEM  logical
  	name table to refer to that image.  Optionally he may
  	wish to copy the .EXE file into SYS$SYSTEM.  The
  	advantage of the latter step is to minimize the require-
  	ment for adding another KNOWN LIST for the INSTALL command,
  	since SYS$SYSTEM is one of the KNOWN LISTS to the INSTALL
  	utility.
  
  		The INSTALL operation is the last step in the
  	process.  Install the shareable image as /OPEN/WRITE/SHARE.
  	
  		The system manager should also include the 
  	assignment of the logical name and the INSTALL step
  	as part of the SYSTARTUP.COM procedure so that these
  	entities are available each time the system is re-booted.
  	These steps may be accomplished as follows:
  
  	$	DEFINE /SYSTEM SHRIMAGE SYS$SYSTEM:SHRIMAGE
  	$	INSTALL SHRIMAGE /OPEN/WRITE/SHARE
  
  	where SHRIMAGE represents the name of the shareable image library.
  		
  		Once the shareable image library has been installed
  	users may reference it at link time as follows :
  
  	$	LINK MYPROG,ANYOBJ,MYLIB/LIB,SYS$INPUT/OPT
  		SHRIMAGE/SHARE
  
  	where ANYOBJ is any optional reference to object modules and
  	MYLIB is any optional reference to other object module libraries.
	An alternative to this command, for example would be to create
	an OPTIONS file, say IMGOPT.OPT, which is accessible to all 
	users. This file would contain the line :

		SHRIMAGE/SHARE

	The associated LINK command would then be :

	$	LINK MYPROG,ANYOBJ,MYLIB/LIB,'IMGSYM'

	where IMGSYM is the global symbol defined as follows :

	$	IMGSYM:==DEV:[DIRECTORY]IMGOPT/OPT