Kermit-11 for RSTS, RSX11M/M Plus and RT11


01-Jun-84 09:33:12 Brian Nelson

Kermit is a protocal developed at Columbia  University  which  has  been
used  to  implement  error  free packet file transfer and communications
between computer systems, both  mainframe  to  mainframe  and  micro  to
mainframe.   The  complete  distribution of Kermit includes many CPM and
MS-DOS versions and mainframe versions for TOPS-10, TOPS-20, UNIX,  VMS,
RSX11M/M+  and  RSTS/E as well as other vendors systems.  Micro versions
include the Robin, Rainbow and Professional 350 as well  as  most  other
popular micro-computers.
The complete distribution is available from Columbia University Computer
Center in New York, NY.
This document describes only the RSTS/E and RSX11M/M+ version  developed
by the author, Brian Nelson.  


This is release 2.17 of Kermit-11 for RSTS and RSX11M/M+.   It  requires
RSTS  version 7.2 or later, RSX11M v4.0 or later, or RSX11M Plus version
2.0 or later, or RT11 version 4.0 or later.  
 
Minimum system requirements to assemble and link Kermit
 
        RSTS    v8.0 or later, with multiple private delimiters and RMS V2
        RSX11M  v4.1 or later, with full duplex terminal driver and RMS V2
        RSX11M+ v2.1 or later, with full duplex terminal driver and RMS V2
        RT11    v5.0 or later, with multiple terminal support
 
Minimum system requirements to run Kermit
 
        RSTS    v7.2 or later, with multiple private delimiters
        RSX11M  v4.0 or later, with full duplex terminal driver
        RSX11M+ v2.0 or later, with full duplex terminal driver
        RT11    v4.0 or later, with multiple terminal support
 
Kermit-11 will run on RSX11M version 4.0 and RSTS/E version 7.2 as  long
as  the task was built without using RMSRES.  To be able to build KERMIT
on RSTS version 7.2 or RSX version 4.0 you will have to  get  RMSLIB.OLB
and  MAC.TSK  from  RSX  v4.1  or  RSTS v8.0.  The need for version 2 of
RMSLIB is due to the use of $SEARCH, $PARSE, $RENAME and  $DELETE.   The
need  for the newest MAC.TSK is due to the use of new directives such as
.SAVE, .RESTORE and .INCLUDE /filename/.


For RSTS please note that you Do Not have to create RMS files as output.
You can instead either type SET RECORD-FORMAT STREAM, modify the default
in K11RMS.MAC or put the SET command in one of the following files:
 
        SY:KERMIT.INI
        LB:[1,2]KERMIT.INI
        SY:[1,2]KERMIT.INI
        KERMIT:KERMIT.INI



                                                           Page 2



 
This version of Kermit supports server mode  and  full  wildcarding  for
SEND  and  GET.  See the HELP command or the file K11HLP.RNO for further
information.
It also supports the CONNECT command, which can be used to dial  out  of
the  system  and talk to another Kermit somewhere else, say to a copy of
20KERMIT.  The connect command has only been tested with a  VADIC  212LS
autodial modem.  Modifications may be needed for the DF03.



                                                           Page 3



                          Installation


RSTS version 7.2 and later


First, please note that you MUST be running RSTS version  8.0  or  later
with  RMS11 version 2 installed on the system to be able to assemble and
link Kermit.  If you have version  7.2  you  can  run  the  non-resident
library version of the task but you will not be able to assemble or link
Kermit.  In all cases the RSTS executive must  have  in  it  the  sysgen
optional 'multiple private delimiters'.

If you have gotten a DOS format tape with the task images on it, you can
copy  either  K11.TSK (for use with RMSRES) or K11NRS.TSK (no RMSRES) to
the system and skip to the paragraph on the HELP file.  Tapes  sent  out
by Columbia will NOT have any task images on them.  See the next section
on 'HEX' files.  If you are running 7.2 you MUST use K11NRS.TSK.
 
        PIP $KERMIT<104>/RTS:RSX=MM0:[*,*]K11.TSK
        PIP $KERMIT<104>/RTS:RSX=MM0:[*,*]K11NRS.TSK
 

If you don't have the task images on tape you can compile (with F77) the
program  called  K11HEX.FTN  or use the Basic+ version called K11HEX.BAS
and create the task image from the so-called 'HEX' file (either  K11.HEX
or K11NRS.HEX).  If you are running 7.2 you MUST use K11NRS.HEX.
      
      f77 k11hex=k11hex
      
      Ready
      
      tkb
      TKB>k11hex=k11hex,lb:f4pots/lb
      TKB>/
      Enter Options:
      TKB>maxbuf=512
      TKB>//
      
      Ready
      
      run k11hex
      Input  file ? k11nrs.hex
      Output file ? kermit.tsk
      Encode or Decode ? decode
      all done
      For RSX, please make  the task image  contiguous as in
      
         PIP [1,54]KERMIT.TSK/CO=KERMIT.TSK
      
      For RSTS, make the task contiguous, set the protection
      to <104> and the rts name to RSX as in
      
         PIP [1,2]KERMIT.TSK<104>/MO:16/RTS:RSX=KERMIT.TSK
      



                                                           Page 4



      K11HEX  --  STOP
      
      Ready
 
Now skip to the paragraph on copying the HELP file.






                                                           Page 5



If you want to assemble and task build Kermit for RSTS version 8


First, it is assumed that MAC.TSK is available via  the  CCL  MAC.   The
batch  control  file  K11ASM.E80 will assemble Kermit.  You will have to
edit it to remove the account number references in it.  The user logical
IN:  must be assigned or MAC and TKB will fail.
Once BATCH has run the control file, you will have in your  account  the
objects for KERMIT.  The next step is to task build KERMIT, using either
K11.CMD or K11NRS.CMD (the former for RMSRES, the later without RMSRES).
These  files  are  TKB  command  files,  they also reference K11.ODL and
K11NRS.ODL.
 
        TKB @K11
 or     TKB @K11NRS
 
To be able to use ONLPAT on the task, you must now run the MAKSIL system
program to merge the symbol table into the task image.


The HELP file


The HELP file can be in one of several locations,  Kermit  will  try  to
find it.  They are:
 
        LB:[1,2]K11HLP.HLP
        SY:[1,2]K11HLP.HLP
        KERMIT:K11HLP.HLP
        HELP:K11HLP.HLP
 
Protection


The Kermit task should have either a <104> protection code  or  a  <234>
protection  code.   If you don not use the <234> the SYSTEM command will
not work for users.  The HELP file should have a <40> on it.



                                                           Page 6



         Patching the distributed task images for RSTS/E


!       RSTS/E Kermit optional patches
!
!       Brian Nelson  30-Mar-84  09:47:07
!
!
!        Example of patching RSTS/E Kermit to disable commands based
!       on user programmer  number.  The  effect  of  the  following
!       patches  is  to  disallow  any user with a programmer number
!       greater than  127  (ie,  100,221)  to  access  the  commands
!       DELETE  ,DIRECTORY,  ERASE  and RENAME. If you would like to
!       do this based  on  project  number  instead  you  can  patch
!       either  ...UIC+0  to  be  the  high  cutoff point instead of
!       patching ...UIC+2, or you can use different project  numbers
!       for  each  command by changing the '377' (which is in octal)
!       to the desired cutoff point. To restict access  to  the  DIR
!       command  to  users  with  a project (group) number less than
!       (10,*), you would patch ..$DIR byte offset zero  from  0  to
!       10.  (the  '.'  is  needed  to force ONLPAT to use a decimal
!       interpretation of the number. 
!
!        At this  time the only other thing you may want to patch is
!       location ..DIRP offset  zero, which  is by  default 1.  This
!       value is checked  against  the user's project  number by the
!       DIRECTORY command.  If the user's project  number is greater
!       than  this number,  the ppn (uic) field  for the DIR command
!       is zeroed,  thus  preventing that  user from looking  at the
!       directory listing  of ANY other  account.  The default is to
!       restrict the use  of ppn's for this  command to  [1,*] users
!       only.  The last patch here changes that to include [2,*].
!
!
!        Please note  that you can ALWAYS edit K11LCL.MAC to get the
!       same thing as applying these patches.
!
!
! Keep users with prog numbers > 127 from using DIR, DEL, REN and ERA.
!
!
File to patch? 
Base address? ...UIC+2
Offset address? 0
 Base   Offset  Old     New?
??????  000000  000000  ? 127.
??????  000002  041000  ? ^Z
Offset address? ^Z
Base address? ..$DEL
Offset address? -1
 Base   Offset  Old     New?
??????  177777     120  ? <LF>
??????  000000     000  ? 377
??????  000001     104  ? ^Z
Offset address? ^Z



                                                           Page 7



Base address? ..$DIR
Offset address? -1
 Base   Offset  Old     New?
??????  177777     114  ? <LF>
??????  000000     000  ? 377
??????  000001     104  ? ^Z
Offset address? ^Z
Base address? ..$ERA
Offset address? -1
 Base   Offset  Old     New?
??????  177777     123  ? <LF>
??????  000000     000  ? 377
??????  000001     105  ? ^Z
Offset address? ^Z
Base address? ..$REN
Offset address? -1
 Base   Offset  Old     New?
??????  177777     115  ? <LF>
??????  000000     000  ? 377
??????  000001     122  ? ^Z
Offset address? ^Z
Base address? ..DIRP
Offset address? 0
 Base   Offset  Old     New?
??????  000000  000001  ? 2
??????  000002  ??????  ? ^C
 




                                                           Page 8



RSX11M/M+


If you have gotten a tape with the task  images  on  it,  you  can  copy
K11RSX.TSK  (no  RMSRES)  to the system and skip to the paragraph on the
HELP file.

Tapes  sent  by  Columbia  will  have  a  so-called  'HEX'  file  called
K11RSX.HEX  which  is fed into the program K11HEX to create the RSX task
image as follows:
      
      >f77 k11hex=k11hex
      >tkb
      TKB>k11hex=k11hex,lb:[1,1]f4pots/lb
      TKB>/
      Enter Options:
      TKB>maxbuf=512
      TKB>//
      >run k11hex
      Input  file ? k11rsx.hex
      Output file ? kermit.tsk
      Encode or Decode ? decode
      all done
      For RSX, please make  the task image  contiguous as in
      
         PIP [1,54]KERMIT.TSK/CO=KERMIT.TSK
         INS $KERMIT/TASK=...KER
      
      For RSTS, make the task contiguous, set the protection
      to <104> and the rts name to RSX as in
      
         PIP [1,2]KERMIT.TSK<104>/MO:16/RTS:RSX=KERMIT.TSK
      
      K11HEX  --  STOP
      
      >
 


Assembling Kermit


First, it is assumed that MAC and TKB are installed.  The  command  file
K11ASM.M41 will assemble Kermit.  The user logical IN:  must be assigned
or MAC and TKB will fail.
 
  as in:        @K11ASM.M41
 
You then task build KERMIT.  The files K11RSX.CMD  and  K11RSX.ODL  will
build Kermit without RMSRES.  They both have comments to show what to do
to use RMSRES.
 
  as in:        TKB @K11RSX
 



                                                           Page 9



The HELP file


The HELP file can be in one of several locations,  Kermit  will  try  to
find it.  They are:
 
        LB:[1,2]K11HLP.HLP
        SY:[1,2]K11HLP.HLP
        KERMIT:K11HLP.HLP
        HELP:K11HLP.HLP
 



                                                          Page 10



RT11


This version of Kermit will run on RT11 version 4.0 or later as long  as
the  executive has multiple terminal support generated.  The use of this
feature enables the user to access DZ11's as well as DL11's.


Installation:

If the distribution has the save image K11RT4.SAV on it, you simple copy
them  with  the HELP file to the system volume and are ready to go.  The
file  K11RT4.SAV  has  been  assembled  with  All  modules  linked  into
K11RT4.SAV  have  been  assembled  with  a prefix file called K11NHD.MAC
which defines macros to simulate SOB, ASH, XOR, MUL and  DIV.   Thus  NO
eis  hardware  is required.  It has been tested extensively on a PDT150,
which does not support EIS instructions.

If the distribution does not contain the save image, you need the  files
K11RT4.HEX  and  K11HEX.FTN  to  generate  the save image from the 'hex'
file.  K11HEX.FTN is a fortran program and must be compiled and  linked.
When  this  has  been  done, run it, setting the file K11RT4.HEX for the
input file, KERMIT.SAV for the output file and DECODE for the  function.
If  you  lack a Fortran compiler, the same thing can be done on a RSTS/E
or RSX11M/M+ host and then transfered via FIT or FLX respectively  to  a
RT11 device.  



                                                          Page 11



                            Directory


 
 Name .Typ    Size    Prot    Date     DB1:[4,2]
README.TXT       1    < 60> 01-Jun-84
K11AAA.AAA       8    < 60> 04-Apr-84
K11HEX.BAS       6    < 60> 06-Apr-84
K11   .CMD       1    < 60> 30-Mar-84
K11NRS.CMD       1    < 60> 30-Mar-84
K11RSX.CMD       1    < 60> 03-May-84
K11RT4.CMD       1    < 60> 28-May-84
K11   .CTL       1    < 60> 23-Mar-84
K11INS.DOC      27    < 60> 30-Mar-84
K11ASM.E80       2    < 60> 25-May-84
K11DAP.E80       5    < 40> 19-Mar-83
K11HEX.FTN       8    < 60> 16-Apr-84
K11HLP.HLP      84    < 60> 31-May-84
K11ATR.MAC      17    < 60> 29-May-84
K11CDF.MAC       4    < 60> 29-May-84
K11CMD.MAC      77    < 60> 29-May-84
K11COM.MAC      12    < 60> 29-May-84
K11CON.MAC      31    < 60> 30-May-84
K11CPY.MAC      19    < 60> 29-May-84
K11CVT.MAC      11    < 60> 29-May-84
K11DAT.MAC       9    < 60> 29-May-84
K11DEB.MAC      15    < 60> 29-May-84
K11DER.MAC      16    < 60> 29-May-84
K11DFH.MAC       6    < 60> 29-May-84
K11ERR.MAC       4    < 60> 29-May-84
K11ER1.MAC       9    < 60> 29-May-84
K11ER2.MAC       9    < 60> 29-May-84
K11ER3.MAC       9    < 60> 29-May-84
K11E80.MAC      82    < 60> 29-May-84
K11HLP.MAC      21    < 60> 30-May-84
K11LCL.MAC      15    < 60> 29-May-84
K11MAC.MAC      19    < 60> 29-May-84
K11M41.MAC      69    < 60> 29-May-84
K11NHD.MAC       4    < 60> 10-Apr-84
K11PAK.MAC     161    < 60> 29-May-84
K11PK .MAC      73    < 60> 29-May-84
K11RMS.MAC      98    < 60> 29-May-84
K11RTC.MAC      31    < 60> 30-May-84
K11RT4.MAC      62    < 60> 29-May-84
K11SER.MAC      44    < 60> 29-May-84
K11SHO.MAC      21    < 60> 29-May-84
K11STT.MAC      35    < 60> 29-May-84
K11SUB.MAC      38    < 60> 29-May-84
K11TRA.MAC       7    < 60> 29-May-84
K1180S.MAC      33    < 60> 29-May-84
K11ASM.M41       2    < 60> 25-May-84
K11DAP.M41       4    < 60> 18-Mar-84
K11   .ODL       3    < 60> 23-May-84
K11NRS.ODL       2    < 60> 25-May-84
K11RSX.ODL       3    < 60> 25-May-84



                                                          Page 12



K11HLP.RNO      80    < 60> 31-May-84
K11INS.RNO      25    < 60> 30-Mar-84
K11ASM.RT4       2    < 60> 31-May-84
K11   .TSK     171    <104> 29-May-84
K11HEX.TSK      66C   <124> 23-Mar-84
K11NRS.TSK     304    <104> 29-May-84
K11RSX.TSK     223    <124> 30-May-84
K11RTT.MAC      26    < 60> 01-Jun-84
K11RT4.HEX     233    < 60> 01-Jun-84
K11RTN.HEX     235    < 60> 01-Jun-84
K11   .HEX     391    < 60> 30-May-84
K11RSX.HEX     509    < 60> 30-May-84
K11NRS.HEX     694    < 60> 30-May-84
K11RT4.SAV     102    <124> 01-Jun-84
K11RTN.SAV     103    <124> 01-Jun-84
 
Total of 4385 blocks in 65 files in DB1:[4,2]