PC-VT -  VT100/102/52 Terminal Emulator

                      (C) Copyright 1984,1985 Mark C. DiVecchio

                                     Version 7.6

































































          Forward


            Many trademarks are used through out  this  document.   I  will
          list and acknowledge them here.

                          IBM, IBM PC, and PC-DOS  are trademarks of
                          International Business Machines Corporation.

                          DEC, VMS, VAX and VT are trademarks of
                          Digital Equipment Corporation.

                          Smartmodem is a trademark of Hayes Microcomputer
                          Products.

            For more details on the operation  of a VT102 or a VT100, refer
          to the  VT102  and  VT100 Video Terminal User Guides published by
          Digital Equipment Corp, Educational Services Department, Maynard,
          Massachusetts 01754.

            Throughout  this document, hexidecimal numbers are followed  by
          the letter "H".  All other numbers are decimal.   Also, the ENTER
          key  on  the keyboard sends a carriage return character  -  ASCII
          code 13. A  carriage  return  function  moves  the  cursor to the
          beginning of  the  current  line.   "ESC"  refers  to  the  ASCII
          character whose decimal value is 26.

            PC-VT WARRANTY

            This program is provided on  an  "as is" basis without warranty
          of any kind, expressed or  implied,  including but not limited to
          the  implied  warranties  of  merchantability and fitness  for  a
          particular  purpose.   The  entire   risk   as   to  quality  and
          performance of this program is  with  you.   Should  the  program
          prove defective, you assume the  entire  cost  of  all  necessary
          repair, servicing, or correction.  In no event will the author be
          liable to you for any  damages,  including any lost profits, lost
          savings, or other incidental or consequential damages arising out
          of the use or inability to use this program.  This warranty gives
          you specific  legal  rights,  and you may have other rights which
          may vary from state  to  state.   Some  states  do  not allow the
          exclusion of implied warranties or  exclusion  of  liability  for
          incidental or consequential damages so the above may not apply to
          you.   You   acknowledge  that  you  have  read  this  agreement,
          understand  it,  and  agree  to   be   bound  by  its  terms  and
          conditions.  You further  agree  that  it  is  the  complete  and
          exclusive statement of the agreement between us, which supercedes
          any proposal or prior agreement,  oral  or written, and any other
          communications between us.













            THANKS

            I would like to thank all of  the  users  who  have  been  kind
          enough  to  send  me  their  ideas  and comments.  It is  through
          feedback of this nature that I can make PC-VT a better  and  more
          useful program.

            For the latest news on PC-VT, read the file on the distribution
          diskette named READ.ME.

                                  Mark C. DiVecchio
                                  9067 Hillery Drive
                                 San Diego, CA 92126

                                     619-566-6810









































                        Copyright 1984,1985 Mark C. DiVecchio        Page 3






          Introduction                                           PC-VT v7.6









                                      Chapter 1

                                     Introduction



            PC-VT is a software emulator which makes the IBM PC function as
          a  DEC  VT102 or a VT100 Video Terminal.  Selection  of  terminal
          type is  made  in the SETUP B display (Chapter 6). PC-VT defaults
          to  VT102  emulation.   PC-VT also  supports  VT52  compatibility
          mode.

            PC-VT emulates the majority of the functions of the  VT100/102.
          Because  of  either  hardware  limitations  of  the  IBM  PC   or
          limitations of  PC-DOS, some functions cannot be emulated.  Other
          functions have been slightly modified.  Throughout this document,
          references  are  made  to  these  changes  and deletions.   PC-VT
          handles all of the necessary functions to perform  as a VT100/102
          emulator.  The vast majority of users  will  never  notice  these
          hardware and PC-DOS mandated changes.

            The typical user will only need to read Chapters 2 through 5 of
          this  manual.   Chapter  6  is  only  necessary  if  any  of  the
          selectable  features  need   to   be  changed  from  the  default
          settings.  PC-VT comes pre-configured for the most popular set of
          features.  Communications parameters default to 1200 baud, 8 data
          bits,  no  parity  and  1 stop bits.   Chapter  7  describes  the
          VT100/102  "USER  MEMORY" which PC-VT emulates  by  creating  and
          using  a  disk  file.   Chapter  8  describes  the  Receive  File
          (Download)  and  Transmit  File  (Upload)  features.   Chapter  9
          describes the use of the Dialing facility which  is Hayes command
          compatible.  The macro key facility is described in  chapter  11.
          The more sophisticated user will find that the  Appendices give a
          complete description of the internal workings of PC-VT.

            DOS path names are supported for  upload/download  if  you  are
          using DOS 2 or later.

            -  Here is a brief list of the functions handled by PC-VT.

                 *  Emulates both VT100 and VT102 Terminals.  Emulates VT52
                    compatibility Mode of the VT100.

                 *  Communication  over an RS232 port configured as  either
                    COM1 or COM2 selectable from the SETUP display.




          Page 4        Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                           Introduction



                 *  Communications support for all of the popular baud rate
                    and data bit/parity bit combinations.

                 *  Full Duplex with no EIA modem control.  Only data leads
                    have to be connected (FDX A mode).   Suitable  for  use
                                                                          1
                    with a null modem (direct) connection  to  the  host
                    computer or with a modem which does not  require  modem
                    control signals.

                 *  VT52 Compatibility Mode.

                 *  Support  for  Hayes  dialing commands  and  includes  a
                    Dialing Directory with 10 entries.

                 *  ALT F1 thru ALT F10 as Macro keys.

                 *  Full receive parity checking can be enabled.

                 *  Both Numeric and Application Keypad modes.

                 *  Full cursor control.

                 *  Full feature Upload and Download file capability.  Both
                    ASCII  and  XMODEM (CRC capable) are  supported.   Path
                    name support is included if you  are  using  DOS  2  or
                    later.   ASCII  file  upload  includes  a   "handshake"
                    capability to compensate for slow host systems.

                 *  Capability to transmit a sustained Break.

                 *  NO SCROLL key XON/XOFF support.

                 *  Connection of a printer as LPT1 or LPT2 including local
                    print screen operations.

                 *  Capability to  echo all displayed characters to LPT1 or
                    LPT2 as hardcopy record of a terminal session.

                 *  Using  special  ALT key keystrokes, access  to  several
                    special function procedures.

                 *  SETUP A and SETUP B displays.

                 *  Full XON/XOFF support for both transmit and receive.



          ----------

          1. Throughout  this  manual,  the host refers to the computer "on
          the other end of the line" with which PC-VT is communicating.



                        Copyright 1984,1985 Mark C. DiVecchio        Page 5






          Introduction                                           PC-VT v7.6



                 *  ON LINE, LED "Lx" and KBD LOCKED lights  are  supported
                    via the use of  line  25  of the PC display as a status
                    line.  (4 LED are supported for the VT100 emulation,  1
                    for the VT102.)

                 *  For the more sophisticated  user,  the  majority of the
                    ANSI standard  and  DEC  private  Escape  sequences are
                    supported.

            -  Run DOS  functions  or  other  programs  without terminating
               PC-VT or disconnecting from the host.

            -  Use of the environment string 'PC-VT=' in order  to find the
               parameter files.

            -  Here is a brief list of what PC-VT can not handle.

                 *  Half duplex  modes  (HDX  A and HDX B) and special full
                    duplex modes (FDX B and FDX C).

                 *  Features   used   only   in   these    non    supported
                    communications modes.

                 *  Test and Adjustments Escape sequences.

                 *  Certain  display  attribute  handling  for  normal  and
                    reverse  video.   The IBM PC does  not  handle  reverse
                    video (black on white) the same way as  the  VT100/102.
                    The differences are detailed throughout this manual.

                 *  As mentioned earlier, functions with no IBM PC hardware
                    such as Smooth Scroll mode, 132 column mode, underscore
                    on   PC's  using  the  color  graphics  display   card,
                    Alternate Character ROM modes, and double  height/width
                    character modes.

            As an aid to  the  user  of PC-VT, PC-VT uses the speaker built
          into the IBM PC to indicate attempted illegal operations.   PC-VT
          beeps under the following conditions:

            1.  When the keyboard has been locked  by the host and a key is
                typed,

            2.  When an undefined key is pressed on the keyboard,

            3.  When a control character of 7 (Bell) is received,

            4.  When an attempt is made to perform an  illegal or undefined
                operation in a SETUP or the DIALING display.

            5.  When the  MODEM has lost communications or cannot transmit,
                PC-VT  times-out  after  trying  to  send  a character  for



          Page 6        Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                           Introduction



                one-half second.






















































                        Copyright 1984,1985 Mark C. DiVecchio        Page 7






          Required Hardware and Software                         PC-VT v7.6









                                      Chapter 2

                            Required Hardware and Software



            PC-VT  requires  an  IBM  PC  with  either  the  Monochrome  or
          Color/Graphics card, an 80  column  display,  64K  of  memory  (a
          better way  to  put  this,  is  enough for DOS plus about 32K for
          PC-VT), one disk drive and one RS-232  port.  The RS-232 port can
          be  jumpered  as COM1 or COM2.  A line printer,  if  present,  is
          supported if it  is  connected  to  a  parallel  port jumpered as
          either  LPT1  or LPT2.  The PC-DOS MODE command can  be  used  to
          route  LPT1  or LPT2 output to a COM port if a serial printer  is
          attached.  PC-VT  will  operate  under PC-DOS 1.1 or 2.x .  PC-VT
          more  closely  emulates  the  VT100/102  if  the  IBM  PC  has  a
          Color/Graphics card and  display.   Only minor reductions in user
          friendliness  occur with the Monochrome display.  PC-VT  supports
                            2
          the IBM fixed disk .

            PC-VT will support the  Hayes  Smartmodem  or compatible cards.
          Chapter 9 gives the details for their use.  The modem card can be
          configured as  COM1  or COM2.  If a standalone Modem is used, the
          RS-232 port in the IBM PC can also be configured either  as  COM1
          or COM2.

            A comment on DOS  :  If  you  don't have DOS 2.0 or 2.1, please
          invest the money and buy it.  The new versions of DOS added a lot
          of functionality to the IBM  PC, if you are running DOS 1.1 , you
          will not see that increased functionality.











          ----------

          2. The next chapter describes how to use  this  program  with the
          fixed disk.



          Page 8        Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         Starting PC-VT









                                      Chapter 3

                                    Starting PC-VT



            Place the supplied diskette into one of your  diskette  drives.
          Set the default  diskette  letter  in  DOS to that drive.  If you
          have a modem which requires manual  dialing,  dial  up  the  host
          computer and turn on the Modem.   Start  the  program  by  typing
          PC-VT.  PC-VT comes preinitialized  to  communicate  at 1200 baud
          with 8 data bits, no parity, and 1 stop bit.  If these parameters
          are not correct for your  installation  they can be changed.  See
          the discussion of the SETUP  displays  for instructions on how to
          change parameters.

            PC-VT creates and uses three files on  the disk to save default
          parameters.   The   files   are   PARAMS.DAT,   DIALER.DAT,   and
          MACRO.DAT.  These  files are automatically created in the default
          directory  on  the default drive.  If you are using  DOS  2.0  or
          later, you can specify an environment string which PC-VT will use
          to create and locate those three files.  You can specify the PATH
          command which  DOS  will  use to locate the PC-VT program itself.
          With these two features, you can execute PC-VT  without regard to
          which directory you currently have set.

            Use the set command as follows:

            set PC-VT=d:path

            Where 'd' is the drive letter and  'path' is the pathname.  The
          pathname can  be  any string which is acceptable to the DOS CHDIR
          command.  Some examples:

                  set PC-VT=              PC-VT will use the default
                                          directory on the default disk.
                  set PC-VT=c:            PC-VT will use the default
                                          directory on the 'c' drive.
                  set PC-VT=a:\           PC-VT will use the root
                                          directory on the 'a' drive.
                  set PC-VT=b:\able       PC-VT will use the directory
                                          named 'able' on the 'b' drive.

            Again, if  you  don't  bother with this option, PC-VT will just
          use the default directory on the default drive.




                        Copyright 1984,1985 Mark C. DiVecchio        Page 9






          Starting PC-VT                                         PC-VT v7.6



            As  PC-VT  starts  up,  it  will  initialize the COMx port  and
          establish  the  connection to the modem.  The CRT will  show  the
          communications display .  Lines 1 through  24  are  used  as  the
          emulated VT100/102 screen which has 24 lines.  Line 25 is used as
          a status line.  The first thing that you will  see  on line 25 is
          the word "ON LINE" and the version number of PC-VT in  the  lower
          left.  This indicates that PC-VT is  operating  normally  and  is
          ready to  communicate.   If  you have a Hayes or other compatible
          Modem, you can now automatically dial the  host's  number.   Type
          CTRL-F9 to enter the DIALING display.  See Chapter 9 for detailed
          instructions on how to use  this  DIALING  facility.   Most  host
          systems require that the terminal initiate communications so type
          ENTER.  Your host computer should now be responding.   From  this
                                                            3
          point on, PC-VT runs as a VT100/102 Video Terminal .

            In addition to the items described above, the  Status line also
          shows the status of the attached  modem if the cable to the modem
          carries all signals or if the  modem  is  an  internally  mounted
          unit.  These three icons are displayed:

            -  DSR - Data Set Ready - the modem is ready to accept data.

            -  CD - Carrier Detect - the modem has  detected  a  carrier on
               the phone line.

            -  CTS  -  Clear  To  Send  -  the  modem   has  completed  the
               establishment of a connection and  is  ready to send data to
               the Host.

            If you are using a "smart" modem, the modem may signal  CD  and
          CTS  even  when not connected to the Host.  There  is  usually  a
          switch on the modem to switch these two  lines  to  their correct
          operation.  Keep in mind that  PC-VT  doesn't  care  about  these
          lines, it just displays them for your information.

            Using PC-VT on the IBM fixed disk is  possible.   There  are no
          special requirements.  Copy the  program  PC-VT.EXE  to the fixed
          disk  and  use the 'set' command as described above  if  desired.
          Then just start up PC-VT.

            As an added feature  to PC-VT for users of DOS 2.+ , a new copy
          of  Command.COM  can  be  started  without  terminating PC-VT  or
          breaking the host connection.  To do this, just  type ALT-F (hold
          down the 'Alt' key and then press the 'f'  key).   You will see a

          ----------

          3. If  at  this  point,  nothing  is working or the PC beeps with
          every key  you  depress,  most likely the COMx to Modem interface
          was  not  correctly  initialized.    Terminate  and  restart  the
          program.  PC-VT will reset and will re-initialize the COMx port.



          Page 10       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         Starting PC-VT



          DOS prompt appear  on  the  screen.   You can now execute all DOS
          commands and even start up other programs.  Be  careful,  though,
          that you  do  not run a program that uses the same communications
          port or disk files as being used by PC-VT.  The other program may
          leave the communications port in  an  unknown state and PC-VT may
          not be able to regain  control of it.  When you wish to return to
          PC-VT, type "exit" at the  Command.COM  prompt.  You will then be
          returned to the PC-VT communications display.  The screen will be
          cleared.  PC-VT  uses the environment string 'COMSPEC=' to locate
          the command processor.













































                        Copyright 1984,1985 Mark C. DiVecchio       Page 11






          Stopping PC-VT                                         PC-VT v7.6









                                      Chapter 4

                                    Stopping PC-VT



            Since CTRL-C is a valid key for the VT100/102, PC-VT intercepts
          both that key and CTRL-BREAK before DOS can use them to terminate
          the program.

            You can terminate PC-VT in one of two ways:

            -  Type CTRL-F8 or

            -  Go  to  the SETUP, DIALING, or MACRO display and  then  type
               CTRL-BREAK or CTRL-C.  As  with  other  PC-DOS programs, the
               type  ahead  buffer  must  be  empty  for  CTRL-C  to   work
               correctly.

            The screen  will  clear,  control will return to PC-DOS and the
          PC-DOS prompt should appear.  The host connection is  not  broken
          (DTR  and  RTS  are  kept  active)  and  restarting  PC-VT   will
          re-establish communications.


























          Page 12       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments









                                      Chapter 5

                                 Keyboard assignments



            Since the keyboard on the  IBM  PC  is  not  the  same  as  the
          VT100/102, certain keys have to be mapped.  The basic keyboard is
          the same  of  course.   The keypad, cursor keys and certain other
          control keys are in different positions  on  the  two  keyboards.
          The other major difference is the lack of separate cursor keys on
          the PC (the cursor keys and the keypad occupy the same keys).

          Delete Key :    The backspace key on the IBM PC keyboard emulates
                          the DELETE key on the VT100/102. An option on the
                          SETUP B display enables you to change the IBM  PC
                          backspace key to send an ASCII 8 instead  of  the
                          ASCII 127 per the VT10x definition.

          Cursor Keys :   The four cursor  keys  on  the  IBM  PC  keyboard
                          emulate the four  cursor  keys  on the VT100/102.
                          NUM LOCK must be off for these keys to  function.
                          If  NUM  LOCK is set, the  keypad  generates  the
                          numeric characters shown on the keys.

          Function Keys :
                          In Numeric Keypad mode, F1 thru F4 on  the IBM PC
                          keyboard emulate the PF1 thru  PF4  keys  on  the
                          VT100/102.

                          In Application  Keypad mode, F1 thru F10 map onto
                          the VT100/102 keypad as follows  (PC-VT  displays
                          the  Greek  letter  "alpha"   on  the  status  to
                          indicate that this mode is set):


                          IBM PC key              VT100/102 key

                          F1                      PF1
                          F2                      PF2
                          F3                      7
                          F4                      8
                          F5                      4
                          F6                      5
                          F7                      1
                          F8                      2



                        Copyright 1984,1985 Mark C. DiVecchio       Page 13






          Keyboard assignments                                   PC-VT v7.6



                          F9                      0
                          F10                     0
                          Shift F1                PF3
                          Shift F2                PF4
                          Shift F3                9
                          Shift F4                - (minus sign)
                          Shift F5                6
                          Shift F6                , (comma)
                          Shift F7                3
                          Shift F8                ENTER
                          Shift F9                . (period)
                          Shift F10               ENTER

                          This assignment was selected  to  closely  follow
                          the   physical  layout  of  the  keypad  on   the
                          VT100/102. Observe that the  VT100/102  has  four
                          columns of keys  in  the  keypad.  PC-VT emulates
                          the two left  columns  with the function keys and
                          emulates  the two right columns with the  shifted
                          function keys.  It is expected that a user who is
                          familiar  with  the  VT100/102  keypad  and   has
                          memorized  the  position of each key,  will  have
                          little trouble using this function  key  mapping.
                          Note that the "0" key and  the  "ENTER"  key  are
                          mapped onto two of the PC keys.  This is  because
                          on the VT100/102, the  "0"  and  "ENTER" keys are
                          double width.  The drawing on the next page shows
                          this mapping  in a pictorial format.  The name of
                          the IBM PC key is in the upper left of each "key"
                          pictorial.  The emulated key  or function is then
                          shown in the center of the pictorial.

                          Note : NUM LOCK is handled locally in the IBM PC.
                          For the  keypad keys to work correctly when using
                          PC-VT, NUM LOCK should not be set.




















          Page 14       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments




                               KEYPAD FUNCTION MAPPING




                 FUNCTION KEYS               "SHIFT" FUNCTION KEYS
              --------------------------  --------------------------
              ............  ............  ............  ............
              .F1        .  .F2        .  .F1        .  .F2        .
              .          .  .          .  .          .  .          .
              .   PF1    .  .   PF2    .  .   PF3    .  .   PF4    .
              .          .  .          .  .          .  .          .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F3        .  .F4        .  .F3        .  .F4        .
              .          .  .          .  .          .  .          .
              .    7     .  .     8    .  .     9    .  .     -    .
              .          .  .          .  .          .  .          .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F5        .  .F6        .  .F5        .  .F6        .
              .          .  .          .  .          .  .          .
              .    4     .  .     5    .  .     6    .  .     ,    .
              .          .  .          .  .          .  .          .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F7        .  .F8        .  .F7        .  .F8        .
              .          .  .          .  .          .  .          .
              .    1     .  .     2    .  .     3    .  .   ENTER  .
              .          .  .             .          .  .          .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F9        .  .F10       .  .F9        .  .F10       .
              .          .  .          .  .          .  .          .
              .     0    .  .     0    .  .     .    .  .   ENTER  .
              .          .  .          .  .          .  .          .
              ............  ............  ............  ............









                        Copyright 1984,1985 Mark C. DiVecchio       Page 15






          Keyboard assignments                                   PC-VT v7.6




          Special key mapping for the EDT Editor :
                          In application keypad  mode,  which is set by the
                          DEC  EDT  text editor, the following  keys  cause
                          special  Escape  sequences   to  be  transmitted.
                          Observe that some of  these special keys transmit
                          sequences  that  would  require   two   or   more
                          keystrokes on the VT100/102. PC-VT  displays  the
                          Greek  letter  "alpha"  in  the  status  line  to
                          indicate that this mode is active.


                  IBM PC key              EDT function performed

                  Del key                 DEL C
                  Backspace               Deletes the character to the
                                          left of the cursor (DELETE key
                                          on the VT100/102)
                  ALT =                   DELETE key on the VT100/102
                  Ins key                 OPEN LINE
                  Home key                TOP
                  End key                 BOTTOM
                  PgUp key                BACKUP SECT
                  PgDn key                ADVANCE SECT
                  CTRL-Home key           Deletes the word to the left
                      or                  of the cursor (LINEFEED key
                  CTRL-Enter              on the VT100/102)
                  CTRL-End key            ADVANCE DEL EOL - Erases from
                                          the cursor to the end of the
                                          line.
                  CTRL-PgUp key           BACKUP PAGE
                  CTRL-PgDn key           ADVANCE PAGE
                  CTRL-Left Arrow key     BACKUP EOL - Move cursor to
                                          the end of the previous line.
                  CTRL-Right Arrow key    ADVANCE EOL - Move the cursor
                                          to the end of the current line.
                  SHIFT-Tab               Moves the cursor to the
                                          beginning of the line
                                          (BACKSPACE key on the VT100/102).
















          Page 16       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments




                          VT100/102 SPECIAL EDT KEY MAPPINGS




                 FUNCTION KEYS               SHIFTED FUNCTION KEYS
              --------------------------  --------------------------
          For Functions in (), press GOLD Key First.
              ............  ............  ............  ............
              .F1        .  .F2        .  .F1        .  .F2        .
              .          .  .          .  .          .  .          .
              .  GOLD    .  .  HELP    .  .  FNDNXT  .  .   DEL L  .
              .          .  .          .  .  (FIND)  .  .  (UND L) .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F3        .  .F4        .  .F3        .  .F4        .
              .          .  .          .  .          .  .          .
              .  PAGE    .  .  SECT    .  . APPEND   .  .   DEL W  .
              .(COMMAND) .  . (FILL)   .  .(REPLACE) .  .  (UND W) .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F5        .  .F6        .  .F5        .  .F6        .
              .          .  .          .  .          .  .          .
              . ADVANCE  .  . BACKUP   .  .   CUT    .  .   DEL C  .
              . (BOTTOM) .  .  (TOP)   .  . (PASTE)  .  .  (UND C) .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F7        .  .F8        .  .F7        .  .F8        .
              .          .  .          .  .          .  .          .
              .  WORD    .  .   EOL    .  .  CHAR    .  .  ENTER   .
              .(CHNG C)  .  . (DEL EOL).  .(SPECINS) .  .  (SUBS)  .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F9        .  .F10       .  .F9        .  .F10       .
              .  LINE    .  .  LINE    .  .  SELECT  .  .          .
              . (OPEN    .  . (OPEN    .  .  (RESET) .  .  ENTER   .
              .   LINE)  .  .   LINE)  .  .          .  .  (SUBS)  .
              ............  ............  ............  ............








                        Copyright 1984,1985 Mark C. DiVecchio       Page 17






          Keyboard assignments                                   PC-VT v7.6




                    VT100/102 SPECIAL EDT KEY MAPPINGS..continued




                PC KEYPAD KEYS as MAPPED into EDT
          --------------------------------------------------------------------
          For Functions in (), press GOLD Key First.
                        ............  ............  ............  ............
                        .7         .  .8         .  .9         .  .-[minus]  .
                        .          .  .          .  .          .  .          .
                        .  TOP     .  .  CURSOR  .  .  BACKUP  .  .          .
                        .          .  .    UP    .  .   SECT   .  .          .
                        ............  ............  ............  ............


                        ............  ............  ............  ............
                        .4         .  .5         .  .6         .  .+[plus]   .
                        .          .  .          .  .          .  .          .
                        .  CURSOR  .  .          .  .  CURSOR  .  .          .
                        .   LEFT   .  .          .  .   RIGHT  .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
                        ............  ............  ............  .          .
                        .1         .  .2         .  .3         .  .          .
                        .          .  .          .  .          .  .          .
                        .  BOTTOM  .  .  CURSOR  .  . ADVANCE  .  .          .
                        .          .  .   DOWN   .  .  SECT    .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
          ..........................  ..........................  .          .
          .0                       .  ..[period]               .  .          .
          .                        .  .                        .  .          .
          .      OPEN LINE         .  .         DEL C          .  .          .
          .        (LINE)          .  .        (UND C)         .  .          .
          ..........................  ..........................  ............
















          Page 18       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments




                    VT100/102 SPECIAL EDT KEY MAPPINGS..continued




                PC KEYPAD KEYS as MAPPED into EDT - HOLD DOWN CTRL KEY
          --------------------------------------------------------------------
                        ............  ............  ............  ............
                        .7         .  .8         .  .9         .  .-[minus]  .
                        . DELETE TO.  . CURSOR TO.  .  BACKUP  .  .          .
                        . START OF .  . START OF .  .   PAGE   .  .          .
                        . WORD     .  . LINE     .  .          .  .          .
                        ............  ............  ............  ............


                        ............  ............  ............  ............
                        .4         .  .5         .  .6         .  .+[plus]   .
                        . CURSOR TO.  .          .  . CURSOR TO.  .          .
                        . END OF   .  .          .  . END OF   .  .          .
                        . LAST LINE.  .          .  . LINE     .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
                        ............  ............  ............  .          .
                        .1         .  .2         .  .3         .  .          .
                        . ERASE TO .  .          .  . ADVANCE  .  .          .
                        . END OF   .  .          .  .  PAGE    .  .          .
                        . LINE     .  .          .  .          .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
          ..........................  ..........................  .          .
          .0                       .  ..[period]               .  .          .
          .                        .  .                        .  .          .
          .                        .  .                        .  .          .
          .                        .  .                        .  .          .
          ..........................  ..........................  ............

















                        Copyright 1984,1985 Mark C. DiVecchio       Page 19






          Keyboard assignments                                   PC-VT v7.6




                   VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPINGS




                 FUNCTION KEYS               SHIFTED FUNCTION KEYS
              --------------------------  --------------------------
          For Functions in (), press GOLD Key First.
              ............  ............  ............  ............
              .F1        .  .F2        .  .F1        .  .F2        .
              .          .  .          .  .          .  .          .
              .  GOLD    .  .  HELP    .  .   DEL L  .  .  NOT     .
              .          .  .          .  .  (UND L) .  .  USED    .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F3        .  .F4        .  .F3        .  .F4        .
              .          .  .          .  .          .  .          .
              .  PAGE    .  .  FNDNXT  .  .   DEL W  .  .  NOT     .
              .(COMMAND) .  .  (FIND)  .  .  (UND W) .  .  USED    .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F5        .  .F6        .  .F5        .  .F6        .
              .          .  .          .  .          .  .          .
              . ADVANCE  .  . BACKUP   .  .   DEL C  .  .  NOT     .
              . (BOTTOM) .  .  (TOP)   .  .  (UND C) .  .  USED    .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F7        .  .F8        .  .F7        .  .F8        .
              .          .  .          .  .          .  .          .
              .  WORD    .  .   EOL    .  .  CUT     .  .  ENTER   .
              .(CHNG C)  .  . (DEL EOL).  . (PASTE)  .  .  (SUBS)  .
              ............  ............  ............  ............


              ............  ............  ............  ............
              .F9        .  .F10       .  .F9        .  .F10       .
              .  LINE    .  .  LINE    .  .  SELECT  .  .          .
              . (OPEN    .  . (OPEN    .  .  (RESET) .  .  ENTER   .
              .   LINE)  .  .   LINE)  .  .          .  .  (SUBS)  .
              ............  ............  ............  ............








          Page 20       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments




             VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPINGS..continued




                PC KEYPAD KEYS as MAPPED into EDT
          --------------------------------------------------------------------
          For Functions in (), press GOLD Key First.
                        ............  ............  ............  ............
                        .7         .  .8         .  .9         .  .-[minus]  .
                        .          .  .  CURSOR  .  .          .  .          .
                        .  TOP     .  .    UP    .  .  BACKUP  .  .          .
                        .          .  .(REPLACE) .  .   SECT   .  .          .
                        ............  ............  ............  ............


                        ............  ............  ............  ............
                        .4         .  .5         .  .6         .  .+[plus]   .
                        .  CURSOR  .  .          .  .  CURSOR  .  .          .
                        .   LEFT   .  .          .  .   RIGHT  .  .          .
                        . (APPEND) .  .          .  . (SPECINS).  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
                        ............  ............  ............  .          .
                        .1         .  .2         .  .3         .  .          .
                        .          .  .  CURSOR  .  .          .  .          .
                        .  BOTTOM  .  .   DOWN   .  . ADVANCE  .  .          .
                        .          .  .  (SECT)  .  .  SECT    .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
          ..........................  ..........................  .          .
          .0                       .  ..[period]               .  .          .
          .                        .  .                        .  .          .
          .      OPEN LINE         .  .         DEL C          .  .          .
          .        (LINE)          .  .        (UND C)         .  .          .
          ..........................  ..........................  ............
















                        Copyright 1984,1985 Mark C. DiVecchio       Page 21






          Keyboard assignments                                   PC-VT v7.6




             VT52 COMPATIBILITY MODE SPECIAL EDT KEY MAPPINGS..continued




                PC KEYPAD KEYS as MAPPED into EDT - HOLD DOWN CTRL KEY
          --------------------------------------------------------------------
                        ............  ............  ............  ............
                        .7         .  .8         .  .9         .  .-[minus]  .
                        . DELETE TO.  . CURSOR TO.  .  BACKUP  .  .          .
                        . START OF .  . START OF .  .   PAGE   .  .          .
                        . WORD     .  . LINE     .  .          .  .          .
                        ............  ............  ............  ............


                        ............  ............  ............  ............
                        .4         .  .5         .  .6         .  .+[plus]   .
                        . CURSOR TO.  .          .  . CURSOR TO.  .          .
                        . END OF   .  .          .  . END OF   .  .          .
                        . LAST LINE.  .          .  . LINE     .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
                        ............  ............  ............  .          .
                        .1         .  .2         .  .3         .  .          .
                        . ERASE TO .  .          .  . ADVANCE  .  .          .
                        . END OF   .  .          .  .  PAGE    .  .          .
                        . LINE     .  .          .  .          .  .          .
                        ............  ............  ............  .          .
                                                                  .          .
                                                                  .          .
          ..........................  ..........................  .          .
          .0                       .  ..[period]               .  .          .
          .                        .  .                        .  .          .
          .                        .  .                        .  .          .
          .                        .  .                        .  .          .
          ..........................  ..........................  ............

















          Page 22       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                   Keyboard assignments




          Shift Tab :     The shift tab key sends a backspace character  to
                          the host.  Emulates the VT100/102 BACKSPACE  key.
                          If you  want  the  IBM PC backspace key to send a
                          BACKSPACE (ASCII 8) you  can  change  this on the
                          SETUP B display.

          CTRL-ENTER :    This key  combination sends a line feed character
                          to the host.

          CTRL-@ :        This key combination sends a NUL character (ASCII
                          0) to the host.  Used by  Emacs  running  on  DEC
                          VAX.

          SCROLL LOCK :   The SCROLL LOCK key on  IBM  PC alternately sends
                          XON and XOFF and emulates the NO  SCROLL  key  on
                          the  VT100/102. PC-VT displays the word "SCR"  on
                          the status line of the display to remind you that
                          the SCROLL  LOCK  key  has  been  depressed once.
                          Depressing  the key again resets SCROLL LOCK  and
                          clears the reminder.

          NUM LOCK :      The  NUM  LOCK  key  places the IBM PC keypad  in
                          numeric mode.  The NUM LOCK key functions locally
                          in  the   PC  only  and  does  not  transmit  any
                          characters to the host computer.  PC-VT  displays
                          the word "NUM" on the status line of the  display
                          to remind you that the  NUM  LOCK  key  has  been
                          depressed once.  Depressing the key again  resets
                          NUM LOCK and clears the reminder.

          CAPS LOCK :     The CAPS  LOCK  key places the IBM PC keyboard in
                          uppercase mode.   The  CAPS  LOCK  key  functions
                          locally in the PC only and does not transmit  any
                          characters to the host computer.  PC-VT  displays
                          the word "CAP" on the status line of the  display
                          to remind you that the CAPS  LOCK  key  has  been
                          depressed once.  Depressing the key again  resets
                          CAPS LOCK and clears the reminder.

          CTRL-F1 :       PC-VT enters the SETUP display.  See Chapter 6.

          CTRL-F2 :       This   command   lets  you  change  the  default
                          directory for  uploading  and  downloading files.
                          See Chapter 8.

          CTRL-F3 :       See Chapter 8.

          CTRL-F4 :       See Chapter 8.

          CTRL-F5 :       Print  screen.   The  screen  is  printed on  the
                          selected  line  printer  (LPT1   or   LPT2),   if



                        Copyright 1984,1985 Mark C. DiVecchio       Page 23






          Keyboard assignments                                   PC-VT v7.6



                          present.   The  line printer is selected  in  the
                          SETUP  B display.  Performs the same function  as
                          receipt of a "ESC [ i" sequence.   If  the  Print
                          Termination  Character  is  set in  the  SETUP  B
                          display, a  Form Feed will be performed after the
                          screen is printed.

          CTRL-F6 :       Echo  to selected line printer  (LPT1  or  LPT2).
                          Toggles  On/Off  echoing  to  the  selected  line
                          printer,  if  present.   The  line   printer   is
                          selected in  the  SETUP  B  display.   Prints all
                          characters received  or  transmitted  to/from the
                          host.  Characters displayed on  the  status  line
                          (line  25) are never printed.  Performs the  same
                          function as receipt of "ESC [ ?   5 i" and "ESC [
                          ?  4 i" sequences.

          CTRL-F7 :       To  send a sustained  break  to  the  host,  type
                          CTRL-F7.  Confirmation of the operation is a beep
                          at the start of the break along with another beep
                          at the end  of  the operation.  If the disconnect
                          character feature  is  selected  in  the  SETUP B
                          display,  PC-VT sends an EOT character (ASCII  4)
                          before it sends the break.

          CTRL-F8 :       Terminates PC-VT and returns to DOS.

          CTRL-F9 :       Enters the DIALING display.   See  Chapter  9 for
                          instructions.

          CTRL-F10 :      Complete restart.  Performs the  same function as
                          receipt of  a "ESC c" sequence.  All features and
                          tab stops  are reloaded from the USER MEMORY disk
                          file.  PC-VT then restarts.

          ALT-K :         Enters  the Macro display.  See  Chapter  11  for
                          instructions.


















          Page 24       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         SETUP Displays









                                      Chapter 6

                                    SETUP Displays



            The SETUP displays are accessed  by  typing  CTRL-F1  from  the
          communications display.  SETUP A is entered first.  If you have a
          Color/Graphics  card, the contents of the communications  display
          are preserved and are restored when you  exit SETUP.  If you have
          a Monochrome card, the communications display is cleared when you
          enter SETUP.

            The SETUP  display  can  also used to cancel PC-VT.  The CTRL-C
          and  CTRL-BREAK  keys are disabled while  in  the  communications
          display.  To cancel PC-VT, type CTRL-F1 to enter this display and
          then type CTRL-C or CTRL-BREAK.




          6.1 SETUP A


            The  SETUP  A display is used to perform the  functions  listed
          below.   The  bottom two lines of the display represent  the  tab
          stops which are set.  The bottom line  counts the columns and the
          line above it shows a "T" in each  column  where  a  tab  is set.
          Here are the functions available in SETUP A:

          Exit SETUP :    The  ESC  key  or  the  CTRL-F1  key  combination
                          returns PC-VT to the communications display.

          Reset :         The  "0" key clears the  tabs  and  features  and
                          reloads them  from  the  USER  MEMORY  disk file,
                          PARAMS.DAT, on the  default  drive.   PC-VT  then
                          returns to the communications display.

          Set/Clear Tabs :
                          The "2"  key  sets  or clears a tab at the column
                          position  of  the  cursor.  The  left  and  right
                          arrows, the tab key, the space bar, and the ENTER
                          key can be used to move the cursor  to the column
                          in which you want to set or clear the tab.  A "T"
                          will appear to indicate that a tab was set or the
                          "T" will be blanked to indicate that  a  tab  was



                        Copyright 1984,1985 Mark C. DiVecchio       Page 25






          SETUP Displays                                         PC-VT v7.6



                          cleared.   In either case, the character will  be
                          highlited to indicate that a change was made.

          Clear All Tabs :
                          The "3" key clears all tab stops.  All of the "T"
                          tab stop indicators will be cleared.

          Go to SETUP B :
                          The "5" key selects the SETUP B display.

          Store into USER MEMORY :
                          The "shift S" key  stores  all  currently set tab
                          stops and features selected by  SETUP  B  into  a
                          disk file  on the PC-DOS default drive.  The name
                          of the file is PARAMS.DAT.

          Reset :         The  "shift R" key clears the tabs  and  features
                          and reloads  them from the USER MEMORY disk file,
                          PARAMS.DAT, on the default drive.  PC-VT  remains
                          in the SETUP A display.

          Select General Default :
                          The "shift D" key clears any user  set  tabs  and
                          features (from  SETUP B) and resets them to PC-VT
                          defined defaults.

          Select Tab Default :
                          The "shift T" key clears any user  set  tabs  and
                          resets them to every 8 columns as follows:

                          Columns 9, 17, 25, 33, 41, 49, 57, 65, and 73.

                          A "T" will appear in each of these columns on the
                          second  line  from  the  bottom  of  the SETUP  A
                          display to indicate that a tab is set.

            Incr/Decr Line Turnaround Character =  xx  (ASCII  :  y):  This
          character is used in conjunction with ASCII  file  upload.   When
          uploading, PC-VT  can  be told to wait for this character (the =t
          option) to be sent by the  Host before PC-VT sends the next line.
          For our  purposes,  a line ends when a carriage return (ASCII 13)
          is  uploaded.  The value of  xx  is  the  decimal  value  of  the
          character, and y is the actual ASCII character.  The character is
          not displayed if it is less than 32 or  equal  to 255. The "shift
          L" key will increment this value and the "shift K" will decrement
          it.  You must execute a "store into  USER MEMORY" command to save
          the  new  value of this character on disk.  Otherwise,  the  next
          time that you start PC-VT,  the  original value is restored.  The
          first time that PC-VT starts, this character is set to the dollar
          sign character, decimal 36.





          Page 26       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         SETUP Displays







          6.2 SETUP B


            The  SETUP  B display is used to perform the  functions  listed
          below.  The bottom line of the display  represents  the  features
          which are set or reset.  See  the next section for details of the
          features.   The  number  of  data  bits  and the parity type  are
          displayed.  The COM port speed is displayed.   The  selected  COM
          port is displayed.  LPTx is displayed to  indicate  the  selected
          line printer (either LPT1  or  LPT2).   Here  are  the  functions
          available in SETUP B:

          Exit SETUP :    Hit  the  ESC key or type CTRL-F1 to exit SETUP B
                          and return to the communications display.

          Go to SETUP A :
                          The "5" key selects the SETUP A display.

          Toggle 1/0 :    The "6" key sets(1) or resets(0) a feature at the
                          column position  of  the  cursor.   The  left and
                          right arrows, the tab key, the space bar, and the
                          ENTER key can be used  to  move the cursor to the
                          column  which  you  want  to  set  or  clear  the
                          feature.  Features displayed with  an "X" are set
                          to an automatic  default  and  cannot be changed.
                          Other features will change from a "1" to a "0" or
                          from a "0" to a "1" to indicate that the state of
                          the feature  has been changed.  The digit will be
                          highlited to indicate that a change was made.  To
                          preserve these features in  your USER MEMORY disk
                          file you must perform a "shift  S  -  Store  into
                          USER MEMORY"  command  in  the  SETUP  A display.
                          Otherwise,  the old values will be reloaded  when
                          you again start up PC-VT.

          COM Port Selection :
                          COM1 or COM2 can be selected by flipping the  4th
                          bit of the 6th group of feature bits shown on the
                          bottom of the SETUP B display.  The word COM1  or
                          COM2 will display next to the word MODEM on  this
                          display to indicate which RS232 port is in use by
                          PC-VT.  If you want to change ports, just  go  to
                          SETUP B display, space over to the 4th bit of the
                          6th group and then type the "6" key.   This  will
                          cause the 1 or 0 in  the  feature  bit  to  flip.
                          Then return to the SETUP A display by typing  "5"
                          and  store  the  new  value into USER  MEMORY  by
                          typing Shift-"s".



                        Copyright 1984,1985 Mark C. DiVecchio       Page 27






          SETUP Displays                                         PC-VT v7.6



          Modem Speed Control :
                          The "7" key  causes  PC-VT to display the various
                          Modem  speeds supported.  The currently  selected
                          speed is displayed  under  the MODEM title on the
                          CRT.  Type the "7" key repeatedly until the speed
                          you need is  displayed.   The  new speed selected
                          will be highlited  to  indicate that a change was
                          made.  The supported speeds are:

                          100 baud                150 baud
                          300 baud                600 baud
                          1200 baud (default)     2400 baud
                          4800 baud               9600 baud

                          To  preserve  this speed selection in  your  USER
                          MEMORY disk file you must perform a  "shift  S  -
                          Store into USER MEMORY"  command  in  the SETUP A
                          display.   Otherwise,  the  old  values  will  be
                          reloaded when you again start up PC-VT.

          Select Data/Parity Bits :
                          The "shift P" key causes  PC-VT  to  display  the
                          various  data  bits/parity bits  supported.   The
                          currently   selected    Data   bits/Parity   bits
                          combination  is  displayed on the CRT  under  the
                          MODEM  title.  Type the "shift P" key  repeatedly
                          until the data bits/parity bits  combination  you
                          need  is  displayed.  The new selection  will  be
                          highlited  to  indicate that a change  was  made.
                          The supported combinations are:

                          7O      7 data bits - odd parity
                          7E      7 data bits - even parity
                          7N      7 data bits - no parity
                          8O      8 data bits - odd parity
                          8E      8 data bits - even parity
                          8N      8 data bits - no parity (default)

                          To    preserve   these   Data   bit/Parity    bit
                          combinations in your  USER  MEMORY  disk file you
                          must perform a "shift S - Store into USER MEMORY"
                          - command in the SETUP A display.  Otherwise, the
                          old values  will be reloaded when you again start
                          up  PC-VT.   If  you  are running a  212A  modem,
                          certain   of   the  data   bits/parity/stop   bit
                          combinations  are  invalid.    Check  your  modem
                          manual for the valid combinations.

                          Note that actual  parity  checking  is enabled by
                          setting  a  feature  in  this  display.    Parity
                          checking defaults to off.




          Page 28       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         SETUP Displays



          Set Answerback Message :
                          The "shift A" key permits you to enter a  message
                          with  which  PC-VT  will  use  to  respond to  an
                          Enquire control character.  Any character with an
                          ASCII code from 0 to  127  can be entered in this
                          message (Including the use of the ALT key and the
                          keypad to enter special  characters).   To  enter
                          the  message, type "shift A". PC-VT will  display
                          the prompt "A=".   The  prompt  will be highlited
                          and blinking.   You may then type in the message.
                          The  first  character  typed  is   considered   a
                          delimiter  by PC-VT.  This character must not  be
                          present  in the answerback message itself and  is
                          used only to  bracket  the  message since control
                          characters like carriage  return  can  be part of
                          the message.  Following  the  message,  type  the
                          delimiter  character  and  the  message  will  be
                          stored in  memory.  If you make a typing mistake,
                          you  must type the delimiter character and  start
                          the process  over  again.   This  is  because the
                          backspace key will not act as a text  editor  but
                          will  actually  be   entered   as   part  of  the
                          answerback message.  While you are entering  this
                          message, non-displayable characters will be shown
                          as a diamond.   The  message will be highlited to
                          indicate  that  a  change   is  being  made.   To
                          preserve this message  in  your  USER MEMORY disk
                          file you must perform a "shift  S  -  Store  into
                          USER MEMORY" - command  in  the  SETUP A display.
                          Otherwise,  the  old  message, if  any,  will  be
                          reloaded when you again start up PC-VT.

                          The default answerback message  is null, that is,
                          nothing is transmitted in  response to an Enquire
                          control character.


          6.2.1 SETUP B Features and Defaults

            The SETUP  B  display is used to select features of PC-VT.  The
          features  are  listed  below  along  with  their  defaults.   The
          procedures for changing  and  saving these features was described
          in the first part of this subsection.

          Group 1         Default Value
                          X = feature is not supported

          Scroll          X       The IBM PC does not support
                                  smooth scroll.

          Auto Repeat     1       0 = Disable autorepeat. PC-VT can only
                                  approximate this function since



                        Copyright 1984,1985 Mark C. DiVecchio       Page 29






          SETUP Displays                                         PC-VT v7.6



                                  it is handled within the keyboard.

                                  1 = Enable autorepeat (default).

          Screen          0       0 = dark background (default)
          Background              1 = light background

          Cursor          0       0 = underline cursor (default)
                                  1 = block cursor

          Group 2         Default Value
                          X = feature is not supported

          Margin Bell     X       Margin bell is not supported.

          Key Click       X       Key Click is not supported.

          ANSI/VT52       1       Select terminal mode.
                                  0 = VT52 compatibility mode.
                                  1 = ANSI mode (default). That is, either
                                  VT100 or VT102 depending on the setting
                                  of the bit in Group 6 below.

          Auto XON/XOFF   1       0 = XOFF is ignored. PC-VT's buffer may
                                  overflow with out warning or indication.
                                  1 = XOFF stops PC-VT from transmitting.
                                  PC-VT stops transmitting characters when
                                  an XOFF is received and will transmit
                                  an XOFF when 90% of its receive buffer
                                  is full (230 characters). It will then
                                  transmit XON when the buffer has been
                                  emptied to 10% full (26 characters).
                                  If the host ignores the XOFF character
                                  and continues to send, PC-VT will
                                  display a checkerboard character to
                                  indicate that data has been lost. When
                                  PC-VT receives an XOFF, an 'X' is
                                  displayed in column 41 of the status
                                  line. If you try to type a character
                                  when the 'X' is displayed, PC-VT beep
                                  and reject the character. See the
                                  'alt-x' key definition in the
                                  appendix for more details.
                                  (default)

          Group 3         Default Value
                          X = feature is not supported

          Character Set   0       0 = Select US Characters.
                                  The US character set is selected as the
                                  default (default).
                                  1 = Select UK Characters.



          Page 30       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         SETUP Displays



                                  The UK character set is selected as the
                                  default.

                                  (Note that the only difference between
                                  the two is the shift 3 character. In the
                                  US set, it is the "#" sign. In the UK set,
                                  it is the UK Pound sign.)

          Auto Wrap       0       0 = Auto wrap off.
                                  If the cursor is at the right margin and
                                  another character is received, PC-VT
                                  displays that character and all following
                                  received characters at the right margin
                                  position effectively writing over one
                                  another (default).
                                  1 = Auto wrap on - If the cursor is at
                                  the right margin and another character
                                  is received, PC-VT will perform a
                                  carriage return and line feed before
                                  displaying that character.

          Line Feed /     0       0 = LF/NL off - Typing ENTER
          New Line                sends only a carriage return
                                  to the host. The host must echo a
                                  carriage return and line feed to
                                  move the cursor to the beginning
                                  of the next line (default).
                                  1 = LF/NL on - Typing ENTER
                                  sends both a carriage return
                                  and a line feed to the host. A line
                                  feed is processed just like a
                                  carriage return.

          Local Echo      0       0 = Local echo off.
                                  - The host must echo back all typed
                                  characters in order for them to be
                                  displayed on the screen (default).
                                  1 = Local echo on - PC-VT will
                                  automatically display all characters
                                  typed. The host need not echo them
                                  back.

          Group 4         Default Value
                          X = feature is not supported

          Print           1       0 = none - No control characters
          Termination             are sent to the line printer following
          Character               a print screen operation.
                                  1 = Form feed - A form feed is
                                  sent to the line printer following
                                  a print screen operation (default).




                        Copyright 1984,1985 Mark C. DiVecchio       Page 31






          SETUP Displays                                         PC-VT v7.6



          Print Extent    1       0 = Scrolling region - A print
                                  screen operation will print the
                                  scrolling region as set by the
                                  host computer only.
                                  1 = Full screen - A print screen
                                  operation will print the entire
                                  screen (default).

          Stop Bits       0       0 = 1 stop bit
                                  is used by the RS232 interface (default).
                                  1 = 2 stop bits are used by
                                  the RS232 interface.

          Receive Parity  0       0 = Parity on received
                                  data is not checked (default).
                                  1 = Parity checking is enabled. PC-VT
                                  displays a '!' character in place of the
                                  character with the bad parity.


          Group 5         Default Value
                          X = feature is not supported

          Backspace       0       0 = Send the backspace key as 7Fh (ASCII 127)
                                  - the VT10x DELETE key (default).
                                  1 = Send the backspace key as 08h
                                  - the IBM PC standard.
                                  When you are doing this, you can still send a
                                  DEL (ASCII 127) by typing ALT = . (Press the
                                  Alt key and the equal sign key at the same
                                  time.)

          Disconnect      0       0 = Terminal ignores the
          Character               disconnect character (default).
          Enable                  1 = If PC-VT receives the
                                  disconnect character ( an EOT
                                  with an ASCII value of 4),
                                  it transmits a sustained Break
                                  and disconnects from the host
                                  computer.

          Disconnect      X       Not supported.
          Delay

          Auto            X       Not supported. This feature does
          Answerback              not affect transmission of the
          Enable                  answer back message if a control
                                  character 5 (Enquire) is received.

          Group 6         Default Value
                          X = feature is not supported




          Page 32       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                         SETUP Displays



          Line Printer    0       0 = LPT1 is selected (default).
                                  1 = LPT2 is selected.


          Slow Host       1       0 = Send XOFF when buffer is half full.
                                  1 = Send XOFF when buffer is 75% full.
                                  (default)

                                  This Switch was added mostly for PRIME 2550
                                  users. When PC-VT sends an XOFF to the host,
                                  it expects fairly rapid attention. The VAX's
                                  are very fast, the PRIME's are very slow.
                                  If you are experiencing loss of data, set
                                  this switch to 0. Note, PC-VT will put the
                                  '#' character into its communications buffer
                                  if an overflow occurs.


          Terminal type   0       0 = PC-VT emulates a VT102 (default).
                                  1 = PC-VT emulates a VT100.


          COM Port        0       0 = PC-VT uses COM1 as the communications
                                      port (default).
                                  1 = PC-VT uses COM2 as the communications
                                      port.


          Group 7         Default Value
                          X = feature is not supported

          Power           X       Not under PC-VT control.

          WPS Terminal    X       Not yet supported.
          Keyboard

          Clock           1       0 = Do not display the clock and MODEM status
                                  on the Status Line.
                                  1 = Display the time of day clock and MODEM
                                  status on the Status Line (default).

          256 Char        0       0 = If 8 bit data is selected for receive,
                                  the 8th bit is cleared to binary zero
                                  if it is on received data. PC-VT will
                                  display characters only from the first
                                  128 ASCII codes. (XMODEM always uses
                                  all 8 bits.) (default)
                                  1 = If 8 bit data is selected for receive,
                                  the 8th bit is interpreted as the high
                                  order bit of an 8 bit ASCII character.
                                  this permits 256 character codes to be
                                  displayed on the screen. This is NOT



                        Copyright 1984,1985 Mark C. DiVecchio       Page 33






          SETUP Displays                                         PC-VT v7.6



                                  a VT function and the use of this option
                                  may cause unreliable results.





















































          Page 34       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                    The PARAMS.DAT File









                                      Chapter 7

                                 The PARAMS.DAT File



            PC-VT maintains a USER MEMORY file on  disk.  This file is used
          to record user selected features and tab stops.  The file is read
          each time that you start up PC-VT so  your selected configuration
          is restored each time.

            If this version of PC-VT is a  replacement for an older version
          which you may have, you should delete the old PARAMS.DAT file and
          let  PC-VT  create  you  another  copy.   The  older  version  of
          PARAMS.DAT may not be compatible with  the  enhancements  in  the
          newer versions of PC-VT.  The  latest  versions of PC-VT will not
          even start up with old versions of  the PARAMS.DAT file.  It will
          display  a  message  indicating  that  the  old  file  should  be
          deleted.  Just delete the old  file  and restart PC-VT.  You will
          have to reset the baud rate and any other options which  you  had
          set since PC-VT sets these to default  values when it creates the
          new PARAMS.DAT file.




          7.1 Creation


            The  file  is  automatically  created  with  default values  as
          defined throughout  this  document  if the file does not exist on
          the default drive.  The diskette supplied with the  package has a
          default copy of the file.




          7.2 Location


            The  file  name  is  PARAMS.DAT.   The  file is created in  the
          directory pointed to by the 'PC-VT=' string in  the  environment.
          If there is no  such  string  in the environment or you are using
          DOS 1.0 or 1.1, the file  is created on the PC-DOS default drive.
          The chapter on starting PC-VT describes how to use this string.




                        Copyright 1984,1985 Mark C. DiVecchio       Page 35






          The PARAMS.DAT File                                    PC-VT v7.6







          7.3 Updating


            The  file  is  rewritten  upon request while  in  the  SETUP  A
          display.




          7.4 Error Messages


            There  are   several   messages   generated   by   PC-VT  while
          manipulating this file.

          "New USER MEMORY File Created":
                          PC-VT could not  find  PARAMS.DAT  on the default
                          disk drive so it created a file with the  default
                          feature   selections   and  tab   stops.    PC-VT
                          continues.

          "Disk Directory Full":
                          PC-VT could not find  space  in  the directory of
                          the default disk drive  when  it  tried to create
                          the PARAMS.DAT file.  PC-VT terminates.

          "Disk Full While Writing USER MEMORY File":
                          PC-VT ran out of space on the default disk  drive
                          while   creating  the  PARAMS.DAT  file.    PC-VT
                          terminates.

          "Disk Swap Error - See User Manual":
                          PC-VT  found a different diskette in the  default
                          drive from  the time that the directory entry was
                          created and  the  file  PARAMS.DAT  was  written.
                          Since the time  between  these two events is very
                          small, this  error  message  indicates  a  severe
                          hardware or  system  failure.   PC-VT terminates.
                          This error should never  happen  if  PC-VT is run
                          from a fixed disk.

          "Error While Opening USER MEMORY File":
                          PC-VT failed to successfully open the  PARAMS.DAT
                          file  on  the default disk.  This  usually  means
                          that the disk directory  has been damaged.  PC-VT
                          terminates.





          Page 36       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                    The PARAMS.DAT File



          "USER MEMORY File Access Error":
                          An error occurred while  reading  the  PARAMS.DAT
                          file  from the default disk.  Usually means  that
                          the  file  has   been  accidentally  overwritten.
                          PC-VT terminates.

          "Can't find PARAMS.DAT.  F1 to cancel, space to try again.":
                          This usually  means  that  the  default  diskette
                          drive is empty or the door is open.  Correct  the
                          situation and hit the space key to continue.













































                        Copyright 1984,1985 Mark C. DiVecchio       Page 37






          Transmitting and Receiving Files                       PC-VT v7.6









                                      Chapter 8

                           Transmitting and Receiving Files



            PC-VT  has  complete  transmitting   (upload)   and   receiving
          (download)  facilities.  These facilities are accessed using  the
          CTRL-F4 and CTRL-F3 keys.  These keys can be  activated  whenever
          you  are  in the communications display.   PC-VT  performs  these
          functions on any ASCII character or binary file.  The Binary file
          transfer  uses  the  XMODEM  protocol  and   must   be   over   a
          communications line set  at  8  data  bits, no parity, and 1 stop
          bit.  XMODEM can be used to  transfer  ASCII  files  for  greater
          error detection  capability.  Both the ASCII and XMODEM protocols
          are compatible with RBBS software.

            In the descriptions which follow, the computer referred  to  as
          the host, is assumed to be a  VAX-11 running VMS.  All references
          to an IBM PC  filename  include  a  drive  letter,  the path, the
          filename   and    the    file    extension,    for    example   -
          a:\usr\bin\file.ext.  If no drive letter or path is given,  PC-VT
          will access the current PC-DOS default directory.  You can change
          the default drive and directory by typing CTRL-F2.   See the last
          section in this chapter for details.




          8.1 Transmitting ASCII Files (Uploading)


            To transmit or upload an ASCII  file to the host, the host must
          be set to receive the file and then PC-VT can be told to transmit
          it.  The host  computer  can  be  told to execute a program which
          reads the terminal or more simply, the VMS  COPY  command  can be
          used.  Once you have started PC-VT and logged on to the host, you
          will see the "$"  command  line  prompt.   You  can  use the COPY
          command as follows:


                          COPY TT: <filename>

            The host will then wait for characters to be transmitted by the
          terminal.  To request PC-VT to  start  uploading,  type  CTRL-F4.
          You will be prompted for the name of the PC file to upload.  Type



          Page 38       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files



          the filename followed by ENTER.  Typing just  ENTER  cancels  the
          transmit request.  If PC-VT finds the file as  specified, it will
          transmit it to the host.  If the file is  not  found, you will be
          prompted again for the filename.  The file  is displayed as it is
          transmitted.

            At the end of the file, PC-VT inquires if  you  want  a  CTRL-Z
          (ASCII code 26) sent to the host.   The CTRL-Z will terminate the
          VMS COPY command.  An  upper  or  lower  case  "y"  must be typed
          followed by ENTER to send the CTRL-Z.

            PC-VT strips all Line Feed characters before it  transmits  the
          file  (ASCII  code  10).  All other characters  are  transmitted.
          PC-VT detects the end of the PC file by  looking  for a CTRL-Z as
          it reads the disk file.

            A very useful  feature  of  this  routine,  is  that it handles
          XOFF/XON characters  received from the host during the uploading.
          This prevents the host from losing  data if it is busy.  The host
          will  send  an  XOFF  if  its  buffer  is  filling.   PC-VT  will
          automatically  stop  transmitting   until   a   XON  is  received
          indicating that the host has  emptied  its buffer.  You should be
          sure that this  feature  is  enabled  under your logon on the VMS
          system.  To do this, use the VMS SET command:

                          SET TERMINAL /HOSTSYNC

          This  command  should also be put in your LOGIN.COM  file  unless
          your VMS system sets this feature as a default.

            If you wish to cancel the transmission  while the file is being
          transmitted, simply type CTRL-F4 at any time.  PC-VT will  prompt
          with the CTRL-Z message and then  terminate  the  upload.   PC-VT
          ignores all other keys typed during an upload  except the CTRL-F4
          key.

            If you don't request the transmission of a CTRL-Z, you can type
          CTRL-F4 again and send another file.  The  new  file  transmitted
          will be  read  by the same COPY command entered earlier.  You can
          use  this  to append many files to one another  as  you  transmit
          them.

            There  are   several   messages   generated   by   PC-VT  while
          transmitting a file:

          "Current default directory is >":
                          The current default directory is displayed.   For
                          DOS 1.1 users, this is just the default drive.

          "Drive d: xxxxxx bytes free":
                          The number of free bytes on the default drive  is
                          displayed.   This  is displayed only if  you  are



                        Copyright 1984,1985 Mark C. DiVecchio       Page 39






          Transmitting and Receiving Files                       PC-VT v7.6



                          using DOS 2.0 or later.

          "Enter Name of the PC File to Transmit
                          [d:][path][filename[.ext]][={x,c,t}]
                          (Hit  ENTER  to  cancel   upload  and  return  to
                          emulator):":
                          PC-VT is  asking  for  the name of the PC file to
                          transmit.  Type  the  filename  in  the  standard
                          PC-DOS  format and hit ENTER.  Typing just  ENTER
                          cancels the transmitting routine.   If  your  DOS
                          supports path names,  they  can be used here.  If
                          you do not specify a drive or  path,  PC-VT  will
                          access   the  default  directory.   The   default
                          directory  can  be  changed  with   the   CTRL-F2
                          command.  See the  last  section  in this chapter
                          for details.  The =x and =c options start up  the
                          XMODEM protocol.  The  =t  option  starts up file
                          transfer   with  handshaking.   These  are   both
                          explained below.

          "Should a CTRL-Z be transmitted?  (y or n) :":
                          PC-VT detects  CTRL-Z as an end of file indicator
                          and  does  not  transmit  that code to  the  host
                          unless you  respond  positively  to  this  query.
                          Type an upper or lower case "y" followed by ENTER
                          and PC-VT will transmit  a  CTRL-Z.   If you type
                          any other character  or  just  ENTER, CTRL-Z will
                          not be transmitted.  With this  feature,  CTRL-F4
                          can be activated  again  and several PC files can
                          be concatenated into one host file.

          "Transmission Complete":
                          File uploading is complete.

          "Transmission Canceled":
                          A  CTRL-F4 was typed during a file  transmission.
                          The uploading is immediately canceled.

          "Filename is not in correct format":
                          The filename entered in  response to the filename
                          inquiry  is  not in the standard  PC-DOS  format.
                          You may reenter the filename.

          "File not found as specified":
                          PC-VT could not find  the  file  on the specified
                          disk.   Usually caused by either the wrong  drive
                          letter, directory or a  mistyped  filename.   You
                          may reenter the filename.







          Page 40       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files





          8.1.1 Uploading with Handshake

            If you append an "=t"  on the end of the filename when you type
          it in, PC-VT will upload the ASCII file as described above except
          that the program will wait  for  a turnaround character before it
          sends the next line.  The turnaround  character  is  set  in  the
          SETUP-A display.  This  feature  is  useful  if  the  host is not
          buffered.  PC-VT won't send any characters  until  the  host  has
          processed  the  last  line  transmitted and prompts  for  another
          line.  This turnaround character is  sometimes  called  a  bypass
          character.  For a typical VAX system  you may want to set this to
          a linefeed (ASCII 10)  or  a  dollar sign (ASCII 36) which is the
          default  value  for  PC-VT.   In  addition,  a  CTRL-Z   is   not
          transmitted at the end of the file.  This upload as well  as  the
          regular ASCII upload can be canceled by  typing  CTRL-F4.   Other
          keys are ignored while the upload is in progress.

            Operation is as follows: you initiate the  upload  by  pressing
          CTRL-F4.  You give PC-VT the filename  with  the  "=t"  appended.
          PC-VT sends the first  line  of  the file up to a carriage return
          (ASCII 13). PC-VT then waits until the host  sends the turnaround
          character.  PC-VT then sends  the  next  line of the file up to a
          carriage return and so on.  Following the  last line of the file,
          the keyboard is enabled again for you to type to the host.

            Two dynamic features make this easier to use:

            1.  The turnaround character can be changed in the middle of an
                uploaded file.  To do this, enter an  ASCII 1 into the file
                followed by the new  turnaround  character  when you create
                the file.  The ASCII 1 (a control A) signals PC-VT that the
                next  character  read from the file is to set  as  the  new
                turnaround  character.   Neither the ASCII 1  nor  the  new
                turnaround  character  is  sent  to  the  host.   This  new
                turnaround  character  will  be  visible  in  the  SETUP  A
                display.  This does mean that you cannot have an ASCII 1 in
                any uploaded text handshake file  but  that should not be a
                problem since ASCII 1 is rarely used in a text file.

            2.  An ASCII 2 (a control B)  in the file signals PC-VT to wait
                for 1 second before proceeding to the next character.  This
                is  a  "pause"  feature.   You  can  have as many of  these
                characters in  a  row as you like to make up longer pauses.
                The ASCII 2 is not sent  to the host.  This also means that
                you  cannot  have an ASCII 2 in any upload  text  handshake
                file  but  that should not be a problem since  ASCII  2  is
                rarely used in a text file.

          The scanning for these two special control characters only  takes
          place if you  started  the  upload  with the "=t" option.  If you



                        Copyright 1984,1985 Mark C. DiVecchio       Page 41






          Transmitting and Receiving Files                       PC-VT v7.6



          started  a  regular  upload,  that  is  with  no  option,   these
          characters are uploaded just like all others and the handshake is
          disabled.  If while  you  are  setting  up your files, you make a
          mistake and PC-VT is waiting  for  prompt which will never occur,
          just press CTRL-F4 and PC-VT returns  to  normal  keyboard  input
          mode.


          8.1.2 Example of a transmission session

            This is typical of  what  you  would see and type to transmit a
          file to the host.

          $ copy tt: up.fil
                  "hit the CTRL-F4 key"
          Current default directory is
          >a:\usr\me\pcvt
          Drive a: 3435423 bytes free
          Enter Name of the PC File to Transmit
          [d:][path][filename[.ext]][={x,c,t}]
          (Hit ENTER to cancel upload and return to emulator)
          b:\mydire\pc.asc
                  "Now the PC file named b:\mydire\pc.asc is transmitted,
                  you will see the file displayed on the CRT as it is
                  echoed back from the host. The path name is accepted only
                  if you are running PC-DOS 2.0 or later."
          Should a CTRL-Z be transmitted? (y or n) : y
                  "A CTRL-Z(ASCII code 26) is sent to the host."
          Transmission complete
          ^Z
                  "The host file named up.fil is closed. The host COPY
                  command is terminated."
          $


          8.1.3 A Useful VAX .COM Upload file

            This simplified  Upload  facility  will upload a file from a PC
          disk file to a VAX system running VMS.

            Create a file on the VAX system named  "pcup.com" consisting of
          the following commands:

          $ on error then goto err1
          $ on control_y then goto ctrl
          $ if p1.eqs."" then -
            inquire p1 "Enter Name of VAX File to Contain Uploaded Data    "
          $ if p1 .eqs. "" then goto ctrl
          $ set term/nobroad
          $ write sys$output "<ESC>[?22h"
          $ copy tt:  'p1'
          $ exit:



          Page 42       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files



          $ set term/broad
          $ exit
          $ err1:
          $ write sys$output "A VAX error has occurred. Please try again."
          $ ctrl:
          $ write sys$output "Upload Canceled."
          $ goto exit

          The symbol <ESC> is the ESCAPE character 27.

            Once you have started PC-VT on  the PC and you have logged onto
          a VAX, upload files from the PC to the VAX by:

                  1. type this in response to the "$" VMS prompt:
                          @pcup <filename>

                  2. If you did not enter the filename on the command line,
                     the facility will ask you for the name of the VAX file
                     which you wish to create with the uploaded data
                     (include directory information if needed)
                     for example : dra1:[user1.dire.lev2]z.com
                     If you just enter carriage return, the upload is
                     canceled.

                  3. the facility will ask you for the name of the PC file
                     which you wish to upload (include disk drive letter
                     if needed) for example : zzzzz.com
                     If you just enter carriage return, the upload is
                     canceled.

                  4. the rest is automatic. The data will display on the
                     PC's CRT while it is being uploaded. The upload is
                     complete when the "$" VMS prompt appears.

                  5. To abort the upload before it is complete, type:

                          CTRL-F4

                     The VAX file will contain whatever data was uploaded
                     to the point where you aborted the upload. You may
                     see some extra characters displayed on the CRT screen,
                     this is just the communications buffer emptying.













                        Copyright 1984,1985 Mark C. DiVecchio       Page 43






          Transmitting and Receiving Files                       PC-VT v7.6







          8.2 Transmitting Binary Files (Uploading)


            PC-VT supports the XMODEM protocol for  binary  or  ASCII  file
          transfer.  Support is  included  for both checksum error checking
          compatible with PC-TALKIII  and  for  Cyclic Redundancy Code(CRC)
          error  checking.   This transfer method requires  that  the  host
          computer be capable of handling this protocol.

            To run XMODEM,  follow  the instructions for transmitting ASCII
          files but include "=x" after the filename("=c" is equivalent  for
          transmit).  The XMODEM module  is  automatically  started and the
          transfer proceeds without further  intervention.  The transfer is
          started  in  checksum  mode,  the  receiver  has  the  option  of
          switching to CRC mode.

            To cancel the transfer while it is progress, type CTRL-X.  This
          may require a  few  seconds  to  take  effect  because PC-VT must
          gracefully terminate the protocol.

            Refer to already published texts  for  details  on  the  XMODEM
          protocol.




          8.3 Receiving ASCII Files (Downloading)


            To receive an ASCII file, PC-VT must be told to start receiving
          and then the host  must  be  told  to  transmit  it.  To activate
          Receive File, type CTRL-F3.  This can  be done at any time in the
          communications display.  PC-VT will ask for the filename on which
          to write the  received  characters.  Just typing ENTER terminates
          the receive request.  If the file already exists,  PC-VT will ask
          if you wish to overwrite it.   If you type "y" followed by ENTER,
          PC-VT deletes the old file and starts to create another.

            Once Receive File (or downloading) is  activated,  and  a  Line
          Feed character  is received, ALL further characters received from
          the host except 00H and 7FH  are written onto the disk file.  You
          can now tell the  host to type out a file and PC-VT will write it
          onto the IBM PC disk.  To VMS, type:

                          Type <filename>






          Page 44       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files



            (PC-VT does not write out data to disk until  a  Line  Feed  is
          received in order to permit you  to  enter  the  "Type"  command.
          This prevents the  "Type"  command  from  being  written  to  the
          file.)

            When you wish to terminate Receive File,  simply  type  CTRL-F3
          again.  PC-VT closes the disk file and resumes normal mode.

            Note that since PC-VT cannot tell the difference between a file
          and any other characters sent by the host, all characters (except
          as noted - 00H and 7FH) received go onto  the  disk  file.   This
          includes   ESCAPE   sequences  and  all  VMS   command   language
          interaction.  This can be a useful feature if you are programming
          with some of these sequences and  your  program  is  not  working
          correctly.  PC-VT preserves these characters  on  disk  for  your
          inspection.  Once the file is closed, you  will have to exit from
          PC-VT  and  enter  a  text  editor  to  strip  off  any  unwanted
          characters from the file.

            PC-VT puts an End of File indicator at the end of the disk file
          before it closes the file.  For the  IBM  PC  this  is  a  CTRL-Z
          character, ASCII code 26.

            As a reminder, "RCV" is displayed on line 25 while Receive File
          is active.

            The receipt of a CTRL-Z character will terminate  Receive  File
          and close the received file.

            If you type CTRL-BREAK to terminate PC-VT, the received file is
          closed as if a CTRL-Z character was received.

            Receive File terminates if it runs out of  disk  space  for the
          downloaded file.  The last block (up to 512 characters)  received
          is lost and no  CTRL-Z  -  End of File indicator is written.  The
          file, however, is closed.

            There are several messages generated by PC-VT while receiving a
          file:

          "Current default directory is >":
                          The current default directory is displayed.   For
                          DOS 1.1 users, this is just the default drive.

          "Drive d: xxxxxx bytes free":
                          The number of free bytes on the default drive  is
                          displayed.   This  is displayed only if  you  are
                          using DOS 2.0 or later.

          "Enter     Name     of     the     PC     File     to     Receive
                          [d:][path][filename[.ext]][={x,c}] (Hit ENTER  to
                          cancel download and return to emulator):":



                        Copyright 1984,1985 Mark C. DiVecchio       Page 45






          Transmitting and Receiving Files                       PC-VT v7.6



                          PC-VT is  asking  for  the name of the PC file to
                          receive.   Type  the  filename  in  the  standard
                          PC-DOS  format and hit ENTER.  Typing just  ENTER
                          cancels  the  receiving  routine.   If  your  DOS
                          supports path names,  they  can be used here.  If
                          you do not specify a drive or  path,  PC-VT  will
                          access   the  default  directory.   The   default
                          directory  can  be  changed  with   the   CTRL-F2
                          command.  See the  last  section  in this chapter
                          for details.

          "Filename is not in correct format":
                          The filename entered in  response to the filename
                          inquiry  is  not in the standard  PC-DOS  format.
                          You may reenter the filename.

          "Insert diskette with received file.  Hit ENTER to continue....":
                          PC-VT found  a  different  diskette  in  the disk
                          drive than the one  it  opened  the download file
                          on.   Replace the original diskette in the  drive
                          and hit the ENTER key.

          "File already exists.  Do you want to overwrite it?  (y or n)":
                          The filename which you  entered  already  exists.
                          If you respond with a lower  or  upper  case  "Y"
                          followed by  the ENTER key, PC-VT will delete the
                          file and create a new one  with  the  same  name.
                          Any  other  response,  preserves  the  file   and
                          receive file is canceled.

          "File is being overwritten":
                          PC-VT confirms that the old file has been deleted
                          and a new file is being created.

          "Not enough directory space.  Receive terminated":
                          PC-VT  could  not  create the  file  because  the
                          directory on the specified diskette was full ,the
                          file was marked read-only,  or the path specified
                          is invalid.

          "Disk full.  Receive terminated":
                          PC-VT ran out of space on  the  disk.   The  file
                          already  written  is  closed.  A  CTRL-Z  is  not
                          placed at the end of the file.   The  last  block
                          (up to 512 characters) received is lost.










          Page 46       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files





          8.3.1 Example of a receive session

            This is typical of what you would see and  type  to  receive  a
          file from the host.  Comments are quoted.

          $        "hit the CTRL-F3 key"
          Current default directory is
          >a:
          Drive a: 32234  bytes free
          Enter Name of the PC File to Receive
          [d:][path][filename[.ext]][={x,c}]
          (Hit ENTER to cancel download and return to emulator)
          b:receive.txt
                  "RCV is displayed on line 25 and any characters sent
                  by the host are copied to the PC disk file."
          type host.dat
                  "The host file named host.dat is received by PC-VT
                  and placed on the PC disk file named b:receive.txt."
          $       "hit the CTRL-F3 key"
                  "The file is closed and RCV is cleared from line 25."


          8.3.2 A Useful VAX .COM Download file

            This simplified Download facility will download a file  from  a
          VAX system running VMS to a PC disk file.

            Create a file on the VAX system named  "pcdown.com"  consisting
          of the following commands:

          $ on error then goto err2
          $ on control_y then goto ctrl
          $ if p1.eqs."" then -
            inquire p1 "Enter Name of VAX File to Download    "
          $ if p1 .eqs. "" then goto ctrl
          $ open for008 'p1'/error=err1
          $ close for008
          $ set term/nobroad
          $ write sys$output "<ESC>[?21h"
          $ copy 'p1' tt:
          $ write sys$output "^Z"
          $ exit:
          $ set term/broad
          $ exit
          $ err1:
          $ write sys$output "VAX File Not Found."
          $ ctrl:
          $ write sys$output "Download Canceled."
          $ goto exit
          $ err2:



                        Copyright 1984,1985 Mark C. DiVecchio       Page 47






          Transmitting and Receiving Files                       PC-VT v7.6



          $ write sys$output "A VAX error has occurred, Please try again."
          $ goto ctrl

            The symbol  <ESC>  is the ESCAPE character 27. The symbol ^Z is
          the CTRL-Z character 26.

            Once you have started PC-VT on  the PC and you have logged onto
          a VAX, download files from the VAX to the PC by:

                  1. type this in response to the "$" VMS prompt:
                          @pcdown <filename>

                  2. If you did not enter the filename on the command line,
                     the facility will ask you for the name of the VAX file
                     which you wish to download (include directory
                     information if needed)
                     for example : [upload]xmit.com
                     If you just enter carriage return, the download is
                     canceled.

                  3. the facility will ask you for the name of the PC file
                     which you wish to create with the downloaded data
                     (include disk drive letter if needed)
                     for example : a:pcfile.dat
                     If you just hit carriage return, the download is
                     canceled. If the name which you give for the PC file
                     already exists, PC-VT ask if you want to overwrite the
                     file. If you answer "y", all the new data will replace
                     the old data on the PC file. If you answer "n" or just
                     hit carriage return, the download is canceled.

                  4. the rest is automatic. The data will display on the
                     PC's CRT while it is being downloaded. The download
                     is complete when the "$" VMS prompt appears.

                  5. To abort the download before it is complete, type:

                          CTRL-F3

                     The PC file will contain whatever data was downloaded
                     to the point where you aborted the download. You may
                     see some extra output on the CRT screen, this is just
                     the communications buffer emptying.












          Page 48       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                       Transmitting and Receiving Files







          8.4 Receiving Binary Files (Downloading)


            PC-VT supports the XMODEM protocol for  binary  or  ASCII  file
          transfer.  Support is  included  for both checksum error checking
          compatible with PC-TALKIII  and  for  Cyclic Redundancy Code(CRC)
          error  checking.   This transfer method requires  that  the  host
          computer be capable of handling this protocol.

            To  run  XMODEM, follow the instructions  for  receiving  ASCII
          files but  include  "=x"  after the filename for checksum mode or
          "=c" for CRC mode.  The XMODEM module  is  automatically  started
          and the transfer  proceeds  without  further intervention.  Since
          PC-VT is the receiver, you have the option of selecting the error
          checking mode.  Checksum mode will detect  all  burst  errors  of
          less than 8 bits in length and 99.6% of all burst  errors  longer
          than  8  bits.  CRC mode will detect all single  and  double  bit
          errors, all  errors  with an odd number of bits, all burst errors
          of length 16 or less  and  99.997%  of  all  17  bit  and  longer
          bursts.  The CRC supported is the CCITT recommended x^16 + x^12 +
          x^5 + 1.

            To cancel the transfer while it is progress, type CTRL-X.  This
          may require a  few  seconds  to  take  effect  because PC-VT must
          gracefully terminate the protocol.  PC-VT  does  not  delete  the
          partial file already created on disk but  closes it and leaves it
          for you to examine and delete.

            Refer to already published texts  for  details  on  the  XMODEM
          protocol.




          8.5 Changing the Default Directory


            For users of PC-DOS version  2.0  or later, PC-VT supports path
          names.  PC-VT will access the  default  drive and path unless you
          explicitly enter them.  You can  change  the  default  values  by
          typing  CTRL-F2  from  the communications  display.   PC-VT  will
          display the  current  default,  ask for the new default, and then
          display the complete new default path.  The input to this command
          follows the  syntax  for the CHDIR command to DOS.  The amount of
          free space on the default drive is also displayed.

            Here is what you would see and type:




                        Copyright 1984,1985 Mark C. DiVecchio       Page 49






          Transmitting and Receiving Files                       PC-VT v7.6



          Current default directory is
          >c:\level1
          Drive c: 34543  bytes free
          Enter new default directory
          [[d:][\][dirname][\dirname[...]]]
          >level2                         ;here you type the change
          Default directory is now
          >c:\level1\level2
          Drive c: 34543  bytes free

            When you type in the new directory, you  can  enter  the change
          just as you would enter a change to the CHDIR command:

            -  a drive letter followed by a ":"  will change the drive only
               (since  DOS  remembers the path associated  with  each  disk
               drive, the default directory will be set  to  whatever  path
               had been active on the specified drive) - b:

            -  a path name starting at the root - a:\mydir\nextdir

            -  the root - a:\

            -  a directory name starting at the current directory - nextdir

            If  the  path  is  illegal  or not found, an error  message  is
          displayed.





























          Page 50       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                        DIALING Display









                                      Chapter 9

                                   DIALING Display



            The DIALING display is accessed  by  typing  CTRL-F9  from  the
          communications display.  If  you  have a Color/Graphics card, the
          content  of  the  communications  display  is  preserved  and  is
          restored when you exit DIALING.   If  you have a Monochrome card,
          the communications display is cleared when you exit DIALING.




          9.1 Instructions for DIALING


            The DIALING display is used to handle Hayes or Hayes compatible
          modems.  The display can hold  10  names and phone numbers.  Each
          entry is broken into two fields.   A name can be typed in columns
          1 to 20. This is for your information only.  PC-VT does  not  use
          this information but it is stored on  the disk file.  The dialing
          commands and phone number can be  stored in columns 21 to 70. The
          "!"  above  column  21 is to remind you that, when dialing, PC-VT
          sends the data in columns  21 thru 70 to the modem as the dialing
          command.

            When PC-VT  starts  up, it looks for a Dialing Directory on the
          default  drive  or  the  drive  and  directory pointed to by  the
          environment string 'PC-VT='.  If it  does  not  find  one,  PC-VT
          creates a  blank  directory.   The  name  field  is  filled  with
          dashes.  The command field contains  "ATDT"  in  the  first  four
          columns and is then filled with spaces.

            The  first  thing that you need to do is enter the name of  the
          number's owner.  You can use the cursor  keys, the Enter key, the
          Tab key, the Home key and the End key  to  position the cursor to
          any  line.   The  "Ins"  key  will insert a space at  the  cursor
          position and the "Del" key will delete  a character at the cursor
          position.  Move the cursor to column  1 and type in the name.  It
          should not go  past  column  20.  Then to enter the phone number,
          move  the  cursor to column 24 using the TAB key and type in  the
          number.  The  new  directory can be saved by pressing the F4 key.
          The number can be dialed by pressing the F1 key.




                        Copyright 1984,1985 Mark C. DiVecchio       Page 51






          DIALING Display                                        PC-VT v7.6



            Press any  key  while the dialer is running will cause PC-VT to
          stop dialing  and return to the communications display.  Pressing
          CTRL-BREAK will cancel PC-VT.

            Here  is  how  each  of  cursor  control keys function in  this
          display:

            -  Left arrow - moves the cursor one column  to  the  left.  If
               the cursor is already in column 1,  the speaker beeps and no
               action is taken.  Use this key for  a backspace then enter a
               space to clear any character that may have been mistyped.

            -  Right arrow - moves the cursor one  column to the right.  If
               the cursor is already in column 70, the speaker beeps and no
               action is taken.

            -  Up arrow - moves  the  cursor  up one row.  If the cursor is
               already in the top row  of  the directory, the speaker beeps
               and no action is taken.

            -  Down arrow  -  moves the cursor down one row.  If the cursor
               is already in the bottom  row  of the directory, the speaker
               beeps and no action is taken.

            -  Home  -  moves the cursor to column 1 of the top row of  the
               directory.

            -  End - moves the cursor  to column 1 of the bottom row of the
               directory.

            -  Enter - moves the cursor  to column 1 of the next row of the
               directory.  If  the  cursor  is already in the bottom row of
               the directory,  the  cursor is moved to column 1 of that row
               and the speaker beeps.

            -  Tab - moves the cursor to column 24 of the current row.

            -  Ins - inserts a space at  the  cursor  position.   This  key
               operates within either the name field (columns 1 thru 20) or
               the number field (columns 21 thru 70). All  characters  from
               the cursor to right of the field are moved one column to the
               right.  Anything in the rightmost column  of  the  field  is
               lost.  If you Ins within the name field, the number field is
               not affected.

            -  Del - deletes a character at the cursor  position.  This key
               operates within either the name field (columns 1 thru 20) or
               the number field (columns 21 thru 70). All  characters  from
               the right of the cursor to the rightmost column of the field
               are moved one column to the left.   A space is inserted into
               the rightmost  column  of  the field.  If you Del within the
               name field, the number field is not affected.



          Page 52       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                        DIALING Display




            In addition, as a simple Macro style logon facility, PC-VT does
          a little more work.   If  you  enter the tilde key (the ~), PC-VT
          will translate that into a  carriage  return (ASCII 13) when sent
          to the Modem.   This  permits  you  to send multiple lines to the
          Modem.  Also, PC-VT will interpret the  CTRL-W key as a wait of 5
          seconds and the CTRL-B  as  a  wait of 1 second.  The CTRL-W will
          appear in  the  directory  as an underlined up-down arrow and the
          CTRL-B will appear as  a  Happy  Face.   A  CTRL-X  will stop the
          dialing at that point in the line.  PC-VT  will  then,  as usual,
          send  its  final carriage return to the Modem.  The  CTRL-X  will
          appear in the directory as an up-arrow.   Only  your  imagination
          will  limit  you as to how you can use this.  You can have  PC-VT
          dial your host,  wait  10  seconds,  enter  your  userid, wait 10
          seconds, and then enter your password.

            Special notes on the directory: You have complete control  over
          the entire directory from columns 1  to 70. You can type over the
          "ATDT" command and you can  type  any special modem commands like
          "," or ";".  You can enter any  key (including the Backspace key)
          except the control keys listed above  into  the  line.   You  can
          change the "ATDT" to any  other  modem command.  For example, you
          can change the last line to  "ATM2;" and when you move the cursor
          to that line and press F1, the Modem will be commanded to turn on
          the speaker at all times.  Just remember that PC-VT will send any
          character in columns 21 to  70 to the Modem when you press the F1
          key.  PC-VT always sends a  carriage  return right after it sends
          the character in column 70. For  users of the PCjr, you can enter
          the CTRL-N command required by the junior's internal modem.

            In the  examples  below,  the  CTRL-W  is shown as a ?  and the
          CTRL-X is shown  as  a  ^  since most line printers printing this
          document can't print control characters.

                  Here are some possible entries:

                              !
          Mark C DiVecchio----ATDT,,555-1212
          The computer--------ATDT 1 - 506 - 555 - 1234,,,,,222* 432#
          Speaker on----------ATM2;
          Full Logon----------ATDT,555-1212~?????~?userid~password^

            In that last example,  the  Modem  is summoned, it is to wait 2
          seconds for  the  dial tone (a Hayes modem command), it dials the
          number, waits 25 seconds  for  the  connection,  sends  a  single
          carriage return which wakes up the host, waits  5 seconds, enters
          the userid and then enters the password.  Note  the final CTRL-X.
          This is needed to tell PC-VT not to send the spaces  between  the
          password and column 70 to the host since they may be seen as part
          of the password.





                        Copyright 1984,1985 Mark C. DiVecchio       Page 53






          DIALING Display                                        PC-VT v7.6



            One other thing is done by this facility in order to get around
          the buffer size within the mode.  Spaces  and dashes in the phone
          number are not  sent  to  the  Modem.   With  several Modems, the
          buffers could overflow if all  50  characters in the phone number
          field  were  sent.    PC-VT   resumes  sending  spaces  after  it
          encounters the first  tilde.   This  means  that  spaces  can  be
          included as part of the logon sequence.

            Here are the functions available in DIALING :

          Exit DIALING :  The  ESC  key returns PC-VT to the communications
                          display.

          Dial :          The "F1" key dials the number in the line pointed
                          to  by  the cursor.  PC-VT then  returns  to  the
                          communications display.

          Read Directory :
                          The  "F3"  key  clears  the   displayed   dialing
                          directory and  reloads  it  from  the  disk file,
                          DIALER.DAT, on the default drive.  PC-VT  remains
                          in the DIALING display.

          Store Directory :
                          The  "F4"  key  stores  the   displayed   dialing
                          directory into  a disk file on the PC-DOS default
                          drive.  The name of  the  file  is DIALER.DAT.  A
                          message will  appear at the bottom of the display
                          to indicate  that the new directory is written to
                          disk.

          Hang up :       The "F5"  key  sends the commands to the MODEM to
                          hang up the  phone.   This  procedure takes about
                          2-3 seconds due to the MODEM protocol.  A message
                          will  appear  at  the  bottom of the  display  to
                          indicate that the line  is  hung  up.  PC-VT uses
                          the Hayes commands "+++"  and  "ATH0"  to do this
                          function.




          9.2 The DIALER.DAT File


            PC-VT maintains a Dialing Directory file on disk.  This file is
          used to  record  user  inputted  phone  numbers  or  other  Modem
          commands.  The file is read each  time that you start up PC-VT so
          your dialing directory is restored each time.






          Page 54       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                        DIALING Display







          9.3 Creation


            The file is automatically created as an empty  directory if the
          file does not exist on the default drive.   The diskette supplied
          with the package has a default copy of the file.




          9.4 Location


            The  file  name  is  DIALER.DAT.   The  file is created in  the
          directory pointed to by the 'PC-VT=' string in  the  environment.
          If there is no  such  string  in the environment or you are using
          DOS 1.0 or 1.1, the file  is created on the PC-DOS default drive.
          The chapter on starting PC-VT describes how to use this string.




          9.5 Updating


            The file  is  rewritten  upon  request  while  in  the  DIALING
          display.




          9.6 Error Messages


            There  are   several   messages   generated   by   PC-VT  while
          manipulating this file.

          "New Dialing Directory Created":
                          PC-VT could not  find  DIALER.DAT  on the default
                          disk drive so it created  a  blank  file.   PC-VT
                          continues.

          "Disk Directory Full":
                          PC-VT could not find  space  in  the directory of
                          the default disk drive  when  it  tried to create
                          the DIALER.DAT file.  PC-VT terminates.





                        Copyright 1984,1985 Mark C. DiVecchio       Page 55






          DIALING Display                                        PC-VT v7.6



          "Disk Full While Writing Dialing Dir":
                          PC-VT ran out of space on the default disk  drive
                          while   creating  the  DIALER.DAT  file.    PC-VT
                          terminates.

          "Disk Swap Error - See User Manual":
                          PC-VT  found a different diskette in the  default
                          drive from the time that the disk directory entry
                          was created and the  file DIALER.DAT was written.
                          Since the time  between  these two events is very
                          small, this  error  message  indicates  a  severe
                          hardware or  system  failure.   PC-VT terminates.
                          This error should never  happen  if  PC-VT is run
                          from a fixed disk.

          "Error While Opening Dialing Directory":
                          PC-VT failed to successfully open the  DIALER.DAT
                          file  on  the default disk.  This  usually  means
                          that the disk directory  has been damaged.  PC-VT
                          terminates.

          "Dialing Directory Access Error":
                          An error occured  while  reading  the  DIALER.DAT
                          file  from the default disk.  Usually means  that
                          the  file  has   been  accidentally  overwritten.
                          PC-VT terminates.

          "Can't find DIALER.DAT.  F1 to cancel, space to try again.":
                          This usually  means  that  the  default  diskette
                          drive is empty or the door is open.  Correct  the
                          situation and  hit  the  space  key  to continue.
                          PC-VT continues.























          Page 56       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                      PC-VT Status Line









                                      Chapter 10

                                  PC-VT Status Line



            PC-VT uses line 25 of  the monitor as a status line when in the
          communications display.  The VT10x only  requires  24  lines  for
          proper operation.  The meaning of each of the fields displayed is
          summarized in this chapter.

          ON LINE         PC-VT is actively  monitoring  the COMx port.  It
                          is on line to a host only if you have established
                          the connection.

          LOCAL           PC-VT is performing some  local function and data
                          received on  the COMx port will not be displayed.
                          The data will not be lost but  will  be  buffered
                          and then  displayed when PC-VT returns to ON LINE
                          mode.  Note that on the  PCjr  this  may  not  be
                          true.  If the PCjr is doing a diskette operation,
                          all other  interrupts are masked off.  If data is
                          received on the COMx line, it will be lost.

          Vx.x            The version number of PC-VT.  Please include this
                          number if you write to the author.

          KBD LOCKED      The host computer  has  locked the keyboard.  The
                          host  is  also  responsible  for  unlocking   the
                          keyboard.

          CAP             The  Caps  Lock  key  has been depressed  on  the
                          keyboard.

          NUM             The  Num  Lock  key  has  been  depressed on  the
                          keyboard.

          SCR             The Scroll Lock key has  been  depressed  on  the
                          keyboard.  This key  functions  as  the NO SCROLL
                          key on the VT10x.

          "alpha"         The Greek letter "alpha" is displayed to indicate
                          that PC-VT is in  applications keypad mode.  This
                          permits the  PC's  function  and  keypad  keys to
                          transmit special codes.  See  chapter 5. The host
                          controls entrance and exit to this mode.



                        Copyright 1984,1985 Mark C. DiVecchio       Page 57






          PC-VT Status Line                                      PC-VT v7.6



          X               The  letter 'X' indicates that the host's  buffer
                          has filled up and that the host will  not  accept
                          any more  characters from the PC. This will clear
                          automatically   when   the  host's   buffer   has
                          emptied.  See the definition of the alt-x key for
                          more details.

          HH:MM:SS        The time of day is displayed.  This can be turned
                          off by resetting the CLOCK bit  in  the  SETUP  B
                          display.

          DSR             This indicates that the modem has raised its Data
                          Set Ready line.  This  indicator  as  well as the
                          next two modem  status  indicators  can be turned
                          off by resetting the CLOCK bit  in  the  SETUP  B
                          display.   Most smart modems keep this line  high
                          at all times to indicate that the modem is  ready
                          to receive commands.   Note  that  PC-VT does not
                          really  care.   It   displays   this   only   for
                          information.

          CTS             This indicates  that  the  modem  has  raised its
                          Clear To Send  line.   Some  modems maintain this
                          line  high  at  all  times.  There is  usually  a
                          switch on the modem which will cause this line to
                          function normally.   Note  that  PC-VT  does  not
                          really  care.   It   displays   this   only   for
                          information.

          CD              This indicates  that  the  modem  has  raised its
                          Carrier Detect line.  Some modems  maintain  this
                          line  high  at  all  times.  There is  usually  a
                          switch on the modem which will cause this line to
                          function normally.   Note  that  PC-VT  does  not
                          really  care.   It   displays   this   only   for
                          information.

          L1L2L3L4        These represent the LED's on the VT10x.  All four
                          are  used  on the VT100, only L1 is used  on  the
                          VT102, and none are used on the VT52.















          Page 58       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                          Macro Display









                                      Chapter 11

                                    Macro Display



            The  Macro  display  is  accessed  by  typing  ALT-K  from  the
          communications display.  The Macro display is used to update  the
          currently defined Macro keys.  If you have a Color/Graphics card,
          the content of the communications display  is  preserved  and  is
          restored when you exit Macro.  If you have a Monochrome card, the
          communications display  is cleared when you exit Macro.  Actually
          sending a  Macro  is  done by typing ALT-F1 thru ALT-F10 directly
          from  the   communications  display.   Only  these  10  keys  are
          supported by the Macro processor.




          11.1 Instructions for Macro


            The Macro display is used to create,  update and save Macro key
          definitions.  The  display  can  hold  10  Macro  keys.   The  10
          definable keys  are  listed on the left of the screen.  The Macro
          commands are stored in columns 21 to 70. The "!"  above column 21
          is to remind you that, when expanding a  macro,  PC-VT  sends the
          data in columns 21 thru 70 to the modem as the Macro command.

            When PC-VT starts  up,  it  looks  for a Macro Directory on the
          default  drive  or  the  drive  and  directory pointed to by  the
          environment string 'PC-VT='.  If it  does  not  find  one,  PC-VT
          creates a blank directory.

            You can use the  cursor  keys,  the Enter key, the Home key and
          the End key to  position  the  cursor to any line.  The "Ins" key
          will insert a space at the cursor position and the "Del" key will
          delete a  character  at  the cursor position.  Move the cursor to
          the first column of the key which you want to define.  Then enter
          the definition.  The new directory  can  be saved by pressing the
          F4 key.  The macro can  be sent by pressing the F1 key.  Once you
          are back  in  the  communications display, you can send the macro
          just by pressing the  ALT-Fx  key.   There  is  no  need to press
          ALT-K.





                        Copyright 1984,1985 Mark C. DiVecchio       Page 59






          Macro Display                                          PC-VT v7.6



            Press any key while the  Macro  is being transmitted will cause
          PC-VT to stop the expansion  and  return  to  the  communications
          display.  Pressing CTRL-BREAK will cancel PC-VT.

            Here  is  how  each  of  cursor  control keys function in  this
          display:

            -  Left arrow - moves the cursor one column  to  the  left.  If
               the cursor is already in column 21, the speaker beeps and no
               action is taken.  Use this key as a  backspace  then  type a
               space to clear the character.

            -  Right arrow - moves the cursor one  column to the right.  If
               the cursor is already in column 70, the speaker beeps and no
               action is taken.

            -  Up arrow - moves  the  cursor  up one row.  If the cursor is
               already in the top row  of  the directory, the speaker beeps
               and no action is taken.

            -  Down arrow  -  moves the cursor down one row.  If the cursor
               is already in the bottom  row  of the directory, the speaker
               beeps and no action is taken.

            -  Home - moves the cursor to column 21 of  the  top row of the
               directory.

            -  End - moves the cursor to column 21 of the bottom row of the
               directory.

            -  Enter - moves the cursor to column 21 of the next row of the
               directory.  If  the  cursor  is already in the bottom row of
               the directory, the cursor is moved to  column 21 of that row
               and the speaker beeps.  If you want to  use  the  'Enter' as
               part of the Macro definition, use the tilde  key '~'.  PC-VT
               will replace the tilde with a carriage return when the macro
               is expanded.

            -  Ins  -  inserts  a  space  at  the  cursor  position.    All
               characters from the cursor to  right  of the field are moved
               one column to the right.  Anything in the  rightmost  column
               of the field is lost.

            -  Del - deletes a  character  at  the  cursor  position.   All
               characters from the right of the  cursor  to  the  rightmost
               column of the  field  are  moved  one column to the left.  A
               space is inserted into the rightmost column of the field.

            Special notes on the directory: You have complete control  over
          the entire  directory  from  columns 21 to 70. Just remember that
          PC-VT will send any character in columns 21 to  70  to  the  Host
          when you invoke the macro.  PC-VT does not send a carriage return



          Page 60       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                          Macro Display



          after it sends the character in  column 70. If you want a return,
          enter the tilde character.  If you don't put  in  a  tilde, PC-VT
          sends whatever characters you have defined  and  then  just  goes
          back into keyboard  input  mode.   You  can  type  in  additional
          characters or manually press the enter key.

            In addition, PC-VT does  a  little  more  work.   As  mentioned
          above, if  you  enter the tilde key (the ~), PC-VT will translate
          that into a  carriage  return  (ASCII  13) when sent to the Host.
          This permits you  to  send  multiple  lines.   Also,  PC-VT  will
          interpret the CTRL-W key as a wait of 5 seconds and the CTRL-B as
          a wait of 1 second.  The CTRL-W will appear in the  directory  as
          an underlined up-down arrow and the CTRL-B will appear as a Happy
          Face.  A CTRL-X will stop the Macro expansion  at  that  point in
          the line.   PC-VT  will  then return to keyboard input mode.  The
          CTRL-X will  appear  in  the directory as an up-arrow.  Only your
          imagination will limit you as to how you can use this.   You  can
          have  PC-VT  enter a command, wait 10 seconds, enter  an  option,
          wait  6  seconds, end a job and log you off the host.  All  other
          control  characters  can  be  entered into the  macro  definition
          including backspace  and  CTRL-C.   They will be sent to the host
          when the macro is expanded.

            In the  examples  below,  the  CTRL-W  is shown as a ?  and the
          CTRL-X is shown  as  a  ^  since most line printers printing this
          document can't print control characters.

                  Here are some possible entries:

                              !
          Alt F1--------------run myjob~^
          Alt F2--------------mail~?1~???~~~~ex~^
          Alt F3--------------ATDT5551212~^

            It is always wise to put a  CTRL-X  a the end of every macro so
          that PC-VT knows exactly where to stop sending.   PC-VT will send
          the spaces out to column 70 if you leave off the CTRL-X.  In most
          cases this probably won't matter but  when  trailing  spaces  are
          significant(like in a password), you will need the CTRL-X.

            You can also use the Macro  key definition to dial thru a smart
          modem.  Simply put the dialing command in as a Macro.  Then press
          the appropriate Alt key from the communications display.

            Here are the functions available in Macro :

          Exit Macro :    The  ESC  key returns PC-VT to the communications
                          display.

          Dial :          The "F1" key sends the macro in the  line pointed
                          to  by  the cursor.  PC-VT then  returns  to  the
                          communications   display.   To  send  the   macro



                        Copyright 1984,1985 Mark C. DiVecchio       Page 61






          Macro Display                                          PC-VT v7.6



                          directly  from  the communications  display,  you
                          just   need  to  press  ALT-Fx  right  from   the
                          communications display.   There  is  no  need  to
                          press ALT-K first.

          Read Directory :
                          The "F3" key clears the displayed Macro directory
                          and reloads  it from the disk file, MACRO.DAT, on
                          the default drive.   PC-VT  remains  in the Macro
                          display.

          Store Directory :
                          The "F4" key stores the displayed Macro directory
                          into a disk file on the PC-DOS default  drive  or
                          the drive and directory specified in the 'PC-VT='
                          string in  the environment.  The name of the file
                          is  MACRO.DAT.   A  message will  appear  at  the
                          bottom of the display  to  indicate  that the new
                          directory is written to disk.




          11.2 The MACRO.DAT File


            PC-VT maintains a Macro Directory  file  on disk.  This file is
          used to record user inputed  macro  key definitions.  The file is
          read each time that you start up PC-VT so your Macro directory is
          restored each time.




          11.3 Creation


            The file is automatically created as an empty  directory if the
          file does not exist on the default drive.   The diskette supplied
          with the package has a default copy of the file.




          11.4 Location


            The  file  name  is  MACRO.DAT.  The file  is  created  in  the
          directory pointed to by the 'PC-VT=' string in  the  environment.
          If there is no  such  string  in the environment or you are using
          DOS 1.0 or 1.1, the file  is created on the PC-DOS default drive.
          The chapter on starting PC-VT describes how to use this string.



          Page 62       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                          Macro Display







          11.5 Updating


            The file is rewritten upon request while in the Macro display.




          11.6 Error Messages


            There  are   several   messages   generated   by   PC-VT  while
          manipulating this file.

          "New Macro Directory Created":
                          PC-VT  could  not find MACRO.DAT on  the  default
                          disk drive  so  it  created  an  empty directory.
                          PC-VT continues.

          "Disk Directory Full":
                          PC-VT could not find  space  in  the directory of
                          the default disk drive  when  it  tried to create
                          the MACRO.DAT file.  PC-VT terminates.

          "Disk Full While Writing Macro Dir":
                          PC-VT ran out of space on the default disk  drive
                          while  creating   the   MACRO.DAT   file.   PC-VT
                          terminates.

          "Disk Swap Error - See User Manual":
                          PC-VT  found a different diskette in the  default
                          drive from the time that the disk directory entry
                          was  created and the file MACRO.DAT was  written.
                          Since the time  between  these two events is very
                          small, this  error  message  indicates  a  severe
                          hardware or  system  failure.   PC-VT terminates.
                          This error should never  happen  if  PC-VT is run
                          from a fixed disk.

          "Error While Opening Macro Directory":
                          PC-VT failed to successfully open  the  MACRO.DAT
                          file  on  the default disk.  This  usually  means
                          that the disk directory  has been damaged.  PC-VT
                          terminates.

          "Macro Directory Access Error":
                          An error occurred  while  reading  the  MACRO.DAT
                          file  from the default disk.  Usually means  that



                        Copyright 1984,1985 Mark C. DiVecchio       Page 63






          Macro Display                                          PC-VT v7.6



                          the  file  has   been  accidentally  overwritten.
                          PC-VT terminates.

          "Can't find MACRO.DAT.  F1 to cancel, space to try again.":
                          This usually  means  that  the  default  diskette
                          drive is empty or the door is open.  Correct  the
                          situation and  hit  the  space  key  to continue.
                          PC-VT continues.















































          Page 64       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                             List of Control Characters









                                      Appendix A

                              List of Control Characters



            These appendices  describe  the  internal  operation  of PC-VT.
          They show the various control  characters  and  Escape  sequences
          which PC-VT interprets as commands.  The character  "ESC"  is  an
          ASCII control character with  the  decimal  value  of  27.  These
          appendices can be skipped if your  only use of PC-VT is simply as
          a VT100/102 Video Terminal.

            ASCII codes from 0 to 31 and 127 are control characters.  PC-VT
          responds to these characters as listed in the following table.

                          Hex
          Name            Code    Function

          Null            0       This character is ignored. It can be used
                                           4
                                  as a fill  character.

          End of Text     3       Not supported. PC-VT ignores this
                                  character.

          End of          4       This character can be selected as a
          Transmission            disconnect character by the SETUP B
                                  display. If selected, its receipt will
                                  cause PC-VT to disconnect from the
                                  communications line by sending a Break.

          Enquire         5       Causes PC-VT to transmit its answerback
                                  message. The answerback back message is
                                  set in the SETUP B display.

          Bell            7       Causes PC-VT to Beep the IBM PC speaker.

          Backspace       8       Causes PC-VT to move the cursor back one
                                  column and delete the character there.
                                  If the cursor is already in column 1,

          ----------

          4. A fill character is sometimes used  to  take  up  space  in  a
          messages for timing reasons.



                        Copyright 1984,1985 Mark C. DiVecchio       Page 65






          List of Control Characters                             PC-VT v7.6



                                  this character is ignored.

          Horizontal Tab  9       Causes PC-VT to move the cursor to the
                                  next tab stop. If there are no tab stops
                                  between the current cursor position and
                                  column 80, the cursor is moved to column
                                  80. The tabs stops can be set in
                                  the SETUP A display.

          Line Feed       10      This causes the cursor to move down one
                                  line in the current column. If the
                                  cursor moves below the screen output
                                  area, the lines above the cursor move up
                                  one line, and a blank line is added to
                                  the bottom of the screen. The operation
                                  of this key is modified by the Line Feed/
                                  New Line feature selected in SETUP B.

          Vertical Tab    11      Handled as a line feed.

          Form Feed       12      Handled as a line feed.

          Carriage Return 13      The cursor is moved back to the left
                                  margin. Cursor remains in the current
                                  line.

          Shift Out       14      Causes PC-VT to change its character set
                                  to the G0 character set. The G0 character
                                  set is selected by the Select Character
                                  Set Escape sequence.

          Shift In        15      Causes PC-VT to change its character set
                                  to the G1 character set. The G1 character
                                  set is selected by the Select Character
                                  Set Escape sequence.

          XON (Device     17      Causes PC-VT to continue or restart
          Control 1)              sending characters.

          XOFF (Device    19      Causes PC-VT to stop transmitting
          Control 3)              characters. It does not stop PC-VT
                                  from sending XON or XOFF.

          Cancel          24      Causes PC-VT to interrupt and cancel any
                                  in process Escape control sequence.

          Substitute      25      Not supported. PC-VT ignores this
                                  character.

          Escape          27      Indicates the start of a special Escape
                                  control sequence.




          Page 66       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                             List of Control Characters



          Delete          127     This character is ignored when received.

                  All other control characters are ignored.




















































                        Copyright 1984,1985 Mark C. DiVecchio       Page 67






          Received Escape Sequences                              PC-VT v7.6









                                      Appendix B

                              Received Escape Sequences



            PC-VT  constantly  monitors the communications line  for  these
          incoming  Escape  sequences.   When   they  are  received,  PC-VT
          performs the function as shown.  The  Escape  character  and  the
          characters which  follow  it and are part of the sequence are not
          displayed.  When  receiving (downloading) a file, PC-VT does copy
          these characters to the PC  disk  file being created.  The Escape
          character is shown below as "ESC" and is the ASCII character with
          the value of 27.

          Keypad Character Selection

          ESC =           Select Alternate Keypad  Mode  - Set the keyboard
                          to transmit the Alternate Keypad set of character
                          codes.

          ESC >           Select  Numeric Keypad Mode - Set the keyboard to
                          transmit the  Numeric  Keypad  set  of  character
                          codes.

          Select Character Sets

          ESC ( A         Select U.K.  Character  Set  as G0 - The standard
                          IBM PC  character set is selected for ASCII codes
                          0 to 34 and 36 to 127.  ASCII code 35 is replaced
                          by  the  extended  character 156,  the  UK  Pound
                          sign.

          ESC ( B         Select U.S.  Character  Set  as G0 - The standard
                          IBM PC  character set is selected for ASCII codes
                          0 to 127.

          ESC ( 0         Select Special Characters and Line Drawing Set as
                          G0 - A special character and line drawing set  is
                          selected.  The set is identical  to  the  IBM  PC
                          character  set  for ASCII codes 0  to  95.  ASCII
                          codes 96 to 127 are shown below.

          ESC ) A         Select U.K. Character Set as G1- The standard IBM
                          PC character set is selected for ASCII codes 0 to
                          34 and  36  to  127. ASCII code 35 is replaced by



          Page 68       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                              Received Escape Sequences



                          the extended character 156, the UK Pound sign.

          ESC ) B         Select U.S.  Character  Set  as G1 - The standard
                          IBM PC  character set is selected for ASCII codes
                          0 to 127.

          ESC ) 0         Select Special Characters and Line Drawing Set as
                          G1 - A special character and line drawing set  is
                          selected.  The set is identical  to  the  IBM  PC
                          character  set  for ASCII codes 0  to  95.  ASCII
                          codes 96 to 127 are shown below.


                  Special Character and Line Drawing Set

                  ASCII Code      Character       IBM PC ASCII Code

                  0 - 95          Same as the standard IBM PC character set.
                  96              Diamond                           4
                  97              Large Block                     219
                  98              Horizontal Tab (right arrow)     26
                  99              Form Feed (up triangle)          30
                  100             Carriage Return (left arrow)     27
                  101             Line Feed (up arrow)             24
                  102             Degree Symbol                   248
                  103             Plus/Minus Sign                 241
                  104             New Line (down arrow)            25
                  105             Vertical Tab (up/down arrow)     23
                  106             Upper Right Corner              217
                  107             Lower Right Corner              191
                  108             Lower Left Corner               218
                  109             Upper Left Corner               192
                  110             Crossing Lines                  197
                  111             Horizontal Line                 196
                  112             Horizontal Line                 196
                  113             Horizontal Line                 196
                  114             Horizontal Line                 196
                  115             Horizontal Line                 196
                  116             Left T                          195
                  117             Right T                         180
                  118             Top T                           193
                  119             Bottom T                        194
                  120             Vertical Line                   179
                  121             Less Than or Equal To           243
                  122             Greater Than or Equal           242
                  123             Pi Symbol                        20
                  124             Not Equal Sign (squiggle)       247
                  125             UK Pound Sign                   156
                  126             Centered Dot                    250
                  127             blank                            32





                        Copyright 1984,1985 Mark C. DiVecchio       Page 69






          Received Escape Sequences                              PC-VT v7.6



          Display Attributes

          ESC [ m         Select   Graphic   Rendition  -  Reset  Display
                          Attribute to Default per SETUP B display.

          ESC [ 0 m       Same as "ESC [ m".

          ESC [ 1 m       Select  Graphic  Rendition  -  Select  Display
                          Attribute to Bold.

          ESC [ 4 m       Select  Graphic  Rendition  -  Select  Display
                          Attribute to  Underline  (IBM  Monochrome Display
                          only - ignored for Color/Graphics Board).

          ESC [ 5 m       Select  Graphic  Rendition  -  Select  Display
                          Attribute to Blink.

          ESC [ 7 m       Select  Graphic  Rendition  -  Select  Display
                          Attribute to Reverse Video.

                          Normal video  and reverse video cannot be used at
                          the  same  time.  The other three  modes  act  on
                          normal video and reverse  video and are additive.
                          That is, The sequence "ESC  [ 7 m ESC [ 5 m ESC [
                          1  m  "  will produce  blinking,  high  intensity
                          reverse video.  Then , "ESC [ m" will  reset  the
                          display to the default, usually white on black.

                          PC-VT supports multiple parameters for the Select
                          Graphic  Rendition  sequence.  For  example,  the
                          three sequences in the  previous paragraph can be
                          coded as "ESC [ 7 ; 5 ; 1 m".

          Scrolling Margin

          ESC [ Pt ; Pb r
                          Set  top  and  bottom  scrolling  margins  -  The
                          scrolling region is  set  include  display  lines
                          starting at Pt and  ending  at  Pb inclusive.  Pt
                          and Pb must  be  between  1  and  24.  Pb must be
                          greater than or equal to Pt. If Pt is omitted, it
                          defaults to 1. If Pb is omitted, it  defaults  to
                          24.

          Cursor Movement Commands

          ESC [ Pn A      Cursor Up - Move cursor up Pn lines.  If omitted,
                          Pn is assumed to be  1.  If the cursor is already
                          at  the  top  of  the  screen,  this sequence  is
                          ignored.  If Pn is greater  than  the  number  of
                          lines to the top of the  screen,  the  cursor  is
                          moved to the top of the screen.



          Page 70       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                              Received Escape Sequences



          ESC [ Pn B      Cursor  Down  -  Move  cursor  down Pn lines.  If
                          omitted, Pn is assumed to be 1. If  the cursor is
                          already  at  the  bottom   of  the  screen,  this
                          sequence is ignored.   If  Pn is greater than the
                          number of lines to the bottom of the screen,  the
                          cursor is moved to the bottom of the screen.

          ESC [ Pn C      Cursor Right - Move cursor right Pn  columns.  If
                          omitted, Pn is assumed to be 1. If  the cursor is
                          already at the  right  margin of the screen, this
                          sequence is ignored.   If  Pn is greater than the
                          number  of  columns to the right  margin  of  the
                          screen, the cursor  is  moved to the right margin
                          of the screen.

          ESC [ Pn D      Cursor  Left  - Move cursor left Pn columns.   If
                          omitted, Pn is assumed to be 1. If  the cursor is
                          already at the left  margin  of  the screen, this
                          sequence is ignored.   If  Pn is greater than the
                          number  of  columns  to  the left margin  of  the
                          screen, the cursor is moved to the left margin of
                          the screen.

          ESC [ Pl ; Pc H
                          Cursor  Position  - Move the cursor  to  absolute
                          line given by Pl and absolute column given by Pc.
                          Pl must be between 1 and 24. Pc must be between 1
                          and 80. If omitted, Pl  and  Pc are assumed to be
                          1.

          ESC [ Pl ; Pc f
                          Same as "ESC [ Pl ; Pc H".

          ESC [ H         Cursor Position (Home) - Move  the  cursor to the
                          top left of the screen.   Same  as  the  sequence
                          "ESC [ 1 ; 1 H" or "ESC [ 1 ; 1 f".

          ESC [ f         Same as "ESC [ H".

          ESC [ D         Index -  The  cursor is moved down one line.  The
                          cursor remains in  the  same column.  A scroll up
                          is performed if the cursor moves below line 24.

          ESC [ M         Reverse Index - The cursor is moved  up one line.
                          The cursor  remains in the same column.  A scroll
                          down is  performed if the cursor moves above line
                          1.

          ESC [ E         Next  Line  -  The  cursor is moved to the  first
                          column  of   the  next  line.   A  scroll  up  is
                          performed if the cursor moves below line 24.




                        Copyright 1984,1985 Mark C. DiVecchio       Page 71






          Received Escape Sequences                              PC-VT v7.6



          ESC [ 7         Save  cursor  -  The  current  cursor  position
                          (line,column),   display   character   attribute,
                          selected  character  set,  and  origin  mode  are
                          saved.

          ESC [ 8         Restore  Cursor  - The cursor position and  other
                          saved  attributes  are  restored  to  the  values
                          recorded by the last "ESC [ 7" sequence.  If  the
                          save cursor  Escape  sequence  was  not  received
                          since  PC-VT was started, no values are  restored
                          and the cursor is moved to the top left margin.

          Tab Stops

          ESC H           Horizontal Tab Set - A tab stop is set the column
                          position occupied by the cursor.

          ESC [ g         Tabulation Clear - The tab, if any, at the column
                          position occupied by the cursor is cleared.

          ESC [ 0 g       Same as "ESC [ g".

          ESC [ 3 g       Tabulation Clear - All tabs are cleared.

          Editing Functions

          ESC [ Pn @      Insert Character - Inserts Pn characters starting
                          at the  cursor  position.   Character(s)  to  the
                          right of the cursor  column  move  right.  Pn, if
                          omitted,  is assumed to be 1. Character(s)  moved
                          off of the right of the display are lost.

          ESC [ Pn P      Delete Character - Deletes Pn characters starting
                          at the cursor position.   Characters to the right
                          of the deleted  character(s)  move  left.  Pn, if
                          omitted, is  assumed to be 1. Spaces are inserted
                          at the right as needed.

          ESC [ Pn L      Insert  Line  - Inserts Pn lines before the  line
                          containing cursor.   The  current  line  and  all
                          lines below  it  move  down  the  display.  Lines
                          which move below the  bottom scrolling margin are
                          lost.  Pn, if omitted, is assumed to be 1.

          ESC [ Pn M      Delete  Line  - Deletes Pn lines starting at  the
                          line containing  the  cursor  and  below.   Lines
                          below the deleted lines move up.  New blank lines
                          are created to  fill  the bottom of the scrolling
                          area.  If omitted, Pn is assumed to be 1.

          Erasing




          Page 72       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                              Received Escape Sequences



          ESC [ K         Erase In  Line  - The line occupied by the cursor
                          is erased from the  cursor  to  the  end  of  the
                          line.

          ESC [ 0 K       Same as "ESC [ K".

          ESC [ 1 K       Erase  In  Line - The line occupied by the cursor
                          is erased from the beginning of the line  to  the
                          cursor.

          ESC [ 2 K       Erase  In  Line - The entire line containing  the
                          cursor is erased.

          ESC [ J         Erase In  Display  -  The screen from the current
                          cursor position to the bottom left of the display
                          is erased.

          ESC [ 0 J       Same as "ESC [ J".

          ESC [ 1 J       Erase In Display - The screen  from the top right
                          of the  display to the current cursor position is
                          erased.

          ESC [ 2 J       Erase In Display - The entire screen is erased.

          Print Commands

                          These commands are ignored if there is no printer
                          attached to the PC  or  if  the  printer  is  not
                          ready.  LPT1 or LPT2 is selected on the  SETUP  B
                          display.

          ESC [ ?  5 i    Media Copy - Turn on Auto  Print.  All characters
                          locally or echoed by the host are printed on  the
                          selected line printer,  if  present, as soon as a
                          carriage return is received.

          ESC [ ?  4 i    Media Copy - Turns off Auto Print.

          ESC [ 5 i       Media  Copy  -  Turns on Print  Controller.   All
                          characters received from the host  are  displayed
                          on the selected line printer, if present, as soon
                          as  a  carriage return is received.   Nothing  is
                          displayed on the CRT.

          ESC [ 4 i       Media  Copy -  Turns  off  Print  Controller.   A
                          carriage return and  line  feed should be sent to
                          the  selected  line printer  before  transmitting
                          this  sequence  to be sure that  the  printer  is
                          ready for the next  print  sequence  and that the
                          print carriage is at the left margin.




                        Copyright 1984,1985 Mark C. DiVecchio       Page 73






          Received Escape Sequences                              PC-VT v7.6



          ESC [ i         Media Copy  -  The screen as defined by the print
                          extent in the SETUP B display is  copied  to  the
                          selected  line printer, if present.  A form  feed
                          is  sent  to  the  selected line printer  at  the
                          conclusion of the  printing  if  the  Termination
                          Character feature is set in the SETUP B display.

          ESC [ ?  1 i    Media Copy - The  line  containing  the cursor is
                          printed  on  the  selected   line   printer,   if
                          present.

          Reports

          ESC [ 5 n       Device  Status  Report - The status of PC-VT  and
                          hardware is reported with this response:

                          "ESC [ 0 n " PC-VT is OK.

          ESC [ ?  15 n   Device Status Report - The status of the selected
                          line printer is reported with these responses:

                          "ESC [ ?  13 n " No printer on system
                          "ESC [ ?  10 n " Printer ready
                          "ESC [ ?  11 n " Printer not ready.

          ESC [ 6 n       Device Status Report - The position of the cursor
                          is reported with this response:

                          "ESC [ Pl ; Pc R" The cursor is currently at line
                          Pl and column Pc.

          ESC [ c         Device  Attribute  Report - PC-VT reports that it
                          is  a  VT102 or VT100 Video  Terminal  compatible
                          device with the responses:

                          "ESC [ ?  6 c" I am a VT102
                          or
                          "ESC  [  ?   1  ;  0  c" I am a VT100, basic,  no
                          options.

                          The  response  depends  upon  the  state  of  the
                          Terminal Type bit in the SETUP B display.

          ESC [ 0 c       Same as "ESC [ c".

          ESC Z           Same as "ESC [ c".

          Reset

          ESC c           Reset to  Initial  State  - PC-VT is reset to its
                          initial state  by reading the USER MEMORY file on
                          the  default  drive.    The   program   is   then



          Page 74       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                              Received Escape Sequences



                          restarted.

          Keyboard LEDs

          ESC [ q         Load  LED (LEDs off) - The emulated LEDs  on  the
                          status line 25 of the display is turned off.

          ESC [ 0 q       Same as "ESC [ q".

          ESC [ 1 q       Load LED (L1 on)  -  The  emulated  LED L1 on the
                          status line 25 of the display is turned on.

          ESC [ 2 q       Load LED (L2 on)  -  The  emulated  LED L2 on the
                          status line 25 of the display is turned on.

          ESC [ 3 q       Load LED (L3 on)  -  The  emulated  LED L3 on the
                          status line 25 of the display is turned on.

          ESC [ 4 q       Load LED (L4 on)  -  The  emulated  LED L4 on the
                          status line 25 of the display is turned on.

          VT52 Compatible Mode

          ESC <           Enter ANSI mode.

          ESC =           Enter alternate keypad mode.

          ESC >           Exit alternate  keypad  mode  to  numeric  keypad
                          mode.

          ESC F           Select special graphics character set.

          ESC G           Select US/UK character set.

          ESC A           Cursor up.

          ESC B           Cursor down.

          ESC C           Cursor right.

          ESC D           Cursor left.

          ESC H           Home cursor.

          ESC Y Pl Pc     Direct cursor address.

          ESC I           Reverse line feed.

          ESC K           Erase to end of line.

          ESC J           Erase to end of screen.




                        Copyright 1984,1985 Mark C. DiVecchio       Page 75






          Received Escape Sequences                              PC-VT v7.6



          ESC ^           Enter auto print mode.

          ESC _           Exit auto print mode.

          ESC W           Enter printer controller mode.

          ESC X           Exit printer controller mode.

          ESC ]           Print screen.

          ESC V           Print current line.

          ESC Z           Identify what  you are.  PC-VT responds with "ESC
                          / Z".

                          PC-VT  still  responds  to  DEC  private   escape
                          sequences while in VT52 compatibility mode.

          Set Mode

          ESC [ 2 h       Keyboard  Action   -   The  keyboard  is  locked.
                          Pressing  any  key  causes PC-VT  to  beep.   The
                          message "KBD LOCKED" is  displayed on status line
                          25 of the CRT.

          ESC [ 4 h       Insert-replacement  -  Insert  mode is  selected.
                          Any  characters  received  cause  the  characters
                          currently on the screen  from the cursor position
                          to the right to be  moved  one  position  to  the
                          right.  The  newly  received  character  is  then
                          inserted in the vacated space.

          ESC [ 12 h      Send-Receive  Mode  - Sets host echo.  Characters
                          typed  at the keyboard are not locally  displayed
                          unless they are sent back by the host.

          ESC [ 20 h      Line  Feed  /  New Line - Sets PC-VT to  transmit
                          both a carriage return and  line  feed  when  the
                          ENTER key is pressed.  Causes received line feed,
                          form feed and vertical tab characters to move the
                          cursor to the left column of the next line.

          ESC [ ?  1 h    Cursor Key  -  Set  the  Cursor  keys to generate
                          Application   Mode  functions.   Valid  only   in
                          Application Keypad mode.

          ESC [ ?  5 h    Screen  -  Sets the screen to reverse video mode.
                          The display attribute  is  set to black on white.
                          The entire  display is flipped to black on white.
                          All characters received after this  sequence  are
                          displayed in black on white.




          Page 76       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                              Received Escape Sequences



          ESC [ ?  6 h    Origin  -  Set  the home position to the top left
                          margin of the scrolling  region  set  by the "Set
                          top and bottom margins" sequence "ESC [ Pt  ;  Pb
                          r" .

          ESC [ ?  7 h    Autowrap - Sets  autowrap  on.   When  the cursor
                          gets to the right margin and another character is
                          received,  a  carriage return and line  feed  are
                          sent to the display.

          ESC [ ?  8 h    Autorepeat - Sets  autorepeat  on.   This  is the
                          normal operation of the  IBM  PC  keyboard.  If a
                          key is held down,  it  starts  to repeatedly send
                          it's code to the running program. This is default
                          setting for PC-VT.

          ESC [ ?  18 h   Print Form Feed -  PC-VT sends a Form Feed to the
                          selected line  printer  at  the  conclusion  of a
                          print screen  operation.   This  is  the  default
                          setting.

          ESC [ ?  19 h   Print Extent - The full  screen is printed on the
                          selected  line  printer  by  the   print   screen
                          sequence.  This is the default setting.

          ESC [ ?  21 h   Receive File - Performs the same  function as the
                          CTRL-F3 key on the keyboard.  PC-VT private.

          ESC [ ?  22 h   Transmit File - Performs the same function as the
                          CTRL-F4 key on the keyboard.  PC-VT private.

          Reset Mode

          ESC [ 2 l       Keyboard  Action  -  The  keyboard  is  unlocked.
                          Pressing any  key causes the character to be sent
                          to the host.  The "KBD LOCKED" message is cleared
                          from the status line.

          ESC [ 4 l       Insert-replacement   -   Replacement  mode  is
                          selected.  Any characters  received overwrite any
                          characters on the screen  at the cursor location.
                          This is the default setting.

          ESC [ 12 l      Send-Receive  Mode - Sets local echo.  Characters
                          typed at the keyboard are locally displayed.

          ESC [ 20 l      Line  Feed  / New Line - Resets PC-VT to transmit
                          only  a  carriage return when the  ENTER  key  is
                          pressed.  Causes received line  feed,  form  feed
                          and vertical tab characters to move cursor to the
                          same  column  of  the  next  line.   This is  the
                          default setting.



                        Copyright 1984,1985 Mark C. DiVecchio       Page 77






          Received Escape Sequences                              PC-VT v7.6



          ESC [ ?  1 l    Cursor Key - Reset  the  Cursor  keys to generate
                          ANSI (Cursor Mode) control sequences.  Valid only
                          in Application Keypad mode.   This is the default
                          setting.

          ESC [ ?  5 l    Screen  -  Resets the screen to normal mode.  The
                          display  attribute is changed to white on  black.
                          The  entire  display  is   flipped  to  white  on
                          black.All characters received after this sequence
                          are displayed in white on  black.   This  is  the
                          default setting.

          ESC [ ?  6 l    Origin - Reset the home  position to the top left
                          of the screen.  This is the default setting.

          ESC [ ?  7 l    Autowrap  -  Sets  autowrap off.  When the cursor
                          gets to the right margin and another character is
                          received, the cursor remains  at the right margin
                          and  characters  overlay  one  another  until   a
                          carriage return is received.   This  the  default
                          setting.

          ESC [ ?  8 l    Autorepeat - Sets autorepeat off. PC-VT can  only
                          simulate this function since repeat is handled in
                          the  keyboard  by the 8048. When  PC-VT  receives
                          this escape  sequence,  it  clears  the  keyboard
                          buffer of any characters.

          ESC [ ?  18 l   Print  Form  Feed - PC-VT performs a print screen
                          operation without a terminating form feed.

          ESC [ ?  19 l   Print  Extent  - Only the scrolling region of the
                          screen is printed on the selected line printer by
                          the print screen sequence.





















          Page 78       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                           Escape Sequences Transmitted









                                      Appendix C

                             Escape Sequences Transmitted



            Control  keys  which  do  not have a  defined  ASCII  code  are
          translated into Escape sequences  for  transmission  to the host.
          These keys  are  cursor keys and keypad keys.  Both sets of these
          keys can transmit different sequences.  The  codes  sent  by  the
          keypad  keys  are selected by the "Set Numeric Keypad"  and  "Set
          Application keypad" commands.  The codes for the cursor keys  are
          selected by the "Set Cursor" and "Reset  Cursor"  mode  commands.
          Note that setting numeric keypad mode, resets  the  cursor  mode.
          Set and reset cursor mode only  function  in  application  keypad
          mode.  This VT100/102 defined numeric keypad mode has nothing  to
          do with the PC NUM LOCK  key.  The NUM LOCK key functions locally
          in the PC only per the IBM documentation.


          VT100/102 Cursor Keys

          Key     Reset (Cursor) Mode     Set (Application) mode

          Up      ESC [ A                 ESC O A
          Down    ESC [ B                 ESC O B
          Right   ESC [ C                 ESC O C
          Left    ESC [ D                 ESC O D


          VT100/102 Emulated Keypad Keys

          IBM PC          Emulated        ANSI Numeric    ANSI Alternate
          Key             VT100/102 Key   Keypad Mode     Keypad Mode

          F10             0               0               ESC O p
          F7              1               1               ESC O q
          F8              2               2               ESC O r
          Shift F7        3               3               ESC O s
          F5              4               4               ESC O t
          F6              5               5               ESC O u
          Shift F5        6               6               ESC O v
          F3              7               7               ESC O w
          F4              8               8               ESC O x
          Shift F3        9               9               ESC O y
          Shift F4        -(minus)        -(minus)        ESC O m



                        Copyright 1984,1985 Mark C. DiVecchio       Page 79






          Escape Sequences Transmitted                           PC-VT v7.6



          Shift F6        ,(comma)        ,(comma)        ESC O l
          Shift F9        .(period)       .(period)       ESC O n
          Shift F8        ENTER           ENTER           ESC O M
          F1              PF1             ESC O P         ESC O P
          F2              PF2             ESC O Q         ESC O Q
          Shift F1        PF3             ESC O R         ESC O R
          Shift F2        PF4             ESC O S         ESC O S



          VT52 Cursor Keys

          Key     Reset (Cursor) Mode     Set (Application) mode

          Up      ESC A                   ESC A
          Down    ESC B                   ESC B
          Right   ESC C                   ESC C
          Left    ESC D                   ESC D


          VT52 Emulated Keypad Keys

          IBM PC          Emulated        ANSI Numeric    ANSI Alternate
          Key             VT100/102 Key   Keypad Mode     Keypad Mode

          F10             0               0               ESC ? p
          F7              1               1               ESC ? q
          F8              2               2               ESC ? r
          Shift F7        3               3               ESC ? s
          F5              4               4               ESC ? t
          F6              5               5               ESC ? u
          Shift F5        6               6               ESC ? v
          F3              7               7               ESC ? w
          F4              8               8               ESC ? x
          Shift F3        9               9               ESC ? y
          Shift F4        -(minus)        -(minus)        ESC ? m
          Shift F6        ,(comma)        ,(comma)        ESC ? l
          Shift F9        .(period)       .(period)       ESC ? n
          Shift F8        ENTER           ENTER           ESC ? M
          F1              PF1             ESC P           ESC ? P
          F2              PF2             ESC Q           ESC ? Q
          Shift F1        PF3             ESC R           ESC ? R
          Shift F2        PF4             ESC S           ESC ? S












          Page 80       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                          Responses to Escape Sequences









                                      Appendix D

                            Responses to Escape Sequences



            PC-VT  responds  to  several   control  characters  and  Escape
          sequences.  They are listed  here.   For  a complete description,
          see the Appendices.


          Elicitor                Response

          Enquire                 Answerback message
          Device Status Report    PC-VT responds with emulator status
          Cursor Status Report    Current cursor position is reported
          Device Attributes       PC-VT identifies itself as either a VT100,
                                  a VT102, or a VT52 depending on the bits
                                  set/reset in the SETUP B display.
          Identify Terminal       PC-VT identifies itself as either a VT100,
                                  a VT102, or a VT52 depending on the bits
                                  set/reset in the SETUP B display.



























                        Copyright 1984,1985 Mark C. DiVecchio       Page 81






          Special ALT Key Definitions                            PC-VT v7.6









                                      Appendix E

                             Special ALT Key Definitions



            PC-VT uses ALT-K to startup the Macro Key facility and ALT-F to
          startup the PC-DOS Command Processor.

            Additionally, several special ALT key commands are available to
          the user of PC-VT.  They were  implemented to aid in the debug of
          this program.  Most  of  these  will  be  useful  only under very
          special circumstances  but  some  will be of general use.  To use
          these  commands,  hold  down  the  ALT key and at the  same  time
          depress the key listed.  They work  only  in  the  communications
          display,  they  do  not  work in the  SETUP,  DIALING,  or  MACRO
          displays.   The  author  of  this  program  makes  no  claims  or
          guarantees about these keys and you use them at your own risk.

          ALT Key plus            Function

          E               Echo toggle.  This  key  toggles the state of the
                          echo  flag.   If  the  host is not  echoing  back
                          characters,  you  can type alt-e and  PC-VT  will
                          echo the characters to the display.

          F               Fork. This key sequence starts up another copy of
                          Command.COM.  This  is  done  without terminating
                          PC-VT or breaking the  host connection.  Once the
                          new Command.COM is  started,  you can run any DOS
                          function or  other  PC  program.   You  should be
                          careful that you don't  run  a  program that uses
                          the  same communications port as PC-VT is  using.
                          The  other  program  may  leave  the  port in  an
                          unexpected state.   PC-VT may not then be able to
                          get control of  the  port again.  Also be careful
                          that you don't alter any files which PC-VT may be
                          using.  To  exit from the new copy of Command.COM
                          and return to  PC-VT,  type "exit" at the command
                          prompt.

          G               Print current  line.   The  line  containing  the
                          cursor  is  printed on the selected  printer,  if
                          present.  Performs the same function  as  receipt
                          of a "ESC [ ?  1 i" sequence.




          Page 82       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                            Special ALT Key Definitions



          K               Macro Key  Directory.   Start  up  the  Macro Key
                          Directory.   See  the  entire  chapter  on  Macro
                          Keys.

          M               Toggles "Ignore Nulls" mode.  Null(ASCII  0)  and
                          Delete(ASCII 127) characters are not normally put
                          into the communications buffer.  This  switch  on
                          causes those characters  to  be put in the buffer
                          just as all other characters.   These  characters
                          are eventually ignored by PC-VT,  the  difference
                          is that they now take up  I/O  buffer  space  and
                          cannot be used as "filler" or timing characters.

          N               Toggles "Ignore  ESCAPE"  mode.   Received ESCAPE
                          sequences are not acted upon.  They are displayed
                          as regular characters on  the screen.  The ESCAPE
                          character  itself   is   displayed   as  "<ESC>".
                          Toggling this switch  at  the wrong time may lead
                          to unpredictable results.  Autowrap is  set  when
                          this switch is set.

          O               Test  Insert  Characters command.   Performs  the
                          same function  as  receipt  of  a  "ESC  [  5  @"
                          sequence.

          P               Test  Delete  Characters command.   Performs  the
                          same function  as  receipt  of  a  "ESC  [  5  P"
                          sequence.

          R               Restart PC-VT.  Clear COMx  port and restart from
                          the beginning.  Selected features and  tab  stops
                          are not changed.  Host  connection is not broken.
                          This  command  is  useful  if you make  the  host
                          connection  after PC-VT is started and COMx  port
                          needs to be initialized.

          T               Clear the screen.  Cursor  not  moved.   Performs
                          the  same  function as receipt of a "ESC [  2  J"
                          sequence.

          X               Reset XOFF Flag.   If  PC-VT has received an XOFF
                          character, it will not transmit anything.  If you
                          type a  character,  PC-VT  will  beep  and ignore
                          you.  This is  part  of the VT10x definition.  If
                          something happens  and  PC-VT  receives  an  XOFF
                          because of garbage on the line, you can reset the
                          XOFF flag by typing alt-x.

            The following  ALT  keys work only in Numeric Keypad mode ( the
          default mode).





                        Copyright 1984,1985 Mark C. DiVecchio       Page 83






          Special ALT Key Definitions                            PC-VT v7.6



          ALT Key plus            Function

          B               Transmits  the answerback message.  Performs  the
                          same  function  as receipt of a  Enquire  Control
                          Character (ASCII 5).

          D               Turn off  Print  Only  Mode.   Performs  the same
                          function as receipt of a "ESC [ 4 i" sequence.

          S               Turn  on  Print Only Mode.  All  characters  sent
                          from the host are printed on the selected printer
                          only.  Performs the same function as receipt of a
                          "ESC [ 5 i" sequence.

          1               Report   Cursor  Position.   Performs  the   same
                          function as receipt of a "ESC [ 6 n" sequence.

          2               Report   Terminal  Status.   Performs  the   same
                          function as receipt of a "ESC [ 5 n" sequence.

          3               Report  Printer   Status.    Performs   the  same
                          function  as  receipt  of  a  "ESC  [  ?   15  n"
                          sequence.

          4               Report  Device  Attributes.   Performs  the  same
                          function as receipt of a "ESC [ c" sequence.

          8               Clear Tab Stop.   Performs  the  same function as
                          receipt of a "ESC [ 0 g"  sequence.   You  should
                          use the SETUP A display.

          9               Set Tab  Stop.   Performs  the  same  function as
                          receipt of a "ESC  H"  sequence.   You should use
                          the SETUP A display.

          0               Clear All Tab Stops.   Performs the same function
                          as receipt of a "ESC [ 3 g" sequence.  You should
                          use the SETUP A display.

















          Page 84       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                PC-VT Technical Details









                                      Appendix F

                               PC-VT Technical Details



            This  appendix  will  list  some  of   the   details   of   the
          implementation of PC-VT for the  user  who wishes to interface to
          the program in some non-standard way.

            PC-VT has been tested on PC-DOS 1.1, 2.0, and 2.1 on the IBM PC
          and the IBM PCjr.  I can't vouch for any compatibles.

            BIOS calls used by PC-VT:


                  10H     to handle the display of characters and control
                          sequences while communicating with the host.

                  11H     to determine the type of monitor on the system
                          and to determine if a line printer is present.

                  14H     to initialize the COM port.

                  16H     to look at the CAPS LOCK, NUM LOCK, and SCROLL
                          LOCK key status.

                  17H     to get the printer status and to print characters.

                  1AH     to directly read the binary time of day clock.

          PC-DOS calls used by PC-VT:

                  21H     the general DOS utility call with AH equal to

                          6H      to read characters from the keyboard
                          9H      to display error messages on the CRT.
                          0AH     to read filenames from the keyboard.
                          10H     to close disk files.
                          11H     to check disk for the existence of files.
                          13H     to delete old download files.
                          14H     to perform sequential disk reads.
                          15H     to perform sequential disk writes.
                          16H     to create new download files.
                          19H     to get the current default drive.
                          1AH     to set Disk Transfer Addresses.



                        Copyright 1984,1985 Mark C. DiVecchio       Page 85






          PC-VT Technical Details                                PC-VT v7.6



                          25H     to set the interrupt vectors for the
                                  COM port, the critical error handler
                                  and the CTRL-BREAK key.
                          29H     to parse upload/download filenames.
                          2CH     to get the time of day.

                          DOS 2.+ routines

                          2EH     to set VERIFY on.
                          30H     to determine the DOS version number.
                          33H     to set/clear BREAK checking.
                          3CH     to create a file with a pathname.
                          3DH     to open a file with a pathname.
                          3EH     to close a file with a pathname.
                          3FH     to read from a file with a pathname.
                          40H     to write to a file with a pathname.
                          41H     to delete a file with a pathname.
                          47H     to get the current default directory.
                          4EH     to check for the presence of a file
                                  with a pathname.
                          54H     to determine the state of the VERIFY switch.

                  22H     to terminate the program if the hardware
                          configuration does not fit PC-VT requirements.
                          This is before the CTRL-BREAK handler is
                          initialized.

                  23H     to terminate the program and restore the
                          CTRL-BREAK address in DOS. This is the "normal"
                          way to terminate PC-VT.

            In  order  to get the highest speed out of  the  RS-232  ports,
          PC-VT does direct input/output to those ports.   PC-VT  uses  I/O
          addresses:

                  COM1    COM2
                  ----    ----
                  3F8H    2F8H    Data input/output register
                  3F9H    2F9H    Interrupt enable register
                  3FAH    2FAH    Interrupt identification register
                  3FBH    2FBH    Line control register
                  3FCH    2FCH    Modem control register
                  3FDH    2FDH    Line status register
                  3FEH    2FEH    Modem status register

          for this purpose.   PC-VT  gets  these  address  from  PC-DOS  by
          looking at the two  words  starting  at  address  400  (segmented
          address 40:0) for the starting  port  addresses for COM1 and COM2
          respectively.  This  enhances  compatibility  with IBM-compatible
          systems which may use non  standard  communications  port  device
          address.  Note  that  the IBM PCjr does not assign COM ports like
          the  PC.  PC-VT has to do a little special work but it will  keep



          Page 86       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                PC-VT Technical Details



          them straight (jr switches the addresses if the internal modem is
          installed).

            PC-VT sends a BREAK to  the host by setting bit 6 of the RS-232
          Port's Line Control Register for at least one-half  second.   The
          bit is then cleared.

            PC-VT controls the Speaker to cause it  to beep by doing direct
          I/O to addresses 42H,43H, and 61H.

            If you use an external MODEM or a  direct  connect,  PC-VT does
          not require that all 25 lines of the DB-25 connector on  the  COM
          port be connected.  Actually, only  pin  2 (transmit data), pin 3
          (receive data), and pin 7  (signal  ground)  need  be  connected.
          PC-VT does not use Clear to Send (CTS), Data Set Ready  (DSR)  or
          any other Modem status line.  This is the FDX A mode of VT100/102
          operation.  Since some Modems require a basic handshake with  the
          COM port, PC-VT sends Data Terminal Ready (DTR) and Ready to Send
          (RTS) out of the  COM  port.   These 2 lines are not cleared when
          you  terminate  PC-VT.    This   permits  the  connection  to  be
          maintained  while  you go back to DOS.  Be careful  because  this
          means that the phone will not  hang  up  automatically  when  you
          terminate PC-VT.  If you  have  a  Hayes  compatible  modem,  you
          should use the F5 function of the DIALING display to be sure.  If
          your modem is manual, then physically hang up the phone.

            Receive parity checking, if set, checks not only receive parity
          but also  data  overrun and framing errors.  PC-VT puts a '!'  in
          the buffer when a character with bad parity  is received.  Parity
          checking must be enabled in the SETUP B display.

            PC-VT also does direct I/O to the 8259  Programmable  Interrupt
          Controller (PIC).  It uses  port  address  21H  for  reading  the
          interrupt source and address 20H for clearing that interrupt.

            The communications buffer in  PC-VT  is  256  bytes  long.   To
          prevent buffer overflow, the XON/XOFF support sends XOFF when 190
          unprocessed characters  are  in  the buffer (the 75% point of the
          buffer).  Then, XON is sent when the buffer backlog is reduced to
          26 characters (the 10% point of the buffer).  If the host ignores
          the  XOFF   character  transmitted,  PC-VT  will  display  a  '#'
          character  when  the buffer overflows.  All  characters  received
          while the buffer is in the overflow condition are discarded.  For
          those with  slow  hosts, a feature in the SETUP B display changes
          the XOFF timing to the 50% point of the buffer.  This  seemed  to
          be needed for Prime  2550  hosts  and  hosts  communicating  thru
          Gandolf or Micom line concentrators.

            Since the IBM PC does not have some  of  the  special character
          and line drawing set characters, PC-VT  makes  use  of  the  best
          available representation.  See the description for the "ESC )  0"
          sequence for the description of the selected representation.



                        Copyright 1984,1985 Mark C. DiVecchio       Page 87






          PC-VT Technical Details                                PC-VT v7.6



            PC-VT will handle ASCII characters for codes greater than  255.
          This will work only when the COM port is initialized for  8  bits
          of data transfer.  If a code greater  than 127 is received, PC-VT
          can display the character defined in the IBM  documentation.   In
          this way, PC-VT is  compatible  with  RBBS  systems  using  these
          extended  characters  while  maintaining  compatibility  with  VT
          terminals.  The  "256  char" bit must be set in the SETUP display
          for these extended characters to be displayed.  Some hosts  don't
          strip this 8th bit even  when  communicating  with  plain  ASCII.
          This will cause some mighty unusual behavior.   Be  careful  when
          you use this feature.

            The NUM LOCK key will act per the IBM documentation.

            Undefined or illegal Escape control sequences are ignored.

            PC-VT does not "look" into PC-DOS directly for  any reason with
          the exception of finding the  COM1  and COM2 port address.  PC-VT
          should be compatible with all future releases of PC-DOS.

            An error in either DOS or  the BIOS code, causes a problem with
          the cursor.  When PC-VT starts, it cannot ascertain  the shape of
          the cursor due to this error.  Although PC-VT will be able to use
          either the underline or block cursor, it may not be able to reset
          the  cursor  to  the  original  size  upon exit.  This will  work
          correctly when IBM fixes DOS.

            Older versions of PC-VT would not pass CTRL-C  on  to  the host
          computer because the  CTRL-C  was  intercepted  by  PC-DOS  as  a
          program termination  command.  This and future versions have been
          modified  to  have PC-DOS and PC-VT ignore CTRL-C in  most  cases
          when reading from the keyboard or outputing to the console.  This
          was done by using DOS function 6H for  keyboard  input  and using
          BIOS calls for most console output.  Now CTRL-C  is  sent  to the
          host.   To  terminate  PC-VT  you  can  type  CTRL-F8  from   the
          communications display or still use  CTRL-C  from  the  SETUP  or
          DIALING displays.  Because of the fact that other PC-DOS function
          calls still check for CTRL-C,  I  could only suppress checking of
          that control key when the 6H direct console input DOS call or the
          10H console output  BIOS  was  used.   There are a few cases when
          standard PC-DOS calls had to be used for  output.   In  the SETUP
          and DIALING  displays,  PC-VT still uses DOS call 9H to display a
          line.  Typing CTRL-C in either  of  these displays will cause the
          program will  to  be  terminated.  In most cases, when "LOCAL" is
          displayed in the status line, CTRL-C will terminate  PC-VT.   You
          should normally use CTRL-Y for VMS program termination.

            If you are using DOS 2.x, you should not have executed a "BREAK
          ON" command.  If you have,  PC-VT  clears BREAK checking while it
          is running and restores it as it terminates.





          Page 88       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                PC-VT Technical Details



            With the addition of XMODEM file transfer  with  CRC  checking,
          PC-VT as made a commitment to accurate file transfer.  In support
          of this, if you are running DOS 2 or later, PC-VT sets the VERIFY
          switch on  during  its run.  The VERIFY switch is restored to its
          initial value as PC-VT terminates.

            PC-VT is not compatible with Extended Batch Language  (EBL)  or
          with SCRLOCK.  I have not tested PC-VT running on any system with
          non-IBM DOS "patches" or auxiliary programs.

            A  comment  on the operation of PC-VT on the  IBM  PCjr;  PC-VT
          version  7.0  and up will operate on the PCjr.   There  are  some
          hardware differences which you should be aware of.   Since  PC-VT
          requires  an  80 column display, the DOS mode command  should  be
          executed using 'bw80' as the parameter.  This most  likely  means
          that you cannot use a TV set for a display.  If you are using the
          PCjr internal modem for XMODEM data transfer, don't  forget  that
          you must set the modem  with a "^NF 4" command.  When the PCjr is
          doing a disk access, all  other  interrupts are turned off.  This
          means that if data comes down the comm line,  it  will  be  lost.
          For this reason, I do not recommend using ASCII file transfer for
          receiving a file.  Use XMODEM.   Sending  a file using ASCII mode
          should work ok.  The PC-VT distribution diskette  has  an  XMODEM
          program written in FORTRAN for  the  VAX running VMS.  The dialer
          will work fine if you change the  modem dialing command from ATDT
          to the characters required by the PCjr modem.

            A comment on the 8250 serial  chip; Some of the 8250 chips used
          in  PC's  and  on  PC compatible serial  ports  do  not  function
          correctly.   Specifically,  they  do  not   generate   interrupts
          correctly  to  the  8088.  PC-VT  is  interrupt driven and if  an
          interrupt is lost, unusual things  may  happen.  I have seen this
          on  newer  PC's and PCjr's.  I have an older PC and I have  never
          seen the problem on my system.  This lost  interrupt causes PC-VT
          to think that the communications  line  is  always  busy.   PC-VT
          tries  to  send each character typed but times out.   PC-VT  then
          beeps at  you  to indicate something is wrong.  You can clear the
          error  on  older  versions  of  PC-VT  by typing alt-r.  On  this
          version of PC-VT, I have implemented a software  fix  recommended
          by National  Semiconductor.  Look at the PCjr Technical Reference
          Manual, bottom of page A-66.














                        Copyright 1984,1985 Mark C. DiVecchio       Page 89






          User-Supported Software                                PC-VT v7.6









                                      Appendix G

                               User-Supported Software



            This program and documentation are copyrighted.

            Permission to copy:

            Individuals,  clubs  and  other  non-profit  organizations  are
          granted permission by the author to freely copy  this program and
          documentation and share it with their members, so long as:

            -  No  price  is  charged  for the software  or  documentation.
               However, a distribution cost may be charged for  the cost of
               the diskette, so long as it is not more than $9 total.

            -  Club members  are informed of the user-supported concept and
               encouraged to support it with their donations.

            -  The program and documentation are not modified  in  any  way
               and are always distributed together.

            Commercial  users  of  this  program  are  required  to  submit
          payment.

                             The User-Supported concept:

                               User-Supported Software
            If you are using this program and find it to be of value your
                contribution will be appreciated.  ($35 is suggested)

                                  Mark C. DiVecchio
                                  9067 Hillery Drive
                                 San Diego, CA  92126

                Regardless of whether you make a contribution, you are
                   encouraged to use, copy and share this program.

            User-supported  software  is  an  experiment  in   distributing
          computer programs, based on these beliefs:

            -  That the value and utility  of  software is best assessed by
               the user on his/her own system.




          Page 90       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                User-Supported Software



            -  That  the  creation of personal computer  software  can  and
               should be supported by the computing community.

            -  That copying of  programs  should be encouraged, rather than
               restricted.

            Anyone may request  a  copy  of  a  user-supported  program  by
          sending a blank double sided double density,  formatted  disk  to
          the author of the program.   An  addressed,  postage-paid  return
          mailer must accompany the disk (no exceptions, please).   A  copy
          of the  program,  with documentation on the disk, will be sent by
          return mail.  The  program  will  carry  a  notice  suggesting  a
          contribution to the  program's  author.  Making a contribution is
          completely voluntary on the part of each non-commercial user.

            Free distribution of software and voluntary payment for its use
          eliminates costs for advertising and copy protection schemes.

            Users obtain quality software at reduced cost.  They can try it
          out before buying, and do so at their own pace and in the comfort
          of  their  own home or office.  The best programs  will  survive,
          based purely on their quality and usefulness.

            Please join the experiment.

            If you believe in these ideals, your contribution is  solicited
          to help make them work.

            The following invoice is provided for those  of you who wish an
          invoice  for  your  tax  records.   Perhaps  it  will  serve  the
          purpose.
























                        Copyright 1984,1985 Mark C. DiVecchio       Page 91






          User-Supported Software                                PC-VT v7.6




                                 --------------------
                                       INVOICE
                                 --------------------




                      Purchased from:
                           Mark C. DiVecchio
                           9067 Hillery Drive
                           San Diego, CA  92126


               DATE:     /     /                     Invoice No. 101
               --------------------------------------------------------------
                                                    PRICE     PRICE
               PRODUCT                    QTY       EACH      EXTENDED
               -------------------------  ---       -----     --------

               PC-VT Terminal Emulator
                  and Condensed Manual              $35
                  Registration Fee v7.6

               PC-VT Distribution Disk               $9
                  Includes Postage and
                  Handling

               Copy of PC-VT and Documentation
                  on your Preformatted DSDD
                  Diskette Returned in your
                  Postage Paid Mailer                N/C
                                       --------------------------------------
                                                  SUBTOTAL

               6% Sales Tax (CA Residents only)

                                       --------------------------------------
                                       PLEASE PAY THIS AMOUNT           TOTAL
                  -----------------------------------------------------------



                  Please make check payable to :Mark C. DiVecchio


                  You may retain this Invoice for your tax records.








          Page 92       Copyright 1984,1985 Mark C. DiVecchio






          PC-VT v7.6                                User-Supported Software


























































                        Copyright 1984,1985 Mark C. DiVecchio       Page 93






          PC-VT







                                        Index


          ! - Parity Error Character 32, 87
          # - Buffer Overflow Character 33, 87
          8 Bit ASCII 33, 88
          8250 UART 89
          8259 PIC 87
          Application Keypad mode 13
          ASCII file transfer with handshake 41
          Autorepeat 29, 77, 78
          Backspace Key 32
          Beep 6
          BREAK 24
          Bypass Character 41
          Cable, Interface 87
          Calling COMMAND.COM 82
          CAPS LOCK 23
          Changing the default directory 49
          Clearing all Tabs 26
          Clearing COM port 83
          Clearing the Screen 83
          COM Port Addressing 86
          COM Port Selection 27, 33
          Communications Buffer Handling 87
          Communications Display 10
          Cursor Problem 88
          Default directory, changing 23
          Dialing Directory Fetching 54
          Dialing Directory Saving 54
          Dialing Facility 24
          DIALING key 51
          ECHO Local/Remote Toggle 82
          EDT Editor 16
          Error Messages 36
          Error Messages - Dialing Directory 55
          Error Messages - Macro Directory 63
          Feature Defaults 29
          Feature Saving 26
          Hanging up the phone 54
          Line Printer Selection 33
          Line Turnaround Character 41
          Logon Macros 53
          LPT Selection 33
          Macro Directory Fetching 62
          Macro Directory Saving 62
          Macro Facility 24
          MACRO KEYS 59
          NO SCROLL 23









          PC-VT



          NUL Character Key 23
          NUM LOCK 14, 23
          Parity Checking 32
          PC-VT= 9, 35, 55, 59, 62
          PCjr 89
          PRIME 2550 Users 33
          Printer Echo 24
          Printing the Screen 23
          Receiving (Downloading) Files 23
          Restart 24
          Running Programs from PC-VT 82
          SCRLOCK 89
          SCROLL LOCK 23
          Selecting Autowrap 31
          Selecting Cursor Mode 30
          Selecting Defaults 26
          Selecting Features 27
          Selecting Local Echo 31
          Selecting Modem Parameters 28
          Selecting Modem Speed 28
          Selecting Screen Background 30
          Selecting Stop Bits 32
          Selecting Tab Defaults 26
          Setting and Clearing Tabs 25
          Setting Answerback Message 29
          SETUP 23
          SETUP key 25
          Smart Macros 61
          Status Line 6, 10, 23, 30, 57
          Terminating PC-VT 12, 24
          Time of Day 33
          Transmitting (Uploading) Files 23
          UK Character Set 30
          Using the IBM fixed disk 10
          VT BACKSPACE Key 23
          VT CURSOR keys 13
          VT DELETE key 13
          VT FUNCTION keys 13
          VT LINEFEED Key 23
          VT100/VT102 Selection 33
          VT52 Selection 30
          XMODEM 44, 49
          XOFF-How to clear it 83
          XON/XOFF 30


















          PC-VT







                             Table of Contents


          Chapter 1 Introduction                                      4

          Chapter 2 Required Hardware and Software                    8

          Chapter 3 Starting PC-VT                                    9

          Chapter 4 Stopping PC-VT                                    12

          Chapter 5 Keyboard assignments                              13

          Chapter 6 SETUP Displays                                    25

             6.1 SETUP A                                              25
             6.2 SETUP B                                              27

                6.2.1 SETUP B Features and Defaults                   29

          Chapter 7 The PARAMS.DAT File                               35

             7.1 Creation                                             35
             7.2 Location                                             35
             7.3 Updating                                             36
             7.4 Error Messages                                       36

          Chapter 8 Transmitting and Receiving Files                  38

             8.1 Transmitting ASCII Files (Uploading)                 38

                8.1.1 Uploading with Handshake                        41
                8.1.2 Example of a transmission session               42
                8.1.3 A Useful VAX .COM Upload file                   42

             8.2 Transmitting Binary Files (Uploading)                44
             8.3 Receiving ASCII Files (Downloading)                  44

                8.3.1 Example of a receive session                    47
                8.3.2 A Useful VAX .COM Download file                 47

             8.4 Receiving Binary Files (Downloading)                 49
             8.5 Changing the Default Directory                       49

          Chapter 9 DIALING Display                                   51

             9.1 Instructions for DIALING                             51
             9.2 The DIALER.DAT File                                  54
             9.3 Creation                                             55









          PC-VT



             9.4 Location                                             55
             9.5 Updating                                             55
             9.6 Error Messages                                       55

          Chapter 10 PC-VT Status Line                                57

          Chapter 11 Macro Display                                    59

             11.1 Instructions for Macro                              59
             11.2 The MACRO.DAT File                                  62
             11.3 Creation                                            62
             11.4 Location                                            62
             11.5 Updating                                            63
             11.6 Error Messages                                      63

          Appendix A List of Control Characters                       65

          Appendix B Received Escape Sequences                        68

          Appendix C Escape Sequences Transmitted                     79

          Appendix D Responses to Escape Sequences                    81

          Appendix E Special ALT Key Definitions                      82

          Appendix F PC-VT Technical Details                          85

          Appendix G User-Supported Software                          90