SIX -- a simple text extractor
      		     Version 3.0, 12/8/85

1. INTRODUCTION

      SIX is a utility designed to select records from files, based
      upon the record's position in the file.  It is useful for listing
      the beginnings of files, the ends, or the middles.

      It is designed to do its job extremely quickly, and so is optimized
      for sequential files with variable length records.  Currently, other
      file types are not supported, but will be in later releases.

2. THE FILES IN THIS DIRECTORY

      The following files are provided:

         6.MAR		-- source for the main program
   
         AAAREADME.DOC  -- the obligatory list of files
   
         ERR.MAR	-- source for error routines
   
         EXTCLD.CLD	-- command language definition file used to define
         		   the verb SIX system-wide.
   
         EXTCLD.CLD	-- command language definition file used by SIX
         		   for internal parsing.
   
         LOAD.COM	-- command procedure to create SIX.EXE
   
         MAC.MAR	-- source for assembler macros.  They must be put
         		   into a macro library before compiling the routines.
   
         MESS.MSG	-- message definition file.  This must be processed
         		   into an object file and link with the rest.
   
         SIX.DOC	-- this document.
   
         SIX.HLP	-- help entry for this utility.
   
         STACK.MAR	-- source for routines to handle the record-testing
         		   stack.

3. INSTALLING THE UTILITY

      A. BUILDING THE EXECUTABLE

         Use the command "@LOAD.COM", which will compile and link, and do
         all the miscellaneous file handling necessary.

         For increased efficiency, the system manager can install the image
         with the characteristics of Sharable and Header-resident.  This
         will speed up response time and decrease system overhead.

      B. DEFINING THE COMMAND

         The command SIX may be defined in two ways, either system-wide
         using the DCL command definition utility, or by individual users
      	 for themselves alone.

         Privileges are required to define SIX system wide, use the command

      		$ SET COMMAND/TABLE=SYS$SHARE:DCLTABLES.EXE EXTCLD

         If the verb is not defined, users can define it themselves, 
         using the following command

      		$ SIX  :==  $<six-directory>6

         This must be redefined each time you log on, unless it is put
         into your login.com.

         where <six-directory> is the full specification of the disk and
         directory where 6.EXE will be found.

      C. INSTALLING THE HELP

         The help file provided can be added to the system help library
         using the following command

      		$ LIBRARY/HELP SYS$HELP:HELPLIB SIX

4. SYNTAX AND USE

      See SIX.HLP for more details.

5. COMMENTS

      SIX is a simplified version of X, the not-yet-implemented super
      text extractor.  That one will probably never arrive because I
      cannot find an acceptable expression syntax.

      I don't have anything to say for this version, except perhaps that
      I'm sorry I didn't have time to finish the sections to process
      non-sequential-variable-length-record files.  That and possibly
      other improvements will be along eventually.

      There are no known bugs.

6. SUGGESTIONS

      Feel free to send comments and suggestions to

      	Gregory C. Lowney
      	Physics Hall  FM-15
        University of Washington
        Seattle, Washington 98195

      or to bitnet address GREC@UWAPHAST.