; - FILE FNDFIL.DOC
;

	Fndfil is a program that searches all file headers on a disk trying
to locate a logical block within a file.  This can be useful when the
Error Logger indicates disk errors.  The error log reports certain errors by
logical block number (LBN).  The error log report of what LBN's are bad does 
not lend itself to easily resolving these bad spots on the disk.  This 
program helps you to identify what files these LBN's are in.  It additionally
computes the virtual block number within the identified file.  Once identified,
individual blocks of corrupted files can hopefully be restored or recreated 
from backups and thus eliminate the cause of the system errors.


	Please direct comments and suggestions to:



		Barry Zion
		The Federal Reserve Bank of N.Y.
		95 Maiden Lane  -  7th floor annex
		New York, N.Y. 10045

		tel: (212) 791-5585


	To run the program:

	$RUN FNDFIL

	DISK TO SEARCH ON [logical names ok]: name
	enter a device such as "DJA1:" or
	      a logical name such as "SYS$SYSDEVICE:"

	LOGICAL BLOCK # TO SEARCH FOR: nnnnnnnnnn
	enter a decimal LBN in the range 1 - max
		where max is the highest LBN for the particular disk

	FIND FIRST OCCURRENCE ONLY [default=N] : 
	enter "Y" if you wish the program to search all valid file headers
		in case there is a multiply allocated block,

	enter "N" if you wish to find only the first file header
		this mode may save some time if the located FILE ID is 
		low


	Fndfil outputs a header message indicating the 32-bit HEX LBN it is 
searching for.  Then if any file header's retrieval pointers are mapping
the LBN various information pertaining to the header are displayed.  Once the 
program finishes you may wish to verify via a directory command that  the file
is indeed accessible.  You can also get more information about the file by
using the command procedure DMPHDR.COM to display ther file header of the file
locateed by fndfil. Define a command as follows:

	$DMPHDR:==@DMPHDR
	$! then type 
	$DMPHDR filename

	Substitute in the file name(s) output by fndfil and check the various
file header fields.

	If you answered "N" to the find first occurrence question FNDFIL 
will continue searching all file headers even if a file is found.  This 
is extra insurance in case of a severely corrupt file system in which a 
block is allocated to more than one file.  When all file headers are exhausted
a file header summary is displayed showing in use and free file headers 
as follows:

SEARCH OF ALL FILE HEADERS COMPLETED ON SYS$SYSDEVICE:

FILE HEADER SUMMARY

     SCANNED IN USE FILE HEADERS :      2711
     SCANNED  FREE  FILE HEADERS :       148
FILE HEADERS YET TO BE ALLOCATED :     47163
--------------------------------------------
MAX FILE HEADERS FROM HOME BLOCK :     50022




		FNDFIL CAN BE BUILT BY INVOKING @FNDFILBLD.CMD

	This command file will assemble and link all modules of fndfil.
And when you're ready to fix all the bugs I so cleverly and unknowingly left
in the program you can use @FNDFILDBG.COM.  This will create FNDFILDBG.EXE.


*******************************************************************************

	To test FNDFIL use the command file @tstfndfil.com.  This command 
file will DUMP the file header of the newly created FNDFIL.EXE.  You can then 
use this data as input to the program.  This will see if fndfil can at least 
find itself!  Enter the LBN of the first (or any other) block of FNDFIL.TSK as 
specified by the dmp.  A sample DMP follows:



Dump of file SYS$SYSDEVICE:[BARRY.FNDFIL]FNDFIL.EXE;1 on 27-FEB-1986 12:09:30.14
File ID (2652,44,0)   End of file block 64 / Allocated 66

                             File Header

Header area
    Identification area offset:           38
    Map area offset:                      65
    Access control area offset:           255
    Reserved area offset:                 255
    Extension segment number:             0
    Structure level and version:          2, 1
    File identification:                  (2652,44,0)
    Extension file identification:        (0,0,0)
    VAX-11 RMS attributes
        Record type:                      Fixed
        File organization:                Sequential
        Record attributes:                <none specified>
        Record size:                      512
        Highest block:                    66
        End of file block:                64
        End of file byte:                 498
        Bucket size:                      0
        Fixed control area size:          0
        Maximum record size:              512
        Default extension size:           0
        Global buffer count:              0
        Directory version limit:          0
    File characteristics:                 Contiguous best try
    Map area words in use:                2
    Access mode:                          0
    File owner UIC:                       [000320,000021]
    File protection:                      S:RWED, O:RWED, G:RE, W:
    Back link file identification:        (1765,129,0)

Identification area
    File name:                            FNDFIL.EXE;1      
    Revision number:                      1
    Creation date:                        26-FEB-1986 16:29:03.06
    Revision date:                        26-FEB-1986 16:29:03.83
    Expiration date:                      <none specified>
    Backup date:                          26-FEB-1986 20:12:31.97

Map area
    Retrieval pointers			**********	  
        Count:         nn        LBN:   * nnnnnn *<== enter this as the LBN
					**********
Checksum:                                 38148