QUIC Font Editor









Michael N. LeVine
Naval Weapons Center
Code 3514
China Lake
Ca 93555
(619)939-3970
 avn 437-3970


MACINTOSH is the trademark of Apple Computer
MACSnVAX is the trademark of Eye Research Institute of Retina Foundation
QUIC is the trademark of QMS Inc
TALARIS is the trademark of Talaris Systems Inc
VAX is the trademark of Digital Equipment Corp



	The QUIC font editor is provided as a utility to allow the user of
TALARIS laser printers to generate their own fonts. It is provided as is.
While the author has attempted to get all the bugs and logical errors out,
no guarantee can be given that all the errors have been found. Any one using
this program does so at his own risk. Through out this document it is assumed
that the reader has access to and is familiar with "QUIC PROGRAMMING MANUAL 
VERSION 3.2" January 1987 Talaris Systems Inc.


			Setting up QUIC Font Editor

	The font editor is supplied in source form only. It requires the
following files:

QUIC.FOR	program source
CHARACTER.FOR	include file-font information
SCREEN.FOR	include file-screen management information

other files

QUIC.DOC	This document
*.dat		Sample font data files

	To build QUIC just issue the following commands:

$ FOR QUIC
$ LINK QUIC

add to the system login command file the symbol

$ QUIC :== $ddxxn:[dirloc]QUIC


The editor does not need to be installed in the system.
NO SPECIAL PRIVILEGES ARE REQUIRED.
The program does use up system resources-it is a CPU, memory and disk hog. The
account it is run under must have either unlimited CPU time or a minimum
of 1 hour before timeout. To keep it from thrashing itself to death, the
working set should be on the order of 3000 pages and the pagefile quota
at least 35000 (I had trouble at times with using up 25000 page file quota
an not being able to save the font data to a file. Font data files are on the
order of 5000-6000 blocks each so be sure the user has plenty disk space
available.
The editor is designed for a printer using 300dpi  resolution and
a maximum character bitmap of 300*300 dots (1 inch square). This can be
modified by editing the parameter statements in CHARACTER.FOR but any
increase in size drastically affects the data file size on disk, and the
program virtual memory size.





			Using the QUIC Font Editor 

	The placement of the font editor in the generation of a font:






	On a Macintosh				Off line
	
	1 Generate a font			1 On paper-design each
	2 Using Mac/Full Paint			  character of the font
	  make a paint document
	  all the font characters
	  in it
	3 Using MACSnVAX-upload
	  the paint document to
	  the VAX



				Using the editor

				1 Define and design font
				2 Save/update font data file
				3 Generate QUIC font definition
				  text file



				Download and use font

				1. Down load the font definition
				   file to the laser printer
				2. Use new font.



			Macintosh Font design and VAX download

	Using either MACPAINT or FULLPAINT utilities, the user generates
a paint document containing a picture of one or more of the characters in
the font. This can be done by either using the text option to type out 
the characters in an existing MACINTOSH font, or to draw the characters
with the utility.

				NOTE
	The Macintosh and the utilities MACPAINT/FULLPAINT
	operate at a pixel density of 72dpi while the Talaris 
	laser printers and the font editor operate at a pixel 
	density of 300dpi. This results in any character generated
	by the font editor will be only .24 of the size it had
	in the Paint document.


	The document is then loaded using MACTERMINAL/VERSATERM on
the MACINTOSH side and MACSnVAX (found on the Spring 86 VAX Sig tape)
on the VAX side using the procedures outlined in the MACSnVAX documentation.

	If the system uses another utility to up load files from a Mac,
the subroutine LOAD_MACPAINT_FILE is where the read and decode is done.
Only this routine needs to be rewritten for different formats. If you do
so, please forward this revision tome so I can pass it on to other users.



		Using the QUIC Font Editor

	The font editor is written using the screen management (SMG$)
service calls. It is an interactive menu driven program intended for use
only on such SMG$ supported devices as VT1xx,VT2xx,VT3xx, etc.

	When started, the editor has a short delay while all the internal
data structures are initialized. When this is completed, the main menu is
then presented:


			QUIC Font Editor

			    Main Menu

[1] Init all font data structures     
[2] Read font data file               
[3] Modify font parameters            
[4] Edit character                    
[5] Write font data file              
[6] Write font QUIC file              
[7] Exit                              
[8] Spawn subprocess/command          



		Main Menu Item 1-Init all font data structures

Inititalizes all internal font data structures. Done automatically when the
image is run. Prompts for Yes or No to see if you really mean it.

		Main Menu Item 2-Read font data file

If you are updating,adding to, or modifying a font you previously were
working on and had saved with option 5, you must first read it in with
this command before you can continue. If data from another font is still
in memory-the user is prompted to see if he or she wants to really
overwrite it with the data from the file. The user is prompted for the
name of the file containing the data.

		Main Menu Item 3-Modify font parameters

Before creating/modifying characters, certain basic font wide parameters 
must be set, as well as several optional font wide parameters. For more
information-see section below on font parameters menu.

		Main Menu Item 4-Edit character

Enter the sub menu to edit the characters in the font. See the section below
on character editing sub menu. User is notified if the minimum font wide
parameters have not been set and is not allowed to enter this sub menu until
they are defined.

		Main Menu Item 5-Write font data file

This is the compliment to item 2, write out the font and character data
currently in memory. If no font is active, the user is notified and no
output is generated. The user is prompted for the name of the name of the
data file to be generated.

		Main Menu Item 6-Write QUIC data  file

This is the command to generate the font definition file. If no  font is
active-the user is notified and not allowed to proceed. The user is
prompted for the name of the file to write, direction of font and
what family of laser printer is the target. For more information
see  "QUIC Programming Manual Version 3.2" chapter 7 under  section 7.7.2.9
(Character Descriptions). NOTE I have checked out the program output for
Talaris 800 and 1500 laser printers. for others I have made my best guess
for the P and L options, but I recommend checking out how how the X and Y end
up as portrait or landscape and use those.

		Main Menu Item 7-Exit

Done-exit the program. The user is prompted for a Yes or No to be sure that
he or she really means it.

		Main Menu Item 8-Spawn Subprocess/Command

Allows the user to spawn off a command or subprocess to do other work
(such as reading new mail) without exiting the editor. The user is
prompted for the command. If an empty line is entered then a subprocess
is created and upon LOGOUT returns to the editor. If a command is entered,
it is executed as a subprocess and upon completion, the user returns to the
main menu.


			Modifying Font Parameters

In this sub-menu, the user is setting required and optional font wide
parameters. These are further explained in the "QUIC Programming Manual
Version 3.2" chapter 7 under  section 7.7.2.8 Advanced Format Font Definition
Syntax Parameters. Part of the menu is shown below-absent from the example
below but displayed by the program is a diagram of the glyph and bitmap
including labels corresponding to the parameters that can be modified here.
On entry of the menu character-the value is prompted for. On entry the
value is checked and if in error-a message is written at the bottom of the
screen and the user must enter any character to continue.
The Z command returns the user to the main menu.

			Font Definition Menu

Font is (un)defined
Items A,B,C,&D required to define font
all others optional

[A] Font number (0-32767) = 0
[B] Font version (0-9) = 0
[C] Font name = '                    '
[D] Glyph height (1-999) = 0
[E] Baseline offset (1-999) = 0
[F] Line spacing (1-999) = 0
[G] Underline offset (1-255) = 0
[H] Dble underline offset (1-255) = 0
[I] Underline thickness (1-255) = 0
[J] Bold horizontal offset (1-255) = 0
[K] Bold vertical offset (1-255) = 0
[L] Superscript offset (1-255) = 0
[M] Subscript offset (1-255) = 
[Z] Exit


			Edit Character

This menu level and below is where you will be spending most of your
time in the editor. Various options are open as can be seen below:

		
				Character Edit
[A] List all active characters
[B] Select character to edit
[C] Set character defaults

[D] Convert font to proportional
[E] Convert font to non proportional
[F] Copy one character over another
[G] Copy character from another font

[L] Load Mac/Full-paint doc.
[Z] Exit


	Character Edit item A-List all active characters

Generates a list of all characters that have had the minimum required 
parameters defined and been entered via the B command. When the list 
is complete-the editor waits for the user to enter any character before 
returning to the Character Edit menu. All characters are displayed in 
the following format which is also used in the menu's below the B 
command, each character is displayed in the format xx-fl where xx is 
the hex value of the ascii-character (0-FF%x), f is an optional flag
and l is the equivalent ascii character or shifted ascii character if a 
flag is present. The flags are: ^ -> control character, ascii value is
ascii value of letter -'20'x ; # -> shifted control character ,ascii value
is ascii value of letter + '20'x ; * -> shifted character, ascii value is
ascii value of letter+40. The special case of the delete character is
handled as follows  '7F'x is replaced by 'dl' and 'FF'x is replaced by 'DL'.

	Character Edit item B-Character to edit

Prompts for the hex ascii value of the character to be edited. An
invalid input returns a message at the bottom of the screen and the
user must enter any character to continue. For more information on
the menus below the B  command- see below under Character to edit.

	Character Edit item C-Character Defaults

This enters a sub menu similar to the font definition menu, only here
you are setting the default parameters for all currently undefined
characters in the font. When the value is entered, it is checked to
see if it is in range, if not then a message is placed at the bottom
of the screen and the user must hit any character to continue, otherwise
the complete font data structure is scanned and the corresponding
value is loaded for each character that is still undefined. These
values are also used by the convert font to proportional and convert
font to nonproportional commands.

	Character Edit item D-Convert font to proportional

Scans all defined characters, empty characters (like space) are not
touched, all others are left shifted in their bit map until the left
most bit in the bitmap is in the left most column,the bitmap is reduced
in width until the right most bit of the pattern is in the right most
column of the bit map, the glyph is reduced in width to bitmap width +
2*default horizontal offset.

	Character Edit item E-Convert font to nonproportional

Scans all defined characters, if any are wider than the default bitmap
width, the user is notified and no action is taken. If key default
parameters are too small or not set-the user is notified and no action 
is taken. For all defined characters the glyph  width is widened to 
default bitmap width +  2*default horizontal offset, the bitmap width
is widened to the default bitmap width and each character is centered
in its bitmap.

	Character Edit item F-Copy one character over to another

Prompts the user twice, once for the source character value in hex
and again for the destination character in hex. If the source is not
defined, the user is notified and no action is taken. If the destination
character is defined, the user is notified and given the opportunity to
quit or continue.

	Character Edit item G-Copy character from another font

Prompts the user three times, the first time for the character ascii
value in the other font data file; second is for the ascii value of
the character in the current font to be loaded; finally the name of
the font file to load the character from. 

	Character Edit item L-Load MAC/FULL-PAINT document

Loads into an internal buffer a decoded bitmap of a MACPAINT or FULLPAINT
document uploaded from a MACINTOSH via MACSnVAX. The user is prompted for
the name of the paint document file. The decoded document remains in the
buffer until the program exits or a new document is loaded.

	Character Edit item Z-Exit

Returns to the top level menu.
	


	Character to edit menu-submenu to character edit menu command B

The character to edit command brings up the first of two screens. The first
screen is similar to the one used by the set character default parameters
and set font parameters  menu's. This menu allows the user to set or modify
the character unique parameters. For more information on these parameters,
see "QUIC Programming Manual Version 3.2" chapter 7 under  section 7.7.2.7
starting after "Separators". The additional commands are Y to drop down
to the actual bitmap edit screen and Z to return back up to the Character
Edit menu.

			Character Definition Menu

Character is (un)defined
Items A,B,& C required to define char.
all others optional

    Character is 00%X-^@

[A] Glyph Width (1-999) = 0
[B] Bitmap Height (1-300) = 0
[C] Bitmap Width (1-300) = 0
[D] Vertical offset (-999 to 999) = 0
[E] Horiz. Offset (-999 to 999) = 0

[W] Reset character undefined
[Y] Edit bitmap
[Z] Exit


		Edit Bitmap Menu

The actual editing of each characters bitmap is done at this menu level.
The menu looks as follows:

Character is 00-^@
Bit map height   1 dots, width   1 dots')
Cursor position- row   1 Col   1

[X] set bit at cursor
[O] clear bit at cursor

arrow keys   move cursor one bit
prefix to arrow keys
[S] move cursor one full screen
[H] move cursor one half screen
[P] shift pattern in bitmap by one bit
[E] shift pattern in bitmap to specified edge
[C] center pattern in bitmap in specified plane

[A] Align Mac/Full paint buffer and load

[Z] Exit


Not shown here but on the actual menu display on the right hand side of the
screen is a window on the bitmap-displaying a 20 by 20 window (the window
is square-it is the terminal that distorts it). The set bits are shown by
'X', clear bits are blanks,  and in the case where the bitmap is smaller
that the window in one dimension, the area outside of the bitmap is shown
as dots. The location of the cursor is in reverse video and the horizontal
line (if defined) of the baseline is shown just to the right of the window
by 'BL', the same applies to under line  (U1) and double underline (U2).

Movement of the cursor and bitmap revolves around the arrow keys. Hitting
any arrow key moves the cursor in that direction by one row or column, 
prefixing the arrow key by H or S makes that move by either 10 or 20
(half screen or full screen) rows or columns. The other prefixes cause the
pattern to move within the bitmap but the cursor stays in its current
location. The P prefix moves the entire pattern on bitmap one step in the
specified direction, all bits that fall off the end in that direction are
lost, and the new bits on the other end are all blanks (when cleaning up
a character loaded from a MAC/FULL-PAINT file this is a way to get rid of
bits rather than clearing each one in a row/column individually). The E
key causes the pattern to be moved so that the bit closest to the specified
edge is now at that edge of the bitmap. The C command causes the pattern
to be centered in the specified plane (left or right arrows specify the
horizontal plane and the up or down the vertical).


The A command or ALIGN command is used to load part of the previously
loaded MAC/FULL PAINT document into the character bitmap. The command
prompts the user for a row and column in the document. This is aligned
with the upper left hand corner (1,1) of the character bitmap and that
portion of the document in loaded into the bitmap.

The Z command returns the user back to the next higher level menu.


		Downloading and using the font

To down load the font, you need only spool it to the laser printer.
The QUIC file contains all the commands needed to delete any old
font definitions, and insert the new one.

To use the font, either put in the first line of the text file the 
QUIC command line shown below and spool it to the laser printer or
insert it into SYS$LIBRARY:TALDEVCTL.TLB use /SETUP=xxxx in the 
PRINT command where xxxx is the library name given that string.

^PY^-^IOo^IC0000^ILllll^ISnnnnn^IJ00500^IT00500^IBwwwww^O^PN^-

Before making the substitutions-read "QUIC Programming Manual Version 3.2" 
chapter 7 under  the specified sections:

Where
	Portrait	Landscape
o	P		L		section 5.15
wwwww	10500		07500		section 6.2.4



also

nnnnnn	Font number			section 7.6.1.1
llll	Lines per inch			section 7.5