The original title of this programs was HOGS, and it was begun by Bob Marshall. 
It has been heavily modified by Dale E. Coy, and renamed TOPC (for obvious
reasons).  The original documentation follows, and then a description of
the modifications and new features:

HOGS is a program that produces a display which is similar to the display
presented by MONITOR PROCESS/TOPCPU, except that it presents more information
about each process. MONITOR presents the process name and the PID, but this is
not real useful in most cases. HOGS presents the following information for the
top ten CPU users for the last sample interval : 

Username, PID, Cur prio./Base prio., Image name, Process State (i.e, COM, LEF,
etc.), Process Type (Batch, Interactive, Detached, etc), Total CPU minutes
since process creation, CPU % during interval) 

The display is updated every five seconds, until the user enters control-Y (the
sample interval is easily changed). Any broadcast messages the user receives
while running HOGS are trapped by the program and displayed upon exiting from
the program. All processes with the same username as that of the calling
process are displayed in bold characters (except for the current process). 

HOGS uses the Screen Management routines. It requires a terminal which is
capable of displaying 24 rows and 132 columns. 

HOGS must be installed with WORLD privilege, since SYS$GETJPI is used to obtain
information about all processes on the system. As supplied, HOGS requires VMS
4.4 or higher. If run under lower versions, then references to the SMG routine
SMG$SET_CURSOR_MODE must be removed. 

Installation instructions
-------------------------

   $ FOR HOGS           (If you modify the source file)
   $ LINK/NOTRACE HOGS  (If you modify the source file)

   $ INSTALL :== $INSTALL/COMMAND_MODE
   INSTALL> ADD disk:[directory]HOGS/OPEN/HEADER/SHARED/PRIV=WORLD
   $ HOGS :== RUN disk:[directory]HOGS

   (The INSTALL lines go in SYSTARTUP; the last line goes in the
    user's LOGIN.COM file or the system login file)


Written by : Bob Marshall
Lockheed Missiles and Space Co.
P.O. Box 3504, O/51-02/ B/586W
Sunnyvale, Calif. 94088
(408)756-5737


                      Modifications and Additions (TOPC)

DISPLAY:

Interactive processes now have the Username and 'I' highlighted.
Interactive processes over certain priority/CPU time thresholds are highlighted
	in various ways.  The thresholds are tailorable for your situation.
Some display enhancements were made: use of bars and lines instead of letters,
	display labeling, etc.

ENHANCEMENTS:

The broadcast message trapping has been expanded:  up to 65534 characters
or 1024 messages are trapped.  (tailorable).  The display, upon exit, was
enhanced, as was the notification of number of messages being held.

Exit from TOPC is by either pressing <ctrl>Y or the 'EXIT' (F10) key on
VT200/300 terminals. 

NEW FEATURES:

The display now updates only every 30 seconds, for reduced CPU load.  However,
pressing any key will immediately update the display.

Pressing <ctrl>W will refresh (repaint) the screen.

Pressing '$' or the 'DO' (F16) key will spawn a subprocess for executing
DCL commands.  In the subprocess, pressing Return (empty line) will return
to the TOPC display.  This feature is particularly useful for things like
STOP/ID=nnnnnn.

A BUILD_TOPC.COM is provided to properly compile and link TOPC, so that
it can be installed with WORLD privilege.