«FONTS» 5=Z05EMP,6=Z05EPP







THE RNO COMMAND LINE 

[B________________________________________________________________________________[a

FORMAT  RNO  file-spec[,...]  [qualifier...] 
[B________________________________________________________________________________[a

PARAMETERfile-spec[,...] 

                Specifies the names of one or more  files to be processed by RNO
                into one document.  The files contain text and RNO commands.  If
                you omit directory specifications  or device names,  the current
                defaults are used.  If no file type is given, [B.RNO[a is assumed.

                The document is created  as a file  having the same name  as the
                first or only input file.   The file  is created  in the current
                default directory.  The output file type is [B.DOC[a, unless the in-
                put file type is [B.RNT[a; then the output file type is [B.TOC[a.

                If no file-spec is supplied, it is prompted for.

[B________________________________________________________________________________[a

QUALIFIERS/CHAPTERS=(first[,last]) 
/APPENDICES=(first[,last]) 

                Causes only  the indicated range of chapters or appendices to be
                output.  The 'first' value must be specified.   If 'last' is not
                specified,  the last chapter  or appendix in the document is as-
                sumed.  The default is to print every chapter and appendix.  You
                cannot use both /CHAPTERS  and /APPENDICES in a single execution
                of RNO.

/CONTENTS[=file-spec] 
/TOC[=file-spec] 

                Causes RNO to create,  in addition to  the main output file,  an
                intermediate file  containing RNO commands  for creating a table
                of contents for the document.   The default is to produce no in-
                termediate file.   If a /CONTENTS or /TOC qualifier is specified
                with no file-spec, then the file  will be created with  the same
                name and location as the main output file,  except that the file
                type will be [B.RNT[a.  If an incomplete file-spec is used, the name
                of the main output file will provide defaults as needed  (except
                for the file type [B.RNT[a).  An example of creating a full document
                MYDOC.MEM with a table of contents is:

                        $ RNO MYDOC /CONTENTS 
                        $ RNO MYDOC.RNT 
                        $ COPY MYDOC.TOC,MYDOC.DOC MYDOC.MEM 


                                      [B 1 [a

                              [BTHE RNO COMMAND LINE[a



/CRLF 
/NOCRLF 

                Specifies the type of carriage control used in  the output file.
                If /CRLF is used (the default),  the output file is given "NONE"
                carriage control attributes,  and each line of the file contains
                an explicit carriage return and line feed.   These show up  when
                editing the output file, making it hard to read.

                IF /NOCRLF is specified,  the file is given "LIST" carriage con-
                trol attributes.   This makes the output  file easier to read in
                editors,  but can interfere with underlining,  escape sequences,
                half spacing, equations, or long output lines.

/DEBUG 
/NODEBUG 

                Causes all input lines to be copied to the SYS$OUTPUT file (nor-
                mally the terminal screen or the  batch log file).   This can be
                helpful in determining the exact conditions of an error.

/DOWN=n 

                Causes 'n' blank lines to precede any header information at  the
                top of every page.   The number of text lines on a page is unaf-
                fected by this qualifier;  using /DOWN=5 with /PS=55 will create
                60-line pages,  with the top five lines  always blank.   The RNO
                commands TOP MARGIN and PAGE SIZE (fourth parameter) can be used
                similarly, but they DO subtract from the number of text lines.

/EPRINT 
/NOEPRINT 

                If /NOEPRINT is specified (the default),  all error messages are
                displayed on SYS$OUTPUT.  If /EPRINT is specified, non-fatal er-
                ror messages are placed in the output file, and fatal error mes-
                sages are displayed on SYS$OUTPUT.

/EVEN 
/NOEVEN 

                If  /EVEN is specified  (the default),  even-numbered pages  are
                output; /NOEVEN causes all even-numbered pages to be suppressed.
                /NOEVEN  and  /NOODD are designed for printing  on both sides of
                the paper on a letter-quality printer;  the odd pages  are first
                printed with /NOEVEN, then the paper is turned over and the even
                pages are printed with /NOODD.  Extra margins for binding can be
                produced by using /RIGHT with /NOEVEN.







                                      [B 2 [a

                              [BTHE RNO COMMAND LINE[a



/FF 
/NOFF[=n] 

                If /FF is specified  (the default), an ASCII form-feed character
                is used at the end of each page.  For most printers, this causes
                an advance to the top of the next page.   No form-feed is placed
                at the beginning of the first page.

                /NOFF is used if the printer  does not recognize form-feeds,  or
                when  the output text  must be free  of form-feeds.   The end of
                each page is padded with blank lines to advance the paper to the
                beginning of the next page.   'N' is the paper length,  in lines
                (normally 66).  'N' must be less that 128.  If 'n' is omitted or
                0, then 66 is used.

/HYPHENATE 
/NOHYPHENATE 

                If /HYPHENATE  (the default)  is specified,  RNO  will hyphenate
                words to fill lines,  as specified with the RNO commands  ENABLE
                HYPHENATION and AUTOHYPHENATE.  If /NOHYPHENATE is specified, no
                hyphenation  (either automatic or manual)  will be done, and the
                RNO command ENABLE HYPHENATION will have no effect.

/LOG[=ALL] 
/NOLOG 

                If /LOG is specified,  RNO will display (on SYS$OUTPUT) the full
                name of each input, output, and table-of-contents file used.  In
                addition, /LOG=ALL causes the name of each referenced macro file
                and REQUIRE file to be displayed.  Note that in /2PASS mode each
                input and REQUIRE file will show up twice; a special log message
                is displayed to indicate the beginning of the second pass.

/MACROS=(file-spec[,...]) 
/NOMACROS 

                If /MACROS is specified, RNO will read the specified file(s) and
                process all macro definitions found.  All lines not within macro
                definitions are ignored.   RNO will also process macros on files
                defined in the search list logical name RNO$MACROS;  those files
                are checked before the /MACROS files.   If duplicate macro names
                are found,  the last occurrence found is used and  no diagnostic
                message is issued.  If /NOMACROS is specified, RNO will not pro-
                cess macros on RNO$MACROS files.

/ODD 
/NOODD 

                If /ODD is specified (the default),  odd-numbered pages are out-
                put; /NOODD causes all odd-numbered pages to be suppressed.  See
                /EVEN above for more information.



                                      [B 3 [a

                              [BTHE RNO COMMAND LINE[a



/OUTPUT=file-spec 

                Allows the specification of  an output file name  or destination
                directory different from  the default.   The default name is the
                name of the first  or only input file, with a file type of  [B.DOC[a
                unless the input file type is [B.RNT[a, for which the default output
                file type is [B.TOC[a.   By default,  the output file is created  in
                the current default directory.

/PAGES=(first[,last]) 

                Causes  only  the indicated  range of pages  to be output.   The
                'first' value must be specified.  If 'last' is omitted, the last
                page in the document  is assumed.  The default is to print every
                page.  If the document is chapter-oriented, then the /APPENDICES
                or /CHAPTERS qualifier should also be used.

/PASTHRU 
/NOPASTHRU 

                The /PASTHRU qualifier is not used unless the /OUTPUT  qualifier
                is used to send the output document  directly to a terminal  (as
                in /OUTPUT=SYS$OUTPUT);  in this case, /PASTHRU  is the default.
                It causes RNO to use PASTHRU  I/O mode to write the output file.
                See help on the VMS command  SET TERMINAL /PASTHRU  for informa-
                tion on PASTHRU mode.  If /NOPASTHRU is used, the output will be
                written to the terminal normally.  The .RNT file is not affected
                by this qualifier.

/PRINT 
/NOPRINT 

                If /PRINT is specified, the output file is sent to the SYS$PRINT
                output queue for printing,  and the file is deleted  after being
                printed  (this does not apply to the .RNT file).  The default is
                /NOPRINT.

/PS=(lines[,columns]) 

                Sets the initial output page size to the indicated values.  This
                initial setting is in effect until the first  PAGE SIZE  command
                is used.   The 'lines' value must be between 16 and 127, and the
                'columns' value must be between 16 and 255.   The default values
                are 58 lines by 60 columns.

/RIGHT=columns 

                Adds extra space to the left margin.  The space provided by this
                qualifier  is in addition to that provided by the  RNO  commands
                LEFT MARGIN and ENABLE BAR.





                                      [B 4 [a

                              [BTHE RNO COMMAND LINE[a



/UC 
/NOUC 

                When /UC is used, all output will be in upper case.  The default
                is /NOUC, which allows normal case conversion.

/UL=option 

                Controls the method of producing underlining on the output file.
                'Option' must be one of the characters [BB[a, [BL[a, [BN[a, or [BS[a.

                    [BB[a causes underlining via a spacing-backspace.  This is de-
                      signed for small personal printers such as LA50s.  It is
                      not recommended if sub/superscripts or unusual fonts are
                      used; ASCII character 137 (octal) must be an underscore.

                    [BL[a is the default.   Underlining is done via an overprinted
                      line containing underscore characters.  If /NOCR is used
                      the line will not be overprinted,  but will show up as a
                      separate line (i.e. similar to /UL=S, with underscores).

                    [BN[a causes underlining to be suppressed.  This overrides the
                      RNO command ENABLE UNDERLINING.

                    [BS[a causes underlining  to be simulated  with hyphens on the
                      next line.  This can be used on printers which can't use
                      the B or L options.   This option  may sometimes  add an
                      extra line to a page to accommodate underlines; to avoid
                      this, the RNO command "LAYOUT n,s" with s>0 can be used.
                      This reserves an extra line for possible underlines.

/VARIANT=(label[,...]) 
/NOVARIANT 

                Controls the processing  of conditional text.   Conditional text
                is bracketed with the RNO commands  IF, IF NOT, ELSE, ENDIF, IM-
                MEDIATE IF, and IMMEDIATE IF NOT, which reference 'labels'.  The
                bracketed text is processed or ignored  depending on whether the
                same labels were defined with the /VARIANT qualifier.   There is
                an equivalent RNO command, VARIANT.   The RNO command NO VARIANT
                undefines labels.  By default no labels are defined.

/VERSION 

                Causes RNO to display on the SYS$OUTPUT file its current version
                number and date, in the format:

                        NSWC RNO Rev n.nnn Created dd-mmm-yyyy hh:mm 

                If /VERSION is used, but no file-spec is supplied on the command
                line which invokes RNO, then it displays the version information
                and exits; no document is produced.  If a file-spec is supplied,
                RNO displays the version AND produces the document as specified.


                                      [B 5 [a

                              [BTHE RNO COMMAND LINE[a



/WAIT 
/NOWAIT 

                /WAIT causes RNO to pause and display a prompt  at the beginning
                of every page, so that paper can be manually fed or forms can be
                adjusted.   This must only be used when the output is being sent
                directly to a printer which you control (e.g. /OUTPUT=SYS$OUTPUT
                is used and you have a printer attached to your terminal).   The
                default is /NOWAIT.  The prompt message is:

                                Adjust page & press "return" 

/WRNMSG 
/NOWRNMSG 

                /NOWRNMSG  causes warning messages to be suppressed; the default
                is /WRNMSG.   Warning messages indicate  conditions in the input
                which may cause difficulties; no actual problem may occur.

/X9700 
/NOX9700 

                /X9700  enables features useful for producing documents on XEROX
                laser printers using the LASER utility; the default is /NOX9700.
                If /X9700 is used, the RNO commands DJDE and FONTS are made act-
                ive, escape sequences for changing fonts are defined, overstrik-
                ing is done in a LASER-compatible mode,  and the  VARIANT  label
                'X9700' is defined.

/2PASS 
/NO2PASS 

                /2PASS causes RNO to perform two passes on the input files.  The
                default is /NO2PASS.  There is a RNO command  .TWO PASSES  which
                is equivalent to /2PASS.

                Two-pass mode allows references to precede definitions for enti-
                ties created by the  RNO  commands  DEFINE SUBSTITUTION,  DEFINE
                ITEM, and DEFINE NUMBER.   Naturally, a document will take about
                twice as long  to create in two-pass mode.   Error messages come
                out differently in  two-pass  mode;  all messages about multiple
                substitute definitions appear in pass 1, and all other non-fatal
                messages appear in pass 2.   All fatal errors  appear only once,
                and may cause output to be missing.   TYPE commands are executed
                in pass 2 and bypassed in pass 1.










                                      [B 6 [a