Compand

		    File Compression/Expansion Utility





Michael N. LeVine
Code 3514
Naval Weapons Center
China Lake
Ca 93555
(619) 939-3970
 avn  437-3970


				Abstract

	Compand is a utility using the DEC supplied DCX$xxxx data compression
and expansion  subroutines. Compand will analyze the specified file and  then
generate  a  compressed  file  or will expand a compressed  file  back to  its
original  contents and  file characteristics. No  special  user  privileges are
required to use  this  utility. This  program  allows  the user  to keep those
large seldom used files on disk without taking up that much space.





				Building COMPAND

The Compand package consists of 3 files

COMPAND.DOC	this file
COMPAND.MAR	source file
COMPAND.CLD	DCL command definition file
COMPAND_ERR.MSG Error message file
COMPAND.COM	Command file to build COMPAND
it is built as follows

$ @COMPAND
$ COPY COMPAND.EXE  ddd:[ssss]COMPAND.EXE
$ COPY COMPAND.CLD  eee:[ffff]COMPAND.CLD

edit the file COMPAND.CLD and in each location where the image to be 
executed is specified


	IMAGE "dev:[dir string]COMPAND.EXE"

modify the device and directory string to match where the executable is
located. Then put into the system wide LOGIN.COM to include the line


$ SET COMMAND eee:[ffff]COMPAND.CLD




			Compressing a file

To compress a file use one of the three commands available as shown below

$ COMPAND/ACTION=COMPRESS[/LOG][/OUTPUT=outfile[.ext]]   file 
or
$ COMPRESS[/LOG][/OUTPUT=outfile[.ext]]   file 
or
$ SQUEEZE[/LOG][/OUTPUT=outfile[.ext]]   file 

all the above mean the same. The commands SQUEEZE and COMPRESS translate
to COMPAND/ACTION=COMPRESS. In its minimal form, the command will be

$ COMPRESS xxx.ext

the file xxx.ext will be analyzed, and then compressed into a new file
by the name xxx.CMP. This file contains the following information:
	1. Data from the file header to allow recreation of the original
	file with all the same file characteristics.
	2. Any file ACL's
	3. Original file name
	4. Compression map
	5. Compressed data (each compressed record corresponds to one
	disk block in the original file.

by default the name of the output file is the same as that of the input
file only with the extension of .CMP  .

The switches available to the user are

/OUTPUT=output_file_name

this switch overrides the default name of the output file as outlined above
but any fields not specified will revert to the default.

/LOG

causes the utility to output what phase it is in during compression or
decompression and when done - the relative sizes of the compressed and
expanded files.

				NOTE
	Upon completion, both the compressed and expanded  files
	are residing on disk. When you are sure the translation
	is correct, delete the original file.

				NOTE
	The compressed file can in turn be itself compressed and
	depending on the redundency in the map, can possibly gain
	more file size reduction. To get back to the original contents
	require the same number of decompression operations as there
	were compression operations performed.


			Decompressing a file

To decompress a file use one of the three commands available as shown below

$ COMPAND/ACTION=DECOMPRESS[/LOG][/OUTPUT=outfile[.ext]]   file 
or
$ DECOMPRESS[/LOG][/OUTPUT=outfile[.ext]]   file 
or
$ EXPAND[/LOG][/OUTPUT=outfile[.ext]]   file 

all the above mean the same. The commands EXPAND and DECOMPRESS translate
to COMPAND/ACTION=DECOMPRESS. In its minimal form, the command will be

$ COMPRESS xxx

The file xxx.CMP will be decompressed and the resulting file will have
the same name as the file that was used to generate the compressed file.


The switches available to the user are

/OUTPUT=output_file_name

this switch overrides the default name of the output file as outlined above
but any fields not specified will revert to the default which is the 
original file name.

/LOG

causes the utility to output what phase it is in during compression or
decompression and when done - the relative sizes of the compressed and
expanded files.

				NOTE
	Upon completion, both the compressed and expanded  files
	are residing on disk. When you are sure the translation
	is correct, delete the original file.


			Error messages

	Any RMS, DCX or system service errors that occur  will  cause
COMPAND to  stop and  exit  with  that error. Internal  error messages
are as follows (all messages proceeded by "%COMPAND-"):

W-DATCHKSUM,Checksum of expanded data does not match that of original data

	COMPAND calculates and stores in the compressed file overhead data
	area the checksum of the original  data. During  expansion, it  is
	calculated again on the expanded data. If the two checksums do not
	match, this message is output. The resulting expanded data  is  not
	deleted but the user should carefully check the resulting  expanded
	file for accuracy.

I-LARGEFILE,Compressed file larger than original data file

	The compressed data file produced by COMPAND contains an overhead
	block containing data to  recreate the  original  file, checksums,
	original file name, compression map, etc. If the uncompressed data
	file contains little redundant information  or is  small to  start
	with, the compressed data file can be larger than the original
	compressed form. If this occurs, this message will be displayed.

F-MAPCHKSUM,Checksum of data compression map does not match

	During the compression analysis phase of generating a compressed
	file, a compression map is generated  for the  compression  phase.
	This map is required for the decompression of the file so the map
	is stored  in the  compressed file.  To ensure data  integrity, a
	checksum  is calculated and stored in the overhead area. When the 
	map is read back in, the checksum is recalculated and the  values
	are compared. If they  do  not  match, COMPAND  exits  with  this
	message.

F-OVERCHKSUM,Checksum of COMPAND overhead data does not match

	When the compressed file is generated, an overhead block is
	written first which contains data to  recreate the  original
	file, checksums, original file name, etc. The last  word  of
	the overhead block contains its checksum. During the expansion
	phase, the block is read in and the checksum is recalculated
	and if the checksums do not match, COMPAND exits with this message