Directions for SETUP_LAT_DEVICES.COM

SETUP_LAT_DEVICES.COM is used to manage LAT-based printer queues and ports. 
It uses a definition file which contains a DEFINE/END structure for each 
queue or port to be defined.  The definition file is specified by the logical 
name LAT_PRINTERS.  If not defined the file SYS$MANAGER:LAT_PRINTERS.DEF is 
used.

SETUP_LAT_DEVICES.COM performs the following functions to fully setup the 
queue:

	- Determines an available LTA device by starting with LTA9999 and 
scanning down until it locates a free device.  If the command file's first
parameter is specified as STARTUP, the scan for a free device is skipped.  
Instead, the first queue uses LTA9999, the second LTA9998, etc.  This 
option is intended for use at system startup.

	- The port is then created using LATCP.  The system logical 
QUEUE$queue-name is defined to be the LTAnnnn: device name.  This is 
useful for users who can only specify the spooled device rather than the
actual queue.  In addition, the users are assured that the logical will 
always be defined properly, rather than depending on a given LTA always 
using the same queue.

	- The port is properly setup based upon the entry in the queue 
definition file.

	- The queue is defined based upon the entry in the queue defintion 
file.  The queue is defined as /ON=QUEUE$queuename so that LTA 
independence is maintained.

The full syntax of a queue definition follows:

DEFINE	QUEUE queue-name
	ALIAS = alternate queue-name
	DECSERVER = DECserver-name
	PORT = DECserver port-name
	TYPE = printer-type
	DESCRIPTION = description of queue
	DEVICE = intermediate spooling device
	FORM = default form
	OWNER = [UIC]
	ACE = Access control entry
		·
		·
		·
	PROTECTION = S,O,G,W protection code
	OPTIONS = any qualifiers for INIT/QUEUE which are not already specified
	DISPLAY = any text to display
END

A description of each verb follows:


DEFINE QUEUE queue-name

	Signifies the start of a queue definition.


ALIAS = alternate queue-name

	Specifies an alternate name for the queue.  This is useful in 
instances where the queue name is being changed.  The old name would be 
defined as an ALIAS name for a period of time.  This allows a smooth 
migration to the new queue name.  See example below.


DECSERVER = DECserver-name

	Specifies the DECserver name where the printer to be serviced is 
attached.  This statement must be specified for each queue.


PORT = DECserver port-name

	Specifies the DECserver port where the printer to be serviced is 
attached.  If a number is specified, PORT_ is prepended to form PORT_n.  
Note that the DECserver port must be setup separately.


TYPE = printer-type

	Specifies the type of printer.  The following names are currently 
recognized:
		HPLJ	HP Laserjet printer
		HPPLT	HP Plotter
		LA50	DEC LA50 printer
		LA120	DEC LA120 printer
		LG02	DEC LG02 printer (can also be used for LG01)
		LQP02	DEC LQP02 printer
		LQP03	DEC LQP03 printer
		LN03	DEC LN03 printer
		LP11	Any "plain" printer (no special formatting)


DESCRIPTION = description of queue

	Specifies a textual description to be displayed when a SHOW QUEUE
command is used to display the queue.  Note that this only applies to VMS 
V5 systems.


DEVICE = intermediate spooling device

	Specifies the disk device to which data to be printed is temporarily 
stored when data is directed to the port name rather than the queue.  Note, 
if quotas are enabled, users must have sufficient quota on the disk.


FORM = default form

	Specifies the default form associated with the queue.


OWNER = [UIC]

	Specifies the owner of the queue.  The brackets ( [ and ] ) are 
optional.


ACE = Access control entry

	Specifies and access control entry associated with the queue.  
Multiple ACE statements can be contained within the queue's definition.  
Note that this only applies to VMS V5 systems.


PROTECTION = S,O,G,W protection code

	Specifies the standard VMS protection to be applied to the queue.


OPTIONS = any qualifiers for INIT/QUEUE which are not already specified

	This statement can contain any special purpose qualifiers to be 
appended to the INITIALIZE/QUEUE command when the queue is created.  This 
is intended to handle all other qualifiers that are not supported elsewhere.


DISPLAY = any text to display

	Causes the text given to be displayed at the terminal when the
definition is being processed.


END

	Specifies the end of the queue's definition.  This statement is 
required.

¹ Signifies a required keyword


The full syntax of a port definition follows:


DEFINE	LATPORT	port-name ¹
	DECSERVER = DECserver-name ¹
	PORT = DECserver port-name ¹ ²
	SERVICE = service-name ¹ ²
	TYPE = printer-type
	OWNER = [UIC]
	ACE = Access control entry
		·
		·
		·
	PROTECTION = S,O,G,W protection code
	OPTIONS = any qualifiers for SET DEVICE which are not already specified
	DISPLAY = any text to display
END


¹ Signifies a required keyword
² One of PORT or SERVICE must be specified for a LATPORT defintion