Compressing Virtual Readonly Disk

by 
Glenn C. Everhart

The compressing virtual disk package consists of three images when run:

1. A program that compresses an entire disk onto two files (on another
disk somewhere) which contain the compressed data and some pointers to
allow random access decompression...usual space savings is around 50%.

2. A virtual disk driver that becomes the new disk driver that will have
the data from the original disk that was compressed, and

3. A privileged image which hooks onto the driver and talks with it,
and reads the two files with compressed data (over DECnet if the filespec
has a node:: in it) and delivers decompressed data to the driver as
read operations demand it.

This is useful where you have archival data on disks and want to keep
it online for read access, but want to take up less disk blocks to do
it. The present system allows you to do so by:

1. running the CMPDSK program to compress a disk somewhere onto a
couple files

2. connecting a unit of the driver (DTdriver)

3. running a detached process and passing it the device unit name and
the filename of the compressed data files (they are always file and
file_idx, so you pass the first only).  The DTHOST_START.COM procedure
automates this step to facilitate use.

4. Mount the DTAn: disk /nowrite and point any logicals pointing at the
original disk at it instead.

5. Reuse the original disk space for something else.

(Note that the program can also allow you to mount a backup/physical
tape as a disk, so you can use back/physical to do backups, yet still
recover individual files or collections from the savesets. Backup/physical
(or hsc backup>) runs faster than normal or /image backup by a factor
of usually around 2.)


Build:

On vax, use build.com to build the images and copy *.exe to sys$system.
Also copy dthstimg.cld to sys$system.


On alpha (note: this is for vms 7.0 and later...small mods for 6.2 and
 earlier might be needed in the driver):

$macro/migr/obj=dthstimg.obj dthstimg_s264
$macro/migr qlzw
$fort/nocheck grabrecord
$fort/nocheck getgeo
$fort/nocheck cmpdsk
$macro/migr dtdriver_S264
$@dtdriver.lnk
$link/native/sysexe=select dthstimg+qlzw+getgeo+grabrecord
$link/native cmpdsk+qlzw

Now copy *.exe and dthstimg.cld to sys$system.


You may in either case copy dthost_start.com to sys$system too.

dthstimg.doc has more info.

The DTAn: disks are connected via


$ sysman io connect dta0:/noada/driver=sys$system:dtdriver
$ sysman io connect dta1:/noada/driver=dtdriver
$ sysman io connect dta2:/noada/driver=dtdriver

On vax, up to 4 units are permitted; on alpha, up to 20. New
drivers can be loaded for more, just change the name
"dtdriver" in dptab to "dtbdriver" or "dtcdriver" or so on
and use names DTB0: to DTB3: for dtbdriver, and so on. Source
is provided so this is easy.

The DT devices should be mscp serveable. However, it is also
possible to make the files accessible remotely and have people
run this code on their workstations, accessing the disks
information over decnet via FAL. Since the files are opened
readonly, sharing is perfectly OK.