## Slide 1: Firewall Forensics
Deciphering firewall logs in order to figure out what is going on

## Slide 2: Firewall forensics FAQ
Latest FAQ at: http://www.robertgraham.com/pubs/firewall-seen.html
These slides at: http://www.robertgraham.com/slides/first2k
These slides are just a guided presentation of the FAQ
Notes: These slides are just a graphical representation of the contents in the firewall-seen.html FAQ

## Slide 3: What you will get out of this
Understand ~70% of the entries you see in your firewall reject logs
Techniques for figuring out the other 30%
An understanding of what hackers are up to

## Slide 4: Agenda
8:30am – 12:30 am
Context around firewalls
  OSI model, sniffers, packet headers, IDS
Port guide
  The meat.
Packet Zen
  Beyond the real meaning of these fields.
Q&A
Notes: Most of the time will be spent on figuring out the meanings of these ports

## Slide 5: [CONTEXT]
Packet switching
OSI Model
Headers
Raw packets from sniffers

## Slide 6: Packetization…
Communication is broken down into packets. A firewall log entry represents a single packet.
It looks to us as a smooth communication
On the wire, it is a stream of packets
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111

## Slide 7: …Packetization
What this means
  We only get a small glimpse into the big picture
  We have to act as detectives reconstructing the crime from a limited number of clues
  We won’t always be right

## Slide 8: How firewalls work
Packets that pass rules are allowed in, packets that don’t match the rules are rejected. We generally are interested in looking at the reject rules.

## Slide 9: OSI 7-Layer Model
Application
Transport
Network
Physical
Data Link
Presentation
Session
Moves data between machines
Moves data between applications
Moves data to the next hop
Moves data to the wire
Formats the data
Notes: Quick recap of the OSI model

## Slide 10: OSI 7-Layer Model
Application
Transport
Network
Physical
Data Link
Presentation
Session
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
Src = 10.10.0.9 Dst = 209.31.36.212 Proto = 17 (TCP) IP Length = 78 ID = 1109 Frag/flags = 0 TTL = 111
Adapter = eth1
Src port = 137 (nbt) Dst port = 137 (nbt) Flags = 0

## Slide 11: Sniffer packet capture
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
00 00 D0 B7 58 92 A1 00 40 05 A4 79 32 08 00 45 00 ...X...@..y2..E.
10 00 4E 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F .N.U....6D......
20 24 D4 00 89 00 89 00 3A EF B5 D0 72 00 00 00 01 $......:...r....
30 00 00 00 00 00 00 20 43 4B 41 41 41 41 41 41 41 .......CKAAAAAAA
40 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 AAAAAAAAAAAAAAAA
50 41 41 41 41 41 41 41 00 00 21 00 01 AAAAAAA..!..
Offset
ASCII
Hexadecimal dump 2-hex-digits == 1-byte

## Slide 12: Sniffer #2: Just hex
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
00 D0 B7 58 92 A1 00 40 05 A4 79 32 08 00 45 00
00 4E 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F
24 D4 00 89 00 89 00 3A EF B5 D0 72 00 00 00 01
00 00 00 00 00 00 20 43 4B 41 41 41 41 41 41 41
41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41
41 41 41 41 41 41 41 00 00 21 00 01

## Slide 13: Sniffer #3: OSI breakdown
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
00 D0 B7 58 92 A1 Ethernet 00 40 05 A4 79 32 08 00
45 00 00 4E IP header 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F 24 D4
00 89 00 89 UDP header 00 3A EF B5
D0 72 00 00 00 01 00 00 00 00 00 00 20 43 4B 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 00 00 21 00 01

## Slide 14: Sniffer #4: IP breakdown
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |Version| IHL |Type of Service| Total Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Identification |Flags| Fragment Offset | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Time to Live | Protocol | Header Checksum | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Source Address | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Destination Address | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
45 00 00 4E 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F 24 D4

## Slide 15: OSI Network Layer: IP
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |Version| IHL |Type of Service| Total Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Identification |Flags| Fragment Offset | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Time to Live | Protocol | Header Checksum | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Source Address | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Destination Address | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Options | Padding | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
RFC 792

## Slide 16: OSI Network Layer: ICMP
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Type | Code | Checksum | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
RFC 791
More data follows, depending upon type and code.
For example, a ping (type=8) will contain a data field of opaque data.

## Slide 17: OSI Transport Layer: TCP
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Source Port | Destination Port | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Sequence Number | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Acknowledgment Number | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Data | |U|A|P|R|S|F| | | Offset| Reserved |R|C|S|S|Y|I| Window | | | |G|K|H|T|N|N| | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Checksum | Urgent Pointer | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Options | Padding | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
RFC 793

## Slide 18: OSI Transport Layer: UDP
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Source Port | Destination Port | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Length | Checksum | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 19: IDS vs. Firewall
Firewall
  What passes the rules
  Based on ports and IP addresses
IDS
  Suspicious looking packets regardless of rules
  Based on patterns all throughout the packet and state
  Anomalies are normal, so IDS is noisier, especially outside a firewall

## Slide 20: Q&A
Questions from me:
  What types of firewalls do you use (ipchains, Checkpoint, etc.)
  Who uses sniffers?
  Who uses IDS?
  Any other techniques (e.g. honeypots)?

## Slide 21: Q&A
Questions?

## Slide 22: §1.1 Destination Ports
The most important indicator of what’s going on

## Slide 23: Resources
Official ftp://ftp.isi.edu/in-notes/iana/assignments/port-numbers
  Official list inaccurate more often than not.
Comprehensive http://advice.networkice.com/advice/Exploits/Ports/
  Has a lot of info on what ports are being used in the real world, often with hyperlinks to relevant text.

## Slide 24: Port 7 Smurf/Fraggle
h4x0r
host
host
host
host
Internet
ping 192.0.2.255
Or UDP port 7
Or other UDP ports
Spoof victim
Router uses MAC address FF:FF:FF:FF:FF:FF for IP address 192.0.2.255
Subnet = 192.0.2.xxx
victim

## Slide 25: Port 21 FTP
Warez storage
  Will test for read/write directories
Bounce
Buffer overflows
--compress attack
Banner check
  220 rh5.robertgraham.com FTP server (Version wu-2.4.2-academ[BETA-15](1) Sat Nov 1 03:08:32 EST 1997) ready.

## Slide 26: Port 23 Telnet
Mapping Network
  Cisco routers, APC UPSs, Ascend dial-ups, Solaris servers, Ethernet switches, etc.
Looking for crackable accounts
  Red Hat Linux release 5.0 (Hurricane) Kernel 2.0.31 on an i486 login:

## Slide 27: Ports 67,68 BOOTP,DHCP
www
cable-modem home users
On DSL, cable-modems, users share a single virtual Ethernet where broadcasts are seen.

## Slide 28: Port 111/135 portmapper
portmap
nfs
mountd
cmsd
ttydb
111
2049
635
32801
32807
h4x0r
Where is cmsd?
It’s at port 32801
Exploit!!!
Hacker is looking for a specific service to exploit, or dump all mappings to find any service that might be exploitable.

## Slide 29: Port 113 identd/auth
POP IMAP SMTP
user
user
user
user
Internet
Client contacts e-mail server on port 110,143,25. In order to log the connection, the e-mail server connects back to port 113. Usually allows access regardless if this succeeds, but it slows down e-mail transfer if blocked by firewall.

## Slide 30: Port 139 NetBIOS
Website
WinNT
|
log connection
|
resolve IP w/DNS
|
resolve IP w/NetBIOS
user
user
user
user
Internet
DNS

## Slide 31: Ports 109, 110, 143
POP and IMAP
Text based protocol
Logon with username/password
Buffer overflows in many, many servers.

## Slide 32: Port 139 (cont.)
§10 key points
  You don’t have to be running windows yourself
  Come from
    Client utilities that auto-resolve (ping, tracert)
    WinNT web servers (e.g. IIS)
    Logfile analyzers (e.g. WebTrends)
    Personal firewalls (e.g. BlackICE Defender)
  Usual appear due to failure of DNS

## Slide 33: Port 1080 SOCKS
h4x0r
IRC wars Online games Trojan scans
cable-modem home users
socks 1080
victim
yahoo.com
Attack on IRC server tunneled within SOCKS on the way to the bounce machine, who then creates the real IRC connection to server
socks(IRC)
IRC
6667
SOCKS user continues to surf net unaware that this is going on

## Slide 34: Port 3128 squid
h4x0r
yahoo.com
user
user
user
user
http://yahoo.com/index.html
/index.html
Hacker wants to forward all his requests through your proxy
scans attacks anonymity

## Slide 35: Port 1524 ingreslock
One of many typical ports on UNIX
Hacker breaks into machine, then creates a “root shell” listening at a port, then connects to the port.
May compromise the machine on a public port like 110/POP, the attempt to connect on this port.

## Slide 36: Port 6970 RealAudio
server
host
host
host
host
Client goes to server (url = pnm://server/foo.rm) Server creates a real-time stream of UDP packets
Outgoing TCP
Return UDP stream

## Slide 37: Port 5632 pcANYWHERE
h4x0r
pcANYWHERE scan
cable-modem home users
Home users unintentionally scan their neighbors
Hackers scan people intentionally

## Slide 38: Port 13223 PowWow
Dial-up users
B
A
PowWow Users

## Slide 39: Port 13223 (cont.)
Dial-up users
B
A
PowWow Users
User A hangs up, releases address
User B dials up, and is assigned A’s old address
PowWow users try to reconnect to A, thereby flooding B with connections

## Slide 40: Port 33460 traceroute
h4x0r
..11
..12
..13
..10
traceroute 192.0.2.11
Firewall sees:
Weird TTLs
ICMP TTL exceeded
UDP ports around 33460

## Slide 41: Q&A
Questions?
Are there ports that people have seen on their firewall that you would like discussed?

## Slide 42: §1.2 Source ports
Usually, ports are random and are meaningless.
Sometimes, the pattern can indicate the source of the attack.
Sometimes useful.

## Slide 43: Port 20 FTP
server
host
host
host
host
FTP client programs open a port for the server to connect to, then tell the server this port using the “PORT” command.
>PORT 192,0,2,73,4,1
Connection to client in order to send the requested file

## Slide 44: Port 20 (cont.)
server
host
host
host
host
Web browsers use PASV mode instead, which passes through firewalls. Some FTP clients cannot support PASV mode, such as Windows FTP command-line program.
>PASV
With PASV, server tells client another port to connect to

## Slide 45: Port 53 DNS
host
host
host
host
Stateless packet filters allow any packet with source address of 53 in order to allow for DNS.
ACCEPT src=53 to receive DNS replies
h4x0r
Sends all packet w/ src=53
DNS

## Slide 46: Port 61000 IP Masquerade
server
host
host
host
host
Hosts are assigned “private” addresses, the NAT changes the source address to be that of the NAT; also changes source ports to above 61000.
192.168.x.x 10.x.x.x
63.98.231.129

## Slide 47: §1.4 Windows Trojans
30% chance that a port probe you’ve never seen before is from somebody scanning for a Windows remote admin trojan like Back Orifice.
Infection
  Post trojan to IRC/usenet/chatrooms/mass-emails
  Scan net for infected users

## Slide 48: Sub7: Get PC Info
Notes: Finds out the full information of the machine, from computer name to platform to key to monitor resolution etc.

## Slide 49: Sub7: Keylogger/Redirector
Notes: Imagine if the user is working on encrypted files on the file server. Logging the keystrokes still gets the user all the information, though it may not be formatted well.
The hacker can forward attacks through the system into the corporation, including reconnaissance like port scanning or direct attacks.The redirector allows a compromised desktop to attack other systems

## Slide 50: Sub7: Find Files
Notes: User can find and read any file, including those on mapped (shared) drives.

## Slide 51: Sub7: Read Passwords
Web-site cached passwords
Dialup logins
Domain logins
Windows login
Share passwords
Can sniff network passwords
Notes: Dialup logins including VPN passwords.

## Slide 52: Sub7: Tracking Mobile Machines
Can contact hacker every time user logs in; Allows hacker to find mobile notebooks
Notes: Provides a number of ways to install into the system and can “morph” in order to avoid scanners (it can be recompiled to avoid detection by anti-virus apps) and allows for random port start. Also send email notification every time compromised desktop starts up.

## Slide 53: Sub7: Other Features
Full screen capture
Full control over mouse and keyboard to insert attacks
  (i.e. when user steps away from desk).
Upload further programs to system and run them

## Slide 54: Conclusion
We estimate that there are at least 10,000 hackers who play with these trojans

## Slide 55: §1.13 Trapping the hacker
For deciphering persistent scans
  Run a sniffer to capture the packets
  Use netcat to accept the TCP connection
  Use NAT to shunt to honeypot server

## Slide 56: Q&A
Have people found trojans in their networks?

## Slide 57: §2 ICMP
ICMP is not a transport protocol
  But trojans/rootkits can carry data
  You can’t break in directly with ICMP
ICMP is control-messages
  So hackers can reset some configuration
  Effective DoS
Some firewalls map type/code to src/dst ports
  Just saves on log format; they aren’t related.

## Slide 58: Type 0 Echo Reply
host
host
host
host
Firewalls often accept ping replies
h4x0r
Sends ping reply with command in data field
victim
Host compromised with DDoS tools like Trin00/TFN
Victim is flooded from this and other DDoS machines

## Slide 59: Type 3 Destination Unreachable
Contains copy of the original packet that went in the opposite direction
  Firewalls don’t log it; so you should probably use a sniffer if you see these on an ongoing basis and need to figure out what they mean.

## Slide 60: Type 3 code 3 Port Unreachable
Decoy UDP scans
Stale DNS
Multi-response DNS
NetBIOS/Windows activity
Traceroute when it reaches the end

## Slide 61: Type 3 code 4 Frag error
Part of path MTU discovery
  Fragmentation better handled at TCP layer
  Sets DF on all packet
  If routers must fragment, informs TCP to lower its packet size
  Many internal links have small packet sizes
The one ICMP you need to allow through

## Slide 62: Type 8 PING
Ping requests
  Quite normal, but…
  Ping sweeps heavily used to map the network
Payload often important
  Use sniffer or IDS to track it

## Slide 63: §3.1 Source Routing
client
..11
..12
..13
..10
Client specifies route the packet should take by listing the routers along the way

## Slide 64: §3.1 Source Routing
h4x0r
10.1.2.3
63.23.45.67
10.1.2.1
63.23.45.68
Normally, 10.x.x.x is not reachable from Internet
Send to 10.1.2.3 through 63.23.45.68
Intermediate routers do not know how to route to 10.x.x.x, but they do know how to get to 63.x.x.x

## Slide 65: §3.x Address
255.255.255.255 broadcast
169.254.x.x are Windows failed DHCP
127.x.x.x are “localhost”, should never appear on the wire
192.0.2.x are for “examples”
0.0.0.0 sometimes comes from hackers

## Slide 66: §3.x Address
10.x.x.x, 192.168.x.x.x, 172.16.x.x-172.31.x.x are “local”: internet routers refuse to route them
  Should never see this as a destination coming in from the Internet, unless you are on a VLAN like DSL or cable-modem
  You will sometimes see these as source addresses when doing a traceroute

## Slide 67: §3.x Address
24.x.x.x is from a cable modem
209.x.x.x, 63.x.x.x, 216.x.x.x are newer CIDR allocations
  You will see a lot from these ranges just for normal activity

## Slide 68: §3.9 Decoy scans
host
host
host
host
h4x0r
Spoofs own address to hide among many other addresses
victim
You see replies back from victim back to many of your machines
Victim sees requests from all over net and replies to them

## Slide 69: §5.2 Strobe/scan/nmap
h4x0r
host
host
host
host
Internet
sscan 192.0.2.232
Looks for some well known ports only:
1 22 23 25 53 79 110 111 143 1114 2766 6000 31337

## Slide 70: Q&A
Questions?

## Slide 71: HTTP logon summary

## Slide 72: Reading Hex
Human numbers are usually base-10
  0123456789
Hex is base-16
  01234567890abcdef
A 4-bit number has 16-combination
An 8-bit byte has two 4-bit numbers

## Slide 73: Hex2
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 ...
0 1 2 3 4 5 6 7 8 9 a b c d e f 10 11 12 ...
My mother calculates her age in hex.
55 = 48 (I.e. 3*16) + 7
Ergo 37 (hex) years old

## Slide 74: Hex3
00 00 D0 B7 58 92 A1 00 40 05 A4 79 32 08 00 45 00 ...X...@..y2..E.
10 00 4E 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F .N.U....6D......
20 24 D4 00 89 00 89 00 3A EF B5 D0 72 00 00 00 01 $......:...r....
30 00 00 00 00 00 00 20 43 4B 41 41 41 41 41 41 41 .......CKAAAAAAA
40 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 AAAAAAAAAAAAAAAA
50 41 41 41 41 41 41 41 00 00 21 00 01 AAAAAAA..!..
Some are pretty easy to read. Above, the 4 bytes 0a 0a 00 09 you can read as 10.10.0.9 (it’s the location of the IP addres)

## Slide 75: Endian
Humans read from right to left
  123 is hundred-twenty-three, not three-hundred-one (321)
Computers can read numbers in either direction
  One a byte-by-byte basis

## Slide 76: Hex4
00 00 D0 B7 58 92 A1 00 40 05 A4 79 32 08 00 45 00 ...X...@..y2..E.
10 00 4E 04 55 00 00 80 11 36 44 0A 0A 00 09 D1 1F .N.U....6D......
20 24 D4 00 89 00 89 00 3A EF B5 D0 72 00 00 00 01 $......:...r....
30 00 00 00 00 00 00 20 43 4B 41 41 41 41 41 41 41 .......CKAAAAAAA
40 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 41 AAAAAAAAAAAAAAAA
50 41 41 41 41 41 41 41 00 00 21 00 01 AAAAAAA..!..
04 55 = 4*256 + 5*16 + 5 = 1109
04 55 = 5*4096 + 5*256 + 0*16 + 4 = 21674

## Slide 77: IP ID fields
Jul 23 18:10:09 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1109 F=0x0000 T=111
Jul 23 18:10:13 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1365 F=0x0000 T=111
Jul 23 18:10:23 gandalf kernel: Packet log: input DENY eth1 PROTO=17 10.10.0.9:137 209.31.36.212:137 L=78 S=0x00 I=1621 F=0x0000 T=111
Notice that the numbers increase by 256 each time
The hex sequence is:
04 55
05 55
06 55
This indicates the packets were sent by a Windows machine, which bytes swaps many fields.

## Slide 78: TTL fields
The TTL field is decremented by 1 by each router (occasionally by more on slow links)
Machines start with 255, 128, or 64. Thus, a TL of 110 indicates the packet came from 18 hops away.
Likewise, bizarre TTLs indicate possible spoofing.

## Slide 79: Q&A
Questions?

## Slide 80: [FIN]

## Slide 81: Other ports
If time, go back and discuss ones that were skipped over.
25 SMTP
  Spammes hunting for you, missing MX
98 Linuxconf
443/500 SSL/Ipsec
119 NNTP
  @Home scans their customers

## Slide 82: Other ports
SNMP
  Like pcANYWHERE, heavily scanned for by hackers but also done inadvertently
177/513 xdmcp/rwho
  Standard UNIX broadcasts