## Slide 1: CampusWide: Overview and Exploits
Acidus
(Acidus@resnet.gatech.edu)
www.yak.net/acidus/
Interz0ne Conference 9/27/2002

## Slide 2: Presentation Overview
Transaction systems 101
  What they are
  History
System Specs
  Overview
  Server (AP/NP/Database)
  Infrastructure
  Cards
  Readers

## Slide 3: Overview Continued
Simple Transaction
Exploits
  Reader to Device Exploits
  Reader to Server Exploits
  Card Based Exploits
Securing an existing system
  Photos of GT Worthless Security
  How to really protect the system

## Slide 4: Transaction Systems 101- What they are
“One Card solutions”
  Debt Card (Bookstore, food court)
  Meal Plan
  Library (Copy Machines, checking out books)
  Building Access (Computer Labs, Offices, Labs)
  Access to Sporting Events
Important! - Not just a debit card, it is the key to the whole school network

## Slide 5: Transaction Systems 101 - History
Special Teams (1984)
Icollege (Envision)
AT&T (CampusWide)
Currently: BlackBoard Transaction System (Unix and NT)
Technology basically remains unchanged since 1984.

## Slide 6: System Specs - Overview
Simple System
  Central Server with a database
  Network interface
  Hub spaced Network of data lines
  Daisy-chained Readers

## Slide 7: Server
Applications Processor (AP)
  Holds Database dbvista or Oracle
Network Processor (NP)
  Interface to all incoming data (RS-485, Ethernet, modem)
  Convert to commands the AP can understand

## Slide 8: Server - Specs
HP9000, but any RISC processor will do
Battery back-up
4 gig Tape drive for backups
Normally Isolated from rest of network

## Slide 9: Server - Interfacing
Originally only from console, or 19,200 serial lines
There are third party GUI’s to the database
These change from school to school. No standard
GT uses ?”Osiris”? For Door Entry

## Slide 10: Infrastructure
Uses RS-485
  Doesn’t have protocol defined in standard
  Used to control devices on factory assembly lines
  Robust, has 2 data lines; uses difference between the 2
  Short dist: 10 Mbit, Nearly a mile: 9600 baud. Repeaters extend range

## Slide 11: Infrastructure continued
IP Converters
  Developed by Blackboard
  Use existing Ethernet, ATT said this was bad idea (Any duplex network can work)
  Hooks 16 devices to a box (Pentium w/ NIC), which encrypts, sends out TCP/IP
  Keys can be updated remotely
  Encryption unknown. High end: DES, Low end: XOR, key around 8 bytes

## Slide 12: Infrastructure Continued still
Merchant Dial-ups
  Blackboard also created these
  Low Cost, monthly fee
  Before expensive lines needed to be run
  Basically just a modem in a box
  Lets you talk directly to the NP!

## Slide 13: The Card
Contains your standard ABA Track II.
The card simply holds an account number which appears on the card
These are printed on site using Polaroid card printers, just like at the DMV

## Slide 14: The Card - GT Buzzcard Center

## Slide 15: The Card - GT Buzzcard Center

## Slide 16: The Card - GT Buzzcard Center

## Slide 17: The Card - GT Buzzcard Center

## Slide 18: Readers
3 types
  Self-Vending readers (The bulk of them)
  Door entry readers
  Point of Sale (POS)

## Slide 19: Readers - Overview
Small, Black with either the ATT or Blackboard Logo
Made of metal or plastic
All data out of a reader is in RS-485, so it is backward compatible
Transmits at 9600 baud
I/O: 2x16 LCD with 16 key keyboard and activation LED's

## Slide 20: Readers - Overview continued
Can store offline transactions in NVRAM
Code is in boot ROM and Flashable RAM
Boot very quickly, normally under 15 seconds

## Slide 21: Readers - Self Vending
Most common reader and most varied
Laundry, Vending, Copy machines
Easiest to hack because they are isolated
All work basically the same. Talk to NP, confirm or deny transaction, then send signals to device.
Can tell if Offline

## Slide 22: Readers - Self Vending

## Slide 23: Readers - Door Entry
Small and tricky
Can’t tell they are offline
Can hold a local database of 4000-16000 card numbers in NVRAM
Uses this if it can’t reach NP
Works just like vending, when confirmation received from NP, tell the magnetic door lock to release

## Slide 24: Readers - Door Entry

## Slide 25: Readers - POS
Most complex and large
Rare compared to others
Access will normally be restricted since they are almost always manned

## Slide 26: Readers- Value Transfer Station
The “Holy Grail”

## Slide 27: Readers - Value Transfer Station
Lets you deposit money on card
Feed in all of your dollar bills, then it sends the signal
Also allow temp cards (very bad)

## Slide 28: A Simple Transaction
Want to buy a load of wash
Select washer on laundry reader then swipe card
Reader takes account number off card and sends along with reader ID to the NP through RS-485 lines
IP Converter may be in between reader and NP, but it doesn’t know and doesn’t care.

## Slide 29: A Simple Transaction Continued
NP receives signal (be it IP or RS-485) and converts it to a query for the AP.
AP looks in account, deducts $1, sends back a confirmation and new balance to NP
NP sends this info back to reader
Reader displays new balance

## Slide 30: A Simple Transaction Continued
Reader talks to device. This is device specific. The Device has no idea it is attached to a network.
For Laundry, Reader sends coin pulses to board in washer where coin validation normally attaches
Laundry machine thinks 4 quarters dropped in and gives you a load of wash

## Slide 31: Exploits - Overview
System is relatively secure provided that the data lines are protected
But, dial-up could be hacked or phone number social engineered out of stupid pizza boy.
IP Converter releases packets into the wild. Careful analysis of traffic could show their IP addresses.

## Slide 32: Exploits - Reader to Device
Device is stupid, doesn’t know its on a network, so reader must simulate what that device is used for (in this case, quarter pulses)
To compromise, simply access lines from reader to device, and then simulate quarter pulses yourself
No way for machine to know the difference

## Slide 33: Exploits - Reader to Device
Pros
  Very low risk: By their nature these are isolated
  Very easy to hack: Most devices attached to these are coin based.
  Communication is always 1 way from reader to device so there’s no complex handshaking to spoof

## Slide 34: Exploits - Reader to Device
Cons
  Many be difficult/impossible to get at date lines between reader and device (ex: coke reader is mounted inside coke machine)
  Leaves physical evidence in the way of stripped wire, etc

## Slide 35: Exploits - Reader to Server
Readers are stupid and can be fooled Ex:
  Attach laptop to back to coke machine, grab all raw data after swiping card
  Plug laptop to wall, send data to NP, record all that comes back
  Attach laptop to coke machine, play NP’s response, get a coke
  Replay NP’s response, get another coke

## Slide 36: Exploits - Reader to Server
RS-485 doesn’t define standard, but who cares? Signal may be encrypted, but again, who cares?
If you get the raw data, that doesn’t matter
VTS comes in here. It doesn’t send the “x $ was deposited onto y account” until you tell it to

## Slide 37: Exploits - Reader to Server
The Buzzcard Director confirmed that this can be done
Would require analysis of packet, but, by depositing known $ on known account, it could easily be done

## Slide 38: Exploits - Reader to Server
Pros
  Very low risk: By their nature these are isolated
  RS-485 to RS-232 adapters relatively cheap ($50-$100)
  No physical evidence: Most readers contain plugs into RS-485 networks, so no cut wires
  Faster than Reader to Device spoofing
  Only way to spoof coke machines

## Slide 39: Exploits - Reader to Server
Cons
  Though confirmed, have not personally tested.
  Reader could be smart, and wonder why it got a reply from server when none was sent. (Note: Even this is easily remedied. Swipe card, have you laptop ignore all data it receives from the reader, wait a second, and then send confirm)

## Slide 40: Exploits - Reader to Server
Cons continued
  Data dumps from NP to reader would most likely only work on that reader, since packet most likely contains reader ID
IP Converter Spoofing
  IP address could be found by monitoring buildings.

## Slide 41: Exploits - Reader to Server
IP Converter Spoofing continued
  Data in normal packets as well as swiping the multiple machines (up to 16) that the converter is on would allow the IP Packet Structure to be deciphered
  Packets could then be sent from anywhere, making machines vend.
  Tell all coke machines in library to all spit out a coke!

## Slide 42: Exploits - Card based
Cards are ABA Standard, normal card capture tool will capture them
Card contains basically just a number, which can be cloned
This number could also be obtained by building a monitoring device on a RS-485 line, and let it harvest
Clone card would work everywhere normal card would

## Slide 43: Security - GT Style!
If Data lines from server to reader and from reader to device are so important, they must be really protected right?
...
Well, not at Georgia Tech! Metal conduit protecting lines commonly stops at hanging ceiling

## Slide 44: Security - MW/MHWMENC
Panels containing equipment normally held on by flat head screws

## Slide 45: Security - MW/MHWMENC
What’s inside
  Repeaters to boost Signals
  Multiplexes to talk to all the Laundry machines

## Slide 46: Security - Laundry Machines
Coils protecting data lines, attached with flat head screws

## Slide 47: Security - Door Readers
Lines for the door readers held on by flat head screws

## Slide 48: Security - Coke Machines
RS485 totally unprotected

## Slide 49: Security - Coke Machines
With Convenient plugs no less!

## Slide 50: Security - Coke Machines
Which plugs into a hub inside that box, which has no lock

## Slide 51: Security - Copy Machine
They didn’t even try with this one!
And the reader is attached to the shelf with… That’s Right! FLAT HEAD SCREWS!

## Slide 52: Security - VTS

## Slide 53: Security - VTS
A Close up of the letters

## Slide 54: Security - Really securing the system
Secure the data lines.
Get rid of IP Converters
For god sakes, you take $9000 from me a year, buy some god damn Torx Screws!

## Slide 55: QUESTIONS?

## Slide 56: Closing
Check www.yak.net/acidus
For much more technical info:
See me for copies of slides or the 2600 Article
Tell your school about how insecure the system is
Make them change it