RIMDOC.DOC
                                                    Page 1

                                                       
                                                       


                                                  DEFINITIONS
ATTRIBUTE:      An attribute is a 1-8 character alphanumeric name
                used to identify a specific column of a relation.
DOMAIN:         A domain is the set of values which are permissible
                in a column of a two-dimensional table of data
                (relation).
KEY:            An attribute may be specified to be "KEY".  This
                specification will cause RIM to build an index for
                the attribute.  Under certain conditions, this
                index will greatly improve the system efficiency
                for queries and updates.
RELATION:       A relation is a two-dimensional table of data.  The
                column headings are the attributes of the relation
                and the rows are the data occurences (tuples).
ROW:            A row is the set of values in a row of a two-
                dimensional table (relation).  A row is sometimes
                referred to as a tuple.
SCHEMA:         The schema is the definition of the relations and
                their attributes that comprise the data base.  The
                relation passwords and constraint rules also are
                part of the schema.





























                                                    Page 2


                                                       
                                                       


                                                    SUMMARY
This document is the user's guide (VAX/VMS) for the Relational
Information Management System, Version 5 (RIM-5).  The information
presented consists of instructions for using RIM-5 as a standalone
system and for using RIM-5 in conjunction with an application
program.
Section 1.0 presents the method of implementation and access for
RIM-5, a discussion of the files used by RIM-5, and the general
syntax of the RIM-5 command language.
Section 2.0 presents instructions for the use of RIM-5 as a
standalone system in both menu and command modes.  In the menu
mode, you are prompted for the inputs required to create, update,
and/or query the data base.  The command mode, as an alternative,
requires the direct input of RIM-5 commands to create, update,
and/or query the data base.  A discussion of all the available
RIM-5 command is presented in this section.
Section 3.0 presents the instructions for the application program
interface.  Any programming language that can call FORTRAN
subroutines can be used.
The appendices present a summary of the RIM-5 commands, a summary
of the application program interface, a sample RIM FORTRAN
program, a list of the current limitations, and a discussion of
the LXLREC free field input routine.



























                                                    Page 3


                                                       
                                                       


                                                 1.0  OVERVIEW
The Relational Information Management (RIM) System was originally
developed as a prototype data base management system by Dennis L.
Comfort and Wayne J. Erickson at The Boeing  Company under NASA
Contract NAS1-14700 (IPAD).  Mr. Erickson at the University of
Washington, and Frederick P. Gray at The Boeing Company made en-
hancements to the system which culminated in RIM Version 4 (RIM-
4) . RIM-5, which is the version of RIM described in this
document, was developed by Mr. Erickson for NASA and Mr. Gray and
Geofferey Von Limbach for Boeing.  RIM is based upon the relational
algebra model for data management and has been used for both en-
gineering and business data.  The system is available as a stand-
alone system and through an application program interface.  The
standalone system may be executed in two modes: menu or command.
The menu mode prompts the user for the input required to create,
update, and/or query the data base.  The command mode requires the
direct input of RIM commands.
RIM-5 includes several enhancements relative to RIM-4, including:
     .   highly portable FORTAN code
     .   additional scientific attribute types for vectors and
         matrices
     .   variable length attributes
     .   improved sort option
     .   improved where clause
     .   an initial set of report writing commands
     .   introduction of tolerance for floating point numbers
     .   additional schema modification commands
     .   enhanced FORTAN interface
     .   RIM-to-RIM communications file
To the interactive/batch user the RIM-5 creation, update, and
query are, for the most part, identical to RIM-4.  Data bases form
RIM-4 must be reloaded for RIM-5, however.  In addition, the ap-
plication program interface has been expanded and modified to ac-
comodate increased capabilities.
















                                                    Page 4


                                                       
                                                       


1.1  IMPLEMENTATION AND ACCESS
RIM is written entirely in FORTRAN 77.  It requires approximately
300000 (decimal) bytes of virtual memory when run as a standalone
program.
Access to RIM depends on the execution method desired.  To execute
the standalone system, the following control statement is needed:
     RUN  [rimact ]RIM
where rimact is the name of the user directory on which RIMABS and
the RIM HELP data base files reside.
To use the RIM application program interface you need to link
RIMLIB to your application program.  This can be done with the
following instruction:
     LINK JOBA,[rimact]RIMLIB/LIB
where rimact is the name of the user directory on which RIMLIB
resides.  JOBA is the name of the object file of your application
program.
1.2 DATA BASE FILES
Each data base consists of three RIM-generated files whose logical
names are formed by suffixing the data base name with a 1,2, and
3.  The first file contains directory data, the second file con-
tains the actual data for each relation, and the third file con-
tains key element pointers.  The default type for these files are
"DAT".  RIM uses logical files FOR005 and FOR006 for input and
output.
If your data base files do not reside on your directory with names
equal to the logical data base files names, you must use the as-
sign control statements prior to the RIM execution to assign
required names to your data base files.  You may also assign your
input and outout files to files other than FOR005 and FOR006  if
desired. (INPUT and OUTPUT commands.)
1.3 GENERAL COMMAND SYNTAX
RIM is used by entering commands, (which start with keywords) in
response to input prompts (which vary according to the submodule
in use).  Three of the commands (DEFINE, HELP, and LOAD), are used
to enter submodules which have their own sets of commands for
defining and loading a data base.  In describing commands, the
following conventions are used:
     relname












                                                    Page 5


                                                       
                                                       


         or                     name of a relation(s)
      relname1,relname2,...
      attname
         or                     name of an attribute(s)
      attname1,attname2,...
      value
         or                     actual values(s)
      value1,value2,...         (value may be a text string,
                                scalar, vector, or matrix)
All relation and attribute names must contain at least 1 and no
more than 8 alphanumeric characters.
Many of the commands in RIM have optional parts.  These optional
parts are enclosed in square brackets.
      [THIS IS OPTIONAL]
Some keywords in the commands are selected from a list of accep-
table keywords.  These keywords are in a vertical list with the
first choice enclosed in braces.
      {CHOOSE}
       ONE
       OF
       THESE
RIM command keywords may be abbreviated.  At least the first
3 characters in the keywords are required.
The following are equivalent:
        1)   SELECT, SELEC, SEL
        2)   INTERSECT, INTER, INT
        3)   DELETE DUPLICATES, DEL DUPLICATES, DEL DUP
All commands in RIM are entered in a free-field format with blanks
and commas as separators.  the following contains a short descrip-
tion of RIM conventions and data generation facilities.  An exten-
sive description, intended for the experienced RIM user, can be
found in Appendix E.
Keywords and data values are separated by blanks or commas.  If a
command is too long for one 80 character line, it may be continued
on succeeding lines by entering "+" as the last character of the
preceding line.  RIM remembers each previous command.  This en-
ables you to re-use all or part of the previous command.  This is
done by using an asterisk to indicate which items of the previous
command are to be re-used.  A single asterisk means re-use the
corresponding  single item of the previous record.  An asterisk
followed by a number n means re-use the next n corresponding
items.  Two asterisks mean re-use all remaining corresponding
items.
The following are all equivalent:
        1)  THIS IS A COMMAND
        2)  THIS +
            IS +
            A +


                                                    Page 6


                                                       
                                                       


            COMMAND
        3)  * IS,A COMMAND
        4)  THIS *2 COMMAND
        5)  THIS **
Multiple commands may be entered on one line separated by a semi-
colon or $.
        THIS IS THE FIRST ; THIS IS THE SECOND $ THIS IS THE THIRD
Comments may be placed anywhere within a command by enclosing the
comment between the characters *( and ).
        *(THIS IS A COMMENT)  THIS IS NOT
When numeric data is to be interpreted as text (alphanumeric)
data, the numerals must be enclosed by quotation marks.
        "1234"
When entering text strings which contain embedded blanks or
commas, the entire string must be enclosed by quotation marks.
        "THIS IS A TEXT STRING"
When entering a text string that contains an item enclosed by
quotation marks, double quotation marks are used.
  "THERE IS A ""QUOTE"" IN THIS STRING"
A text string may require continuation on one or more lines.  The
+ sign continuation can then be used within the quotation marks.
It is not recommended that you use leading blanks in text strings.
Text which does not have embedded blanks or commas does not
require quotes.
Integer data is input as a string of digits without a decimal
point.  A sign may precede the digits.
        123, -63, +56, 0























                                                    Page 7


                                                       
                                                       


Real or floating point numbers must include a decimal point or E
for the exponent.  If a decimal point is not present, the E must
be preceded by an integer.
        1.3, .005, 0., 6.E-1, 6E-1, 0.60, -23.45
The size of real numbers is limited to the range between 1.0E-38
and 1.0E+38.












































                                                    Page 8


                                                       
                                                       


                                              2.0  RIM EXECUTION
Execution of RIM as a standalone program can be effective in two
modes, command mode or menu mode.  The command mode is used when
RIM is executed in the batch environment or for interactive users
who wish to bypass the menu dialogue.  A detailed description of
the commands are given in section 2.1.  The menu mode offers as-
sistance to inexperienced users.  An overview of this mode is
discussed in section 2.2 and a more detailed description of the
menu mode dialogue is given in section 2.3.  The interactive user
may switch freely between menu mode and command mode.
When executing RIM interactively, the first output to your display
will be:
     BEGIN RIM ---- VAX VERSION 5.0  UDXX      YY/MM/DD  HH.MM.SS
     RIM COMMAND MODE
     ENTER "MENU" FOR MENU MODE
UDXX identifies the update level of RIM.  The date and time stamp
indicate current date and time.  At the start of execution you
are in the command mode but you may switch immediately to the menu
mode as indicated. Note that Amiga or Unix or MSDOS versions of RIM
will identify themselves as such, rather than as the VAX version.

     As extensions to basic RIM5, RIM commands may be entered in either
case now. Translation to upper case ends when a " character is
seen to allow literal data to be entered, and translation is only
done for console input. Also, where possible the construct

} command

spawns the command to the host OS. On VMS a LIB$SPAWN call is used
so that effectively all VMS commands are available from within
RIM (permitting long sessions to be broken for interruptions as
needed and returned to without loss of context).


















                                                    Page 9


                                                       
                                                       


2.1  RIM COMMANDS
This section presents a summary of the RIM commands.  You are
restricted from using certain commands based on the knowledge of
assigned passwords.  If no passwords are assigned to the relations
by the data base owner, there are no command restrictions (the
DEFINE submodule excepted).  See figure 2.1-1.
2.1.1  General Commands
                                          DEFINING a Data Base Schema

     The DEFINE submodule (prompt D>) commands are used to define
the structure of the data base and are used in the sequence described
below. The definition of the data base is called the schema. The schema name
corresponds to the name of the data base and is used to form the names
of the files used in the database. Attributes, relations, passwords, and
rules (constraints) are defined using this submodule. To access this
submodule enter:

DEFINE dbname

You must identify the name of the database whose definition you are going to
create or expand by specifying "dbname", the 1-6 character alphanumeric
schema name. This name is used to form the name of the files used to
store the data base. The dbname, when augmented by a single number must
be a legal filename. Once dbname is specified you must identify the owner
password of the data base.

OWNER password

The "password" entered must be a 1-8 character alphanumeric name. When used
in the USER command, this password represents a master password to the
data base. It will override any individual relation passwords. If the
data base already exists and you want to define additional attributes or
relations, "password" is checked against the existing owner password.

     Following the entering of the schema name and owner password, the attributes,
relations, and relation passwords and rules are defined.

     To define attributes enter:

ATTRIBUTES
attname type1 [{length}] [KEY]
                 VAR
attname type2 [{row, col}] [KEY]
                row, VAR
                VAR, VAR
              .
              .
              .


                                                   Page 10


                                                       
                                                       



The attribute definitions are ended when you specify one of the DEFINE
submodule keywords RELATIONS, PASSWORDS, or RULES.

TYPE1 Attributes:

     RIM supports seven "type1" data types: real (floating point), integer,
text, double precision, real vectors, integer vectors and double precision
vectors. You must enter REAL, INT, TEXT, DOUB, RVEC, IVEC, or DVEC
for type1. The default length is one value except for TEXT where it is 8
characters. The length is specified in terms of the number of values and
characters respectively. VAR indicates variable length. The optional KEY
specification causes an index file to be built for this attribute. This 
file is used by RIM to quickly find qualifying rows for retrievals and
updates. If KEY is not specified (nonkey attribute) the index file is not
built. You should consider the cost of building and storing the KEY
attribute pointers on teh index file versus the benefits you will obtain
when deciding if a KEY declaration should be used. No specific rules are
given here; experience should be used as a guide. An attribute can
be changed from KEY to non-KEY and vice-versa by using the BUILD KEY
and DELETE KEY commands described in section 2.1.9. For large
data bases (more than 1000 rows), experience has shown that it is
most efficient not to specify a KEY in the DEFINE submodule
but rather to load the data without keys and then build the index
files using the BUILD KEY command. The greater the number of keys,
the more efficient this method is.

     TYPE2 Attributes

     RIM supports three "type2" data types: real matrices, integer matrices
or double precision matrices. You must enter RMAT,IMAT, or DMAT for
type2. The matrices can be of fixed size, have variable column
dimensions or variable row and column dimensions. You enter the row
dimension first, followed by the column dimension. The default dimension
is 1 by 1. The keyword KEY has the same meaning as for "type1" attributes.

     To define relations enter:

RELATIONS
relname WITH attname1 [attname2 ...]
     ...

     The relation dedfinitions are ended by specifying one of the
DEFINE submodule keywords ATTRIBUTES, PASSWORDS, RULES, or END.

     The attributes must be listed in the order in which they are
to appear in the relation. No attributes can be used which have
not been previously defined, either in the current attributes


                                                   Page 11


                                                       
                                                       


definition subsection or in a previous definition of this data
base. Attributes which are defined but not included in a relation
will not become part of the RIM schema.

     A RIM data base must have attributes and relations defined, but
passwords and constraint rules are optional. If read or modify
passwords are desired enter:

PASSWORDS
{READ PASSWORD}  FOR relname IS password
 RPW

{MODIFY PASSWORD} FOR relname IS password
 MPW


The password definitions are ended by specifying one of the DEFINE
submodule keywords ATTRIBUTES, RELATIONS, RULES, or END.

     A password can be any string of 1-8 alphanumeric characters. When
you are doing queries, loads, or modifications, the current password
is specified by the USER command. If this password does not match
the read, modify, or owner password for a given relation, you
cannot query that relation. If this password does not match the modify
or owner password, you cannot load or modify the relation.

     Constraint rules are another optional section of the DEFINE submodule.
If rules are specified, they are used during the loading process and
during CHANGE commands to screen out rows which do not meet the
constraint rules. Rules may be defined for REAL, INT, and DOUB
attributes of length 1 and for fixed length TEXT attributes. At most
10 rules may be specified for a single relation.

     Tol define constraint rules enter:


RULES
  attname [IN relname] {EQ} value [{AND} attname ...]
                        NE          OR
                        GT
                        GE
                        LT
                        LE


    or




                                                   Page 12


                                                       
                                                       


  attname1 IN relname {EQA} attname2 IN relname [{AND} ...]
                       NEA                        OR
                       GTA
                       GEA
                       LTA
                       LEA


where EQ, NE, GT, GE, LT, ands LE mean equals, not equal to, greater than,
greater than or equal to, less than, or less than or equal to respectively.
EQA, NEA, etc. mean equals attribute, not equals attribute, and so on.

     The rule definitions are ended by specifying one of the DEFINE
submodule keywords ATTRIBUTES, RELATIONS, PASSWORDS, or END.

     Atributes referenced in the rule definitions must have been previously 
defined. By specifying rules, you can restrict an attribute to a range
of values or require that the value of an attribute in one relation
have a specific relationship to the values of an attribute in the
same or a different relation. The comparison operators ending in A
are used when the comparison is to an existing attribute rather than
to a constant. A rule expression may have at most 9 boolean operators.
The method used for constraint checking is that the value of the first
attribute mentioned in the rule is obtained from the input (LOAD or
CHANGE command) and checked against the value specified or against
the existing data base value of the second attribute.

     To complete schema definition and leave the DEFINE submodule you enter
END.

     HELP Command
The HELP command allows you to obtain: a description of the
available RIM commands, a discussion of the general command
syntax, a summary of all available commands, and general news
about the RIM system. HELP is available at any time during
execution except when in the menu mode.
To receive help when in the command mode enter:
HELP [{command name}]
        RIM
        SYNTAX
        WHERE
        SUMMARY
        NEWS
        SORT
        INPUT FORMAT





                                                   Page 13


                                                       
                                                       


                                              CURRENT PASSWORD
SECTION NUMBER     COMMAND
                                            OWNER  MODIFY  READ   NONE
 . 2.4.1        . GENERAL                     X       X      X     X
 . 2.4.2        . DEFINE                      X
 . 2.4.3        . LOAD                        X       X
 . 2.4.4        . DATA BASE QUERY             X       X      X
 . 2.4.5        . SCHEMA QUERY                X       X 2    X 2
 . 2.4.6        . COMPUTATION                 X       X      X
 . 2.4.7        . DATA BASE MODIFICATION      X       X
 . 2.4.8        . SCHEMA MODIFICATION         X       X 1
 . 2.4.9        . RELATIONAL ALGEBRA          X       X
 . 2.4.10       . REPORT GENERATION           X       X      X
 . 2.4.11       . COMMUNICATION               X       X
                    1 EXCEPT CHANGE OWNER        2 EXCEPT PRINT RULES



































                                                   Page 14


                                                       
                                                       


The HELP submodule available inside the HELP submodule are identical to
the HELP commands except that the keyword HELP is omitted.  The
HELP submodule displays information one screen at a time.  After
each screen you will have the option to continue displaying the
text by entering * or to return to the HELP submodule by entering QUIT.
You will remain in the submodule until you enter an END command which
will return to the command mode.
MENU Command
The MENU command places you in the menu mode.  It may be entered
at any point when in command mode except when in the DEFINE, HELP,
or LOAD submodules.  The menu mode is particularly useful for
schema definition and data loading.
        MENU





































                                                   Page 15


                                                       
                                                       


OPEN Command
The OPEN command is required whenever an existing data base is to
be used.  You specify the name of the data base.  RIM uses the
name of the data base to form the names of the three files which
contain the data base.  The data base files must either reside
in your dictionary or you must make a logical file assignment prior
to RIM execution.
OPEN dbname
Only one RIM data base may be open at a time (if you don't close
the present data base before opening a new one, RIM will auto-
matically close the present data base.)  The OPEN command must be
issued before any commands that require data from the data base
can be processed.
CLOSE Command
The CLOSE command permits you to close a RIM data base without
leaving RIM.  This enables you to close one data base, then
open or define a different one, all within one RIM session.
This command is not needed if only one RIM data base is acces-
sed during a RIM session.  This command results in update of
the data base files to reflect all changes you have made to
the data base.
        CLOSE
Note: the current data base will be closed for you when you
leave RIM by issuing an EXIT command.
USER Command
This command is used to specify your user password to RIM.
Your user password is used to check against read and modify
passwords specified for the relations.  Each time this com-
mand is issued, the new password replaces the current user
password.  The default password is the word NONE.
        USER password
INPUT Command
This command is used to specify the name of a file which
contains the RIM commands and/or input data.  Alternate
input file names may be assigned as often as required.
The use of this command allows you to define command pro-
cedures on a file and then have RIM execute the set of
commands without user interaction.
        INPUT filename











                                                   Page 16


                                                       
                                                       


The last command on the alternate input file should be INPUT
INPUT which returns input to the batch input file or your
terminal.  INPUT TERMINAL will, for interactive jobs, do the
same thing.
OUTPUT Command
This command is used to specify the name of the output file.
Specifying a file other than OUTPUT will result in the output
from the RIM commands being placed on the specified file name.
The output file name may be changed as often as desired.  The
use of this command allows the interactive user to get an
offline hardcopy output from RIM.
        OUTPUT filename
OUTPUT OUTPUT will return the output to the batch output file
or your terminal.  OUTPUT TERMINAL will, for interactive
jobs, do the same thing.
ECHO Command
This command is used to control the printing of your input
commands on the output file.  Default is for ECHO printing
enter:
        ECHO
NOECHO Command
The NOECHO command turns off ECHO printing.
        NOECHO
TOLERANCE Command
For attributes which contain floating point numbers, a tolerance
may be used to qualify equality, nonequality and order.  The tol-
erance applies to any real or double precision number you use in a
WHERE clause.  If A is an attribute with value a, and r is a user
specified number used in a WHERE clause, and t a tolerance (posi-
tive, zero, negative), the following are true conditions:
        A EQ r if and only if r-t <= a <= r+t
        A NE r if and only if a < r-t or a > r+t
        A GT r if and only if a > r-t
        A GE r if and only if a => r-t
        A LT r if and only if a < r+t















                                                   Page 17


                                                       
                                                       


        A LE r if and only if a <= r+t
If t is a percentage tolerance, t is to be replaced with t x r/100
in the above expressions to define true conditions for percentage
tolerances.
        TOLERANCE tol [PERCENT]
where tol is the tolerance and the presence or absence of the
keyword PERCENT indicates whether tol is a percentage tolerance
or an absolute tolerance.  The TOLERANCE command can be used
as many times as desired to reset the tolerance.  A tolerance
stays in effect for a session until a new tolerance is speci-
fied.  The default value for tolerance is 0. .
NOCHECK Command
Rule checking applies to the CHANGE and LOAD commands. Default
is that rules, if defined, are enforced.  The NOCHECK command
suppresses the ruler checking.
        NOCHECK
CHECK command
The CHECK command turns on rule checking.  The CHECK and NOCHECK
commands may be issued as many times as required anywhere in
the input stream.
        CHECK
EXIT Command
To leave RIM without dropping your current data base enter:
        {EXIT}
         QUIT           
This command closes your current data base.  Data needed by your data
bases is copied from the incore working areas to the logical files
whose names were determined by the OPEN command or by the data base
name designated in the DEFINE submodule.
RELOAD Command
The RELOAD command is used whenever you want to rebuild the data
files of your data base to recover unused space created by row
deletions, relation removals, and certain attribute changes.
When a row is deleted or a relation removed, its space is not reused
until you issue this command.  In addition, if a variable length















                                                   Page 18


                                                       
                                                       


attribute is modified so that it increases in length, the row is
deleted and replaced with a new one.  the old row becomes unused
space.  If your data base has any KEY attributes, then the access
pointer files maintained for those attributes are also rebuilt.
The syntax for the command is:
        RELOAD
2.1.2  Define Submodule Commands
Define Submodule Commands
The Define submodule (prompt = D> ) commands  are used to define the
structure of the data base and are used in the sequence described
below.  The definition of the data base is called the schema.  The
schema name is the name of the data base and forms the essential part
of the names of the files used for the data base.
Attributes, relations, passwords, and constraints (rules) are defined
using this submodule.  The naming conventions for schema definition
are described in section 2.3.3.  To access this submodule enter:
        DEFINE dbname
You must identify the name of the data base whose definition you are
going to create or expand by specifying the schema name.  This name
is used to form the name of the files used to store the data base
tables.  The dbname, when augmented with a single number must be
a legal filename.  Once dbname is specified you must identify the
owner password of the definition.
        OWNER password
If the data base already exists and you want to define additional
attributes or relations, "password" is checked against the existing
owner password.
        
        ATTRIBUTES
        attname type1 [{length}] [KEY]
                        VAR
        attname type2 [{row,col}] [KEY]
                        row,VAR
                        VAR,VAR
-
-
-













                                                   Page 19


                                                       
                                                       


The attribute definitions are ended when you specify one of the
keywords RELATIONS, PASSWORDS or RULES
Type1 Attributes:
RIM supports seven data types of "type1": real (floating point),
integer, text, double precision, real vectors, integer vectors and
double precision vectors.  You must enter REAL, INT, TEXT, DOUB,
RVEC,IVEC or DVEC for type1.  The default length is one number,
except for TEXT for which it is 8 characters.  The length is speci-
fied in number of values and characters respectively.  VAR indicates
variable length.  The optional KEY specification causes an index file
to be built for the attributes which is used by RIM to quickly find
qualifying rows for retrievals and updates.  The default is that such
an index file is not built (non-key attribute).  You should consider
the cost of building and storing index file data versus the benefits
you will obtain from quicker retrievals when deciding if a KEY declara-
tion should be used.  No specific rules can be given here, experience
should be used to judge.  An attribute can be changed from KEY to NON-
KEY or vice-versa by using the BUILD KEY and DELETE KEY commands des-
cribed in section 2.1.8.  For large data bases (more than 1,000 rows) ,
experience has shown that it is most efficient not to specify a KEY in
the DEFINE submodule but rather to load the data without keys and to
later cause index files to be built using the BUILD KEY command.  The
greater the number of keys, the more efficient this method is.
Type2 Attributes:
RIM supports three data types of "type2": real matrices, integer
matrices or double precision matrices.  You must enter RMAT, IMAT
or DMAT for type2.  The matrices can be of fixed size, have variable
column dimension or variable row and column dimensions.  You enter
the row dimension first, followed by the column dimension.  Default
dimension is 1x1.  The key-word KEY has the same meaning as for
"type1" attributes.
To define relations enter:
        RELATIONS
        relname WITH attname1 [attname2...]
          -
          -
          -
The relation definitions are ended by specifying one of the key-
words ATTRIBUTES, PASSWORDS, RULES, or END which start the other
sections of the DEFINE submodule or finishes the schema definition.










                                                   Page 20


                                                       
                                                       


The attributes must be listed in the order in which they are to
appear in the relation.  No attributes can be used which have not
been previously defined, either in the current attributes definition
subsection or in a previous definition of this data base.  Attri-
butes which are defined but not included in a relation will not be-
come part of the RIM schema.
A RIM data base must have attributes and relations defined, but
passwords and constraint rules are optional.  If read or modify
passwords are desired enter:
        PASSWORDS
        {READ PASSWORD} FOR relname IS password
         RPW
        {MODIFY PASSWORD} FOR relname IS password
         MPW
             -
             -
             -
The password definitions are ended by specifying one of the key-
words ATTRIBUTES, RELATIONS, RULES, or END which start the other
sections of the DEFINE submodule or finishes the data base defini-
tion.  Passwords can be any string of alphanumeric characters up
to 8 characters long.  When you are doing queries, loads, or modi-
fications, the current password is specified by the USER command.
If this password does not match the read, modify, or owner pass-
word for a given relation, you can query that relation.  If this
password does not match the modify or owner password, you cannot
load or modify the relation.
Constraint rules are another optional section of the DEFINE sub-
module.  If rules are specified, they are used during the loading
process or during CHANGE commands to screen out rows which do not
meet the constraint rules.  Rules are specified by relation.  At
most
10 rules may be specified for a single relation.  There are several
options available in the rule definition section.  To define
constraint rules enter:
        RULES
        attname [IN relname]  {EQ} value [ {AND} attname ...]
                               NE            OR
                               GT
                               GE
                               LT
                               LE
or







                                                   Page 21


                                                       
                                                       


        attname1 IN relname {EQA} attname [ {AND} ...]
                             NEA              OR
                             GTA
                             LTA
                             LEA
where:  EQ  = Equals
        NE  = Not equal to
        GT  = Greater than
        GE  = Greater than or equal to
        LT  = Less than
        LE  = Less than or equal to
        EQA = Equals attribute
        NEA = Not equal to attribute
        LTA = Less than attribute
        LEA = Less than or equal to attribute
The rule definitions are ended by specifying one of the key-
words ATTRIBUTES, RELATIONS, PASSWORDS, or END which start
the other sections of the DEFINE submodule or finishes the
schema definition.  Attributes referenced in the rule defini-
tions must have been previously defined.  By specifying
rules, you can restrict an attribute to a range of values or
require that the value of an attribute in one relation have
a specified relationship to the values of an attribute in
the same or different relation.  The comparison operators
ending in A are used when the comparison is to existing
attribute values rather than to a specified constant.  A
rule expression may contain a maximum of 9 Boolean operators.
The method used for constraint checking is that the first
attribute mentioned in the rule is taken from the input
(LOAD or CHANGE command) data and checked against the re-
mainder of the rule expression using existing values in
the data base.
To finish the schema definition you enter the following
keyword and leave the DEFINE submodule:
        END
Example of DEFINE submodule commands:
        DEFINE RIMDS
        OWNER ME
         ATTRIBUTES
          MODEL TEXT KEY
          WEIGHT REAL
          NUMPASS INT
          CARRIER TEXT
          FLIGHTNO INT






                                                   Page 22


                                                       
                                                       


          NAME TEXT KEY                 
          AGE INT
          UPDATE IMAT 4,VAR
         RELATIONS
          AIRPLANE WITH MODEL WEIGHT NUMPASS
          FLIGHTS WITH CARRIER FLIGHTNO MODEL UPDATE
          PEOPLE WITH NAME AGE
         PASSWORDS
          MPW FOR FLIGHTS IS AGENT
          RPW FOR PEOPLE IS BLUE
         RULES
          MODEL IN FLIGHTS EQA MODEL IN AIRPLANE
          AGE GT 21 AND AGE LT 65
          NUMPASS IN AIRPLANE LE 350
2.1.2 Loading a relation
2.1.3  Load Submodule Commands
The LOAD submodule (prompt = L>) commands are used to add rows to
a newly defined relation or to add rows to a relation which
already contains data.  To access this submodule enter:
        LOAD relname
You may now load rows into the relation, one row at a time, by
entering data values in an order corresponding to the attribute
order:
        value1 value2 ... valuen


























                                                   Page 23


                                                       
                                                       


The method used to input values for the different attribute types
is shown below:
        Attribute
          Length or
  Type    Dimension        Valuei                 Remark
REAL,INT   n n=>1      (val1 ... valn)          Parentheses
DOUB,RVEC                                       optional
IVEC,DVEC
REAL,INT   VAR         (val1 val2 ...)          Parentheses
DOUB,RVEC                                       required
IVEC,DVEC
TEXT       any         "text string"            In many cases,
                                              (see section 1.3)
                                                " " is optional
RMAT,IMAT  m,n      ((r1c1...rmc1)(r1c2...) +   Columnwise
DMAT                     ...rmcn))              Parentheses
                                                optional
RMAT,IMAT  m,VAR    ((r1c1...) (r1c2...)...))   Columnwise
DMAT        or                                  Parentheses
           VAR,VAR                              required
-----------------------------------------------------------------------
To finish data loading you enter:
        END
Multiple relations may be loaded from within the LOAD submodule by
re-entering the LOAD command instead of the END command.
Example of LOAD submodule commands:
                USER AGENT
                LOAD AIRPLANE
                DC9 87000.  110
                747SP 200000.  350
                LOAD PEOPLE
                BOB 30
                JOE 32
                ALICE 29
                LOAD FLIGHTS
                UAL 16 "757"  ((1,2,3,4) (4,5,6,7))
                *3 ((2,4,5,8)(1,2,3,4) (4,5,6,7))
                END












                                                   Page 24


                                                       
                                                       


If the value for an attribute is unknown, you enter the characters
-0- for the missing value or use two successive commas.
        L1011 -0- -0- 250
        L1011,,,250
These two input entries have identical meaning.
2.1.3 Querying A Relation
2.1.4  Commands for Querying the Data Base
SELECT Command
The SELECT command is used for displaying or printing data from
one relation.  It has many options.  To print all the data from a
relation:
        SELECT ALL FROM relname
To print selected attribute values from all rows in a relation:
        SELECT attname1 [  attname2 ... attnamen ] FROM relname
The above command will print up to 20 attributes in any order.
The number of attributes is limited by space available in a line.
As a rule of thumb, 7 attributes may be selected when running at
an 80 character interactive terminal and 11 when running in the
batch mode or at an 132 character terminal.
For variable length attributes or for attributes of fixed length
that would otherwise not fit on aline alone or together with
other attributes, you may format the output using the optional
field width control:
        SELECT attname1 [ =fw1 ] [ attname2 [ =fw2 ] ... ] +
        FROM
fwi is the output field width for attnamei.  For a text type
attribute, fwi is the width of the output paragraph in number
of characters, for other attribute types it is the number of
values.  When the field width option is used, RIM will use as
many output lines as required for each row.
The field width defaults depend on the attribute type. For a
fixed width atrtribute, other than matrix, no paragraphing is
attempted. For a fixed length matrix,the default paragraph
width is a full row. The system wil use a field width equal
to the attribute length or column dimension to display the value(s)
of the attribute. For a variable length attribute of type TEXT,
the default field width is 40 characters with paragraphing. For
variable length attribtes of type REAL, INT, DOUB, the default
is 4 values with paragraphing. For variable length vector type
attributes, the default is a display of the length and 3 values
with paragraphing. For variable length matrix attributes the
default is a display of the row and column dimensions and 3
values with paragraphing. Each row starts on a new line.
If a field width is specified, the system will display the
dimension of variable length vectors and matrices and use one
of the specified output positions for these values. However,
if a field width of 1 is specified for such an attribute, the row
and column dimensions will not be displayed.


                                                   Page 25


                                                       
                                                       


Defaults are rather complex.  For a fixed length attribute,
other than matrix, no paragraphing is attempted.  For a fixed
length matrix, the default paragraph width is a full row.  The
system will use the field width required to display the value(s)
of the attribute.  For a variable length attribute of type TEXT,
the default is a display of a maximum of 40 characters with
paragraphing.  For variable length attributes of types REAL, INT,
DOUB, the default is 4 elements with truncation.  For variable
length vector type attributes, the default is 4 elements with
paragraphing (no truncation).  For variable length matrix at-
tributes the default is 4 elements with paragraphing (no trun-
cation).  A row starts on a new line.
Whether field width is specified or not, the system will display
the dimension of variable length vectors and matrices using one
of the output positions.  However, should you specify a width of
one for such an attribute, the row and column dimensions will not
be displayed.
Further information about line width, number of lines per page,
defaults and user specifications is given in section 2.1.10 as
part of the RIM report writing features.
When paragraphing TEXT type attributes, RIM will identify sub-
strings of text separated by blanks.  The substring is placed
on the current line if there is space available.  If the current
line contains less than four characters, the number of characters
that fit on the line are removed from (the front of) the substring
and put on the line (without hyphen) and continued on the next
line.  If the current line contains more than four characters,
the substring will be placed on the next line.
Examples of SELECT command:
SELECT ivecvar FROM rel1
        DIM     IVECVAR
-----------------------------------
         7        1     2       3
                  4     5       6
                  7
         1       10
SELECT imatvv FROM rel1
       ROW    COL    IMATVV
---------------------------------------
        2      5      11     12     13
                      14     15
                      21     22     23
                      24     25
        1      1      11        






                                                   Page 26


                                                       
                                                       


SELECT textv = 9 FROM rel 1
TEXTV
------------
THIS IS
AN EXAMPL
E OF
WRAPAROUN
D OF TEXT
THIS IS
ANOTHER
EXAMPLE
OF TEXT
The attribute name attnamei may be replaced by its correspond-
ing attribute number (attnum1).  The attribute number is deter-
mined by the position of the attribute in the relation.  Specific
elements of a vector or a matrix may also be designated. The general
form of the unconditional SELECT command is:
SELECT {attname1 [ = fw1 ]} [attname2 [= fw2] ...] +
        attnum1 [ = fw1 ]
        attname1(i)
        attname1(i,j)
        attnum1(i)
        attnum1(i,j)
        ALL
FROM  relname
To print all attributes from a relation where certain conditions
are met:
  SELECT ALL FROM relname WHERE condition1 [ {AND} condition2 ...]
                                               OR
Up to ten conditions may be combined using the Boolean operators
AND/OR.  The conditions are combined from left to right.
A LIMIT condition, if used, does not count as one of the 10
conditions.
Each condition may be one of the following forms:
        attname EXISTS
        attname FAILS
        attname EQ MAX
        attname EQ MIN
        attname EQ value
        attname EQS value
        attname NE value        
        attname GT value
        attname GE value
        attname LT value
        attname LE value
        attname EQ list
        attname NE list
        attname1 EQA attname2


                                                   Page 27


                                                       
                                                       


        attname1 NEA attname2
        attname1 GTA attname2
        attname1 GEA attname2
        attname1 LTA attname2
        attname1 LEA attname2
        ROWS EQ rownumber
        ROWS NE rownumber
        ROWS LT rownumber
        ROWS LE rownumber
        ROWS GE rownumber
        ROWS GT rownumber
        ROWS EQ list
        ROWS NE list
        LIMIT EQ number
where:  EQ  = Equals    
        EQS = Contains the text string
        NE  = Not equals
        GT  = Greater than
        GE  = Greater than or equal to
        LT  = Less than
        LE  = Less than or equal to
        EQA = Equals attribute
        NEA = Not equals attribute
        GTA = Greater than attribute
        GEA = Greater than or equal to attribute
        LTA = Less than attribute
        LEA = Less than or equal to attribute
        MAX = Maximum value
        MIN = Minimum value
Attname, attname1, attname2 may refer to an element of a vector
or a matrix.
When an attribute has been assigned a value, then EXISTS will
qualify those attributes.  If an attribute has not been assigned
a value, but was loaded with -0-, then FAILS will qualify those
attributes.
MAX and MIN comparison can only be made for integer, real and
double precision attributes of fixed length equal to 1.
Value in a comparison statement must follow the rules of section
2.1.3 for vectors and matrices, i.e., if the attribute is of
variable length or dimension, parentheses must be used to input
a vector or a matrix value or a list of vector and matrix values.
EQS applies to text strings only.  In such a comparison, value is
a text string and the comparison is true if value is found as a
substring anywhere within the attribute for which comparison is
requested.
NE comparison when applied to matrices or vectors is true if the
length or dimension is different from the length or dimension of
your specified comparison vector or matrix or if any vector or


                                                   Page 28


                                                       
                                                       


matrix elements differs.
GT and LT comparisons for vector and matrix attributes are
"lexicographical", i.e. a comparison is made element by
element (columnwise for matrices) and continued until a true
or false condition is detected.  If no such condition is detected
after the last element is checked, a false condition is assumed.
Comparison is made only for vectors and matrices of the same
sizes as comparison data.
GE and LE comparisons for vector and matrix attributes are similar
to GT and LT comparisons except it continues if an equal condi-
tion is detected and if no condition is detected after the last
element is checked, a true condition is assumed.
Comparison rules for vector attributes apply also to real, integer
and double precision attributes of fixed or variable length.
A list is a simple list (a1, a2, a3,...,an) of values.
The comparison key words ending in A are used when comparing
the value of one attribute to the value of another attribute
in the same row of the relation.
ROWS refer to row numbers in a relation.  Note that a relation is
loaded in input row order but that subsequent operations
(changes) to the data base may cause the order of the rows to
change.
When the LIMIT clause is used, only the first LIMIT number of
the rows that otherwise would qualify will actually qualify.
Processing the WHERE condition can be speeded up greatly if
index processing is used.  Index processing involves using
the indices created for KEY attributes rather than looking
at each row of a relation to find the rows qualified by
the WHERE conditions.  Index processing will be used when
the following are all true:
        1)   The last condition uses an attribute which is KEY
        2)   The last condition uses EQ
        3)   The last condition is not combined by OR with the
             other conditions.
















                                                   Page 29


                                                       
                                                       


The output can be sorted by specifying sorting attributes.  The
sorting order is user specified with default low to high.
        SELECT ... FROM relname
        SORTED BY attname1 [ {=A}  ] { attname2 [={A} ] ...] +
                               D                   D
        [ WHERE ...]
A and D stands for ascending and descending order respectively.
If a sort on more than one attribute is requested, the output will
first be ordered according to the first mentioned attribute.  In
case there are duplicates for the first sort attribute, these will
be ordered by the second sort attribute, duplicates within this by
the third and so on.  A maximum of 5 sorts may be specified.  When
multiple attributes are used, ascending and descending order may
be used in any combination.  Variable length attributes may not be
used as sort attributes.  When fixed length attributes are used as
sort attributes, only the first 20 characters and the first value
is used for sort.
All these options can be described using the following general
syntax:
        SELECT {attname1 [ = fw1 ] [...attname [ = fwn ] ] } +
                attnum1...
                attname1(i)...
                attname1(i,j)...
                attnum1(i)...
                attnum1(i,j)...
                ALL
        FROM relname +
        [SORTED BY attname [{=A} ]... ] +
                              D
        [WHERE condition1 [{AND} condition2 ... ]]
                            OR
If the sum of the lengths (or fwi) of the attributes requested
exceeds the line capacity, the data line will be truncated.
See section 2.1.10 for further expanation of line width control.
TALLY Command
The TALLY command prints a tally for an attribute giving each
unique value and the number of times it occurs in a relation.
The tally is ordered ascending or descending per user input.
Default is ascending.  The WHERE clause is optional and uses
the same syntax as in the SELECT command.
        TALLY attname [{=A}] FROM relname [ WHERE ... ]
                         D








                                                   Page 30


                                                       
                                                       


Examples of SELECT and TALLY commands:
   SELECT ALL FROM AIRPLANE
   SELECT MODEL FROM AIRPLANE
   SELECT ALL FROM AIRPLANE WHERE WEIGHT GT 100000.
   *8 AND NUMPASS LT 200
   SELECT AGE FROM PEOPLE WHERE NAME EQ BOB
   SELECT ALL FROM AIRPLANE SORTED BY MODEL=D
   TALLY MODEL FROM FLIGHTS
   TALLY MODEL FROM FLIGHTS WHERE CARRIER EQ UNITED
   SELECT ALL FROM DIMENS WHERE HEIGHT GTA WIDTH
   SELECT FILE TITLE=4 OWNER FROM PFDATA
2.1.4 Querying the Schema
2.1.5  Commands for Querying the Schema
When you use any of these commands, RIM will display only
the data you are authorized to access according to your
current user password.
LISTREL Command
The purpose of LISTREL is to provide you with information
about the relations in the data base.
There are three formats for the LISTREL command.  The first
consists of simply entering:
        LISTREL
Using LISTREL in this fashion provides you with a list of
all relations currently defined in your data base.  If you
wish to display the definition of a specific relation, then
the syntax is:
        LISTREL relname
The use of LISTREL in this manner also provides a count of
the number of rows defined for the specified relation.
        LISTREL ALL
This command (restricted by user password) will display the
definitions of all relations in the data base, including
counts of the number of defined rows in each relation.
EXHIBIT Command
The purpose of the EXHIBIT command is to allow you to query
the RIM dictionary to obtain the names of all relations
having a specific set of attributes.  For example, if you
want to know which relations contain the attribute attname
you would enter:
        EXHIBIT attname










                                                   Page 31


                                                       
                                                       


You would then obtain either a list of the relations having
this attribute, or a message indicating that this attribute
was not found in any relations in the data base.
The EXHIBIT command also allows you to query fro a list of
attributes(maximum of 10).  Suppose that you wanted to know
which relations contian both attname1 and attname2.  The
command would then be:
        EXHIBIT attname1 attname2
The general syntax of this command is:
        EXHIBIT attname1 [attname2 ... attnamen ]
PRINT RULES Command
This command can be used when the current user password
matches the owner password of the data base definition.  To
obtain a complete list of all constraint rules enter:
        PRINT RULES
2.1.6  Computation Command
COMPUTE Command
The COMPUTE command is used to compute simple functional
values of an attribute.  A WHERE clause is optional and uses
the same syntax as is used in the SELECT command.
  COMPUTE {COUNT} attname FROM relname [WHERE... ]
            MAX
            MIN
            AVE
            SUM
There are some restrictions as to the type and word length
of the attribute when using these computed functions.  All
of these functions exclude any -0- values when making their
computations.  The following table describes the attribute
type and length restrictions for each function:




















                                                   Page 32


                                                       
                                                       


FUNCTION  ATTRIBUTE TYPE       ATTRIBUTE LENGTH
COUNT     any                  any
MIN       any of fixed length  1 for non-text, ANY for text
MAX       any of fixed length  1 for non-text, ANY for text
AVE       int, real, double    1
SUM       int, real, double    1
Examples of COMPUTE command:
    COMPUTE AVE NUMPASS FROM FLIGHTS
    COMPUTE MAX WEIGHT FROM FLIGHTS WHERE NUMPASS LT 100
    COMPUTE COUNT NAME FROM PEOPLE WHERE AGE GT 30
2.1.6 Modification Commands
2.1.7  Data Base Modification Commands
These commands are used to change the contents of the data
base.  a modify or owner password correlation is required in
order to use these commands.
CHANGE Command

     CHANE (Attribute values)

     The CHANGE command is used to change the value of an
attribute in a relation where certain conditions are met.
   CHANGE {attname1}    TO value [IN relname] WHERE ...
           attname(i)
           attname(i,j)
Value has the same form as described in Section 2.1.3.  The
WHERE clause is required and uses the same syntax as in the
SELECT command.  If the relation name is not specified, the
attribute is changed in all relations where the attribute is
found and the conditions are met.

     CHANGE (passwords)

     The read or modify passwords may be changed using the command

CHANGE {RPW} TO newpass FOR relname
        MPW


     CHANGE OWNER

     The CHANGE OWNER command is used to change the name of the data
base owner. Only the curent owner may use this command.

     DELETE ROWS Command
The DELETE ROW command is used to delete selected rows in a
relation.
        DELETE ROW FROM relname WHERE ...
The name of the relation must be specified as well as a


                                                   Page 33


                                                       
                                                       


WHERE clause.  The syntax for the WHERE clause is the same
as in the SELECT command.
DELETE DUPLICATES Command
This command is used to remove any duplicate rows from a
relation.  It is particularly useful on relations which have
been created by any of the relational algebra commands
(JOIN, INTERSECT, SUBTRACT, or PROJECT).  The syntax for
this command is:
DELETE DUPLICATES [attname1, attname2,...] from relname
Duplicates are checked only for the specified (combination
of) attribute(s).  Default is to check the complete row (all
attributes).
Examples of CHANGE, DELETE, and DELETE DUPLICATES commands:
   CHANGE NUMPASS TO 320 IN AIRPLANES WHERE MODEL EQ 747SP
   CHANGE NAME TO ROBERT WHERE NAME EQ BOB
   DELETE ROW FROM AIRPLANES WHERE MODEL EQ DC10
   CHANGE STABILITY TO LOW IN DIMENSIONS WHERE HEIGHT GTA
WIDTH
196z   DEL DUP NUMPASS FRO AIRPLANES

     DELETE RULE

     The DELETE RULE command is used to delete a specified constraining
rule. The USER password must match the owner. Rulenumber is obtained
using the PRINT RULES command. The format of the command is

DELETE RULE rulenumber


2.1.8  Schema Modification Commands
These commands are used to change the data base schema
definition.  Except for the CHANGE OWNER command, a modify
or owner password correlation is required in order to use
these commands.
CHANGE OWNER Command
The CHANGE OWNER command is used to change the name of the
data base password.  Only the current owner is allowed to
use this command.
        CHANGE OWNER TO newowner
RENAME Attribute Command
The RENAME attribute command is used to change the name of
an attribute in the data base definition (schema).
   RENAME attname1 TO attname2 [IN relname]
THe old name is attname1 and the new name is attname2.  if
the name of the relation is not specified, then the name
change takes place in every relation that contains the old
name.  If the relname is specified and attname1 occurs more
than once, the first occurence will be changed.


                                                   Page 34


                                                       
                                                       


RULES and KEY(s) defined for attname1 will automatically be
redefined to apply to attname2.
Examples of RENAME command:
   RENAME MODEL TO VERSION IN AIRPLANES
   RENAME NUMPASS TO CAPACITY













































                                                   Page 35


                                                       
                                                       


BUILD KEY Command
This command is used to change an attribute from non-key to
KEY.  An index is built from existing data values by amking
a pass through current rows of the specified relation.  This
index is then used and maintained just as if the attribute
had been declared to be KEY in the original data base
definition.
        BUILD KEY FOR attname IN relname
Keys are not transferred to relations created by relational
algebra commands.
DELETE KEY Command
This command is used to change an attribute from KEY to
non-key.  The index file for that attribute is deactivated
and no longer maintained or used once the attribute  has
been changed to non-key with this command.
        DELETE KEY FOR attname IN relname
CHANGE PASSWORD Command
The read or modify passwords may be changed by using the
following command:
        CHANGE {RPW} TO newpass FOR relname
                MPW
RENAME RELATION Command
You may change the name of a relation by using the following
command:
        RENAME RELATION relname TO newname
RULES applying to relname will automatically apply to
newname.
REMOVE Command
The REMOVE command is used to remove a relation definition
and its data from the data base.
        REMOVE relname



















                                                   Page 36


                                                       
                                                       


2.1.9  Relational Algebra Command
These commands allow you to create new relations from
existing relations.  All relational algebra commands require
modify permission on the constituent relations.
INTERSECT Command
The purpose of the INTERSECT command is to allow you to
combine the rows of relations into a third relation based on
common values within a set of specified attributes.  The
syntax of the INTERSECT command is:
   INTERSECT relname1 WITH relname2 FORMING relname3 +
   [USING attname1 [attname2 ... attnamen]]
The USING clause identifies the attributes that form the
resulting relation. The attributes used in the INTERSECT
process are the subset of those identified by the USING
clause which are present in both relations.
For example, assume that you have the following two
relations defined:
          REL-1                          REL-2
NAME     DEPT      JOB        DEPT       JOB          PAY       
-----    -----     -----      -----      -----        ----
BOB      A         ENGR       A          ENGR         800
JIM      C         SUPR       B          ENGR         450
BOB      B         ENGR       C          ENGR         750
RAY      C         ENGR
You may INTERSECT two relations restricted to specific sets
of attributes (the USING clause) or use all attributes of
both relations.  In either case RIM will identify the common
attributes and use the common values within these attributes
to identify the conditions for intersect generation.
Suppose you want to INTERSECT the two relations using
attributes DEPT, NAME, and JOB.  The command for this would
be:
INTERSECT REL-1 WITH REL-2 FORMING REL-3 USING DEPT NAME JOB
The result would be the new relation REL-3 shown on the next
page.















                                                   Page 37


                                                       
                                                       


                     REL-3
            DEPT     NAME      JOB
            ----     -----     -----
            A        BOB       ENGR
            B        BOB       ENGR
            C        RAY       ENGR
In this example there are no duplicate rows in REL-3.
However, it is possible that the intersect command will
create duplicate rows.  Since, in general, duplicate rows
are not desired in a relation, they can be removed with the
DELETE DUPLICATES command.  Note also that by specifying
which attributes the INTERSECT is using, you restrict the
number of attributes in the resulting relation to only those
specified in the USING clause.
Suppose you want RIM to use all the attributes in the two
relations.  In this instance you would enter:
   INTERSECT REL-1 WITH REL-2 FORMING REL-4
The result would be REL-4 consisting of the attributes
NAME, DEPT, JOB, and PAY, shown below in the resulting rows:
                      REL-4
           NAME    DEPT     JOB      PAY
           -----   -----    ----     ---
           BOB     A        ENGR     800
           BOB     B        ENGR     450
           RAY     C        ENGR     750
There may be situations where an INTERSECT is impossible to
perform.  These include:
   1)  The name of the resulting relation already exists
   2)  The two relations have no common attributes
   3)  The attributes in the USING clause do not exist in
       the relation being intersected
   4)  The resulting relation exceeds 1021 words
If any of the above situations is encountered, you are
warned of the problem and the INTERSECT command processing
is stopped.  In the case where common attribute names exist
but there are no matching values, the operation will be
successful resulting in an empty relation (0 orws).













                                                   Page 38


                                                       
                                                       


The INTERSECT command is a powerful tool and may be used as
a step towards satisfying queries which require attributes
from more than on relation.
JOIN Command
The JOIN command is a function operating on two relations to
form a third relation.  The purpose of the JOIN is to
juxtapose two relations based on a specified attribute from
each.  The result of the JOIN command is a third relation
containing all of the attributes from both relations.  Rows
are generated in the new relation as a result of the
comparison conditions between attributes being satisfied.
The syntax of the JOIN command is:
   JOIN relname1 USING  attname1 WITH relname 2 USING +
   attname2 FORMING relname3 [ WHERE {EQ} ]
                                      NE
                                      GT
                                      GE
                                      LT
                                      LE
The WHERE clause of the JOIN command is different form the
WHERE clause of the SELECT command.  In JOIN it applies only
to the comparison of the two attributes upon which JOIN is
based.  If the WHERE clause is omitted (default), EQ is
used.
The value of attname1 in the first row of relname11 is
compared to all the values of attname2.  Rows which qualify
are generated in relname3.  The value of attname1 in the
second row of relname1 is compared to all the values of
attname2, etc.  Each row from relname1 may generate 0, 1, 2,
or more rows in relname3.
For example, consider the relations REL1 AND REL2:
          REL1                     REL2
 A        B        C            D        E
---      ---      ---          ---      ---
 1        2        3            3        1
 4        5        6            6        2
 7        8        9
The following JOIN command would produce the result shown.












                                                   Page 39


                                                       
                                                       


        JOIN REL1 USING B WITH REL2 USING D +
        FORMING REL3 WHERE LT
                 REL3
 A        B         C          D         E
---      ---       ---        ---       ---
 1        2         3          3         1
 1        2         3          6         2
 4        5         6          6         2
The JOIN will function correctly on any comparison providing
that you compare attributes of the same data type.  All
attribute names in the resultant relation must be unique in
order for you to obtain accurate results from subsequent
commands using the relation.  Any duplicate attribute names
should be change using the RENAME command before doing
queries or updates to the new relation.  In the case of
duplicate attribute names, RENAME when applied to a specific
relation will change the first attribute name.
There may be situations where a JOIN is impossible to
perform.  These may include:
   1)  The name of the resulting relation already exists
   2)  The attribute in the USING clause does not exist in
       the relation being joined
   3)  The attributes being compared are different data
       types or lengths
   4)  An attribute in either of the relations greater than
       300 computer words
   5)  The resulting relation exceeds 1021 words
If any of the above situations are encountered you are
warned of the problem and the JOIN command processing is
stopped.
PROJECT Command
The function of a PROJECT command is to create a new
relation as a subset of an existing relation.  You may want
to create the new relation from the old one by removing
attributes, removing rows, or both.  The syntax for the
PROJECT command is:
PROJECT relname1 FROM relname2 USING {attname1...attnamen} +
                                      ALL
[WHERE ...]
The WHERE clause is optional but it is specified, it has the
same syntax as in the SELECT command.  You are required to
specify which attributes are to be retained in the new
relation.  The old relation is relname2 and the new relation
is relname1.
For example consider the following relation:
                        PEOPLE
EMPNUM     EMPNAME      BOSS      POSITION        GROUP
------     -------      ------    --------        ------


                                                   Page 40


                                                       
                                                       


 2181      JONES        SMITH     MANAGER         AADE
 3964      ERICKSON     BUSS      APPL-MGR        ACC
 6543      GRAY         PARKER    ASST-MGR        PHOTO
 2233      SCHMITZ      BUSS      APPL-MGR        ACC
To create a new relation with EMPNAME and GROUP as the only
attributes and where now rows contain PARKER as BOSS enter
the command:
    PROJECT TEMP1 FROM PEOPLE USING EMPNAME GROUP +
    WHERE BOSS NE PARKER
                        TEMP1
              EMPNAME         GROUP
              -------         ------
              JONES           AADE
              ERICKSON        ACC
              SCHMITZ         ACC
The PROJECT command is useful to reduce the size of a
relation when only a subset of the data is needed.  RIM will
not eliminate any duplicate rows formed in the new relation.
 You must do that yourself with the DELETE DUPLICATES
command.
There may be situations where a PROJECT is impossible to
perform.  These include:
   1)  The name of the resulting relation already exists
   2)  An attribute in the USING or WHERE clause is not in
       the relation
SUBTRACT Command
The SUBTRACT command is similar to the PROJECT command in
that the new relation is a subset of an existing relation.
The rows, however, are selected based on the data in another
relation rather than on a WHERE clause within the same
relation.  Where the INTERSECT command looked for rows of
two relations which matched up, the SUBTRACT command does
just the opposite.  It looks for rows in the relation which
do not match any rows in the other relation.  The syntax for
the SUBTRACT command is:
  SUBTRACT relname1 FROM relname2 FORMING relname3 +
  [USING attname1 [attname2 ... attnamen]]













                                                   Page 41


                                                       
                                                       


All rows in the new realtion will come from relname2.  If
the USING clause is not specified, then all attributes of
relname2 will be attributes of relname3.  Relname1 is the
relation that rows of relname2 are checked against for
matches.  If a USING clause is specified at least one of the
attributes in the clause must be common to both relations.
As an example consider these two example relations:
         EMPDATA                         BOSSDATA
EMPNUM   EMPNAME   BOSS         BOSS     POSITION    GROUP
------   -------   ------       ------   --------    --------
 2181    JONES     SMITH        SMITH    MANAGER     AADE
 3964    ERICKSON  BUSS         PARKER   ASST-MGR    PHOTO
 6543    GRAY      PARKER       BUSS     APPL-MGR    ACC
 8461    BROWN     WHITE
 2233    SCHMITZ   BUSS
The following command will produce a new relation from
EMPDATA:
 SUBTRACT BOSSDATA FROM EMPDATA FORMING TEMP USING +
 EMPNAME BOSS
The resulting relation TEMP would contain only one row:
                        TEMP
                  EMPNAME  BOSS
                  -------  -----
                  BROWN    WHITE
There may be situations where a SUBTRACT is impossible to
perform. These include:
   1)  The name of the resulting relation already exists
   2)  The relations have no common attributes
   3)  The number of attributes in the USING clause is
       greater than the number in relname1
   4)  An attribute in the USING clause is not in the
       relations
2.1.10  Report Generation Commands
These commands establish a limited report generation
capability.















                                                   Page 42


                                                       
                                                       


NEWPAGE Command
This command causes a new page to be issued.  It applies to
batch output only.  The command is:
        NEWPAGE
BLANK Command
Blank lines can be inserted into the output stream by using
the command:
        BLANK n
where n is the number of blank lines written.
TITLE Command
The command:
        TITLE "titlestring"
causes the text "titlestring" to be printed, centered on the
line.  If the length of "titlestring" is longer than current
lines width it will be truncated and a warning issued.
DATE Command
The command:
        DATE
will cause the current date to be printed, centered on the
line.
LINES Command
This command controls the number of lines per page
(exclusive of title.)  The command is:
        LINES n
will establish page size to n lines.  Default is 56.
WIDTH Command
This command controls the width of a printed line.  The
command:
        WIDTH n
will establish a line width of n characters.  Default is 78
if output is to a terminal, 132 if output is to a batch
printer.  If n is specified to be less than 20, 20 will be
used.

















                                                   Page 43


                                                       
                                                       


2.1.11  Communication Command
UNLOAD Command
The UNLOAD command permits you to off-load a portion or all
of your data base onto a previously designated file (see
OUTPUT command).  The file will contain 80 characters text
records and can be read by RIM as an input file on the same
or on a different computer using the INPUT command.  Default
file name is for006.  The syntax of this command is:
        UNLOAD [dbname = newname] {ALL   } +
                                   SCHEMA
                                   DATA
        [relname1 [ mpw1 ] relname2 [ mpw2 ] ... ]
Specifying SCHEMA will off-load the schema of your data
base, DATA will off-load the data of your data base and ALL
will off-load both schema and data.
Optionally, you may rename your data base by entering dbname
=newname where dbname is the name of the currently open data
base.  By specifying relation names, you will only off-load
data and/or schemas for the specific relations.  The modify
password does not allow you to modify access to the
relation.
There are implicit password restrictions to the unload
command as follows:  If you are the data base owner, you may
off-load any data and/or schema.  If you are not the owner,
you may off-load data and/or schema for the relations for
which you have modify access permission.  Your password
becomes the owner of the off-loaded data base.  Rules, if
any, will only be off-loaded if you are the owner of the
data base and you have used the option ALL.





















                                                   Page 44


                                                       
                                                       


2.2  MENU MODE EXECUTION OVERVIEW
The RIM menu mode provides you with the capability to build
the schema for a new data base and to update an existing
data base definition.
The options (create, update, query, command, and exit)
available in menu mode are shown in figure 2.2-1.
Executions may be terminated at anytime by entering the word
QUIT.  EXIT, in response to an input prompt, will return you
to the top menu.  The data base will be purged following a
QUIT command.








































                                                   Page 45


                                                       
                                                       


               l----------------l
               l  BEGIN RIM 5.0 l
               l----------------l
                      l
                      l
             RIM COMMAND MODE
             ENTER "MENU" FOR MENU MODE
            R>MENU    l
                      l
                      l
             SELECT THE EXECUTION OPTION DESIRED
                 1)  CREATE A NEW DATABASE
                 2)  UPDATE AN EXISTING DATABASE
                 3)  QUERY AN EXISTING DATABASE
                 4)  ENTER COMMAND MODE
                 5)  EXIT
                      l
   l------------------------------------------------l
   l              l             l         l         l
   l              l             l         l         l
CREATE OPTION     l         QUERY OPTION  l       EXIT
SECTION 2.2.1     l         SECTION 2.2.3 l   SECTION 2.1.1
                  l                       l
             UPDATE OPTION         COMMAND MODE
             SECTION 2.2.2         SECTION 2.1
Figure 2.2-1 Section References for the Menu Mode Options
























                                                   Page 46


                                                       
                                                       


2.2.1  Data Base Creation Option
The purpose of this option is to construct a schema by
prompting you for the data base, owner, the names of the
relations, their associated attributes and read/modify
passwords.
After compilation of the schema, you have the opportunity to
interactively load the data base and/or query the data base.
In the command mode, you have available the full set of RIM
commands (section 2.1) allowing the direct definition of the
schema using the DEFINE submodule commands and the loading
of the data base using the LOAD submodule commands.
2.2.2 Data Base Update Option
With this option you may add/modify relations and/or load
additional data into the data base.  If additional relations
are desired, you are prompted for the names of the
relations, their associated attributes and read/modify
passwords.  If additional data is to be loaded, the list of
relations in the data base is displayed and your enter the
required data.  Removal or modification of data in the data
base is done using the RIM data base modification commands.
In this command mode, you have available the full set of RIM
commands (section 2.1) allowing the direct addition of
relations using the DEFINE submodule commands and the
loading of data using the LOAD submodule commands.  The data
base modification commands are used to update existing data.
2.2.3  Query Option
With this option you are prompted for the data base name.
The full set of RIM commands (section 2.1) is available to
you for data base query.  In addition to query, all other
data base activities are available through the RIM command
mode.



















                                                   Page 47


                                                       
                                                       


2.3  RIM MENU MODE INTERACTIVE DIALOGUE
This section presents the questions and menus that appear in
the menu mode.  The response options are also discussed.
The menu mode is accessed by entering MENU anytime in the
command mode when a R> prompt is present.
2.3.1  General Option and Questions
SELECT THE EXECUTION OPTIION DESIRED
        1)  CREATE A NEW DATA BASE
        2)  UPDATE AN EXISTING DATA BASE
        3)  QUERY AN EXISTING DATA BASE
        4)  ENTER COMMAND MODE
        5)  EXIT
SELECT THE UPDATE OPTION DESIRED
        1)  DEFINE ADDITIONAL RELATIONS
        2)  LOAD ADDITIONAL DATA
        The desired update option is selected by entering
        either the integer 1, allowing the definition of
        additional relations, or 2, allowing the loading of
        additional data into the data base.
DO YOU WANT TO QUERY THE DATA BASE AT THIS TIME--Y OR N
        You may switch to the command mode for query by
        entering "Y".  If the query option is not desired
        "N".
2.3.2  Data Base Files
ENTER THE NAME OF THE DATA BASE
        The 1-6 character alphanumeric name assigned to the
        data base is entered here.  The name is used to
        create the names of the logical files that contain
        the data base.





















                                                   Page 48


                                                       
                                                       


2.3.3  Schema Definitions
ENTER THE NAME OF THE DATA BASE
 The 1-6 character alphanumeric name assigned to the data
 base is entered here.  All future references to this data
 will be via the assigned data base name.
ENTER THE NAME OF THE DATA BASE OWNER
 The 1-8 character alphanumeric name of the data base owner
 is entered here.  This name is used as the schema password.
 Additional schema definitions will not be permitted unless
 the user password matches the owner password assigned here.
ENTER THE NAME ASSIGNED TO THIS RELATION
 A 1-8 character alphanumeric name assigned to the relation
 being defined.
ENTER THE READ PASSWORD FOR THIS RELATION
 A 1-8 character alphanumeric string assigned by the owner
 as the read password for the relation being defined.  if
 the owner has assigned a read password the user password
 must match in order to query the relation.  If no read
 password is desired enter NONE.
ENTER THE MODIFY PASSWORD FOR THIS RELATION
 A 1-8 character alphanumeric string by the owner as the
 modify password for the relation being defined.  if the
 owner has assigned a modify password the user password must
 match in order to load or modify the relation.  if no read
 password is desired enter NONE.
ENTER THE ATTRIBUTES OF THIS RELATION
ENTER END WHEN COMPLETE
   attname  type  length (IF >) "KEY" (IF KEY)
Attname = 1-8 character alphanumeric string identifying
          the attribute being defined.




















                                                   Page 49


                                                       
                                                       


Type =  INT    (Integer)
        REAL   (Real)
        TEXT   (Text)
        DOUB   (Double Precision)
        RVEC   (Real Vector)
        IVEC   (Integer Vector)
        DVEC   (Double Precision Vector)
        RMAT   (Real Matrix)
        IMAT   (Integer Matrix)
        DMAT   (Double Precision Matrix)
Length = number of characters (text) or number of values
         (all others)
1,2,3 ..., etc., or VAR    INT
                           TEXT
                           REAL
                           DOUB
                           RVEC
                           IVEC
                           DVEC
     row, column or        RMAT
     row, VAR or           IMAT
     VAR, VAR              DMAT
A variable length (or length greater than one) INT, REAL, or
DOUB can be considered to be functionally identical to IVEC,
RVEC, or DVEC.
KEY = the word key indicates the attribute is key.
Example:  To define a text string attribute (TEXTST) of 60
characters, a real attribute (TEXTST) of 60 characters, a
real attribute (REAL1), an integer key attribute (INT-1),
and a real matrix with dimensions 6x8 (MAT68), the following
entries would be made:
        R> TEXTST TEXT 60
        R> REAL1 REAL
        R> INT-1 INT KEY
        R> MAT68 RMAT 6,8
To end the definition of the attributes for this relation,
the word "END" is entered.
DO YOU HAVE ADDITIONAL RELATIONS TO DEFINE--Y OR N
  Additional relations may be defined by entering the
  character "Y".  If no additional relations are to be
defined at this time, enter "N".









                                                   Page 50


                                                       
                                                       


2.3.4  Data Base Loading
DO YOU WANT TO LOAD THE DATA BASE--Y OR N
 The data base is available for data loading if desired.
 Enter "Y" if you want to load the data base at this time.
 Enter "N" if no data is to be loaded.
SELECT THE RELATION TO BE LOADED
 The relations defined in the data base will be listed.  You
 select the relation to be loaded by entering the integer
 corresponding to the desired relation.
ENTER THE MODIFY PASSWORD FOR THIS RELATION
 No data loading will be allowed for the selected relation
unless the proper modify password is entered here.
ENTER THE ATTRIBUTE VALUES IN THE SPECIFIED SEQUENCE
ENTER END WHEN COMPLETE
 Entering data values at this point loads the data base.
 The values are entered in the order indicated and the value
 entered must correspond to the attribute type.  If a text
 string contains embedded blanks, or commas, or if entirely
 numeric text is entered, it must be enclosed in quotation
 marks .  Unused trailing characters in fixed length text
 strings will be blank filled.  It is recommended that
 leading blanks not be used in text strings.  If vectors or
 matrices are loaded, all values must be specified. Enter
 "END" when data loading is complete.  It is recommended
 that large data bases and data bases that have vectors and
 matrices use the application program interface for loading
 data.
DO YOU HAVE ADDITIONAL RELATIONS TO LOAD--Y OR N
 If you want to load another relation, enter "Y". If all the
 data base to be loaded at this time has been loaded, enter
 "N".



















                                                   Page 51


                                                       
                                                       


3.0  RIM EXECUTION THROUGH THE APPLICATION PROGRAM INTERFACE
Any programming language which can call FORTRAN subroutines
can access and modify a pre-defined RIM data base through
FORTRAN-callable subroutines contained in the RIM
application program interface library(RIMLIB).  Data is
accessed one row at a time.  The RIM data access subroutines
store data in and retrieve data from an array you provide in
your program logic.  In either case the array used must be
large enough to hold one complete row for each relation
accessed.
Attributes which contain text data must be given particular
care.  In general, Hollerith format (left adjusted, blank
filled) is used.  Some textual parameters like those for
data base, relation and attribute names must allow for eight
characters (8H), others like key words such as INT, REAL
etc. must allow room for four characters (4H).  Values of
textual attributes or text strings used in conditional
expressions are passed in an array packed together with
other kinds of information.  Such text strings are left
adjusted with unspecified fill.  The number of words such
text strings occupy depends upon the length of the text
string.  there are special instructions in appropriate
sections on how to pass such attributes.
The application program interface requires you to manage the
data base files.  The data base files must exist on three
properly named logical files before your program can be
executed.
Password checks operate in the application program interface
in much the same way as in the standalone system.  No
password permission is requird for RMOPEN, RMUSER, RMRULE,
or RMTOL.  Read permission is required for all other calls
except RMLOAD and RMPUT  for which modify permission is
required.  Modify permission implies read permission.
3.1  INITIALIZING THE DATA BASE
        CALL RMOPEN  (abname)
        ---------------------
        Input parameter:
           Dbname-- the name of the data base in Hollerith
             format
This routine initializes the internal tables used by RIM and
opens the specified data base by reading the data base
control information into the incore working areas.








                                                   Page 52


                                                       
                                                       


        CALL RMCLOS
        -----------
This routine closes the current data base and copies the
incore working areas to the logical data base files.  This
routine is required (if you have modified the data base)
before your program can access another data base.
3.2  STATUS OF DATA BASE ACTIVITY
When an operation on the data base has been attempted, the
status of the operation is returned to the application
program via the RMSTAT variable in the RIMCOM common block.
This common block must be declared in the calling program as
follows:
        COMMON /RIMCOM/ RMSTAT
        INTEGER RMSTAT
The value of RMSTAT should be checked after each operation.
A non-zero value indicates the operation was not successful.
 as a result, subsequent operations may not function as
expected.  The RMSTAT values and meanings are as follows:
   -1  NO MORE DATA AVAILABLE FOR RETRIEVAL
    0  OK - OPERATION SUCCESSFUL
   10  DATA BASE FILES DO NOT CONTAIN A RIM DATA BASE
   11  DATA BASE NAME DOES NOT MATCH FILE CONTENTS
   12  INCOMPATIBLE DATA BASE FILES (DATE,TIME,ETC)
   13  DATA BASE IS ATTACHED IN READ ONLY MODE
   14  DATA BASE IS BEING UPDATED
   15  DATA BASE FILES ARE NOT LOCAL FILES
   16  DATA BASE HAS BEEN OPENED
   20  UNDEFINED RELATION
   30  UNDEFINED ATTRIBUTE
   40  MORE THAN 10 AND/OR OPERATORS IN THE WHERE CLAUSE
   41  ILLEGAL "LIMIT EQ N" CONDITION
   42  UNRECOGNIZED COMPARISON OPERATOR
   43  EQS ONLY AVAILABLE FOR TEXT ATTRIBUTES
   44  ILLEGAL USE OF MIN/MAX IN THE WHERE CLAUSE
   45  UNRECOGNIZED AN/OR OPERATOR
   46  COMPARED ATTRIBUTES MUST BE THE SAME TYPE/LENGTH
   47  LISTS ARE VALID ONLY FOR EQ AND NE
   50  RMFIND NOT CALLED
   60  RMGET NOT CALLED
   70  RELATION REFERENCE NUMBER OUT OF RANGE
   80  VARIABLE LENGTH ATTRIBUTES MAY NOT BE SORTED
   81  THE NUMBER OF SORTED ATTRIBUTES IS TOO LARGE
   89  SORT SYSTEM ERROR
   90  UNAUTHORIZED RELATION ACCESS
  100  ILLEGAL VARIABLE LENGTH ROW DEFINITION (LOAD/PUT)
  110  UNRECOGNIZED RULE RELATIONS
  111  MORE THAN 10 RULES PER RELATION



                                                   Page 53


                                                       
                                                       


THE FOLLOWING CODES SHOULD NOT BE ENCOUNTERED IN NORMAL USE
   1001 BUFFER SIZE PROBLEM - BLKCHG,BLKDEF
   1002 UNDEFINED BLOCK - BLKLOC
   1003 CANNOT FIND A LARGER B-TREE VALUE - BTADD,PUTDAT
   1004 CANNOT FIND B-TREE BLOCK - BTPUT
   21XX RANDOM FILE ERROR XX ON FILE1
   22XX RANDOM FILE ERROR XX ON FILE2
   23XX RANDOM FILE ERROR XX ON FILE3
   24XX RANDOM FILE ERROR XX ON FILE4
3.3  GENERAL ROUTINES
The following routines are used to set the internal switches
for rule checking, to specify the data base passwords, and
to set the tolerance for real numbers.  These routines may
be called any number of times with the new value overwriting
the current value.
        CALL RMUSER (password)
        ---------------------
        Input Parameters:
          password--the password in Hollerith (8H).
This routine is used to provide the password necessary for
checking data base access, relation read permission and
relation modify premission.
        CALL RMRULE (switch)
        -------------------
        Input Parameters:
         switch--- 0 no rule checking (NOCHECK RULES) (int)
                   1 check rules (CHECK RULES)
This routine turns rule checking on and off (default--on if
rules are defined).
        CALL RMTOL (val,percent)
        ------------------------
        Input Parameters:
         val------the value of the tolerance (real)
         percent--0 if "val" is the absolute tolerance value
                     (int)      
                  1 if "val" is the tolerance percent
This routine sets the tolerance for floating point numbers,
(default: 0.).












                                                   Page 54


                                                       
                                                       


3.4  ACCESSING THE SCHEMA
The following routines are used to obtain information about
the data base schema.
        CALL RMLREL
        -----------
This routine sets an implicit pointer (used by the routine
RMGREL) to the first relation in the data base.  it must be
called before data about any relations may be obtained.  If
there are no relations defined for which the current user
password has read permission, RMSTAT will return 90,
otherwise 0.
   CALL RMGREL (rname,row,mpw,lastmod,numatt,numrows)
   Output Parameters:
     rname---relation name (8H)
     rpw-----read password (.TRUE. or .FALSE.)
     mpw-----modify password (.TRUE. or .FALSE.)
     lastmod-date of last modification of relation data (8H)
     numatt--number of attributes in the relation (int)
     numrows-number of rows of data in the relation (int)
This routine returns the data about the current relation
(the relation indicated by the current pointers) and the
increments the implied pointer to point to the next relation
for which read permission is available.  A successful
execution of this routine sets RMSTAT equal to 0.  I f you
change passwords between calls to RMLREL and RMGREL or
between successive calls to RMGREL, unpredictable results
may occur.  When the last relation is accessed RMSTAT will
be set to -1.
The following example shows how to use RMLREL and RMGREL to
obtain the data about all relations in the data base.
                 .
                 .
                 .
        COMMON /RIMCOM/ RMSTAT
        INTEGER RMSTAT
                 .
                 .
                 .
        CALL RMOPEN (dbname)
        CALL RMUSER (password)
                 .
                 .
                 .
        CALL RMLREL
        IF (RMSTAT.EQ.0) GO TO 100
                 .
                 .



                                                   Page 55


                                                       
                                                       


                 .
    print message that no relations are available
    using the current password
                 .
                 .
                 .
    GO TO 200
100 CONTINUE
    CALL RMGREL(rname,rpw,mpw,lastmod,numatt,numrows)
                 .
                 .
                 .
    printout the data about the relation, etc..........
                 .
                 .
                 .
    GO TO 100
200 CONTINUE
                 .
                 .
                 .
    CALL RMLATT (rname)
    ------------------
    Input Parameters:
       rname --- relation name (8H)
This routine sets an implied pointer to the first attribute
of the specified relation.  if the relation exists and the
current password allows access to relational data, RMSTAT
will return 0.
    CALL RMGATT(aname,type,matvec,var,len1,len2,column,key)
    -------------------------------------------------------
    Output Parameters:
       aname---attribute name (8H)
       type----attribute type (INT,REAL,DOUB,TEXT) (4H)
       matvec--attribute type (VEC or MAT -otherwise
               blank)(4H)
       var-----variable length attribute (.TRUE. or .FALSE.)
       len1----attribute length data as follows (int):
               TEXT-number of characters
               INT,REAL,DOUB,VEC-number of items
               MAT-row dimension
       len2----column location in the relation (int)
               (otherwise 0) (int)
       column--attribute column location in the relation
               (int)
       key-----keyed attribute (.TRUE. or .FALSE.)
This routine returns the data about the current attribute
(the attribute indicated by the implied pointer) and


                                                   Page 56


                                                       
                                                       


increments the implied pointer to point to the next
attribute.  When the last attribute is accessed, RMSTAT will
return -1.
The following example shows the use of RMLREL,RMGREL,RMLATT,
and RMGATT to obtain the data about all attributes for all
realtions.  (the equivalent of LISTREL ALL)
                .
                .
                .
     COMMON /RIMCOM/ RMSTAT
     INTEGER RMSTAT
                .
                .
                .
     CALL RMOPEN(dbname)
     CALL RMUSER(password)
                .
                .
                .
     CALL RMLREL
100  CONTINUE
     CALL RMGREL(rname,rpw,mpw,lastmod,numatt,numrows)
     IF (RMSTAT.NE.0) GO TO 300
     CALL RMLATT(rname)
     DO 200 K=1,numatt
     CALL RMGATT(aname,type,matvec,var,len1,len2,column,key)
     IF(RMSTAT.NE.0) GO TO 300
                .
                .
                .
     printout the relation and attribute data, etc..........
                .
                .
                .
200 CONTINUE
    GO TO 300
300 CONTINUE
                .
                .
                .










                                                   Page 57


                                                       
                                                       


3.5  ACCESSING THE DATA BASE
The routines which access the data base allow the following
operations:
1) GET an existing row of data from aspecified relation and
store it in a local array (must be preceded by a RMFIND).
2) LOAD a new row of data from a local array to the bottom
of a specified relation (must be preceded by a RMFIND).
3) PUT an existing row of data back into a specified
relation after it has been modified (must be preceded by a
RMFIND, RMGET).
4) DELETE an existing row of data from a specified relation
(must be preceded by a RMFIND, RMGET).
Each of the above operations works on one row of data at a
time.  RMGET increments the pointers to point to the next
row.  The initial pointers must be established before the
required operation can be performed (RMFIND).  The rows
returned may be qualified with a WHERE clause (default - all
rows) and the rows may also be returned in a sorted order
(RMGET only).
To support concurrent access to multiple relation, a
parameter is provided to allow the assigning of a number to
identify the set of pointers for a given relation.  In this
way the operations on the data base are related to a number
which in turn corresponds to the pointers for a single
Each of the GET, LOAD, PUT, and DELETE operations work on
one row of data at a time. GET, PUT and DELETE use an
implied row pointer initialized by RMFIND and incremented
by RMGET. You have 6 pointers numbered 0-5 at your disposal.
You may use more than one pointer for a given relation. RMPUT,
which must be preceded by RMGET, simply puts a row back where
it was taken from. RMLOAD, while not specifically using the
pointers from RMFIND, requires a call to RMFIND. In this case
RMFIND simply identifies the relation. RMLOAD adds rows to the
relation, not replacing them like RMPUT.
A call toi RMFIND establishes an implied pointer chain to all
the rows in a relatuion in the internal order of the rows. You may
restrict the number of rows in the implied pointer chain by a call
to RMWHER following the RMFIND call. You may also sort the
rows qualified by the implied pointer chain by calling RMSORT. Thus
for each pointer you want to use, you must first call RMFIND,
then possibly RMWHER and/or RMSORT. You must not call RMGET, RMLOAD,
RMPUT, ro RMDEL between the calls to RMFIND, RMWHER, and RMSORT
unless a new pointer chain is being established.
If a relation is modified (using RMPUT, RMDEL, and RMLOAD), only
one pointer should be in effect for the relation. If more than
one pointer is used, the results are unpredictable.
A pointer may be redefined as many times as desired. Each RMFIND
call redefines the pointer. The logical sequence of RMFIND, RMWHER 


                                                   Page 58


                                                       
                                                       


(optional), RMSORT (optional) calls must be set up prior to
the first call to RMGET. Note that a new RMWHER or RMSORT call
requires a new RMFIND call.
   CALL RMFIND (number,relname)
   ----------------------------
   Input Parameters:
     number---number (0-5) assigns a pointer for the
              relation (int)    
     relname--relation name (8H)
This routine establishes the initial pointer number for a
relation.  A call to RMFIND must be made before calls to
RMGET, RMWHER, RMLOAD, and RMSORT.






































                                                   Page 59


                                                       
                                                       


CALL RMWHER (number,attname,operator,value,numval,nextboo,numboo)
----------------------------------------------------------------
Input Parameters:
  number--number (0-5) identifies the relation pointer for
          this operation (int)
  attname-array of attribute names (may also be attribute
          number, ROWS or LIMIT) where the nth attname
          corresponds to the nth WHERE clause (Hollerith)
  operator-array of operators (EQ,GT,EQA,EXIS,FAIL,etc.)
          where the nth operator corresponds to the nth
          WHERE clause (each 4H)
  value---2-dimensional array of (any type, fixed, or
          variable) where the nth row corresponds to the nth
          WHERE clause
          The organization of the array is dependent on the
          of the array is dependent on the attribute type
          and length.  Let vset represent a list of values
          (in most cases the list has one in vset (see the
          SELECT command).  The rows are organized as
          follows:
          Fixed length attributes--------------------------
           vset(1),vset(2),......,vset(numval)
           where numval is equal to the number o f values in
           the list (note if the EQA condition is used there
           can only be one member in the vset, see the
           SELECT command)
          Variable length attributes------------------------
           TEXT - c(1),0,vset(1),c(2),0,vset(2)............,
                  c(numval),0,vset(numval)
                  where c is the number of characters in the
                  corresponding vset and numval is equal to
                  the number of values in the list.
          INT,REAL,DOUB,VEC - items(1),0,vset(1),items(2),0,
          vset(2)....,items(numval),0,vset(numval)
          where items is the number of items in the
          corresponding vset and numval is equal to the
          number of values in the list
          MAT-rows(1),col(1),vset(1),rows(2),col(2),vset(2),
          ......,rows(numval),col(numval),vset(numval)
          where rows is the number of rows and cols is the
          number of columns in the matrix
Note that a call to RMFIND must precede a call to RMWHER.
  numval-number of values in the list of values (vset) where
         the nth numval corresponds to the nth WHERE clause
         (int array)
  nextboo-array of "AND" "OR" operators (each 4H)
  numboo-number of WHERE conditions (int).
This routine qualifies a set of rows for retrieval (this


                                                   Page 60


                                                       
                                                       


corresponds to the where clause).
For example, if the following WHERE clause were required:
WHERE ATT1 EQ 4 7 12 OR ATT2 EQS "TEXT STRING" AND ATT3 +
GT 5. AND ATT3 EQA ATT4
(ATT1 -- integer length 1)
(ATT2 -- text variable length)
(ATT3 -- real length 1)
(ATT4 -- real length 1)
The arrays would contain:
attname(1)   = 8HATT1
attname(2)   = 8HATT2
attname(3)   = 8HATT3
attname(4)   = 8HATT3
operator(1)  = 4HEQ
operator(2)  = 4HEQS
operator(3)  = 4HGT
operator(4)  = 4HEQA
value(1,1)   = 4
value(1,2)   = 7
value(1,3)   = 12
value(1,4)   = value(1,5) = 0
value(2,1)   = 11
value(2,2)   = 0
value(2,3)   = 4HTEXT
value(2,4)   = 4 H STR
value(2,5)   = 3HING
value(3,1)   = 5.
value(3,2)   = value(3,3) = value(3,4) = value(3,5)=0
value(4,1)   = 4HATT4
value(4,2)   = value(4,3) = value(4,4) = value(4,5)=0
numval(1)    = 3
numval(2)    = 1
numval(3)    = 1
numval(4)    = 1
nextboo(1)   = 4HOR
nextboo(2)   = 4HAND
nextboo(3)   = 4HAND
nextboo(4)   = 0
numboo       = 4
"Value" would be dimensioned (4,5) in the above example.










                                                   Page 61


                                                       
                                                       


CALL RMSORT (number,attname,numsort,sortype)
Input Parameters:
   number --- number (0-5) identifies the pointer for the
              relation sorted (int)
   attname -- array of "numsort" attribute names to sort
              on (each 8H)
   numsort -- number of attributes to sort (int)
   sortype -- sort control numbers, corresponding to
              attname LT 0 causes descending sort,
              GE 0 causes ascending sort (int array)
This routine sorts the data prior to retrieval (this is
equivalent to the SORTED BY clause).
For example, if the following SORTED BY clause were
  required:
    SORTED BY ATT1=A ATT2=A ATT3=D
The array would contain:
        
  attname(1) = 8HATT1
  attname(2) = 8HATT2
  attname(3) = 8HATT3
  sortype(1) = 1
  sortype(2) = 1
  sortype(3) = -1
  numsort  = 3
   CALL RMGET (number,array)
   ------------------------
   Input Parameters:
     Number --- number (0-5) identifies the relation
                pointer for this operation (int).
   Output Parameters:
     Array ---  array to receive the row of data (any type).
                Let "coli" be the column number in the
                relation for the ith attribute (see RMGATT).
                Fixed length attributes--------------------
                 Array (coli) contains the start of the
                 value for the i-th attribute.
                Variable length attributes----------------
                 Array (coli) contains the pointer "N"
                 which points to the start of the attribute
                 data in array.
                Array(N) contains one of the following:
                TEXT - number of characters
                INT,REAL,DOUB,VEC - number of items
                MAT(N+2) ,.....contains attribute values
This routine gets a row of data from the specified relation
and advances the pointer to the next qualifying row (as
determined by RMWHER and RMSORT conditions).



                                                   Page 62


                                                       
                                                       


     The following figure illustrates the organization of fixed and variable
length data in the array. The pointer word, array(p) contains values
as shown. Word p+1 contains 0 or the column dimension for matrix attribute
type.

        Figure 3.5-1 -- Organization of Array

 
     Fixed    Variable        Fixed             Variable Length   Variable
   Length=1    Length       Length=2             Attribute         Length
   Attribute  Attribute   Attribute              Parameters       Attribute
                        /------^--------\
+--+---------+---------+---------+---------+-+---------+---------+---------+-+
|  |         |         |         |         |X|         |         |         | |
>  |    3    |    4    |    5    |    6    |X|    N    |  N+1    |  N+2    | >
<  |         |         |         |         |X|         |         |         | <
|  |         |         |         |         |X|         |         |         | |
+--+---------+---------+---------+---------+-+---------+---------+---------+-+
      VALUE    POINTER   \-------v--------/   /---^---\             VALUE
                              VALUE           * NO. Chars   0
                +---+                           (text)
                | N |                         * NO. Words   0
                +-+-+                           (Int, Real)
                  |                           * NO. Items   0
                  |                             (DOUB, DVEC)
                  |                           * NO. Items   0
                  |                             (Ivec, RVEC)
                  |                           * Row Dimens. Col. Dimens.
                  |                             (Matrix)    (Matrix)
                  |                            \--v--/
                  |                               ^
                  |                               |
                  +-------------------------------+

















                                                   Page 63


                                                       
                                                       


   CALL RMLOAD (number,array)
   -------------------------
   Input Parameters:
     number --- number (0-5) identifies the relation to
                load (int).
     array ---- array containing the row of data to load
                (any type).
                (see RMGET for a description of array)
RMLOAD will load a row of data into a specified relation. Calls
to RMLOAD may be repeated, with each row being loaded at the
bottom of the relation. A call to RMFIND must have preceded
the RMLOAD call to establish the validity of number by
associating it with a relation.
This sequence of calls will modify a row of data in a
specified relation.
    CALL RMGET (number,array)
    ------------------------
              .
              .
              .
    CALL RMDEL (number)
    -------------------
    Input Parameters:
      number --- number (0-5) identifies the relation
                 from which rows are to be deleted (int).
This sequence of calls will delete a row of data in a
specified relation.
Calls to RMPUT and RMDEL must be preceded by calls to RMGET
since neither RMPUT or RMDEL advances the pointer they
operate on to the next row. The RMPUT call works like that
for RMDEL; array in this case is included so the call is


CALL RMPUT (number, array)


     where number is the pointer number 0-5 identifying the
relation to be modified; the row to be modified is established
by a call to RMGET prior to the RMPUT call, and

     array is the array containing the modified row of data.









                                                   Page 64


                                                       
                                                       


RIM Handy Reference Card

DEFINING A DATABASE SCHEMA
         DEFINE dbname
         OWNER password
         ATTRIBUTES
         attname {REAL} [{length}][KEY]
                 INT      VAR
                 TEXT
                 DOUB
                 RVEC
                 IVEC
                 DVEC
         attname {RMAT}  {row,col} [KEY]
                 IMAT     row,VAR
                 DMAT     VAR,VAR
         RELATIONS
         relname WITH attname1 [attname2...]
         PASSWORDS
         {READ PASSWORD} FOR {relname} IS password
         RPW                     ALL
         {MODIFY PASSWORD} FOR {relname} IS password
         MPW                     ALL
         RULES
         attname [IN relname]    {EQ} value [{AND}...]
                                  NE          OR
                                  GT
                                  GE
                                  LT
                                  LE
         attname IN relname      {EQA} attname IN relname [{AND}...]
                                  NEA                       OR
                                  GTA
                                  GEA
                                  LTA
                                  LEA
         END

LOADING A RELATION
         LOAD relname
         value1 value2 ... valueN
         END
         value: SCALARS val1
                TEXT "text string"
                VECTOR (val1, val2, ...)
                MATRIX(r1c1,r2c1,...),(r1c2,r2c2,...)...)

QUERYING A RELATION


                                                   Page 65


                                                       
                                                       


         SELECT {attname1 [=fid1],attname2[=fid2],...} FROM relname +
                 attnum1 [=fid1],...
                 attname1(i),...
                 attname1(i,j)...
                 ALL
                 [SORTED BY attname1 [={A}],[attname2 [={A}]...]]+
                                        D                D
                 [WHERE ...]
         TALLY attname [={A}] FROM relname [WHERE...]
                          D

         WHERE CLAUSE:

         WHERE   attname         {EXISTS}                [{AND}...]
                                  FAILS                    OR
                                  EQS    value
                                  EQ     {value}
                                  NE      MAX
                                  GT      MIN
                                  LT
                                  LE
                                  GE

         WHERE   attname         {EQA}   attname         [{AND}...]
                                  NEA                      OR
                                  GTA
                                  GEA
                                  LTA
                                  LEA

         WHERE   ROWS            {EQ}    rownumber       [{AND}...]
                                  NE                       OR
                                  LT
                                  LE
                                  GE
                                  GT

         WHERE   {attname}       {EQ}    list            [{AND}...]
                  ROWS            NE                       OR

         WHERE   LIMIT           EQ      number          [{AND}...]
                                                           OR
...

QUERYING THE SCHEMA

         LISTREL [relname]
                  ALL


                                                   Page 66


                                                       
                                                       


         EXHIBIT attname1 [attname2...]
         PRINT RULES

COMPUTATION COMMAND

         COMPUTE {COUNT} attname FROM relname [WHERE...]
                  MIN
                  MAX
                  AVE
                  SUM

MODIFICATION COMMANDS

         CHANGE {attname} TO value [IN relname] WHERE ...
                 attname(i)
                 attname(i,j)
         CHANGE {RPW} TO newpass FOR relname
                 MPW
         CHANGE OWNER TO newowner
         DELETE ROWS FROM relname WHERE ...
         DELETE DUPLICATES [attname1,attname2,...] FROM relname
         DELETE RULE rulenumber
         RENAME ATTRIBUTE attname TO newname [IN relname]
         RENAME RELATION relname TO newname
         REMOVE relname

RELATIONAL ALGEBRA COMMANDS

         INTERSECT relname1 WITH relname2 FORMING relname3 +
                 [USING attname1 [attname2,...]]
         JOIN relname1 Using attname1 WITH relname2 USING attname2 +
                 FORMING relname3 [WHERE {EQ}]
                                          NE
                                          GT
                                          GE
                                          LT
                                          LE
         SUBTRACT relname1 FROM relname2 FORMING relname3 +
                 [USING attname1 [attname2,...]]
         PROJECT relname1 FROM relname2 USING +
                 {attname1,[attname2,...]} [WHERE ...]
                  ALL

REPORT COMMANDS

         NEWPAGE
         BLANK n
         TITLE "title"


                                                   Page 67


                                                       
                                                       


         DATE
         LINES n
         WIDTH n

KEY COMMANDS

         BUILD KEY FOR attname IN relname
         DELETE KEY FOR attname IN relname

RIM-TO-RIM COMMAND

         UNLOAD [dbname [=newdbname]]   {SCHEMA} [relname1 [=mpw] +
                                         DATA
                                         ALL
                 [relname2 [=mpw],...]

GENERAL COMMANDS

         INPUT {filename}
                TERMINAL
         OUTPUT {filename}
                TERMINAL
         EXIT
         QUIT
         MENU
         HELP [command name]
         USER password
         ECHO
         NOECHO
         CHECK
         NOCHECK
         TOLERANCE xx.xx [PERCENT]
         RELOAD
         CLOSE

HOST DEPENDENT COMMANDS (note: may be CDC syntax)

         OPEN dbname [=filename],[UN=account],[PW=password],+
                 [DIRECT={R}]
                          W
         ZIP "jet statement"









                                                   Page 68


                                                       
                                                       


                                 Summary of the Application Program Interface
INITIALIZING THE DATA BASE
  CALL RMOPEN (dbname)
         Input parameter:
                 dbname -- the name of the data base in Hollerith format
  CALL RMCLOS

GENERAL ROUTINES
  CALL RMUSER (password)
         Input parameters:
                 password -- the password text
  CALL RMRULE (switch)
         Input parameters:
                 switch -- 0 - no rule checking (Nocheck)
                           1 - check rules (CHECK)
  CALL RMTOL (value,switch)
         Input parameters:
                 value -- the value of the tolerance (real)
                 switch - 0 if "val" is tolerance value (int)
                          1 if "val" is tolerance percent
ACCESSING THE SCHEMA
  CALL RMLREL
  CALL RMGREL(rname,rpw,mpw,lastmod,numatt,numrows)
         Output parameters:
          rname - relation name (text)
          rpw     read password, .TRUE. or .FALSE.
          mpw     modify password, .TRUE. or .FALSE.
          lastmod date of last modification in relation data in
                 yy/mm/dd format
          numatt  number of attributes in relation (int)
          numrows number rows of data in relation (int)
  CALL RMLATT(rname)
         Input parameters:
          rname - relation name in hollerith (text) format
  CALL RMGATT(aname,type,matvec,var,len1,len2,column,key)
         Output parameters:
          aname - attribute name
          type - attribute type (INT, REAL, DOUB, or TEXT)
          matvec- attribute type (VEC or MAT, else blank)
          var    variable length attribute, .TRUE. or .FALSE.
          len1 - attribute length data as follows (int):
                 TEXT - number of characters
                 INT, REAL, DOUB, VEC - number of items
                 MAT - row dimension
         len2 - Column dimension of MAT attributes, otherwise 0 (int)
         column- attribute column location in relation (int)
         key -   keyed attribute (.TRUE. or .FALSE.)



                                                   Page 69


                                                       
                                                       


ACCESSING THE DATA BASE
  CALL RMFIND(number,relname)
         Input parameters:
           number - user assigned number (0-5) used to reference the
                         pointer for the relation (int)
           relname- relation name (characters, H format)
  CALL RMWHER(number,attname,operator,value,numval,nextboo,numboo)
         Input parameters:
           number - number (0-5) which identifies the relation pointer
                 for this operation (int)
           attname - array of attribute names, attribute numbers, the
                 keyword ROWS, or LIMIT
           operator - array of operators (EQ, GT, EQS, EQA, etc.)
           value -  2 dimensional array of WHERE clause "values"
           numval - Number of "values" in list of values
           nextboo - array of "AND" "OR" operators
           numboo - Number of WHERE conditions (int)

  CALL RMSORT(number,attname,numsort,sortype)
         Input parameters:
           number - number (0-5) which identifies the relation pointer
                 for this operation (int)
           attname - array of "numsort" attribute names to sort on
           numsort - number of attributes to sort on (int)
           sortype - sort control numbers: -1 = descending sort,
                         +1 = ascending sort.
  CALL RMGET(number,array)
         Input parameters:
           number - number (0-5) which identifies the relation pointer
                 for this operation (int)
         OUTPUT Parameters:
           array - array to receive the row of data

  CALL RMLOAD(number,array)
         Input parameters:
           number - number (0-5) which identifies the relation pointer
                 for this operation (int)
           array- array containing the row of data to load

  CALL RMPUT(number,array)
         Input parameters:
           number - number (0-5) which identifies the relation pointer
                 for this operation (int)
           array - array containing the modified row of data.

  CALL RMDEL (number)
         Input parameters:
           number - number (0-5) which identifies the relation pointer


                                                   Page 70


                                                       
                                                       


                 to be deleted. (int)




     The following is a small sample program in VAX Fortran to show how
RIM may access the AERODB data base. It prints the following:

1. All information about the schema (LISTREL ALL)

2. The data in the relation REL300 sorted for the airports in
Brazil sorted by descending altitude. CITYNAME is variable length
and the commands are SELECT ALL FROM REL300 SORTED BY ALTITUDE=D
WHERE CITYNAME EQS "BRAZIL".

         LOGICAL RPW,MPW,VAR,KEY
         COMMON/RIMCOM/RMSTAT
         INTEGER RMSTAT
         REAL*8 NAME,LASTMD,NAMEA,NAMEC,IVAR,DB,NAME
         DIMENSION NVAL(20)
         DIMENSION NAMEQS(5)
C OPEN THE DATA BASE
         DBNAME=6HAERODB
         CALL RMOPEN(DBNAME)
C LISTREL ALL
         CALL RMLREL
100      CONTINUE
         CALL RMGREL(NAME,RPW,MPW,LASTMD,NUMATT,NUMROW)
         IF(RMSTAT.NE.0)GOTO 200
         LRP=3HNO 
         IF(RPW) LRP=3HYES
         MRP=3HNO
         IF(MPW)MRP=3HYES
         WRITE(6,110)NAME,LRP,MRP,LASTMD,NUMATT,NUMROW
110      FORMAT(1X,A8,2(1X,A4),1X,A8,2I8)
         CALL RMLATT(NAME)
120      CONTINUE
         CALL RMGATT(NAMEA,ITYPE,MAT,VAR,LEN1,LEN2,NCOL,KEY)
         IF(RMSTAT.NE.0)GOTO 100
         IVAR=5HFIXED
         IF(VAR)IVAR=8HVARIABLE
         IKEY=2HNO
         IF(KEY)IKEY=3HYES
         WRITE(6,130)NAMEA,ITYPE,MAT,IVAR,LEN1,LEN2,NCOL,IKEY)
130      FORMAT(1X,A8,2(1X,A5),1X,A8,3I8,1X,A3)
         GOTO 120
200      CONTINUE
C SELECT ALL FROM REL300 SORTED BY ALTITUDE=D+


                                                   Page 71


                                                       
                                                       


C  WHERE CITYNAME EQS "BRAZIL"
         NAME=6HREL300
         CALL RMFIND(1,NAME)
         IF(RMSTAT.NE.0)GOTO 999
         NAMEQS(1)=6
         NAMEQS(2)=0
         NAMEQS(3)=4HBRAZ
         NAMEQS(4)=2HIL
         NAMEC=8HCITYNAME
         IBOOOP=3HEQS
         CALL RMWHER(1,NAMEC,IBOOOP,NAMEQS,1,0,1)
         IF(RMSTAT.NE.0)GOTO 500
         NAMEA=8HALTITUDE
         CALL RMSORT(1,NAMEA,1,-1)
         IF(RMSTAT.NE.0)GOTO 999
300      CONTINUE
         CALL RMGET(1,NVAL)
         IF(RMSTAT.NE.0)GOTO 500
         NUMX=(NVAL(5)-1)/10+1
         NUMP=6+NUMX
         WRITE(6,400)(NVAL(K),K=1,NUMP)
400      FORMAT(A4,5I6,2X,30A1)
         GOTO 300
500      CONTINUE
         IF(RMSTAT.LT.0)GOTO 1000
999      CONTINUE
         WRITE(6,9001)RMSTAT
9001     FORMAT(' RMSTAT:',I5)
C CLOSE THE DATA BASE
1000     CONTINUE
         CALL RMCLOS
         STOP
         END

















                                                   Page 72


                                                       
                                                       


                                                  LIMITATIONS

     There is no limit on the number of rows of a relation except disk size.

     A row in a relation must fit in 1021 words. If len(i) is the fixed length
(in words) of the ith attribute and var(j) is the length (in words) of
the jth variable length attribute, then
SUM(len(i) for i=1 to max)+sum((var(j)+3) for j=1 to max) must be less
than 1021. This can mean that relations that fit on 60 bit
machines may not fit on 32 bit machines.

     A relation or attribute name must not begin with the character string
"RMRUL".

     The following words may not be used in attribute or relation names:
TO, FROM, BY, USING, WHERE, IN, FORMING, ROWS, LIMIT, DUPLICATE.
Also, names must not be a substring of the above
which is 3 characters or more long starting with the first
character. Thus FOR and FORM are illegal, however FORT is OK.

     In loading data, the value of the first attribute, if it is text,
is limited as follows:
If the relation contains only 1 or 2 attributes, then the following
text strings and their RIM substrings are not allowed as values for
the first attribute:
CHECK, NOCHECK, ECHO, NOECHO, END, HELP, INPUT, OUTPUT, QUIT.
If the relation contains three attributes then the value for the
first attribute may not be HELP or HEL.

     The number of items in one command may not exceed 100.

     The number of rules specified for one relation may not exceed 10.

     The number of conditions used in the SELECT WHERE clause may not
exceed 10.















                                                   Page 73


                                                       
                                                       


                                  Entering Input with the RIM User Interface

     The following discusses the reading and parsing of commands and
data in the standalone system.

     The RIM user interface is a free-field input routine used by the RIM
standalone system which separates user input into items which are
grouped into records.

                                                  Terminology

     1.   LINE - One line of information with a maximum of 80 characters
         including blanks.

     2.   ITEM - One piece of information. An item may be a real number,
         an integer or text. Items are delimited by blanks or commas. Multiple
         blanks count as a single blank. Multiple commas generate null items.

     3.   RECORD - A collection or list of up to 100 items entered in
         response to a single request for data by the calling program.

     4.   INTEGER - all characters must be numeric except that the first
         may be a + or - sign. For example: -1 23 +10000

     5.   REAL - An item of the form I1.I2EI3 where I1 and I3 may be
         signed integers and I2 is an unsigned integer. The entire form is
         not necessary but at least one digit and the . or two digits
         separated by the E are required.

     6.   TEXT - Any single item that is not integer or real. If a text
         item looks like an integer or real it must be enclosed in quotes (").

                                               Composing Records

     Ordinarily records consist of one line. However multiple records may be put
on a line by separating them with dollars or semicolons. Alternatively,
a record may span several lines by ending all but the last line with a
plus. Items must be wholly contained on one line with the exception of
quoted text items and comments.
                                            Special Items - +,(, )

     Equals and left and right parentheses are treated as single items
unless enclosed in quoted text items. Thus a=3. is 3 items, two
text and one real rather than one. "a=3." is one item.
                                                Multiple Commas

     If more than one comma separates 2 items, each additional comma
will generate a text item with 3 characters, "-0-".


                                                   Page 74


                                                       
                                                       


                                             Rules for Text Items

     A quoted text item is terminated by a record separator (dollar
or semicolon). Quoted text items may be continued on multiple
lines. If the trailing quote is omitted on the last item in a
record, the quoted item is terminated at the record separator, if
any, or the last nonblank character on the line. Quotes may be included
in quoted text strings by doubling the quotes (e.g., "a,""b"
yields a,"b as a text string). The total number of characters for all
text strings in a record is limited to 2000.
                                                   Comments

     Comments may be included anywhere in the input stream by enclosing them
between *( and ). For example *( this is a comment). Comments are
completely ignored by the user interface. Empty lines between records
are ignored and may be used to paragraph input. An alternative form
of comment is */ ... / which may be used if you need to have parentheses
inside the comment.
                                                DATA GENERATION

     Activities such as entering large volumes of data can be eased by
using the data generation facilities.

     REPEATING ITEMS ON PREVIOUS RECORD

     A data item of the form *n where n is an unsigned integer, indicates
that the next n items are identical to the corresponding n items in
the previous record.
An isolated * is taken as *1. Double asterisks (**) indicate
that the remaining items in the previous record are to be copied
to the current record.

     REPEATING AN ITEM IN THE CURRENT RECORD - *=N, *=N+STEP

     An item of the form *=n, where n is an unsigned integer, indicates
that the next n items are identical to the immediately preceding
item. An item of the form *=n+step or *=n-step, where step is an
unsigned real or integer, indicates that the next n items are to
be generated by consecutively incrementing the immediately preceding
item.

     GENERATING MULTIPLE RECORDS *+N

     A record beginning with *+n where n is an unsigned integer indicates
that the next n records are to be generated from the preceding
record. Each item of the generated record is formed by adding an
item of the *+n record to the corresponding item of the immediately
preceding record. A zero (integer) item should be inserted


                                                   Page 75


                                                       
                                                       


in an *+n record for text items in the preceding record. The number of
items after the *+n must match the number in the preceding record.

                                           Notes on Generating Items

     When increments are specified, either on the *+n record or as
step on an *=n+step item they must match the item thye are
incrementing in type. It should be noted that the *+n record
generation optuion is based on the expanded representation of
the previous record. The generation does not operate on the card
image of the preceding record if it contains data generation items.
Therefore it is not possible to repeat or increment an asterisk-type
item.

                                                   Examples

     Consider the following 7 input records to illustrate data generation
features:

1 2 3 4 5 6 7 8 9 10 11 12
2 1 *2 4 *=2 1 *=2+2 **
*+1 0 *=3 0 *=5 **
*+1 0 *=11
*+1 *12
*+1 **
**

     Twelve data items are defined by each of these records. Each of the
last six records is translated into the same internal record which
is: 2 1 3 4 4 4 4 1 3 5 11 12
Note - the last 5 records could be replaced by the single record
*+5 **
instead.


                                          Changing Special Characters

     It is possible to change the special characters the user interface
uses to break apart records. These special characters may either be
changed to others or set to null so they are ignored. This is useful
for reading specially formatted files or to allow special characters
to appear as input in text items. To change special characters enter
the following special comment as the only entry on a line between
records:

*(SET KEYWORD=newvalue)

where KEYWORD can be DOLLAR, SEMI, QUOTES, BLANK, PLUS, or COMMA


                                                   Page 76


                                                       
                                                       


and newvalue is either the word NULL or the new special character.
For example if one wanted to use dollar to delimit items rather
than records and not to have commas delimit items one would enter:

*(SET DOLLAR=NULL)
*(SET COMMA=$)

 and commas could now be used in unquoted text strings. Note the function
is altered, so for example the + sign still has its usual function
in real numbers. To restore the original delimiters one could say:

*(SET DOLLAR=$)
*(SET COMMA=,)





































                                                   Page 77


                                                       
                                                       




















































                                                   Page 78


                                                     INDEX





ATTRIBUTES   19

BLANK Command   43
BUILD KEY Command   36

CHANGE Command   33
CHANGE OWNER Command   34
CHANGE PASSWORD Command   36
CLOSE Command   16
COMPUTE Command   32

Data Base Creation Option   47
Data Base Update Option   47
DATE Command   43
Define RELATIONS   20
Define RULES   21
Define Submodule Commands   19, 22
DELETE DUPLICATES Command   34
DELETE KEY Command   36
DELETE ROW Command   33

ECHO Command   17
EXHIBIT Command   31
EXIT Command   18

HELP Command   13

INPUT Command   16
INTERSECT Command   37

JOIN Command   39

LINES Command   43
LISTREL Command   31
Load Submodule Commands   23

MENU Command   15

NEWPAGE Command   43
NOCHECK Command   18
NOECHO Command   17

OPEN Command   16
OUTPUT Command   17
OWNER password   19



                                                   Page X-1


                                                       
                                                       


PRINT RULES Command   32
PROJECT Command   40

Query Option   47

RELOAD Command   18
REMOVE Command   36
RENAME Attribute Command   34
RENAME RELATION Command   36

SELECT command   25, 26, 27
SUBTRACT Command   41

TALLY Command   30
TITLE Command   43
TOLERANCE Command   17
Type1 Attributes   20
Type2 Attributes   20

UNLOAD Command   44
USER Command   16

WIDTH Command   43



























                                                   Page X-2